## Slide 1: Did the recession impact recent decreases in observed sulfate concentrations?
Shao-Hang Chu,
US EPA/OAQPS/AQAD
October, 2011

## Slide 2: Introduction
Purpose: to examine whether the recent economic recession had an impact on the accelerated sulfate decreases observed in 2008 and 2009.
Since Sulfate = f (SO2 emissions and meteorology), a meteorological adjustment technique was first applied to remove the influence of “atypical” meteorology conditions on sulfate concentrations.
Combustion of sulfur-containing fossil fuels, such as coal and oil, leads to
---> SO2 formation, and oxidation of SO2 results in
---> formation of sulfate aerosols in ambient air.
Fossil fuel consumption is closely related to various economic activities: such as electric energy usage, industrial production, transportation, etc.
Comparing the meteorologically-adjusted sulfate trend with observed SO2 emission changes shed the light on whether the accelerated sulfate decline in 2008 and 2009 is a result of :
    Non-conducive meteorological conditions, and/or
    Reduced SO2 emissions due to control measures, and/or
    Decreased power demand in economic recessions, or
    All of the above.

## Slide 4: Percent Change in Sulfate Concentrations and SO2 Emissions Nationwide Data: US EPA 2010

## Slide 5: Data
In this study, we choose to analyze the annual 95th percentile of the daily sulfate concentrations because they tend to be more sensitive to the variation of meteorology and other influencing factors.
24-hour-average sulfate data collected by the CSN monitoring network from 2002 to 2009 in 45 major urban areas in the US were analyzed. The data collection frequency was 1-in-3 days.
2002-2009 meteorological data from NCDC were acquired for this analysis. Among them daily maximum temperature, daily average relative humidity, wind speed, dew point, precipitation, and one day pollutant transport distance were used in meteorology-adjustment calculations.
Acid Rain Program (ARP) and Clean Air Interstate Rule (CAIR) SO2 emissions data, ARP heat input data, and Federal Reserve published Industrial Production Index data were also used in this analysis to assess how much impact lower demand of power in economic recession has on observed sulfate reduction.

## Slide 6: Analysis Approach
In this study, a Quantile Regression model was used to adjust the influence of ‘atypical’ meteorology conditions on the observed annual 95th percentile of sulfate concentrations.
In this study, ARP heat input data of power generating units nationwide were used as a surrogate to reflect electric power demand.
To examine the potential factors influencing the accelerated sulfate decline in 2008 and 2009 in 45 major urban areas nationwide, the 2002-2009 meteorologically-adjusted sulfate concentrations were calculated and an “expected” 2009 sulfate level for each site was also estimated by linear extrapolation of the meteorology-adjusted values based only on 2002-2007 data.
Together with the nationwide SO2 data, ARP and CAIR SO2 data, ARP heat input data, and Federal Reserve published Industrial Production Index data, we studied the differences among the “expected”, meteorologically-adjusted, and observed sulfate concentrations to assess what the major factors were leading to the large decline in observed sulfate concentrations in 2008 and 2009.

## Slide 7: 2007-2009 Sulfate Decrease in Eastern US Due to Meteorology and Emission Changes

## Slide 8: 2007-2009 Sulfate Decrease in Eastern US Due to Meteorology and Emission Changes

## Slide 9: 2007-2009 Sulfate Decrease in Western US Due to Meteorology and Emission Changes

## Slide 10: Changes in 95th Percentile Sulfate 45 Major Urban Areas, Nationwide

## Slide 11: Changes in 95th Percentile Sulfate 30 Major Urban Areas, Eastern US

## Slide 12: Changes in 95th Percentile Sulfate 15 Major Urban Areas, Western US

## Slide 13: SO2 Emissions and Heat Input Trend Nationwide Data: US EPA 2010, 2011

## Slide 14: Federal Reserve's Monthly Index of Industrial Production

## Slide 15: Actual and Projected Percent Changes in SO2 Emissions and Heat Input Data: US EPA 2011

## Slide 16: Impact of Lower Power Demand in 2008-2009 Recession on Accelerated SO2 Emission Decline Data: US EPA 2010
2007 ARP SO2 Emission Rate (ER)
ER07 = 0.64 lb/MMBTU
= 3.2 x 10-4 TON/MMBTU
ARP Heat Input Change Nationwide from 2007 to 2009
DHI = HI2009 - HI2007
= (24.971 – 27.744) x 109 MMBTU
= - 2.773 x 109 MMBTU --- Heat Input Reduction --> Reduced Power Demand
SO2 Emission Change due to Heat Input Decrease from 2007 to 2009 (ER = ER07)
DEHI = ER07 x DHI
= - 8.8736 x 105 TON --- SO2 Emission Decrease due to Lower Power Demand
Observed Total ARP SO2 Emission Decrease Nationwide from 2007 to 2009
DETOT = E2009 - E2007
= (5.724 – 8.934) x 106 TON
= - 3.21 x 106 TON
Percent SO2 Reduction due to lower power Demand in 2008 and 2009 Nationwide
PRHI = 100% x DEHI / DETOT
= 27.64%

## Slide 17: Summary and Discussions
2002-2009 sulfate concentration data in 45 major urban areas in the US have been analyzed. The results indicate that both meteorology and SO2 emission decreases were responsible for the accelerated sulfate decline observed in most urban areas in the US in 2008 and 2009.
  Comparing the long-term SO2 trends with Industrial Production Index and heat input data nationwide, we find:
    Regulations to curb excessive SO2 emissions in the past have not prevented growth of industrial production and electric power usage nationwide.
    An accelerated decline in SO2 emissions from 2008 to 2009 was caused in part by a lower demand for power as evidence in the 10 percent drop in heat input nationwide.
    Had the overall SO2 emission rate remained unchanged from 2007 to 2009, the overall drop in power demand would have resulted in an approximately a 28 % reduction of the total SO2 decreases during this period.

## Slide 18: Summary and Discussions - Continued
  Since SO2 is the precursor to ambient sulfate formation, thus we believe that the reduced power demand during economic recession in 2008 and 2009 have resulted in an approximately 28% of the observed decreases in sulfate concentrations nationwide.
  However, since the sulfate data length from the Chemical Speciation Network are relatively short, the uncertainty of this analysis could be large.
  Further study of recession impact on air quality using longer data records, such as O3 and SO2, are in progress.

## Slide 19: 2007-2009 Sulfate Decrease in Eastern US Due to Meteorology and Emission Changes

## Slide 20: 2007-2009 Sulfate Decrease in Eastern US Due to Meteorology and Emission Changes

## Slide 21: Annual Emissions and Heat Input Acid Rain Program Data: US EPA 2011
YEAR P M SO2 NOX CO2 HEAT INPUT
TONS TONS TONS MMBTU
1995 ARP 12 11,829,936.3 5,839,018.8 2,157,600,978.2 21,755,824,833
1996 ARP 12 12,513,447.4 6,011,296.4 2,231,447,822.7 22,684,158,801
1997 ARP 12 12,942,514.1 6,026,523.6 2,298,376,051.2 23,692,782,506
1998 ARP 12 13,092,853.1 5,966,781.1 2,375,973,376.6 24,831,589,582
1999 ARP 12 12,452,657.2 5,497,118.4 2,385,362,558.9 24,941,902,496
2000 ARP 12 11,202,078.2 5,104,597.4 2,451,484,188.9 25,616,168,438
2001 ARP 12 10,638,086.3 4,707,296.0 2,394,618,120.0 25,244,784,760
2002 ARP 12 10,196,209.9 4,474,615.8 2,423,678,751.1 25,709,497,623
2003 ARP 12 10,594,972.2 4,169,664.6 2,465,544,529.9 26,005,443,914
2004 ARP 12 10,259,212.0 3,763,579.4 2,478,286,032.4 26,353,364,531
2005 ARP 12 10,222,639.0 3,633,349.7 2,539,935,930.3 27,139,944,551
2006 ARP 12 9,392,502.0 3,409,277.7 2,493,325,796.9 26,770,962,742
2007 ARP 12 8,933,517.1 3,283,722.5 2,565,234,238.1 27,744,783,726
2008 ARP 12 7,616,448.7 2,996,593.5 2,517,468,265.7 27,006,801,688
2009 ARP 12 5,724,185.2 1,984,338.9 2,295,922,096.6 24,971,425,330
2010 ARP 12 5,119,750.6 2,061,064.1 2,431,416,282.8 26,473,818,754

## Slide 22: Emission Rate by Fuel Type Data: US EPA 2010
Fuel Type | 2005 |  | 2006 |  | 2007 |  | 2008 |  | 2009 | 
 | SO2 | NOx | SO2 | NOx | SO2 | NOx | SO2 | NOx | SO2 | NOx
Coal | 0.95 | 0.32 | 0.90 | 0.31 | 0.84 | 0.30 | 0.74 | 0.28 | 0.63 | 0.20
Gas | 0.01 | 0.05 | <0.01 | 0.05 | <0.01 | 0.04 | <0.01 | 0.04 | <0.01 | 0.04
Oil | 0.70 | 0.26 | 0.47 | 0.22 | 0.49 | 0.22 | 0.35 | 0.19 | 0.30 | 0.17
Other | 0.27 | 0.42 | 0.29 | 0.29 | 0.26 | 0.20 | 0.28 | 0.16 | 0.27 | 0.11
Total | 0.75 | 0.27 | 0.70 | 0.25 | 0.64 | 0.24 | 0.56 | 0.22 | 0.46 | 0.16

## Slide 23: Percent Change in Fuel Consumption and SO2 Emissions Data: US EPA 2010, EIA 2010
YEAR |  | TOTAL FOSSIL FUEL CONSUMPTION | TOTAL SO2 EMISSIONS | ARP SO2 EMISSIONS
1990 |  | 84 | 179 | 176
2000 |  | 98 | 127 | 125
2005 |  | 100 | 114 | 114
2006 |  | 98 | 105 | 105
2007 |  | 100 | 100 | 100
2008 |  | 97 | 89 | 85
2009 |  | 91 | 73 | 64