## Slide 1: Regional/Global Modeling of PRB Ozone Over the US
Chris Emery, Jaegun Jung, Greg Yarwood, Ralph Morris
ENVIRON International Corporation, Novato, CA
Nicole Downey
Earth System Sciences, LLC, Houston, TX
10th Annual CMAS Conference, October 26, 2011

## Slide 2: Introduction
“Policy Relevant Background” (PRB) Ozone
  Now “North American Background” in 2nd Draft ISA
  Ozone resulting from:
    All natural sources (e.g., biogenic, fires, lightning, global CH4)
    Anthropogenic sources outside North America (no US/Canada/Mexico)
EPA has relied on GEOS-Chem for PRB estimates
  E.g., Fiore et al. (2002,2003), Wang et al. (2009), Zhang et al. (2011)
  Observational research suggests global models:
    Under estimate PRB peaks, short-term variability
    Under estimate stratospheric influence
  Are these still valid criticisms?
  Do high resolution regional models alter PRB estimates?

## Slide 3: Overview
Global modeling using GEOS-Chem:
  Provide boundary conditions for regional modeling
  Simulate base and PRB ozone, sensitivity to:
    Various emission sources, future projections
Regional modeling using CAMx and CMAQ
  Compare base and PRB ozone to GEOS-Chem
    Higher resolution (transport dynamics, emissions, chemistry)
    Independent met/emissions datasets
    Different chemistry and wet/dry removal mechanisms
  “Stratosphere” defined by boundary conditions

## Slide 4: GEOS-Chem Setup
GEOS-Chem v8.3.1 (May 2010) run for 2006
  22.5 resolution, 47 layers, 43 gas/PM species
  GEOS-5 meteorology (3/6-hourly)
  Standard emission inputs, plus:
    Doubled Korea/Japan NOx (code mods from Lin Zhang)
  Standard algorithms/chemistry (LINOZ stratosphere)
  Spinup from July 2005 (IC’s distributed with model)
Two runs:
  North American anthro emissions included (base run)
  North American anthro emissions removed (PRB run)
    Turn off US, Canada, Mexico anthro emissions (model flags)
    Zero shipping, aircraft, biofuel, ag/fertilizer NOx emissions (code mods from Lin Zhang)

## Slide 5: CAMx/CMAQ Setup
CAMx v5.30, CMAQ v4.7.1 run for 2006
  Nested grids, 34 vertical layers to 50 mb (~20 km)
    36 km North American domain (CAMx only)
    12 km western and eastern nests (CAMx & CMAQ )
  Boundary conditions:
    36 km from 3-hourly GEOS-Chem
    12 km from 1-hourly CAMx 36 km
  Standard algorithms/chemistry (CB05)
  Meteorology & emissions from EPA/ORD @ 12-km resolution (1-hourly AQMEII-NA)
  Updated: O&G development emissions in Rocky Mountain area
  Added: lightning NOx from 12-km WRF meteorology
Two runs:
  North American anthro emissions included (base run)
  North American anthro emissions removed (PRB run)

## Slide 6: CAMx/CMAQ Modeling Domains and Evaluation Sites
25 CASTNET ozone sites
Ozonesondes

## Slide 7: Annual 4th Highest MDA8 Base Case

## Slide 8: Model Performance – GC vs. CAMx Paired Predictions(x,t) vs. Observations

## Slide 9: Un-paired Frequency of High Ozone GC vs. CAMx
GC over predicts frequencies in central and eastern US
Both models under predict frequencies in the west
CAMx performs better at highest ozone in the Rockies

## Slide 10: Season-Average Ozonesonde Profiles Observed, GC, CAMx, CMAQ

## Slide 11: Annual 4th Highest MDA8 PRB Run – GC and CAMx
Fires
Fires Removed

## Slide 12: Annual 4th Highest MDA8 PRB Run – CAMx and CMAQ

## Slide 13: PRB Range by Observed Ozone – GC vs. CAMx

## Slide 14: Summary of Results
Base model performance (CAMx vs. GC)
  Obvious differences due to resolution
  CAMx predict highest peaks better, higher correlation
    Higher resolution improves emissions, chemistry, STE transport
  GC tends to over predict means, under predict peaks
    Lower resolution over mixes fresh emissions
  Models are more similar in Rockies
    Too much lightning NOx?
  Preliminary: CMAQ is very similar to CAMx
    CMAQ > CAMx in west, CAMx > CMAQ in east

## Slide 15: Summary of Results
PRB predictions
  Typical range: CAMx = 25-50 ppb, GC = 20-45 ppb
  Full PRB range is much larger:
    Fires and STE increase short-term PRB to 60-100 ppb
    GEOS-Chem PRB never exceeds 60 ppb
  CAMx > GC in west, Rockies by 10-15 ppb
  CAMx ~ GC in central, CAMx > GC east by 5-10 ppb
  CAMx has +PRB slope against obs
    Agrees with Zhang et al (2011) using hi-res GC
  GC has +PRB slope against obs everywhere except east
    Agrees with Fiore et al (2003) using low-res GC
  Preliminary: CMAQ is very similar to CAMx

## Slide 16: Areas for future research
Lightning NOx
  Activity keyed to simulated convection
Wildfire emissions
  Convective/shading influences?
Stratospheric influences:
  Do regional models need an externally defined top BC(x,t)?
  Currently assumed: top BC = top layer concentration

## Slide 17: Thank You
Acknowledgements:
This work is funded by the American Petroleum Institute
Thanks to Harvard GEOS-Chem group for assistance
EPA/ORD provided AQMEII met & emissions