## Slide 1: Overview of the Two-way Coupled WRF-CMAQ Modeling System
Rohit Mathur, Jonathan Pleim, David Wong, Tanya Otte, Rob Gilliam, Shawn Roselle, Jeff Young
Atmospheric Modeling and Analysis Division, NERL, U.S. EPA
Frank Binkowski, Aijun Xiu
Institute for the Environment, UNC

## Slide 2: 2-Way Coupled Meteorology/Air Quality Modeling: Rationale
Concurrent meteorology and chemistry-transport calculation
  High frequency communication between dynamical and chemical calculations
    Requisite for finer scale urban modeling/exposure applications
      Higher temporal integration (Dt << 1 hour) is necessary at finer horizontal grid resolutions (Dx < 10 km).
      Such high rates of data exchange are not practical using I/O disk files
Represent and assess the potentially important radiative effects of pollutant loading on simulated dynamical features and air quality
  Many compounds contribute to poor air quality as well as climate change (e.g., O3 and aerosols)
  Need tools to simultaneously address both issues and their interactions
Consistent treatment of dynamical processes in meteorological and AQ models; reduces redundant calculations

## Slide 3: Air Quality-Climate Interactions Optical and Radiative Characteristics of Aerosols
Direct effects
    Light scattering aerosols (e.g., sulfate)
      Backscatter incoming solar
      Reduce radiation impinging on the Earth’s surface
      cool the surface (negative surface forcing)
      Increase radiation reflected to space
      cool the top of the atmosphere (negative TOA forcing)
    Light absorbing aerosols (e.g., black carbon/soot)
      Absorb incoming solar
      Reduce radiation impinging on the Earth’s surface
      cool the surface (negative surface forcing)
      Absorb outgoing solar reflected from surface and clouds
      Reduce radiation reflected to space
      Warm the top of the atmosphere (positive TOA forcing)
Indirect effects
  Changes in cloud formation and duration resulting from scattering and absorption
  Aerosols act as CCN; impact cloud optical thickness; impact cloud lifetime
Shaocai Yu’s presentation tomorrow

## Slide 4
Flexible design of model coupling allows
data exchange through memory resident buffer-files
flexibility in frequency of coupling
identical on-line and off-line computational paradigms with minimal code changes
both WRF and CMAQ models to evolve independently;
Maintains integrity of WRF and CMAQ
Two-Way Coupled WRF-CMAQ Modeling System: Design and Model Features
Aerosol Optics & Feedbacks
Volume weighted refractive indices
for each wavelength based on
- Composition and size distribution
- SO42-, NO3-, NH4+, Na+, Cl-, EC, POA,
anthropogenic and biogenic SOA,
other primary, water
Both RRTMG and CAM Shortwave
radiation schemes in WRF
Effects of aerosol scattering and
absorption on photolysis
Effects of O3 on long-wave radiation
More on model structure: David Wong’s presentation tomorrow

## Slide 5
Surface PM2.5
Aerosol Optical Depth
Surface SW Reduction
PBL Reduction
Increase in BL pollution (PM2.5)
July 14, 2006 21Z

## Slide 6: Direct Effects on Shortwave Radiation Reaching the Surface With and Without Feedbacks Is the signal detectable relative to measurements?
Slight cooling and better agreement with measurements noted in simulation with aerosol feed-backs

## Slide 7: California Wildfires A High aerosol Loading Case
Widespread wildfires resulted in significant PM pollution during mid/late June 2008 in California and surrounding states
Fuel loading: National Fire DangerRating (NFDR) system
Emission Factors: Fire Emission Production Simulator (FEPS)
Function of fuel class
6/25/08
6/27/08
Without Fires Emissions
With Fires Emissions
Daily-avg. PM2.5

## Slide 8
More pronounced reduction in shortwave radiation due to aerosol loading
Including aerosol direct forcing improves simulation of SW radiation
Shortwave Radiation Reaching the Surface With and Without Feedbacks Comparison with measurements at ISIS site at Hanford, CA
June 26 June 27

## Slide 9
Diurnal Temperature Range (DTR) Proxy for variability in surface solar radiation
Comparison with observed range at site
impacted by wildfire plume
Difference in DTR
w/Feedback – w/o Feedback
June 28, 2008
Reduction in bias in simulated DTR
More widespread observations of DTR could be used to assess aerosol effects

## Slide 10
Without Feedbacks
Maximum 8-hr. O3: June 27 2008
Enhancement due to feedback
at locations where [O3] > 75ppb
With Feedback
Reduction in PBL heights results in increased O3
Feedback effects could have important air quality impacts

## Slide 11
March Average
2006
MODIS AOD
Reduction in surface solar radiation
Reduction in 2M Temperature
Reduction in PBL Height
Model AOD
Looking Ahead:
Spatial Heterogeneity in Aerosol Effects over the Northern Hemisphere
“Dimming”
“Cooling”
“Suppressed ventilation”

## Slide 12
Model AOD
MODIS
Reduction in surface solar radiation
Reduction in 2M Temperature
“Dimming”
“Cooling”
Reduction in PBL Height
“Suppressed ventilation”
Aerosol Radiative Effects: Asia
March 2006 average

## Slide 13
Looking Ahead:
Can models capture past trends in aerosol loading and associated radiative effects?
1989-1991
2007-2009
USEPA/CAMD
Title IV of the CAA achieved significant reductions in SO2 and NOx emissions from EGUs since the 1980s
Tropospheric SO42- burden has reduced significantly
Multi-year WRF-CMAQ simulations to assess the responsiveness of the model to Title IV emission changes are now being set-up
Decrease in AOD
Increase in Surface SW
ΔAOD > 0.4
Preliminary Results:
Can the associated increase in surface solar radiation be detected in the measurements and models (“brightening effect”)

## Slide 14: Summary
Air quality and climate issues are inherently linked
  Spatial and temporal variability of short-lived radiatively active species need to be accurately characterized
A computationally efficient and flexible coupled meteorology-atmospheric chemistry modeling system based on the WRF and CMAQ models has been developed
Direct feedback of aerosols on SW radiation has been tested
  Effects can be large in regions with significant aerosol loading
  Preliminary comparisons with limited measurements show improvements in simulation skill for SW radiation and 2m T
  Air pollutant concentrations can be significantly increased due to reductions in PBL height
Challenge: Assessing the magnitude and directionality of feedback effects on simulated air quality