## Slide 1: The WRF-CMAQ Two-way Coupled Modeling System: Development and Results from Initial Applications
David Wong, Rohit Mathur, Jonathan Pleim, Francis Binkowski, Tanya Otte, Rob Gilliam, Aijun Xiu, Shawn Roselle, Jeffrey Young
Atmospheric Modeling and Analysis Division, NERL, U.S. EPA
CMAS 2011 Conference
Chapel Hill, NC
Oct 24-26, 2011

## Slide 2: Motivation
lack of feedback of atmospheric pollutant loading on simulated dynamics
excessive temporal interpolation of coarsely saved meteorological data
repeated reading and writing of data to/from intermediate files, resulting in reduced data accuracy due to truncation error

## Slide 3: Twoway Model Domain

## Slide 4: Domain Decomposition
RSL-lite
CMAQ

## Slide 5: Twoway Model Execution Sequence

## Slide 6: Execution Performance
 | Execution time | 
 | CAM | RRTMG
WRF only MCIP Offline CMAQ Loose couple system, Total time | 0:19:59 0:02:31 1:18:28 1:40:58 | 0:18:50 0:02:31 1:19:05 1:40:26
Coupling system w/o feedback and call frequency ratio 5:1 | 1:41:12 | 1:48:59
Coupling system w/ feedback and call frequency ratio 5:1 | 1:43:39 | 2:54:25

## Slide 7: Execution Performance (cont’d)
Processor configuration | CAM |  |  |  | RRTMG |  |  | 
 | w/o feedback | speedup | w/ feedback | speedup | w/o feedback | Speedup | w/ feedback | speedup
4x8 | 2:05:06 |  | 2:08:21 |  | 2:13:17 |  | 3:19:25 | 
8x8 | 1:19:46 | 1.57 | 1:21:57 | 1.57 | 1:24:12 | 1.58 | 1:58:21 | 1.68
8x16 | 0:55:28 | 2.26 | 0:55:12 | 2.33 | 0:56:38 | 2.35 | 1:14:14 | 2.69

## Slide 8: General Information
Twoway model (release version) is built using WRF 3.3 and CMAQ 5.0. It requires the latest libraries: IOAPI version 3.1, STENEX and PARIO.
In only implemented with the EM core.
It only supports CAM and RRTMG radiation schemes.
It does not support chemical mechanism, saprc99 and aerosol dynamics, AE5.
Long wave aerosol direct effect has been implemented but has not been thoroughly evaluated. It is considered a research option.

## Slide 9: Environment Variable
RUN_CMAQ_DRIVER | turn on CMAQ portion of the twoway model (default is F)
DO_SW_CAL | turn on short-wave feedback calculation (default is F)
WRF_CMAQ_FREQ | WRF and CMAQ calling frequency (default is 1)
WRF_COL_DIM | WRF west_east_stag dimension size
WRF_ROW_DIM | WRF south_north_stag dimension size
WRF_LAY_DIM | WRF bottom_top_stag dimension size
CMAQ_COL_DIM | number of columns in the CMAQ domain
CMAQ_ROW_DIM | number of rows in the CMAQ domain
TWOWAY_DELTA_X | distance between the WRF and CMAQ lower left corner in the x-direction (default is 5)
TWOWAY_DELTA_Y | distance between the WRF and CMAQ lower left corner in the y-direction (default is 5)
WRF_LC_REF_LAT | Lambert conformal reference latitude
IOAPI_OFFSET_64 | turn of 64bit offset in IOAPI library (default is F)

## Slide 10: Environment Variable (cont’d)
DO_LW_CAL | turn on long-wave feedback calculation (default is F)
CREATE_PHYSICAL_FILE | create intermediate meteorological data for diagnostic purposes (default is F)
FILE_TIME_STEP | time step size of the physical meteorological output file (default = 10000)
SD_TIME_SERIES | turn on sub-domain monitoring capability (default is F)
SD_SCOL | sub-domain starting column
SD_ECOL | sub-domain ending column
SD_SROW | sub-domain starting row
SD_EROW | sub-domain ending row
SD_CONC_SPCS | sub-domain monitoring species list

## Slide 11: Construct the Twoway Model
It requires WRF 3.3, CMAQ 5.0 and Twoway package
Release notes contains detail procedure to construct the twoway model
It also contains a sample of run script

## Slide 12: CA Fire Test Case
Jun 20 – 29, 2008
12km
WRF 3.1 + CMAQ 4.7.1

## Slide 13: CA Fire Test Case (cont’d)

## Slide 14: CA Fire Test Case (cont’d)

## Slide 15: WRF-CMAQ w/feedback minus WRF-CMAQ w/o feedback
15
O3 PM2.5
SW T-2m PBL
Substantial changes in O3 and
PM2.5 due to changes in radiation
and its effect on the PBL evolution

## Slide 16: Summary and Future Work
The impact of the aerosol feedback has been shown.
The twoway model performs in a scalable way and the feedback does not cost much.
Examine the direct aerosol effects using a closed set of aerosol and radiation observations from the DOE/ARM Southern Great Plains site.
Study the impact of ozone on long wave radiation.
Improving the computational efficiency of the more accurate Mie scheme.
Study the aerosol indirect effect.