## Slide 1: Estimation of human exposure to PM2.5 components in U.S. metro areas Using routine measurements and CMAQ!
Prakash V. Bhave, Mary K. McCabe, Valerie C. Garcia
Atmospheric Modeling & Analysis Division
U.S. EPA, Office of Research & Development
CMAS Conference
Chapel Hill, NC
October 28 – 30, 2013

## Slide 2
Take-Home Messages from CMAS 2010 Special Session
Land-use Regression (LUR) is most popular method for estimating exposure beyond central-site monitor -L.Sheppard
AQ Modelers should focus on ↑ spatial resolution; temporal not a major need –M.Brauer
Solutions:
Hybrid of CMAQ+AERMOD, CMAQ+RLINE
Run CMAQ at finer scales (e.g., 4km or 1km)
But…
these don’t take advantage of our strength in modeling @regional scales
within-city monitoring of PM2.5 and O3 is fairy dense – how much value can our models add over LUR or spatial kriging?

## Slide 3: Health Impact of PM2.5 Varies by Region
Ref. Dominici, F. et al. JAMA 2006

## Slide 4: Within-Region Variability
Ref. Franklin, M. et al. JESEE 2007

## Slide 5: Recent Investigations
Baxter, Franklin, Ozkaynak, et al. The use of improved exposure factors in the interpretation of PM2.5 epidemiological results, Air Qual. Atmos. Health, 2013.
Baxter, Duvall, & Sacks. Examining the effects of air pollution composition on within region differences in PM2.5 mortality risk estimates, JESEE, 2012.
Major obstacle:
Routine observations of PM2.5 composition are very limited. Of 139 U.S. cities with chemical speciation network (CSN) sites, only 15 have >1 site.

## Slide 6: Hypothesis
For many locations and chemical species, the PM2.5 composition at a single CSN site is an inadequate estimate of the ambient concentrations across the metropolitan area, for assessing the compositional effects on within-region differences in PM2.5 mortality risk estimates

## Slide 7: Methods
Ambient Measurements
  PM2.5 CSN measurements in 2006 (24h obs, 1-in-3 or 1-in-6)
  Subset data which are only site in their core-based statistical area (CBSA)
  Compute annual avg conc of each species at each site
Model Simulation
  CMAQ v5.0.1 with default options (e.g., CB05tucl, AERO6, ACM2)
  2006 calendar-year simulation
  12km ConUS domain – 459 ×299 × 35 layers
  Emissions: evaluation version D of 2008 NEI w. year-specific fire, mobile, biogenic, & point EGU
  Meteorology: WRF v3.4
  Computed annual avg con for each PM2.5 species (n = 15) in each surface-layer grid cell (n = 137,241) from hourly CMAQ output
  Multiplicative bias correction for each CBSA and species
  Excluded cases where model & obs differed by > 3×
Population Data
  2000 Census block-level data projected to 2005 and aggregated to 12km CMAQ grid cells

## Slide 8: Example of Results
CSN Measurement 4.16 µg/m3
Raw Data
Phoenix-Mesa-Glendale contains exactly 1 CSN monitor.
At that site, the annual-average OC = 4.16 µg/m3 in 2006.

## Slide 9: Example of Results
Area average = 0.71 µg/m3
Raw Data
CMAQ Model Output
CSN Measurement 4.16 µg/m3
CMAQ model provides an estimate of spatial variability in OC across the metro area.
After bias correction, avg. conc. = 0.71 µg/m3. much lower than CSN measurement!
3.0 – 5.0
1.5 – 3.0
1.0 – 1.5
0.5 – 1.0
0.3 – 0.5

## Slide 10: Example of Results
Population Density (km-2)
Area average = 0.71 µg/m3
Raw Data
CMAQ Model Output
0 – 160
161 – 530
531 – 1107
1108 – 1863
3.0 – 5.0
1.5 – 3.0
1.0 – 1.5
0.5 – 1.0
0.3 – 0.5
CSN Measurement 4.16 µg/m3
Population average = 2.24 µg/m3
But population density is correlated with OC concentration.
Accounting for spatial variation in air concentrations & population density, we obtain a more accurate estimate of the average exposure across this metro area.
Population-Averaged Exposure Measurement Error (due to spatial variability) = +1.92 µg/m3
*Using CMAQ, we calculate this error for 14 species across all metro areas with a single CSN site

## Slide 11: Exposure Measurement Error for Organic Carbon in PM2.5
-1.0
+1.0
0
(µg/m3)
* Substantial inter-city variability in exposure measurement error can now be accounted for in large-scale, population-based epidemiological studies
SO4err = +0.63 µg/m3 in Baton Rouge, LA
NO3err = +2.95 µg/m3 in Riverside, CA
Tierr = -8.1 ng/m3 in Colorado Springs

## Slide 12: Summary & Future Work
Exposure measurement error due to spatial variability in ambient concs was estimated fro 15 PM2.5 species in >100 metro areas across the U.S.
Error was typically positive (871 out of 1280 cases studied), because most CSN monitors are in urban center
Errors can be quite large (e.g., OCerr = +1.92 μg/m3 in Phoenix)
Future work: incorporate these exposure errors in future epi studies that investigate the influence of PM2.5 composition on mortality risk.