## Slide 1
Intercomparison of secondary organic aerosol models based on SOA/Ox ratio
Yu Morino, Kiyoshi Tanabe, Kei Sato, and Toshimasa Ohara
National Institute for Environmental Studies, Japan
The 12th Annual CMAS Conference, October 29, 2013
ーContentsー
１．Introduction － SOA modelling in Tokyo
２．Methodology － Box model settings
３．Results － Model evaluation / Source contributions
４．Summary
ーAcknowledgementー
Funds： Grant-in-Aid for Scientific Research from the Japan Society for the Promotion of Science (23710024)
Environment Research and Technology Development Fund (C-1001)
Obs. data： Prof. Y. Kondo and Prof. N. Takegawa (Univ. Tokyo)

## Slide 2: PM2.5 in Japan (2001-2010, annual average)
Urban (N=12)
Rural (N=5)
Roadside (N=16)
Ministry of Environment [2012]
2001 2002 2003 2004 2005 2006 2007 2008 2009 2010
PM2.5 environmental standard in Japan (Sept. 2009 ‒)
Annual mean: 15 μg m-3
Daily mean: 35 μg m-3
１．Introduction

## Slide 3
①Average PM2.5 was higher than 15 μgm-3 in western Japan
Western Japan
Eastern Japan
(including Tokyo Metropolitan Area)
% daily PM2.5
> 35 μgm-3
# daily PM2.5
> 70 μgm-3
Monthly average
PM2.5 (μgm-3)
# Stations×day
2010
2011
2012
2013
１．Introduction
PM2.5 in Japan (2010-2013, monthly average)
Ministry of
Environment [2013]
②Daily PM2.5 exceeds environmental standard in all the seasons.
②Spring
④Autumn
①Winter
②Spring
④Autumn
②Spring
②Spring
②Spring
③Summer
①Winter
Notes: http://www.env.go.jp/air/osen/pm/conf/conf01-04/mat01_2.pdf

## Slide 4: SOA modelling in Tokyo Metropolican Area (Case study in summer 2007)
K | 
Model intercomparison of PM2.5 species (Morino et al., JSAE, 2010)
(CMAQ v4.7.1 and CMAQ 4.6 were used.)
All models significantly underestimated OA.
S1: Komae, S2: Kisai, S3: Maebashi, S4: Tsukuba
１．Introduction
Organic aerosol
Fossil-SOA: Underestimation by a factor of 6-8
Model evaluation of fossil- and biogenic SOA (Morino et al., ES&T, 2010)
(CMAQ –MADRID was used.)
Biogenic-SOA: Underestimation by a factor of 1.5 - 2

## Slide 5
Merit 1：
Merit 2：
SOA (V)
POA
VOC
Emission sources
SVOC1
cond./
evapo.
oxidation
VBS model
Yield model
emis.
emis.
SOA (I/S)
aging
aging
SVOC1
SVOC2
SVOC3
cond./
evapo.
cond./
evapo.
emis.
SVOC3
aging
SVOC2
aging
cond./
evapo.
Merit 1
Merit 2
Simulate primary emissions and oxidation (aging) of SVOC/IVOC (semi-/intermediate- VOC)
Simulate aging processes of oxidation products from VOCs
SOA model development – Volatility basis-set (VBS) model
１．Introduction

## Slide 6
ARO1 + OH = 0.224*HO2 + 0.765*RO2_R + 0.011*RO2_N + 0.055*PROD2
+0.118*GLY + 0.119*MGLY + 0.017*PHEN + 0.207*CRES
+ 0.059*BALD + 0.491*DCB1 + 0.108*DCB2 + 0.051*DCB3
+0.071*TOLAER1 + 0.138*TOLAER2
Yield model
(SAPRC99-AERO4)
UR24
UR25
UR26
etc.
CACM (caltech chemical mechanism)
MCM
(master chemical mechanism)
Near-explicit model
–Explicitly simulate multi-generation reactions
SOA model development – Chemical modules
１．Introduction

## Slide 7
Intercomparison of five SOA models (of different frameworks) to evaluate their characteristics and performance
Preliminary evaluation of volatility basis-set (VBS) model on OA simulation in Tokyo Metropolitan Area
Characteristics of this study | 
Intercomparison of SOA models | A few previous studies of SOA model intercomparison (particularly including both MCM and VBS models)
Box model simulation | Many sensitivity simulations can be made (advantage for MCM calculations)
Evaluation using SOA/Oｘ ratio | Model evaluation less affected by uncertainties of meteorological fields
Comparison for Tokyo data | OA was accurately measured by AMS/sunset-TOT Good correlation between Oｘ and SOA Behaviors of VOC and O3 are well understood
Objectives
１．Introduction

## Slide 8: SOA models
 | # Gas | # reaction | # SVOC | # primary VOCs | Aerosol model | References
MCM v3.2 | 5731 | 16933 | 1902#2 | 105 , | Pankow | Jenkin et al., 2003; Saunders et al., 2003
CACM-MADRID2 | 366 | 366 | 43 | 17 , | MADRID2 | Griffin et al., 2002; Pun et al., 2002
SAPRC99-AERO4 | 79 | 214 | 10 | 24 , | AERO4 | Binkowski and Roselle, 2003
SAPRC99-AERO5 | 88 | 224 | 12 | 24 , | AERO5 | Carlton et al., 2010
SAPRC99-VBS | 92 | 214#3 | 9 | 33 , | VBS | Tsimpidi et al., 2010
#1: estimate of this study、#2: C* ≤ 100 mgm3、#3: exclude aging reactions |  |  |  |  |  | 
Five SOA models simulated in this study
MCM, CACM-MADRID: explicitly simulate multi-generation oxidation.
  - Vapor pressures used in the MCM model was calculated by EPI-Suite (Stein and Brown method). Kp was multiplied by a actor of 500 (Johnson et al., 2006).
AERO4, AERO5: Yield model
VBS: Grouping of SVOC and IVOC based on volatility (~vapor pressure).
  - Speciation of emitted SVOC/IVOC and aging reaction rates was the same with Tsimpidi et al. (2010).
from CMAQ-MADRID
CMAQ v4.6
CMAQ v4.7.1
2. Methodology

## Slide 9: Box model framework
Processes | One box model (domain: 30 x 30 km2, Fig.) including chemical, aerosol, emission, and air mass exchange.
Target period | July 22 – August 12, 2004
Other conditions | Meteo. param. (T, RH, WS, BLH): observational data Background: 20 ppbv for O3, NMHC is from Morino et al. (2011)
Domain
Emissions | EAGrid2000 (Kannari et al., 2007)
Speciation of VOC | Vehicles：JATOP (2012) Evaporative：Ministry of Env. (2003) # VOC emission data are firstly classified for MCM. Then, SAPRC/CACM data are prepared.
Observetion | Period: July 24 – Aug 14, 2004 Site: RCAST, Tokyo Univ # OA and OOA were measured by AMS (Takegawa et al., 2006).
2. Methodology
Obs. site

## Slide 10: Comparison of experimental data and model simulation —high NOx condition
m-xylene
toluene
Obs.
VBS
AERO5
AERO4
Yi: SOA production yield Kom,i：Partitioning coefficient
M0: OA concentration ai: stoichiometric coefficient
○Standard
×No aging
Model simulation of chamber experiment (aromatics VOC + NOx + HONO)
Aging process enhanced SOA production yield was enhanced by a factor of 1.3 ~ 1.5.
3. Results

## Slide 11: Comparison of experimental data and model simulation —high NOx condition
m-xylene
toluene
Obs.
VBS
AERO5
AERO4
○Standard
×No aging
■reduced Yi
Model simulation of chamber experiment (aromatics VOC + NOx + HONO)
Aging process enhanced SOA production yield was enhanced by a factor of 1.3 ~ 1.5.
→ Yi should be reduced by 30-50% to avoid double counting.
Yi: SOA production yield Kom,i：Partitioning coefficient
M0: OA concentration ai: stoichiometric coefficient
3. Results

## Slide 12
O3 and NOx were well reproduced.
OH were reproduced, while HO2 were underestimated.
→ should be examined in future studies.
HNO3 were overestimated. (dry deposition)
Model evaluation in ambient condition – gaseous species
3. Results
OH
HO2
NO2
HNO3
O3
NO

## Slide 13
Under VOC limited condition (e.g., urban area), VOCs+OH reactions are rate-limiting for Ox(=O3+NO2) and SOA production.
Ox production rate:
SOA production rate：
Ratio of SOA and Ox production rate
Ki : VOC+OH reaction rate
Αi : # of HO2,RO2 generated from VOC+OH reaction
Fi : Fraction of RO2 which produce NO2
Yi : SOA production yield
Obs.
S=0.155 mgm-3/ppbv
VBS
S=0.108
CACM
S=0.046
AERO5
AERO4
MCM
S=0.004
VBS —Standard
S=0.108
VBS —Reduced yield
S=0.084
VBS —No aging
S=0.005
AERO5 S=0.016
AERO4 S=0.010
Obs.
S=0.155 mgm-3/ppbv
=
SOA formation potential of VOC
Ox formation potential of VOC
Model evaluation using SOA/Ox ratio
3. Results

## Slide 14
Intercomparison of volatility (C*) distributions
3. Results
Saturation concentration
Saturation concentration
SOA
(aerosol)
SVOC
(gas)
SOA+SVOC
(total)
SOA
SOA+SVOC
Continuous C* distributions in VBS and MCM.
MCM simulated very small [SOA+SVOC] with C*<10 μgm-3.
(aerosol/total)

## Slide 15
Contributions of precursors/sources to Ox and SOA
Contributions of precursor VOCs were estimate from sensitivity simulations (20% recuction of each VOC).
OLE
SVOC
ARO
Contributions of
each precursor VOC
ARO
OLE
others
ALK
Contributions of
emission sources
Vehicles
Paint
Fugitive
Paint
Vehicles
Print
3. Results

## Slide 16: Summary
Five organic aerosol models (MCM, CACM SAPRC99-AERO4, SAPRC99-AERO5, SAPRC99-VBS) were compared using a box model.
Aging reactions enhanced SOA production yield by a factor of 1.3 ~ 1.5 under conditions of chamber experiments. SOA production yield should be reduced by 30-50% to avoid double counting.
SOA/Ox ratio was well reproduced by the VBS model, while other models significantly underestimated the observed ratio.
Source contributions to ambient SOA concentration largely differed among the five models. Choice of SOA model is critical in the source apportionment of SOA.
4. Summay

## Slide 18
モデルー観測データの比較 (VOC成分)
３．結果 －ボックスモデル計算結果、寄与解析
上記の比較を基に、VOCの排出量を補正。右図は補正後のVOC濃度。測定成分(C5H8を除いた14成分)のみ補正した点に注意
MCM, CACM, SAPRC99で芳香族濃度が異なるのは、グルーピングが異なり、OHとの反応速度も異なるため
NMHC濃度の観測値とモデル計算結果
(期間平均濃度、ppbv)
VOC成分の日変動