## Slide 1
George Delic , Ph.D.
HiPERiSM Consulting, LLC
(919)484-9803
P.O. Box 569,
Chapel Hill, NC 27514
george@hiperism.com
http://www.hiperism.com
HiPERiSM Consulting, LLC.

## Slide 2
George Delic
HiPERiSM Consulting, LLC
NEW STRATEGIES FOR IMPROVING PERFORMANCE AND PRECISION IN CMAQ AND GMI MODELS
13th Annual CMAS Conference,
Chapel Hill, NC
27 October, 2013

## Slide 3: Overview: CMAQ from HiPERiSM and the U.S. EPA with Gear solver
  Overview: CMAQ from HiPERiSM and the U.S. EPA
  Hardware platforms, compilers, and episode studied
  Time used by science process in a 24 hour simulation
  JSPARSE versus FSPARSE versions of CMAQ Gear solver
  BLOCKS of cells versus single CELL versions of FSPARSE
  Thread parallel performance metrics
  CMAQ performance with 1 MPI process
  CMAQ performance with 1-8 MPI processes
  Numerical error in U.S. EPA code
  Lessons learned
  Conclusions
  Next Steps for CMAQ development

## Slide 4: Hardware platforms
  Intel: 2x4-core CPU’s = 8 cores
    W5590 Nehalem™
    3.3 GHz
  AMD: 4x12-core CPU’s = 48 cores
    6176SE Opteron™
    2.3 GHz

## Slide 5: Software and compilers
  OS
    Linux 64-bit
  CMAQ versions (Gear solver*)
    U.S. EPA’s uses JSPARSE (serial)
    HiPERiSM uses FSPARSE (parallel)
  Compilers (legend)
    Intel 12.1 (ifort/Intel)
    Portland 13.4 (pgf90)
(*) Requires a sparse linear solver in a linear system Ax=y for chemistry solution: FSPARSE replaces JSPARSE

## Slide 6: Episode studied
  Grid used
    279 X 240 Eastern US domain at 12 Km grid spacing and 34 vertical layers
  CMAQ 4.7.1 24-hour episode
    August 09, 2006, using the CB05 mechanism with Chlorine extensions and the Aero 4 version for PM modeling.
    total output file size: ~ 37.7 GB (137 variables)

## Slide 7: Fraction of total time in 12 x 24 calls (pgf90 on Intel node, 24hr run)
OVERALL: CHEM (60%), AERO (16%), VDIFF (14%)
Chart: 

## Slide 8: JSPARSE version of GEAR
Order all cells in the grid into blocks of cells having similar stiffness
  Disadvantage: this requires a memory copy of concentrations from an array dimensioned by column, row, and level, into a linear array (*)
Gear algorithm is applied to a block of grid cells simultaneously
  Disadvantage: the convergence criterion uses an RMS error over all cells in a block.
(*) This leads to excessive data translation look-aside buffer (TLB) data cache misses that stalls the CPU

## Slide 9: FSPARSE versions of GEAR
BLOCK version of GEAR-HC
  Disadvantages:
    applies blocking of cells and stiffness ordering
    RMS error estimate for each block of cells
CELL version of GEAR-HC
  Advantages:
    no stiffness ordering needed
    the convergence criterion is applied to each individual cell in the grid domain

## Slide 10: CELL version of GEAR
C$OMP DO SCHEDULE (DYNAMIC,MY_CHUNK)
blk_col: DO COL = 1, MY_NCOLS
blk_row: DO ROW = 1, MY_NROWS
blk_lev: DO LEV = 1, NLAYS
………[ call CHEM for a cell ]
END DO blk_lev
END DO blk_row
END DO blk_col
Apply a thread parallel region over a grid column index

## Slide 11: Thread parallel performance metrics
  SPEEDUP:
    U.S. EPA time / thread parallel time
  PARALLEL SCALING:
    1-thread time / p-thread time

## Slide 12: pgf90 compiler on Intel platform (24hr run 1 MPI process)
Chart: 
Chart: 
← CHEM (Gear) wall clock time (seconds) for EPA and GEAR-HC with 1 to 8 threads in CELL version
Parallel CHEM (GEAR-HC) speedup versus EPA for 1 to 8 threads →

## Slide 13: pgf90 compiler on Intel platform (24hr run 1 MPI process)
Chart: 
Chart: 
← CHEM (Gear) wall clock time (hours) for EPA and GEAR-HC with 1 to 8 threads in BLOCK and CELL versions
Parallel CHEM (GEAR-HC) speedup versus EPA for 1 to 8 threads in BLOCK and CELL versions →

## Slide 14: pgf90 compiler on Intel platform (24hr run 1-8 MPI processes)
Chart: 
← CHEM (Gear) wall clock time (hours) for EPA and GEAR-HC with 6 & 8 threads in BLOCK and CELL versions
Parallel CHEM (GEAR-HC) speedup versus EPA for 6 & 8 threads in BLOCK and CELL versions →

## Slide 15: Numerical error in U.S. EPA code
Uses mixed mode arithmetic (DP & SP)
Inconsistent promotion of SP to DP for constants and variables
Worst case in CALCKS for thermal and photolytic reaction rates computed in SP
Inherited SP values amplify precision loss in solve stages
Use of ATOL = 1E-09 is moot

## Slide 16: Lessons learned
Speed up over EPA version ~1.5 with 8 threads (NP=8)
Speed up over EPA ~1.7 with 6 threads (NP=4)
CELL version offers more precision in Gear convergence
  BLOCK version enhances them
  CELL version improves memory model and diminishes them
Performance benefits of FSPARSE
Memory model and TLB data cache misses

## Slide 17: Conclusions
CMAQ computational performance shows ~1.5 to ~1.7 speedup in a thread parallel model for the Gear solver when compared to the U.S. EPA release
The FSPARSE in CELL algorithm yields more precision in a sparse matrix chemistry solver when compared to the U.S. EPA release
The FSPARSE algorithm offers performance gains that are portable across platforms and compilers

## Slide 18: Next steps for CMAQ development
Short term goals
  OpenMP parallel model extensions to other code portions of CMAQ
  Explore port of FSPARSE to GPGPU technology
Long term goals
  Plan for code architecture (re)design throughout the whole of CMAQ to change the memory footprint & increase computational efficiency