## Slide 1: Preliminary comparisons between WRF/CMAQ and in-situ trace gas observations during the Houston, TX deployment of DISCOVER-AQ
Melanie Follette-Cook
Christopher Loughner (ESSIC, UMD)
Kenneth Pickering (NASA GSFC)
CMAS Conference October 27-29, 2014

## Slide 2: Deriving Information on Surface conditions from Column and Vertically Resolved Observations Relevant to Air Quality (DISCOVER-AQ)
Four deployments
  MD – Jul 2011
  CA – Jan/Feb 2013
  TX – Sep 2013
  CO – Jul/Aug 2014
Houston, TX campaign
  9 flight days
  99 missed approaches at four airports
  195 in-situ aircraft profiles
    ~24 per ground site
  Other measurements
    14 Pandoras
    16 Aeronet
    3 EPA NO2 sites
    Ship in Galveston Bay
    3 mobile vans
    TX AQRP ground sites
A NASA Earth Venture campaign intended to improve the interpretation of satellite observations to diagnose near-surface conditions related to air quality

## Slide 3
Continuous lidar mapping of aerosols with HSRL on board B-200
Continuous mapping of trace gas columns with ACAM on board B-200
In situ profiling over surface measurement sites with P-3B
Continuous monitoring of trace gases and aerosols at surface sites to include both in situ and column-integrated quantities
Surface lidar and balloon soundings
DISCOVER-AQ Deployment Strategy
Systematic and concurrent observation of column-integrated, surface, and vertically-resolved distributions of aerosols and trace gases relevant to air quality as they evolve throughout the day.

## Slide 4: Deriving Information on Surface conditions from Column and Vertically Resolved Observations Relevant to Air Quality (DISCOVER-AQ)
Four deployments
  MD – Jul 2011
  CA – Jan/Feb 2013
  TX – Sep 2013
  CO – Jul/Aug 2014
Houston, TX campaign
  9 flight days
  99 missed approaches at four airports
  195 in-situ aircraft profiles
    ~24 per ground site
  Other measurements
    14 Pandoras
    16 Aeronet
    3 EPA NO2 sites
    Ship in Galveston Bay
    3 mobile vans
    TX AQRP ground sites
A NASA Earth Venture campaign intended to improve the interpretation of satellite observations to diagnose near-surface conditions related to air quality

## Slide 5: Daily 1-Hour Max Ozone (ppbv) – All Stations
Relatively clean 3 flight days
Moderate pollution 4
Strongly polluted 2
Chart: Daily 1-Hour Max Ozone (ppbv)
 | 58 | 50 | 77 | 87 | 67 | 56 | 48 | 55 | 78 | 55 | 61 | 79 | 80 | 77 | 38 | 55 | 50 | 59 | 34 | 27 | 39 | 50 | 89 | 58 | 151 | 101 | 77 | 52 | 34 | 50
#1
#2
#3
#4
#5
#6
#7
#8
#9
clouds, heavy
rains, marine air
bay, sea breezes
following cold front
September 1st – 30th

## Slide 6: WRF/CMAQ Simulation
Time period:
28 August –
2 October, 2013
Re-initialize WRF every 3 days
Length of each WRF run: 3.5 days (first 12 hours of each run is discarded)
Initial and Boundary Conditions: North American Regional Reanalysis and MOZART Chemical Transport Model
CMAQ run offline
36 km
12 km
4 km

## Slide 7
Weather Research and Forecasting (WRF) Version 3.6.1 Model Options | 
Radiation | LW: RRTM; SW: Goddard
Surface Layer | Pleim-Xiu
Land Surface Model | Pleim-Xiu
Boundary Layer | ACM2
Cumulus | Kain-Fritsch
Microphysics | WSM-6
Nudging | Observational and analysis nudging
Damping | Vertical velocity and gravity waves damped at top of modeling domain
SSTs | Multi-scale Ultra-high Resolution (MUR) sea surface temperature analysis (~1 km resolution)
CMAQ Version 5.0.2 Model Options | 
Chemical Mechanism | CB05
Aerosols | AE5
Dry deposition | M3DRY
Vertical diffusion | ACM2
Emissions | 2012 TCEQ anthropogenic emissions BEIS calculated within CMAQ

## Slide 8
Preliminary CMAQ evaluation
  DISCOVER-AQ dataset
    Multiple instrument platforms (aircraft in-situ and remote sensing, profiling instruments, and ground based in-situ and remote sensing instruments)
    Variety of meteorological and air quality conditions during the course of each month-long campaign
    Consistent flight patterns result in large sample size
  Ideal for in-depth model evaluation
  The data shown here are in-situ measurements from the P-3B aircraft
    60 sec averages (rather than the native 1 sec resolution) for a more appropriate comparison to the 4 km CMAQ output
  The observations have been collocated in space and time with the CMAQ output

## Slide 9: Ozone
PBL
Median % bias = 0.7 %
FT
Median % bias = -0.8 %
Model over estimated two very clean mornings (9/4 and 9/24) and underestimated severe pollution episode on 9/25
Overall, the model performs well with respect to ozone

## Slide 10
Model output profile following the flight
Data from P3-B
(60 sec average shown)
Model PBL height
9/24/2013
Deep clean layer up to 3 km not captured by model
9/25/2013
Bay breeze not strong enough
(See Loughner et al., presentation tomorrow)

## Slide 11: Ozone
Underestimated enhanced ozone in FT from probable stratospheric intrusion
High ozone corresponds with very dry layer. Most likely stratospheric in origin.

## Slide 12: CO
PBL
Median % bias = -10 %
FT
Median % bias = 6.4 %
Similar to O3, model over estimates CO on very clean mornings and underestimates severe pollution episode on 9/25

## Slide 13: NO2
PBL
Median % bias = -24 %
FT
Median % bias = -16 %
In MD, mobile source emissions were overestimated by as much as 50% (Anderson et al. 2014)
Underestimation shown here could be the result of:
  Texas emissions too low
  Conversion to reservoir species too rapid
Pollution episode on 9/25 also a problem for NO2

## Slide 14: NO
PBL
Median % bias = -40 %
FT
Median % bias = -22 %

## Slide 15: HCHO and Isoprene
PBL
Median % bias = -30 %
PBL
Median % bias = -38 %
Low bias in HCHO could be due to the low bias in isoprene from BEIS

## Slide 16: Overall Median % Biases
 | Overall | PBL | FT
O3 | -0.3 | 0.7 | -0.8
CO | -0.31 | -10 | 6.4
NO2 | -19 | -24 | -16
NO | -32 | -40 | -22
HCHO | -13 | -30 | 3.1
Isoprene | -67 | -38 | -97

## Slide 17: Summary
  In-situ P-3B observations taken during the Houston, TX DISCOVER-AQ deployment were averaged to a temporal resolution of 60 sec to compare with a month-long CMAQ simulation
  CMAQ O3 and CO compared very well with the P-3B observations, with median % biases of < 1% for O3 and <10% for CO
    However, high bias observed on two very clean mornings
    Bay/sea breeze on 9/25 too weak, leading to a low bias in most species
  CMAQ significantly underestimated PBL HCHO and isoprene
    BEIS underestimating isoprene?
  CMAQ also underestimated NOx, but further analysis is required to determine the cause
  Next steps:
    Further evaluation using other DISCOVER-AQ observations
      Ozonesondes, ACAM, Pandora, etc.
    Meteorological sensitivity simulations to examine whether we can improve the meteorology to better capture the pollution event on 9/25/2013