## Slide 1: Global Particulate Matter (PM10 and PM2.5) Emissions from Agricultural Tilling and Harvesting
1 Northeast Institute of Geography and Agroecology, Chinese Academy of Science, Changchun, China 2 Air Resources Lab. (ARL), NOAA Center for Weather and Climate Prediction (NCWCP), College Park, MD
3 Cooperative Institute for Climate & Satellites, University of Maryland, College Park, MD
4 Center for Spatial Information Science and Systems, George Mason University, Fairfax, VA
Wednesday 29 October 2014, Chapel Hill, NC
Weiwei Chen1,2, Daniel.Tong2,3,4

## Slide 2: Objectives
Developing agricultural dust emission inventory:
1. Magnitude
How much PM10 and PM2.5 are annually released?
2. Characteristics
How are the spatial and temporal distributions of emissions?
3. Uncertainty
What are the potential challenges in the inventory?

## Slide 3: PM emissions from agricultural operations
Controlling factors:
Operation types
Soil silt
Soil moisture
Wind speed
Dust impacts:
Air quality
Climate
Human health
Soil degradation

## Slide 4: Method
Emission Algorithm
EF: kg PM10 per acre of operation activity; A: crop area; P: pass times; c: conservation operations; k: PM2.5 coefficient factor
Operation specific
Emission Factors
(EF_opt)
Crop Calendar
(Number of passes)
Crop specific
Emission Factor
(EF_crop)
Crop specific
Acres
Crop specific
Emissions
Crop types
Combined Dust Emission
Meteorology Adjustment
Agricultural Dust Emissions
Workflow to estimate Ag. emission
Input Data
1. Crop areas
Wheat, corn, soybean, barley, millet, potato, rice…
2. Crop calendars
Start and end time and duration for planting and harvesting
3. Emission factors
Tilling, planting, harvesting
4. Others
soil silt, monthly soil moisture, wind speed

## Slide 5: Crop Areas and Calendars
1. Crop Area: Spatial Production Allocation Model (SPAM), SPAM2000v3.02 (You L et al., 2006); crop type: 20; resolution: 5 arc-minute
2. Crop Calendar: Crop planting dates: an analysis of global patterns (William et al., 2010); crop type: 19; resolution: 1 degree
Planting areas
Wheat distribution

## Slide 6: Emission Factors (EF)
EF sources: EPA ; CARB, EEA ,CA (based on field operations); publications
Large range of EF for different tilling operations: 0.1-14 kg PM10 ha-1
EF in dry climate are 10 or 5 times than wet climate
CARB: California Air Resource Board
EEA: Europe Environment Agency

## Slide 7
EFs increase with increasing soil silt, wind speed and decreasing soil moisture (Wang et al., 2010)
Soil moisture is the dominant factor for EF
Sand and clay
Silt and EF
Soil moisture
Emission factor
~35%
< 10%
Wind speed
Emission factor
6 m s-1
Adjustment method: four steps
1. Basic EF: e.g., 5.17 kg ha-2 for joint tilling operation in dry climate condition
2. soil silt content: EF_silt <- EF × soil silt*0.6
3. soil moisture:
M <= 15%, CF=1.0; M > 15% & M <=20 % CF=0.6; M > 25% & M < =30%, CF=0.1; M > 30%, CF=0.1
4. wind speed:
WS >= 6 m s-1, CF=1.5; WS >= 4 & WS <6, CF=1; WS >=2 & WS <4, CF=0.6; WS <=2, CF=0.3
EF adjustment by soil and climate factors

## Slide 8
Crop type | Tillage (kg PM10 ha-1) | Planting/Cutting (kg PM10 ha-1) | Harvest* (kg PM10 ha-1)
wheat | 5.17 | 1.35 | 6.57/2.36
Winter-wheat | 5.17 | 1.35 | 6.5/2.34
maize | 5.17 | 1.35 | 1.88/0.68
Maize2 | 5.17 | 1.35 | 1.88/0.68
soybean | 5.17 | 1.35 | 1.88/0.68
Rice | 1.35 | 0 | 1.88/0.68
Rice2 | 1.35 | 0 | 1.88/0.68
sorghum | 5.17 | 1.35 | 6.5/2.34
Winter-sorghum | 5.17 | 1.35 | 6.5/2.34
cotton | 5.17 | 1.35 | 3.77/1.36
barley | 5.17 | 1.35 | 6.5/2.34
Millet | 5.17 | 1.35 | 1.88/0.68
Potato | 5.17 | 0.34 | 1.88/0.68
Winter-barley | 5.17 | 1.35 | 6.5/2.34
Groundnut | 5.17 | 0.34 | 1.88/0.68
Pulses | 5.17 | 1.35 | 1.88/0.68
Sweet-potato | 5.17 | 0.34 | 1.88/0.68
Basic emission factors (kg PM10 ha-1 per pass) assigned to agricultural activities for different crops

## Slide 9: Spatial distribution for PM10
ton/yr/grid (5 arc-min)
Intense regions:
Central US, Northern China, Pakistan, India, Turkey, Southeast Africa
Spatial distribution of agricultural PM10 emissions

## Slide 10
Conversion coefficients of PM2.5 and PM10:
North and South America, 0.125 (CARB); others, 0.06 (EEA)
Spatial distribution of agricultural PM2.5 emissions
ton/yr/grid (5 arc-min)

## Slide 11
Ten regions are divided mainly based on Paul Ginoux et al., 2012
Comparison with Satellite Observations

## Slide 12
South Asia
Left or top: satellite
Red: anthropogenic source
Yellow: natural sources
Right or down are our data
Regional Comparison
North America, East Asia, North Africa and South Asia

## Slide 13
Australia
Regional Comparison
West Asia, South America and Australia
Most agricultural PM sources are similar with natural sources by AOD data
Emission sources from AOD data are always large than emission area because AOD normally represents transported aerosol plumes
No good here

## Slide 14
Monthly variation of agricultural PM10 emission
Major emission months
North America: 5, 9, 10
Europe: 10
East Asia: 5, 6, 9
North Africa: 6, 7, 10, 12
South Asia: 6, 11
Australia: 5, 12
West Asia: 6, 10, 11
South America: 11, 12
South Africa: 10
North Asia: 5, 9

## Slide 15
Region | Longitude Range | Latitude Range | Tillage Emission (kiloton) | Planting/Cuting Emission (kiloton) | Harvest Emission (kiloton) | Total Emission (kiloton)
North America | 125°W-70°W | 20°N-60°N | 43.0 | 10.9 | 91.8 | 145.8
South America | 85°W-50°W | 55°S-0°S | 13.9 | 3.5 | 22.9 | 40.3
Europe | 9°W-60°E | 40°N-71°N | 41.5 | 10.8 | 31.9 | 84.2
North Africa | 20°W-35°E | 5°N-40°N | 40.8 | 9.9 | 47.0 | 97.7
South Africa | 5°E-50°E | 35°S-5°N | 13.1 | 3.2 | 9.4 | 25.7
West Asia | 35°E-60°E | 5°N-40°N | 12.0 | 3.1 | 20.5 | 35.6
North Asia | 60°E-140°E | 50°N-71°N | 8.0 | 2.1 | 9.3 | 19.4
South Asia | 60°E-100°E | 5°N-30°N | 28.1 | 5.5 | 23.9 | 57.6
East Asia | 60°E-140°E | 30°N-50°N | 31.9 | 7.6 | 24.8 | 64.3
Australia | 110°E-155°E | 45°S-10°S | 8.3 | 2.1 | 19.5 | 29.9
Total | 180°W-180°E | 90°S-90°N | 266.5 | 63.6 | 332.9 | 663.0
Annual PM10 emission for regions
Order: North America > North Africa > Europe > East Asia > South Asia
PM10 emission in America is approximately1/20 lower than NEI (2005)

## Slide 16
Decrease the passes for tilling operations because the use of combined tillage machine are increasing
PM from grassland productions are not involved, which may decrease PM emission in many grassland regions
Local EF values are rare around the world, especially in Asia and Africa
The classes of adjustment by soil and climate factor may give bias for inventory
Emission uncertainty
Four aspects:

## Slide 17
Summary
The inventory could reflect spatial distribution and temporal variation of agricultural PM emissions in major regions
North America, Europe, North Africa, East Asia and South Asia are important regions of PM emissions
Large uncertainty of magnitude due to the lack measurement of EF
Future works
Focus on national PM emission from field activities based on latest crop information by remote sensing method
Apply the emission inventory to CMAQ and test the effect on national air quality
Summary and future works