## Slide 1
Development and Evaluation of an
Interactive Sub-Grid Cloud Framework for the
CAMx Photochemical Model
Chris Emery, Jeremiah Johnson, DJ Rasmussen, Wei Chun Hsieh,
Greg Yarwood (Ramboll Environ)
John Nielsen-Gammon, Ken Bowman, Renyi Zhang,
Yun Lin, Leong Siu (Texas A&M University)
14th Annual CMAS Conference
October 5-7, 2015
Notes: 15 minutes total

## Slide 2
Development and Evaluation of an
Interactive Sub-Grid Cloud Framework for the
CAMx Photochemical Model
Acknowledgments:
Khalid Al-Wali, Texas Commission on Environmental Quality
Gary McGaughey, University of Texas
Kiran Alapaty and Jerry Herwehe, US EPA/NERL
The DISCOVER-AQ program
The START08 program

## Slide 3
Development and Evaluation of an
Interactive Sub-Grid Cloud Framework for the
CAMx Photochemical Model
Topics:
Summarize convective processes and model limitations
Project objectives
Introduce EPA’s convection updates in the Weather Research and Forecasting (WRF) meteorological model
Summarize the new CAMx convective model framework – Cloud in Grid (CiG)
Summarize evaluation of WRF + CAMx/CiG

## Slide 4
Daily convective clouds/rainfall are common during the ozone season
Clouds are often small, but ubiquity and abundance are important:
  Boundary layer mixing and ventilation
  Deep tropospheric transport
  Radiative transfer, energy budgets, photolysis
  Precipitation, aqueous chemistry, wet scavenging/deposition
  Environmentally-sensitive emission sectors (e.g., biogenics)
Importance of convection for atmospheric processes

## Slide 5
Most clouds are not explicitly resolved by model grid scales
  “Sub-grid” clouds /convection (SGC)
  Develop and propagate via stochastic processes
  Physical effects are difficult to characterize accurately
Meteorological models do not export SGC data to PGMs
  SGC must be re-diagnosed
  SGC effects are addressed to varying degrees among PGMs
  Potentially large inconsistencies between models
CAMx implicitly treats effects of diagnosed SGC at grid scale
  Adjusts resolved cloud fields for SGC properties
  Impacts photolysis, aqueous chemistry, wet scavenging
  No cloud convective mixing treatment
Modeling limitations

## Slide 6
Add sub-grid convective module to CAMx
  Vertical transport
  Aqueous chemistry
  Wet deposition
Tie into recent EPA/NERL updates to WRF convection (MSKF)
  Add KF cloud information to WRF output files
  Consistent cloud systems among WRF and CAMx
Test for two aircraft field study episodes:
  September 2013 Houston DISCOVER-AQ
  Spring 2008 START08 over central US
Project Objectives

## Slide 7
CiG defines a multi-layer cloud volume per grid column according to WRF KF output
Stationary steady-state SGC environment between met updates (e.g., 1 hour)
  Grid-scale pollutant profiles are split to cloud and ambient volumes
Convective transport designed for quick solution
  Solves transport for a matrix of air mass tracer per grid column
  Tracer matrix is algebraically applied to pollutant profiles
  Rigorously checked to ensure mass conservation
Aqueous chemistry and wet scavenging (fast) separately processed on in-cloud and ambient profiles
Cloud/ambient profiles are linearly combined to yield final profiles
Ozone chemistry (slow) is applied on the final profiles
CAMx Cloud-in-Grid (CiG) framework

## Slide 8
Schematic of CAMx CiG
Up/downdrafts (Fc) balanced by lateral en/detrainment (E,D) by layer (dz)
Compensating vertical motion (Fa) in ambient air is a function of –(E,D) and cloud fractional area (fc)

## Slide 9
DISCOVER-AQ: September 4, 2013
O3: 20-70 ppb at sfc
60-70 ppb at 4 km
NOy: 1-20+ ppb

## Slide 10
DISCOVER-AQ: September 4, 2013
RadKF (WRF v3.6.1) and MSKF (WRF v3.7) lead to very different cloud patterns
  And different wind, temperature, humidity patterns
  Purely a result of MSKF? Or other changes in WRF v3.7?
MSKF is a better cloud simulation
Resolved + RadKF Clouds
Resolved + MSKF Clouds
12 km CAMx grid

## Slide 11
DISCOVER-AQ: September 4, 2013
NOx ventilation from surface to free troposphere
Reductions near surface, increases aloft
  Agrees with conceptual model for upward ventilation of surface sources
  Patterns reflect local net influence of up/downdrafts among clouds and ambient volumes
Surface
2.8 km
5.4 km

## Slide 12
DISCOVER-AQ: September 4, 2013

## Slide 13
DISCOVER-AQ: September 4, 2013
O3 is effects are similar
Net ventilation from surface to free troposphere
  But mitigated somewhat by inverted boundary layer gradient
Surface
2.8 km
5.4 km

## Slide 14
DISCOVER-AQ: September 4, 2013

## Slide 15
DISCOVER-AQ: September 4, 2013
Some convective columns extend to 200 mb (~12 km)
Clear ventilation of PBL NOx and O3
Free/mid-tropospheric buildup of pollutants
Some deep convective influences on upper tropospheric O3

## Slide 16
Summary:
Convection is locally/regionally important for pollutant ventilation, transport and removal, but is difficult to model
New CAMx/CiG framework includes sub-scale vertical transport and wet removal of gases & PM, plus in-cloud PM chemistry
CiG is operating as designed, but model-measurement comparisons are hindered by WRF’s SGC predictions
Development and Evaluation of an
Interactive Sub-Grid Cloud Framework for the
CAMx Photochemical Model
14th Annual CMAS Conference
October 5-7, 2015

## Slide 17
Development and Evaluation of an
Interactive Sub-Grid Cloud Framework for the
CAMx Photochemical Model
Future work:
Evaluate impacts to PM, deposition
Tie in Probing Tools (SA, DDM, RTRAC)
Tie in lightning NOx
Available in future public release (2016?)
Thank you – Questions?
14th Annual CMAS Conference
October 5-7, 2015

## Slide 18: Extra Slides

## Slide 19
EPA’s WRF updates to convection (Alapaty et al, 2012; 2014)
2012: Link WRF KF cumulus scheme to WRF radiation scheme (RadKF)
  RadKF shades ground: reduces convective PE and rain
2014: Generalize RadKF to multi-scale (MSKF)
  MSKF generates more SGC: more shading, less rain
JJA 2006 WRF Precip
JJA 2006 Solar Rad

## Slide 20
DISCOVER-AQ
Ozone difference (MSKF – RadKF)
2 PM September 4, 2013 (same as slide 10)

## Slide 21
Large underestimates above 8 km
Add NOx sources aloft (aircraft, lightning) and set top BC’s
Add explicit top BC’s from a global model
These improve average profiles over large areas
Convective mixing is important at local scales
Modeling limitations
Comparing CAMx NOy profiles against aircraft and satellite data (Kemball-Cook et al., 2012; 2013, 2014):