## Slide 1: New Measurements of Hygroscopicity- & Size-Resolved Particle Fluxes
Brittany Phillips, K. Dawson, T. Royalty,
R. Reed, M. D. Petters, and N. Meskhidze
Marine, Earth, and Atmospheric Science – NC State
October 7, 2015
14th Annual CMAS Conference, UNC-Chapel Hill
Air Quality Measurements & Observational Studies

## Slide 2: Objectives/Research Questions
Part one:
What is the fraction of sea-spray in the Marine Boundary Layer?
Part two:
Can we measure size- and hygroscopicity-resolved fluxes?

## Slide 3: Motivation: why study sea-spray fluxes?
Marine Aerosol Impacts:
  Climate
  Human Health
  Chemical Reactions
Sea-spray aerosol number concentrations are low
Uncertainty in measurements are high

## Slide 4: Current Literature on Sea-Spray Flux
Limited to a few data points
  Geever et al. 2005
  de Leeuw et al. 2007
  Norris et al. 2012
Measurement system needs to be able to measure a flux of ~104 m-2 s-1
Source: O’Dowd and de Leeuw (2007)
140-260 nm in Diameter

## Slide 5: Flux Measurement Techniques
Eddy Covariance (EC):
Background Image Source: https://en.wikipedia.org/wiki/Eddy_covariance
  Relaxed Eddy Accumulation (REA):
  – empirical coefficient ~0.3-0.8
  - standard deviation of the vertical wind component
Concentration Gradient

## Slide 6: Duck Pier Site (North Carolina)
Preliminary deployment
Question: What is the expected concentration of sea-spray (and the wind speed dependence)?
Source: http://www.frf.usace.army.mil/
Source: Google Maps
U.S. Army Corps of Engineer’s Field Research Facility’s 560 meter long pier.
Duck, NC
Instrument Setup at the Pier

## Slide 7: Measurement System (SMPS and Tandem DMA)
Sonic Anemometer
and
Aerosol Inlet
200 nm dry size selection
RH: 80 %
Humidification
Growth Factor
Distribution
Notes: Full system of instruments include
Sonic Anemometer- wind speed & direction, and temperature
HTDMA: Hygroscopicity Tandem Differential Mobility Analyzer- provides the growth factor distribution for size-selected particles (first DMA)
SMPS: Scanning Mobility Particle Sizer- provides particle size distribution over the range (550-10 nm) (sheath-to-sample flow rate ~5:1)
CCN: Cloud Condensation Nuclei Counter- counts the number of particles capable of activating as cloud nuclei (supersaturation range 0.09-1.25)
SP2: Single Particle Soot Photometer- measures black carbon mass on a particle by particle basis

## Slide 8: Using hygroscopic growth factor to identify sea-spray concentration
200 nm Dry Sized Particle
RH: 80 %
Growth Factor
0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1.0 | 1.1 | 1.2 | 1.3 | 1.4 | 1.5 | 1.6 | 1.7
Kappa (Hygroscopicity Parameter)
Sea-Spray
Very Hygroscopic
Slightly Hygroscopic
Non Sea Spray

## Slide 9
Using hygroscopic growth factor to identify sea-spray concentration
Dust
Ammonium
Sulfate
Sea-Salt
Black
Carbon
RH=20%
RH=80%

## Slide 10: Growth factor distribution (@ RH = 80%)
Kappa (Hygroscopicity Parameter)
Very Hygroscopic
Slightly Hygroscopic

## Slide 11: Derivation of sea-spray fraction
Sea-Spray Fraction: 0%
Sea-Spray Fraction: 8.4%
1
2
1
2
Notes: Low hygroscopicity parameter means slightly hygroscopic
High hygroscopicity parameter means very hygroscopic
Organic species (low to ~0.5)
Sea-salt (~1.3)

## Slide 12: Two measurement modes
A. Scan a range of wet diameters
B. Set target kappa and obtain 1 Hz data
A
B
Notes: Low hygroscopicity parameter means slightly hygroscopic
High hygroscopicity parameter means very hygroscopic
Organic species (low to ~0.5)
Sea-salt (~1.3)

## Slide 13: Aerosol Size Distribution
For 160-240 nm – Concentration varies between 15 and 300 particles/cm-3.

## Slide 14: Sea-Spray Number Concentration (160-240nm)

## Slide 15: Fraction of 200 nm sea-spray vs. wind speed
Higher fraction of 200 nm sized particles were sea-spray (kappa = 1.3) for greater wind speeds
High wind speeds occurred less often
Fraction
Wind Speed Histogram
3 | 9 | 15 m/s

## Slide 16: Sea-Spray Concentration Summary
Sea-spray fraction of 200 nm particles at site varies from ~0-24%
Typical 200 nm sea-spray concentration ~1-10 cm-3
Next objective: Concentration  Fluxes
  Can flux be measured directly?
  HTDMA too slow for EC
Design and validation of REA system

## Slide 17: Hygroscopicity-Resolved Relaxed Eddy Accumulation Flux (Hy-RES REA)
Sea Salt Aerosol Generation
Legend:
Sonic anemometer
Three-way valve
Sample flow
HEPA Filter
Frit
HTDMA System
Updraft/Downdraft Wind Speed Measurement
Solenoid Valve Switching:
Zero Air
Updraft Concentration
Downdraft Concentration
Size-Selection
&
Growth Factor Distribution
80%
Notes: This diagram represents the laboratory validation setup only.
Relaxed Eddy Field setup will include the SP2, SMPS, CCN, and HTDMA.
Two solenoid valves will be used to select up/down drafts separately.
Data presented represent the Wet-Diameter, dry diameters will be measured in the field setup.

## Slide 18: Preliminary System Results
Laboratory Background Flux Time Series
NO Source
Background Lab
Approximate Detection Limit:
~4.93 x 104 m-2 s-1
Source: O’Dowd and de Leeuw (2007)

## Slide 19: Preliminary System Results
High Source Strength Flux Time Series
High Source Strength

## Slide 20: Preliminary System Results
Source Strength Vs. Flux

## Slide 21: Flux Summary
Size-/hygroscopicity-resolved flux setup
  Uncertainty/zero:
  Flux scales with source strength
  Time response: 1 averaged flux data point every 2 hr.
Ready to test in a second field deployment at Duck, NC in Nov 2015.

## Slide 22: Questions?
Acknowledgements: National Science Foundation (NSF), and Field Research Facility (Jeff Waters) at Duck, NC

## Slide 23: Ancillary u* Data

## Slide 24: Ancillary SMPS/SP2 Data
Volume
SMPS Conc.
Surface Area

## Slide 25: Ancillary Wind Rose Plot

## Slide 26: Ancillary Seawater Data

## Slide 27
Ancillary Seawater Data

## Slide 28: Ancillary Seawater Data

## Slide 29: Ancillary Seawater Data

## Slide 30: Ancillary Seawater Data

## Slide 31: Ancillary Seawater Data
Notes: RFU – Relative Florescence Units

## Slide 32: Expected Valid Flux Results
Is the measured flux correct?
Given a change in the source concentration  flux should respond proportionally