## Slide 1: Modeled Source Apportionment of Reactive Nitrogen in the Greater Yellowstone Area
CMAS Annual Conference, October 24-26, 2016, Chapel Hill, NC
Tammy M. Thompson: Colorado State University (now at AAAS); Michael G. Barna, Bret A. Schichtel: National Park Service; C. Thomas Moore: Western States Air Resources Council (WESTAR)

## Slide 2: Outline
Modeling Platform
  Details, Why Use?
  Model Performance within the Grand Tetons based on National Park Service Special Study
Source Apportionment
  Regions/Sectors
  Grand Tetons
    Ammonia concentrations
    Total Nitrogen Deposition
  The Greater Yellowstone Area

## Slide 3: Why care about N deposition
  It’s a fertilizer, and can foster ecosystem change in sensitive environments
    Diatom communities in alpine lakes
    Wildflowers -> sedges
  GYA nitrogen ‘critical load’ at 3 kg/ha/yr
See Fenn et al. (2003) for review of N deposition ecological effects
Notes: 3

## Slide 4: Inter-Mountain West Data Warehouse 2011 Modeling Domain (NPS & Class 1 in Red)
36km / 12km Domains focused on the Western US
2011 National Emissions Inventory with Improvements
  Oil and Gas
  Agriculture
Weather Research and Forecasting (WRF) 2011 met modeling by IWDW for Western US
MOZART BCs
Comprehensive Air Quality Model with Extensions (CAMx)
Fully Evaluated by IWDW

## Slide 5: Grand Trends Study Area
Field campaign: April – September, 2011
Measure N species across Grand Teton National Park

## Slide 6: Annual Average Agricultural NH3 Emissions 2011: Tons/year/km2

## Slide 7
Upper Grand Targhee shows good model performance for key measured Nitrogen Species
Model Values in Blue Measured Values in Red
All Values in µg/m3
Nitric Acid
Particle Nitrate
Ammonia
Particle Ammonium

## Slide 8: Source Regions
From Each Region, Trace Source Sectors Individually:
Agriculture
Oil and Gas
Model Domain Boundaries
All Other Source Sectors

## Slide 9: Trace Regional Air Pollution Emissions to their Contributions in Grids Cells in Grand Tetons NP. We’ll look at three grid cells moving from West to East across the park

## Slide 10: Who is Contributing to Ambient NH3 Concentration on the Western Side of Grand Tetons NP? (2011 Annual Average)

## Slide 11: Who is Contributing to Ambient NH3 Concentration on the Center of Grand Tetons NP? (2011 Annual Average)

## Slide 12: Who is Contributing to Ambient NH3 Concentration on the Eastern Side of Grand Tetons NP? (2011 Annual Average)

## Slide 13
Note the importance of reduced N deposition
Chart: mg N/m2
| Apr | May | Jun | Jul | Aug | Sep | Avg | Jul | Aug | Sep | Avg | May | Jun | Jul | Aug | Sep | Avg | Driggs | Targhee | NOAA CC
Dry NH3 | 14.2172 | 10.3973 | 10.3832 | 10.104 | 13.4129 | 19.3552 | 12.9783 | 7.0721 | 10.1201 | 11.9346 | 9.709 | 4.2564 | 4.9779 | 4.8889 | 10.2416 | 8.8187 | 6.6367
Dry NH4 | 0.54771 | 0.43021 | 0.44244 | 0.43339 | 0.3743 | 0.47841 | 0.45108 | 0.48491 | 0.41655 | 0.47732 | 0.4596 | 0.389 | 0.40716 | 0.39525 | 0.372 | 0.37775 | 0.38823
Wet NH4 | 25.4648 | 27.3438 | 25.1701 | 9.7124 | 15.5655 | 7.6357 | 18.482 | 4.7394 | 5.9687 | 6.2498 | 5.6526 | 23.0175 | 19.7084 | 5.6533 | 18.5846 | 11.1233 | 15.6174
Wet NO3 | 13.9036 | 13.5049 | 11.848 | 7.1935 | 10.1892 | 3.3978 | 10.0062 | 4.4264 | 5.4297 | 2.7351 | 4.197 | 12.795 | 10.2499 | 3.8102 | 11.7283 | 4.6338 | 8.6434
Dry HNO3 | 2.9547 | 3.7386 | 5.8705 | 8.1463 | 8.2105 | 5.5526 | 5.7455 | 10.6605 | 10.6559 | 6.4199 | 9.2454 | 4.0222 | 6.4579 | 9.213 | 9.3315 | 5.8311 | 6.9712
Dry NO3 | 0.38285 | 0.19538 | 0.1299 | 0.062664 | 0.036364 | 0.063631 | 0.14513 | 0.073226 | 0.043046 | 0.06438 | 0.060217 | 0.16997 | 0.11348 | 0.05859 | 0.036938 | 0.045954 | 0.084986
Inorganic Reactive N deposition budgets
Modeled Measured
Chart: mg N/m2
| Apr | May | Jun | Jul | Aug | Sep | Avg | Jul | Aug | Sep | Avg | May | Jun | Jul | Aug | Sep | Avg | Driggs | Grand Targhee | NOAA CC
Dry NH3 | 11.4266 | 15.7735 | 15.59 | 19.3664 | 20.9447 | 9.3715 | 15.1581 | 1.7983 | 14.7343 | 7.387 | 11.0606 | 1.7947 | 7.5543 | 8.4732 | 11.2982 | 4.9389 | 8.1186
Dry NH4 | 0.94082 | 0.85752 | 0.78853 | 0.86484 | 0.83683 | 0.43361 | 0.63522 | 0.11284 | 0.92836 | 0.49794 | 0.71315 | 0.24728 | 0.51309 | 0.79916 | 0.74921 | 0.4534 | 0.6013
Wet NH4 | 16.1764 | 18.9601 | 17.9205 | 16.4018 | 5.9886 | 3.3642 | 4.6764 | 4.2808 | 10.7428 | 12.3485 | 11.5456 | 9.6827 | 6.7289 | 11.0958 | 6.6119 | 4.394 | 5.5029
Wet NO3 | 6.1039 | 7.1646 | 5.5723 | 10.8214 | 4.728 | 1.3128 | 3.0204 | 3.5724 | 7.5828 | 5.0396 | 6.3112 | 1.9707 | 3.4505 | 7.8703 | 4.6482 | 2.2062 | 3.4272
Dry HNO3 | 0.40563 | 0.86714 | 1.5918 | 2.4034 | 2.5962 | 0.92088 | 1.7586 | 0.36257 | 4.4169 | 1.4347 | 2.9258 | 0.14135 | 1.2243 | 2.1422 | 2.3878 | 1.1166 | 1.7522
Dry NO3 | 0.24328 | 0.19563 | 0.086452 | 0.10628 | 0.12182 | 0.066246 | 0.094032 | 0.010085 | 0.11705 | 0.080091 | 0.098573 | 0.019986 | 0.056338 | 0.084184 | 0.11672 | 0.065037 | 0.090881
Notes: The relative importance of N deposition pathways depends on the amount of precipitation (DR v GT).
Dry deposition of ammonia is important in GTNP.
In June and July, precipitation at Driggs (~54 mm each month) was greater than at NOAA Climate Center (~30 mm), consistent with their locations upwind and downwind of the
Teton Range, respectively. Wet nitrogen deposition was also greater at Driggs. In August and September, monthly precipitation was less than 10mmat both Driggs and NOAA Climate Center, while at the higher elevation site, Upper Grand Targhee, 29 mm of precipitation fell in August and 36 mm fell in September. The highest average volume-weighted ion concentrations were of ammonium, calcium, nitrate, and sulfate at all three sites. At both Driggs and NOAA Climate Center, precipitation ion concentrations (μN) decreased in the order NH4 +>NO3 >Ca2+>SO4 2, while at Upper Grand Targhee, the order was NH4 +>Ca2+>NO3 >SO4 2. Nitrogen species were always more abundant than sulfur, on a molar basis, in the precipitation samples.
The absolute amount of precipitation in 2011 was higher than the historical average during the wet period, indicating that dry deposition of NH3 may typically be a more important contributor also to spring nitrogen deposition than that observed during GrandTReNDS

## Slide 14: Source Contribution by Region
(Surprisingly) large contribution from boundary and California
Idaho the most significant source
Wyoming and Utah also make significant contributions
BC
CA
ID

## Slide 15: Monthly Total Deposition by Source Sector

## Slide 16: Conclusions
Most of the N dep at GYA from Idaho; BC’s, CA, UT and Wyo also important
Need better treatment of ammonia
  Measurement studies happening in RMNP now
  Evaluating models with bi-directional flux ammonia modeling capabilities
If industrial agriculture is a large source (it is), then how to address for mitigation?
Expanding both measurement and model capabilities for organic nitrogen