## Slide 1: Ozone Source Apportionment Modeling to Support Policy Initiatives in the Eastern United States
STI-6537
Kenneth Craig, Garnet Erdakos, Lynn Baringer, and Stephen Reid
Sonoma Technology, Inc., Petaluma, CA
15th Annual CMAS Conference
Chapel Hill, NC
October 26, 2016

## Slide 2: Outline
Motivation
Modeling approach
Results: multiple sources examples
Results: single-source example
Summary and insights

## Slide 3: Motivation
Interstate transport has become increasingly important for addressing NAAQS attainment issues.
Source apportionment has become an important tool to quantify source impacts on downwind ozone and guide policy decisions (e.g., CSAPR).
CSAPR modeling provides state-level source contributions.
STI conducted new source apportionment modeling with detailed tagging to support policy initiatives in the eastern United States.

## Slide 4: Modeling Approach
2011 ozone season (May-September) simulation with CAMx version 6.1
Configurations based on EPA’s 2011 modeling platform
  WRF version 3.4
  2011 NEI Version 1
  GEOS-Chem boundary conditions
  Carbon Bond 6r2
Ozone Source Apportionment Technology (OSAT) with APCA
APCA = Anthropogenic Precursor Culpability Analysis

## Slide 5: Source Apportionment Tagging
Category | Tags
Individual coal-fired power plants | 52
Groups of coal-fired power plants (several dozen EGU) | 49
Groups of non-EGU points sources within a region | 12
Non-point sources (biogenic, on-road, non-road, “other”) within 16 regions | 64
Initial and boundary conditions | 2
OSAT regions for non-point source category
Approach

## Slide 6: Source Apportionment Tagging
Simulation | Description
1 | Point source tags (set 1)
2 | Point source tags (set 2)
3 | Geographic tags (e.g., on-road)
Processor: 16 CPU per simulation (2 nodes)
Memory: 10-12 GB RAM per node per simulation
Clock time: 3-4 weeks
Approach

## Slide 7: OSAT Post-Processing
Reflects contributions during time periods when ozone concentrations are highest
Guarantees that daily ozone contributions from all source tags sum to the total modeled 8-hr concentration
Receptor Locations (670 monitors in eastern U.S.)
Hourly gridded OSAT results
Daily peak 8-hr O3 contributions for each tag and receptor
at hour of peak modeled 8-hr O3
Approach

## Slide 8: Access Database
Extracted ozone contributions for all tags at 670 monitoring sites across the eastern U.S.
Developed sample queries to facilitate data exploration
Opportunity for future data mining
Approach

## Slide 9: Ozone Impacts vs. Distance
1 ppb is the proposed NAAQS significant impact level (SIL) for single-source ozone impacts.
Results: Multiple Sources

## Slide 10: Single Receptor Analysis
Ozone contributions in Sussex County, DE, when modeled ozone was greater than 70 ppb (13 days)
(6.11 ppb)
Delaware sources
Non-Delaware sources
Results: Multiple Sources

## Slide 11: Point Source Analysis Brunner Island
York Haven, PA
1411 MW generating capacity
2011 NOx emissions: 16,800 tons
Brunner Island power plant in southeast Pennsylvania and nearby air quality monitoring sites.
www.talenenergy.com
Results: Single Source

## Slide 12: Brunner Island Ozone Impacts
Peak modeled 8-hr ozone impacts from the Brunner Island power plant during the 2011 ozone season.
Results: Single Source

## Slide 13: Brunner Island Ozone Impacts
Peak modeled 8-hr ozone impacts from the Brunner Island power plant on July 20, 2011.
Results: Single Source

## Slide 14: Daily Ozone Contributions
Significant (>0.75 ppb) 8-hr ozone impacts were modeled at one or more PA monitor(s) on 86% (79 of 92) of days during June-August.
Results: Single Source

## Slide 15: Ozone Contributions at Pennsylvania Monitors
Significant (>0.75 ppb) 8-hr ozone impacts were modeled on at least one day at 75% of Pennsylvania monitoring sites.
Results: Single Source

## Slide 16: Impacts on High-Ozone Days
Modeled 8-hr ozone impacts >0.75 ppb from Brunner Island and incremental monitored ozone concentrations above the NAAQS on days when the NAAQS was exceeded at the Sipe Ave. monitor near Harrisburg.
10 ppb
3.34 ppb
6.70 ppb
1.44 ppb
6 ppb
5 ppb
July 2
July 20
July 21
Brunner Island Impact
Monitor increment above NAAQS
Results: Single Source

## Slide 17: Ozone Contributions on Neighboring States
Summary of significant (>0.75 ppb) modeled 8-hr ozone contributions from Brunner Island at monitoring stations in Pennsylvania and neighboring states.
Results: Single Source

## Slide 18: Summary and Insights
Conducted source apportionment modeling to support policy initiatives in the eastern United States
Developed a database to support current analysis and future data mining
Multiple sources examples
  1-ppb impacts possible several hundred kilometers from large NOx sources
  At some receptors, in-state ozone contributions are small compared to out-of-state contributions
Single-source example (Brunner Island)
  Significant (>0.75 ppb) ozone impacts in Pennsylvania on most summer days
  Significant impacts at Harrisburg on three NAAQS exceedance days in 2011
  Significant ozone contributions extend several hundred kilometers into neighboring states
Further discussion: Representativeness of modeling results from a transport perspective

## Slide 19: Trajectory Spatial Probability Density (Difference plots: high-ozone days vs. all days)
2011
2008
Southwesterly transport toward Delaware is less pronounced in 2011 than in other years.

## Slide 20: Contact
sonomatech.com
Kenneth Craig
Group Manager Atmospheric Modeling
kcraig@sonomatech.com
707.665.9900
sonomatech.com @sonoma_tech