## Slide 1
Using Response Surface Model for Hemispheric Transport of Air Pollution (HTAP)
15th Annual CMAS Conference
October 24-26, 2016
Jiani Tan, Joshua S. Fu, Xinyi Dong, Kan Huang
University of Tennessee, Knoxville, TN, USA
October.26th, 2016
Notes: Transport
Not transportation

## Slide 2: Outline
Introduction
  Introduction of HTAP phase II
  Background and motivation of this study
Method
  Framework of CMAQ/ Response Surface Model (RSM)
  Emission and control variables
Results
  Model evaluation
  Source-Receptor (SR) relationship
Discussion & Summary
Notes: 15 second
This results we only show the results of NA

## Slide 3: Brief Introduction of HTAP Phase II
Task Force on Hemispheric Transport of Air Pollution (TF HTAP) was developed by Convention on Long-range Transboundary Air Pollution (LRTAP) Convention in 2004
700 individual experts from more than 28 countries
15 oversea meetings or workshops
This study participants in the phase II starting from 2008
Home page: http://www.htap.org/
Wiki page: http://iek8wikis.iek.fz-juelich.de/HTAPWiki/
Notes: redo
Organize
History-2001, model, papers
PhaseII, what we want to know, why start phase II

## Slide 4: Background and Motivation
Both observational and model evidence: slow down increase of O3 in Europe and North America due to long time control of emissions
But at the same time
  Increasing background O3 concentration
  Trans-oceanic air flow carrying air pollutants.
Issue for policy-maker
  How long-term transport affect receptor regions?
  Will it offset the improvement from emission control policy?
This study focus on:
Pattern and impact of long-term transport of pollutants
Develop a source-receptor relationship for hemispheric transport
Predict the air quality under multiple pollution scenarios and help regional air quality control in the future
Notes: Why is important to know the inter-continental transport?
Background transport
Local air quality control
Previous results: bar plot-> background, transport, compare percentage

## Slide 5: Framework of CMAQ/RSM
Meteorology
WRFv3.6
Air Quality Model
CMAQv4.7.1
Response Surface Model (RSM)
Control Variables
Precursors: SO2,NOx,NH3, NMVOC
Regions: 7
Sectors: 5
Latin Hypercube Sampling (LHS)
MCIP
Control Matrix
Source-receptor Relationship
Emission
HTAPv2.2
+ Megan
+ GFEDv4
Notes: How to transfer from background to method?
1) We define the control factors, and use LHS to create a control matrix

## Slide 6
Emission Inventory
Compiled emission inventory
USA – NEI from US EPA
Canada - Environment Canada
Europe - the European Monitoring and Evaluation Programme (EMEP) and Netherlands Organisation for Applied Scientific Research (TNO)
Asia: Model Inter-comparison Study for Asia (MICS-Asia III)
South America, Africa, Russia- Emissions Database for Global Atmospheric Research (EDGARv4.3)
0.1° × 0.1° spatial resolution
Uncertainty of different emission sectors
Low (L), low-medium (LM), upper-medium (UM), and high (H).
(Janssens et al, 2015)
Notes: Import! Where the emission come from!
We will discuss the results with uncertainty later

## Slide 7: Control Variables
(Janssens et al, 2015)
  SO2: Industry Energy
  NH3: Agriculture
  NOx: Industry Transport Energy
      NMVOC: Industry Transport Resident
}
PM2.5
}
O3
Control sector
Control regions
In this study, we use…
Notes: Why and how we choose control variables
On the basis of the emission inventory, we are able to see the biggest contributor of air pollutions.

## Slide 8: Control Region and Scenario
1-North America (NA) 2-Europe (EU)
3-Russia, Kazakhstan, Uzbekistan (RS)
4-South Asia (SA) 5-East Asia (EA)
6-Southeast Asia (SEA)
7 – North Africa, Mid-East (AM))
RSM scenarios design
1 base run
3 all region emission reduce 20%, 50% and 80%
7 each source region emission reduce 20%
300 runs from LHS control matrix to cover all source categories for factor of 0~1.2
Model set-up
Spatial resolution: 108 km×108 km
Vertical resolution: 44 layers
Chemical options: CB05, aero5
Run period: Jan, Apr, Jul, Dec of 2010
CPU hours: 0.7 million hours
Notes: Color
Model setup – physical and chemical, resolution, top and bottom
Cpu hour, how many runs

## Slide 9: Evaluation of RSM
282 CMAQ results to develop RSM
The rest results to validate RSM using
out of sample method
The RSM model agrees well with the CMAQ model
Notes: Color
Model setup – physical and chemical, resolution, top and bottom
Cpu hour, how many runs

## Slide 10: Source - Receptor Relationship of PM2.5
- North America Region
Notes: na-north america

## Slide 11: Hemispheric Transport of PM2.5 in Spring
unit: µg/m3

## Slide 12: North America as Source Region of PM2.5
Notes: Na as source , no

## Slide 13: Response to 20% Emission Reduction in North America for PM2.5
Change in receptor regions | Europe | Africa & Mid-East | East Asia | South Asia | Russia
Concentration (µg/m3) | -0.112 | -0.037 | -0.008 | -0.025 | -0.006
Percentage (%) | -0.860 | -0.409 | -0.039 | -0.110 | -0.446
Absolute concentration in spring
Percentage of change in spring
unit: µg/m3
unit: %
Notes: Single color
1 figure + table
Among the receptor regions, Europe receives the biggest influence
Winter paper by Xinyi
Among the four season, Spring has highest inter-continental transport

## Slide 14
Impact of North America to Europe and North Africa and Mid-East of PM2.5
Strong seasonal dependent: High hemispheric transport in Spring due to strong westerlies.
Almost linear response in receptors PM2.5 concentration with emission control in North America.
Much stronger impact on Europe than North Africa and Middle East.
Chart: Emission reduction rate in North America (%)
Spring | -0.037 | -0.112 | -0.212 | -0.319 | -0.416
Summer | -0.015 | -0.05 | -0.096 | -0.144 | -0.186
annual | -0.013 | -0.047 | -0.095 | -0.149 | -0.2
Chart: Emission reduction rate in North America (%)
Spring | -0.015 | -0.037 | -0.063 | -0.091 | -0.117
Summer | -0.013 | -0.034 | -0.059 | -0.085 | -0.109
annual | -0.007 | -0.017 | -0.029 | -0.041 | -0.053
(a) NA to Europe
(b) NA to North Africa and Mid-East
Notes: From left to right, the emission control rate is increased from 10% to 50%.
Make sure why the winter is increase

## Slide 15: North America as Receptor Region of PM2.5

## Slide 16
East Asia
Russia
North Africa
Middle East
South Asia
South East Asia
What Would Happen to PM2.5 in North America if Control 20% Emission in…
unit: µg/m3
(2010 spring)
Europe

## Slide 17
Hemispheric impact on North America for PM2.5
Chart: Emission reduction ratio in each source region (%)
| 10.0 | 20.0 | 30.0 | 40.0 | 50.0
AM | 0.002 | -0.004 | -0.015 | -0.028 | -0.038
EU | -0.003 | -0.013 | -0.028 | -0.044 | -0.058
RS | -0.001 | -0.01 | -0.025 | -0.041 | -0.055
SA | -0.008 | -0.023 | -0.043 | -0.064 | -0.082
SE | 0.002 | -0.003 | -0.014 | -0.027 | -0.037
EA | 0.002 | -0.004 | -0.015 | -0.028 | -0.038
The reduction of PM2.5 is close to linear response to the emission reduction in other continents
Asia regions accounts for 50% of the hemispheric transport to North America
50% of impacts come from Asia
Chart: 
| 10.0 | 20.0 | 30.0 | 40.0 | 50.0
EA | -0.038 | -0.087 | -0.143 | -0.199 | -0.252
SA | -0.009 | -0.03 | -0.055 | -0.081 | -0.103
SE | 0 | -0.01 | -0.028 | -0.048 | -0.065
Asia | -0.046 | -0.117 | -0.189 | -0.249 | -0.296
Spring
Impact from Asia
High efficiency to control the emissions from East Asia
Notes: Sample
Explain how to read this figure
unit
Domain and monthly averge
Compare with current results

## Slide 18: Source-Receptor Relationship of O3
- North America Region

## Slide 19: Hemispheric Transport of O3 in Spring
unit: ppbV

## Slide 20: North America as Source Region of O3

## Slide 21: Response to 20% Emission Reduction in North America for O3
Absolute concentration in spring
Percentage of change in spring
unit: ppbV
unit: %
Change in receptor regions | Europe | Africa & Mid-East | East Asia | Russia
Concentration (ppbV) | -0.312 | -0.131 | -0.038 | -0.087
Percentage (%) | -0.625 | -0.219 | -0.069 | -0.215
Notes: Single color
1 figure + table
Among the receptor regions, Europe receives the biggest influence
Among the four season, Spring has highest inter-continental transport

## Slide 22
Impact of North America to Europe for O3
Spring has the highest hemispheric transport from North America to Europe.
Almost linear O3 reduction in Europe with more emission control in North America.
Chart: Emission reduction rate in North America (%)
| 10.0 | 20.0 | 30.0 | 40.0 | 50.0
Spring | -0.196 | -0.312 | -0.392 | -0.48 | -0.605
Summer | -0.157 | -0.188 | -0.16 | -0.142 | -0.182
Fall | -0.069 | -0.099 | -0.108 | -0.12 | -0.149
Winter | -0.014 | -0.04 | -0.072 | -0.1 | -0.122
annual | -0.109 | -0.16 | -0.183 | -0.211 | -0.264
Notes: From left to right, the emission control rate is increased from 10% to 50%.

## Slide 23: North America as Receptor Region of O3

## Slide 24: What Would Happen to O3 in North America if Control 20% Emission in…
unit: ppbV
(2010 spring)
East Asia
Russia
North Africa
Middle East
South Asia
South East Asia
Europe

## Slide 25
Hemispheric Impact on North America for O3
0 0.2 0.4 0.6 0.8 1.0
NOx emission ratio_EA
1.0
0.8
0.6
0.4
0.2
0
VOC emission ratio_EA
O3 response contour in Chapel Hill, NC
51.8
51.5
51.2
50.8
50.5
50.2
ppbV
Control NOx emission in most source regions could reduce the O3 concentration in Los Angeles
Control VOC emission would increase the O3 concentration
Chart: Source regions
| AM | EU | RS | SA | SE | EA
NOx | -0.041 | -0.027 | 0.003 | 0 | 0.024 | -0.735
VOC | 0.049 | 0.032 | 0.042 | 0.042 | 0.042 | 0.025
Both NOx and VOC | 0.004 | 0.001 | 0.042 | 0.039 | 0.062 | -0.714
O3 concentration in Chapel Hill has non-linear response to NOx and VOC emissions from East Asia
Notes: O3 - > nonlinear response
Nox -> capi
O3 nonlinear response contour

## Slide 26: Summary
Preliminary Conclusions:
  Strong hemispheric transport found in spring season.
  North America as source of hemispheric transport:
    Europe receives the highest impact.
    More stringent emission control in North America would result in continuous reduction of PM2.5 and O3 concentrations in Europe.
  North America as receptor of hemispheric transport:
    For PM2.5, Asia accounts for up to 50% of the hemispheric transport to North America, among which East Asia contributes the most in Spring.
    For O3, control NOx emission in source regions reduces the O3 concentration in Los Angeles, but control VOC has opposite result.
Next steps:
  The transport of air pollutants in upper layer of atmosphere.
  Impact of long-term transport on regional scale collaborating with MICS-Asia project.

## Slide 27: Acknowledgement
We acknowledge UT’s National Institute for Computational Sciences (NICS) and ORNL’s OLCF (NCCS) for providing the computer sources for model simulations of this research.

## Slide 28: Thank you for your attention ! Questions ?