## Slide 1: Updating CMAQ secondary organic aerosol properties relevant for aerosol water interactions
Havala O. T. Pye1
With contributions from:
Benjamin N. Murphy1, Lu Xu2, Ng L. Ng2, Annmarie G. Carlton3, Hongyu Guo2, Rodney Weber2, Petros Vasilakos2, K. Wyat Appel1, Sri Hapsari Budisulistiorini4, Jason D. Surratt4, Athanasios Nenes2, Weiwei Hu5, Jose L. Jimenez5, Gabriel Isaacman-VanWertz6, Pawel K. Misztal6, and Allen H. Goldstein6
1US Environmental Protection Agency, Research Triangle Park, NC; 2Georgia Institute of Technology, Atlanta, GA; 3Rutgers University, New Brunswick, NJ; 4The University of North Carolina at Chapel Hill, Chapel Hill, NC; 5University of Colorado, Boulder, CO;
6University of California, Berkeley, CA
Office of Research and Development
National Exposure Research Laboratory, Computational Exposure Division
25 October 2016

## Slide 2: Aerosol Water is ubiquitous
Nguyen et al., 2016 ES&TL
Notes: Aerosol water is a ubiquitous component of particulate matter mass as estimated here by Nguyen et al. The mass of aerosol water is often comparable in magnitude to that of organic aerosol (green) and sulfate (red). This aerosol water has contributions from both organic and inorganic components. Water associated with inorganic constituents is often dominant, but organic water is particularl

## Slide 3: Models represent limited connections between OA and aerosol water
Modeled OA generally does not involve water
Observed OA is largely water soluble as measured by PiLS instrument
Models are beginning to include SOA from IEPOX uptake onto aqueous aerosol:
CMAQ v5.1 (Pye et al., 2013 ES&T)
GEOS-Chem, research version (Marais et al., 2016 ACP)
Obs
Obs
Model (CMAQ)
Concentration during Southern Oxidant and Aerosol Study (SOAS) 2013 [mg m-3]
SOA
POA
soluble
insoluble
POA
other SOA
aqueous SOA

## Slide 4: Models represent limited connections between OA and aerosol water
Should traditional SOA interact with water?
Obs
Obs
Model (CMAQ)
SOA
POA
soluble
insoluble
POA
other SOA
aqueous SOA
Concentration during Southern Oxidant and Aerosol Study (SOAS) 2013 [mg m-3]

## Slide 5: Determine a consistent set of properties for semivolatile SOA
Organic Aerosol in CMAQ v5.1
Aerosol with direct water interaction
POA
Very low volatility SOA
Semivolatile SOA
Types of Aerosol in CMAQ:

## Slide 6: Specify a consistent set of properties: MW, OM/OC, C*, density

## Slide 7: Implementing organic interactions with water
CMAQ includes water associated with inorganic compounds
Aerosol water has contributions from inorganic and organic constituents: Wi + Wo

## Slide 8: Implementing organic interactions with water
CMAQ includes water associated with inorganic compounds
Aerosol water has contributions from inorganic and organic constituents: Wi + Wo
Organic compounds will interact with Wi when one liquid phase exists in the particle:
Occurs when RH>Separation RH (SRH)
You et al., 2013 ACP

## Slide 9: LLPS simulation: Organic interaction with Wi
Parameterize SRH based on OM/OC
Determine liquid-liquid phase separation (LLPS) based on SRH and RH
Organic partitioning medium:
  Include Wi when RH>SRH
  Wo = 0

## Slide 10: LLPS more common in urban areas, during the day
OM/OC
Percentage of time phase separated

## Slide 11: LLPS more common in urban areas, during the day
OM/OC
Percentage of time phase separated
Base Model
Local Hour
Observed
SOAS-CTR

## Slide 12: Wo > 0 simulation: Organic interaction with Wo
Parameterize hygroscopicity (k) of organics based on OM/OC
Calculate water uptake using k-Kohler theory
Organic partitioning medium:
  Do not include Wi
  Include Wo

## Slide 13: Wo highest where OA is high
SOAS

## Slide 14: Aerosol water interactions increase mean error

## Slide 15: Aerosol water interactions increase mean error

## Slide 16: g ≠ 1 simulation: Implement deviations in ideality
Organic partitioning medium:
  Include Wi when RH>SRH
  Include Wo at all times
Consider deviations in ideality via an activity coefficient, g, as a function of mole fraction of water in organic-rich phase

## Slide 17: Specify a consistent set of properties: solubility
Chart: 
| TRP2 | TRP1 | SQT | ISO1 | ISO2 | ISOPNN | MTNO3 | BNZ2 | ALK2 | PAH2 | TOL2 | XYL2 | TOL1 | XYL1 | PAH1 | ALK1 | BNZ1
Biogenic VOC-derived SOA | 2 | 3 | 4 | 6 | 13 | 13 | 29 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Anthropogenic VOC-derived SOA | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 139 | 201 | 214 | 257 | 307 | 382 | 488 | 528 | 565 | 579
Activity Coefficient at Infinite Dilution in Water

## Slide 18: Nonideal simulation improves mean bias, small increase in ME

## Slide 19: Nonideal simulations: good OA speciation
local hour
Total Organic Aerosol
Particulate Organic Nitrates
AMS PMF factor: Less oxidized-oxygenated organic aerosol

## Slide 20: Improvements in OA will improve aerosol water

## Slide 21: Improvements in OA will improve aerosol water
g ≠ 1 simulation

## Slide 22: Summary
Water is an important component of PM2.5
Many traditional SOA species are highly soluble
Water can influence the partitioning of compounds traditionally considered insoluble in models
  Organic aerosol takes up water according to RH
  Organic aerosol interacts with inorganic water
Deviations in ideality (solubility) must be considered
For more information, see our paper: Pye et al., 2016 ACPD
pye.havala@epa.gov