## Slide 1: Source Apportionment Modeling to Investigate Background, Regional, and Local Contributions to Ozone Concentrations in Denver, Phoenix, Detroit, and Atlanta
620000-6759
Kenneth Craig, Garnet Erdakos, Lynn Baringer, and Shih Ying Chang
Sonoma Technology, Inc., Petaluma, CA
16th Annual CMAS Conference
October 23, 2017

## Slide 2: Outline
Motivation
Modeling objectives
Modeling approach
Results
  Background ozone estimates from source apportionment and zero-out modeling approaches
  Source apportionment results from sample receptors
  Ozone estimates from source apportionment with reduced on-road NOX emissions
Summary of findings
Introduction

## Slide 3: Motivation
Background ozone analysis is increasingly important for addressing NAAQS attainment issues.
Source apportionment can be used to quantify source impacts on downwind ozone, assess background ozone, and guide policy decisions (e.g., CSAPR, ozone NAAQS).
STI and EPRI conducted new source apportionment modeling with detailed tagging to support stakeholder needs throughout the United States.
Introduction

## Slide 4: Modeling Objectives
Objectives
  Assess ozone contributions from local, regional, and background emission sources (source apportionment modeling).
  Compare background ozone derived from source apportionment with “zero-out” modeling approaches.
  Assess the impact of uncertain on-road NOX emissions on ozone attribution (brute-force and source apportionment analysis).
Domain
  United States
Focus Cities
  Phoenix, Denver, Atlanta, Detroit
Introduction

## Slide 5: Background Ozone
Natural Background (NB)
  Ozone formed from natural sources of ozone precursor emissions (i.e., no anthropogenic emissions)
North American Background (NAB)
  Ozone concentrations in the absence of North American anthropogenic emissions
U.S. Background (USB)
  Ozone concentration in the absence of United States anthropogenic emissions
Introduction
From U.S. EPA

## Slide 6: Background Ozone
Natural Background (NB)
  Ozone formed from natural sources of ozone precursor emissions (i.e., no anthropogenic emissions)
North American Background (NAB)
  Ozone concentrations in the absence of North American anthropogenic emissions
U.S. Background (USB)
  Ozone concentration in the absence of United States anthropogenic emissions
Introduction
z
From U.S. EPA

## Slide 7: Modeling Approach
2011 ozone season (April to September) simulation with CAMx version 6.3.
Domain, inputs, and configurations based on EPA’s 2011 modeling platform.
  WRF version 3.4
  GEOS-Chem boundary conditions
  Carbon Bond 6r2
Ozone Source Apportionment Technology (OSAT) Version 3.
12 km CONUS modeling domain.
Approach

## Slide 8: OSAT Source Group Regions (1)
CO*
MI*
AZ*
GA*
WRAP
CA
LADCO
CenSARA (N)
SESARM
MARAMA
Canada
Mexico
Offshore
CenSARA (S)
NESCAUM
*Arizona, Colorado, Georgia, and Michigan contain multiple source regions.
Approach

## Slide 9: OSAT Source Group Regions (2)
Approach
Phoenix Metro
(MAG)
Southern AZ
Northern AZ
Phoenix Metro Area: Counties within the Maricopa Association of Governments (MAG).
Western CO
Denver Metro
Eastern CO
Denver Metro Area: Counties in the Denver Metro area and Northern Front Range region.

## Slide 10: OSAT Source Group Regions (3)
Approach
Atlanta Metro Area: Counties within the Atlanta ozone non-attainment area.
Detroit Metro Area: Counties within the Southeast Michigan Council of Governments (SEMCOG).
Atlanta Metro
Other GA Counties
Other MI Counties
Detroit Metro

## Slide 11: Source Apportionment Tagging
Simulation | Description
1 | Natural Sources
2 | Electrical Generating Unit (EGU) Point Source
3 | On-Road Sources
Approach
Natural sources include biogenic, lightning (0.52 Tg/yr), and fire emissions.
Other anthropogenic sources (e.g, non-road, non-EGU point) are calculated as the residual.
Tagging strategy includes contributions from top and lateral boundary conditions.

## Slide 12: OSAT Post-Processing
Reflects contributions during time periods when ozone concentrations are highest.
Guarantees that daily ozone contributions from all source tags sum to the total modeled 8-hr concentration.
Subsequent analysis focuses on ozone contributions on high monitored ozone days (>70 ppb).
Receptor Locations (O3 monitors in AZ, CO, GA, MI)
Hourly gridded OSAT results
Daily peak 8-hr O3 contributions for each tag and receptor
Approach

## Slide 13: U.S. Background Ozone (OSAT): Highest Maximum Daily 8-hr Ozone
Background = boundary conditions, fires (wild and prescribed), lightning, biogenic sources, and international anthropogenic sources.
Highest daily values are associated with fire emissions.
Results

## Slide 14: U.S. Background Ozone (OSAT): Fourth-Highest Maximum Daily 8-hr Ozone
Background = boundary conditions, fires (wild and prescribed), lightning, biogenic sources, and international anthropogenic sources.
Highest daily values are associated with fire emissions.
Results

## Slide 15: Difference in Highest Daily U.S. Background Ozone (OSAT – Zero-Out)
Results

## Slide 16: Focus Receptors (1)
Results
North Phoenix
Rocky Flats
Phoenix
Denver

## Slide 17: Focus Receptors (2)
Confederate
Atlanta
Detroit
East 7 Mile
Results

## Slide 18: Ozone Source Contributions
Averages when monitored 8-hr ozone > 70 ppb
Results – Focus Receptors
Boundary conditions include out-of-domain international and offshore contributions and recirculated U.S. contributions from the global model.
Chart: 
| North Phoenix | Denver – Rocky Flats-N | Atlanta – Confederate Ave. | Detroit – East 7 Mile
U.S. Background | 0.71 | 0.73 | 0.41 | 0.52
U.S. Anthropogenic | 0.29 | 0.27 | 0.59 | 0.48
Boundary Conditions | 0.51 | 0.56 | 0.22 | 0.26

## Slide 19: In-State Ozone Source Contributions
Averages when monitored 8-hr ozone > 70 ppb
Results – Focus Receptors
Chart: 
| North Phoenix | Denver – Rocky Flats-N | Atlanta – Confederate Ave. | Detroit – East 7 Mile
Metro Contribution | 0.1827 | 0.1248 | 0.2464 | 0.119
Other In-State Contribution | 0.0273 | 0.0352 | 0.0736 | 0.051

## Slide 20
Fourth-highest maximum daily 8-hr ozone concentration differences
50% NOX Reduction Impacts on Ozone
Results – NOX sensitivity

## Slide 21: Summary of Findings (1)
Modeled USB ozone in 2011 OSAT simulation
  Highest daily values: 50 to 70 ppb in the West; 40 to 60 ppb in the East
  Fourth-highest daily values: 40 to 60 ppb in the West; 30 to 50 ppb in the East
  Larger percentage of total ozone in the West than in the East
  Zero-out background ozone simulation results were generally higher than OSAT results, with differences largest in the East
  Average modeled contribution of boundary conditions to peak daily 8-hr ozone—and as a percentage of USB— is larger in the West than in the East
  Average modeled in-state anthropogenic contributions to ozone at the selected monitoring sites – 10-20% of total ozone, except at the Confederate Ave. site in Atlanta (32%)

## Slide 22: Summary of Findings (2)
Reducing on-road NOX emissions by 50%
  Reduced modeled fourth-highest ozone throughout most of the U.S.
  Outside of California, reduced ozone more in the East (2 to 8 ppb) than in the West (< 2 ppb); reduced ozone even more in the Southeast around Atlanta
  Increased ozone concentrations within several large urban areas (e.g., Los Angeles, San Francisco Bay Area, Seattle, Denver, offshore Chicago, and New York City), likely due to VOC-limited ozone chemistry

## Slide 23: Contact
sonomatech.com
Garnet Erdakos
Atmospheric Modeling Group
gerdakos@sonomatech.com
707.665.9900
sonomatech.com @sonoma_tech