## Slide 1: High-resolution air quality forecasting for Hong Kong
Christina Hood, Jenny Stocker, David Carruthers, William Grayson, Jonathan Handley, Jimmy Fung, David Yeung
16th Annual CMAS Conference
October 2017

## Slide 2: Outline
Motivation
ADMS-Urban Regional Model Link system
Hong Kong forecasting implementation
Computational performance
Concentration outputs
Further work

## Slide 3: Motivation
Current ‘air quality health index’ at 16 monitoring sites
aqhi.gov.hk

## Slide 4: Motivation
Current ‘air quality health index’ at 16 monitoring sites
Limited forecast (next day)
No detail for wider urban area
Personalised Real time Air quality Informatics System for Exposure (PRAISE-HK) project will
  Create high-resolution air quality forecast for Hong Kong
  Publish forecast via mobile app
  Include route planning and personal health alerts
praise.ust.hk

## Slide 5: ADMS-Urban Regional Model Link system
Combines regional model output (CMAQ, CAMx, EMEP4UK, CHIMERE, WRF-Chem) and local ADMS-Urban modelling for street-scale concentration output
Avoids double-counting emissions by separating regional and local modelling using ‘mixing time’
cerc.co.uk/RML
Concentration within nested domain | = | Regional modelling of emissions | - | Gridded locally modelled emissions (ΔT) | + | Explicit locally modelled emissions (ΔT)

## Slide 6: ADMS-Urban Regional Model Link system
Combines regional model output (CMAQ, CAMx, EMEP4UK, CHIMERE, WRF-Chem) and local ADMS-Urban modelling for street-scale concentration output
Avoids double-counting emissions by separating regional and local modelling using ‘mixing time’
Initial concept published 2012, automated system 2014
Developments since 2014:
  Support for CHIMERE and WRF-Chem added
  System re-built on Linux and automation increased
  Option to apply interpolation to regional model output
cerc.co.uk/RML

## Slide 7: ADMS-Urban RML Windows
Graphical interface, Run Manager for distributing runs across PCs

## Slide 8: ADMS-Urban RML Linux
RML Controller and Run Manager replaced by scripts
Graphical interface replaced by text input files
ADMS-Urban and utilities re-compiled for Linux

## Slide 9: Hong Kong Forecasting Implementation
Example 5x4 km domain

## Slide 10: Hong Kong Forecasting Implementation
Example 5x4 km high resolution domain
3 day forecast, run starts 4 am each day
7 output species
  NO2, NOx, O3, PM2.5, PM10, SO2, CO
Regional modelling from WRF and CMAQ
  Domain resolutions 27 km, 9 km, 3 km, 1 km
2010 emissions inventory
Output concentrations displayed in Google Maps
Trial period: 5th September – 2nd October 2017 (4 weeks)

## Slide 11: Hong Kong Forecasting Implementation
Output concentrations displayed in Google Maps

## Slide 12: Computational performance: run time
Short run time relative to regional modelling
  WRF 1.8 hours, CMAQ 2.5 hours, ADMS-Urban RML 25 minutes (all per forecast day)
ADMS-Urban RML run time dominated by ADMS-Urban local model runs with explicit sources
  varies with density of road segments

## Slide 13: Computational performance: File size
Total output file size for high-resolution domain smaller than CMAQ
File size normalised by output area larger than regional models due to increased output point density
  Average 4577 points/km2
  File size per output point smaller than CMAQ (fewer species)
Model domain | Extent cells |  | Cell size km | File size | 
 | x | y |  | Total MB | Norm MB/km2
CMAQ 3 km | 152 | 110 | 3 | 213 | 0.001
CMAQ 1 km | 179 | 125 | 1 | 278 | 0.012
ADMS-Urban RML | 5 | 4 | (1) | 66 | 3.300

## Slide 14: Concentration outputs: Time series

## Slide 15: Concentration outputs: Interpolation
Option to apply interpolation to regional model output
  Example PM2.5 concentrations for 16th September 2017 3pm local time

## Slide 16: Further work
Expand to bigger domain covering main urban areas of Hong Kong and Kowloon
  Example NO2 for 3pm local time 13th October 2017
CMAQ
ADMS-Urban RML
NO2 µg/m3

## Slide 17: Further work
Expand to even bigger domain covering HKSAR
Update emissions
  3D grid source in ADMS-Urban, automatic emissions conversion from CMAQ to ADMS-Urban
  Time-varying profiles for individual roads
Evaluate concentrations against all available monitors
Release initial app (late 2018)
Incorporate real-time traffic flow and concentration data
Calculate indoor concentrations from outdoor forecast
Include route planning and personalised alerts in app

## Slide 18: Thank you

## Slide 19: Extra slides

## Slide 20: System implementation
Concentration within nested domain | = | Regional modelling of emissions | - | Gridded locally modelled emissions | + | Explicit locally modelled emissions
Meso-scale meteorological data (WRF)
Emissions data
Meteorological data for use in local model
Regional model concentration output
Local upwind background
Local model
Gridded run for background (0.5 hr)
Local model
Main gridded run (ΔT)
Local model
Main explicit run (ΔT)
Nesting background
Key
Utility
Data
Model run
Regional model grid information