## Slide 1: The Load of Lightning-induced Nitrogen Oxides and Its Impact on the Ground-level Ozone during Summertime over the Mountain West States
Daiwen Kang1, Rohit Mathur1, Robert Gilliam1, George Pouliot1, David Wong1 , and Pius Lee2
Computational Exposure Division, National Exposure Research Laboratory, U.S. Environmental Protection Agency, Research Triangle Park
Air Resources Laboratory (ARL), NOAA, College Park, MD
16th Annual CMAS Conference
Chapel Hill, North Carolina, USA
23-25 October, 2017

## Slide 2: NO emissions from lightning strikes
Lightning is one of the major natural sources to produce NOX in the atmosphere
The global lightning NOX (LTNOX) production is estimated to be in the range 2-8 Tg N yr-1 (compare with present-day anthropogenic and biomass burning sources of ~26 Tg N yr-1; ~10-15% of the total NOX budget)
Lightning activity varies spatially over the course of a year, and consequently so do the NO emissions from lightning strikes.
The bulk of the lightning-induced NO is initially injected into the upper troposphere, but can eventually affect surface level air quality due to mixing and transport in the atmosphere.

## Slide 3: Lightning NO Production in CMAQ
To more accurately estimate lightning NO production, in CMAQv5.2, we enhanced the lightning NO production algorithm to utilize hourly NLDN (National Lightning Detection Network) lightning strike data.
The NO yield per lightning flash used in this study is 350 moles/flash.
The vertical distribution of lightning NO is the same in previous CMAQ versions, which is based on Pickering, et al. (1998, JGR).
Detailed model performance evaluations using lightning NO algorithms will be presented tomorrow afternoon at 2:40 in the Model Evaluation and Analysis section.

## Slide 4: Model configuration and simulations
Two-way Coupled WRF-CMAQ
Modeling System (WRF3.8 and CMAQ5.2) with WRF lightning assimilation (Heath et al., 2016)
Domains: 12km horizontal resolution with 35 vertical layers. (1) The continental US (2011) and (2) centered over Boulder, Colorado (2014)
Boundary conditions: hemispheric CMAQ simulations
Simulation period: April-September, 2011 and July-August, 2014
Emissions: 2011 NEI (for 2014 with 3 state specific oil/gas sector emissions and 2024-specific emissions for EGU/fire/biogenic sectors), NH3 bidi, inline biogenic emissions
Without lightning NO (Base) and with lightning NO (NLDN)

## Slide 5: Lightning strikes in July over MWS
Frequent lightning activity was observed over the Mountain West States (MWS) during summer time across many years. Even though the specific locations may change from year to year, the overall lightning strikes seem to be persistent (heavy lightning strikes formed a pattern extending from south-west to north-east).
2011
2012
2013
2014
2015
2016

## Slide 6: Lightning strikes in August over MWS
The lightning strike pattern in August is different from that in July, but significant frequency of strikes still occurs across the years
2011
2012
2013
2014
2015
2016

## Slide 7: Lightning NO emissions in July over MWS
The total column lightning NO emissions when estimated from lightning strikes using the CMAQ lightning production algorithm.
2011
2012
2013
2014
2015
2016

## Slide 8: Lightning NO emissions in August over MWS
Same as last slide, but for August
2011
2012
2013
2014
2015
2016

## Slide 9: Major sources for NOX emissions over MWS
July
August
Total Anthropogenic
Soil
Lightning

## Slide 10: Contribution of Lightning to NO Budget over MWS
The lightning NO emissions contribute up to 50% of the total NOX emissions on specific days in this region and the overall monthly contribution for both months is about 30% of the total NOX emissions.

## Slide 11: Model performance with lightning NO
MB Difference
(NLDN-Base)
Lighting Strikes
AQS
Base
NLDN
MB Difference
(NLDN - Base)
July, 2011
MB Difference (NLDN - Base)

## Slide 12
Lidar Measurements and Model Simulations during DISCOVER-AQ Denver 2014 Field Study
The TOLNet Lidar Ozone (O3) data is available during July and August, 2014
Lidar provides temporal and vertical characteristics of the observed O3
Two-way coupled WRF-CMAQ simulation with/without lightning NO were performed during this period over the 12km domain centered over Colorado.
12km CMAQ domain
Lidar Measurement at The Boulder Atmospheric Observatory (BAO) ESRL Site

## Slide 13
Daily maximum O3 concentrations across the vertical model layers that have Lidar observations
Identify episodic time periods when the model significantly under or over estimated the observed values.
July 26-29:
Greatest O3 mixing ratios were observed, but not captured by the model
Lidar
Base
NLDN

## Slide 14
Max daily O3 (Lidar) and the 24-hr lightning strikes in the vicinity of the location
LTStrike: the sum of the lightning strikes in about 100x100 km2 area centered at BAO Site. This is only a qualitative analysis in terms of the LTStrike impact on O3 production without considering the effects of transport and mixing. But the correlation is rather surprising and the correlation coefficient for July is close to 0.7.
Lightning Active Days

## Slide 15
24-hour lightning strikes detected by the National Lightning Detection Network
July 26
July 27
July 28
July 29
BAO Site

## Slide 16
Lidar and Model Predicted Hourly O3 Profiles
July 26
July 27
July 28
July 29
Mid-Layer Height(m)
Lidar observations show that higher O3 levels were always initiated at the upper middle layers during the photo-chemically active hours, but the model case without lightning NO completely missed the episode.
July 26
July 27
July 28
July 29
Lidar O3 gridded into the model vertical layers
CMAQ (Base) predicted O3 vertical profiles
Hour (MDT)
Hour (MDT)

## Slide 17
Lidar and Model Predicted Hourly O3 Profiles
July 26
July 27
July 28
July 29
Mid-Layer Height(m)
When lightning NO is included in the model simulation, the predicted O3 levels were elevated and came closer to the observed values.
July 26
July 27
July 28
July 29
Lidar O3 gridded into the model vertical layers
CMAQ (NLDN) predicted O3 vertical profiles
Hour (MDT)
Hour (MDT)

## Slide 18
Simulated Hourly O3 difference (NLDN – Base)
When lightning NO is included, the O3 mixing ratios:
Mainly decreased on July 26 at upper layers with significant decrease after 12 pm across all vertical layers.
Increased from July 27 to 29 with significant increase on the last two days (up to 20 ppb increase on July 29)
July 26
July 27
July 28
July 29
Hour (MDT)
Mid-Layer Height(m)

## Slide 19
Observed and Simulated Maximum Hourly O3 Across Vertical Layers (1-19)
From July 26 to July 29, the Base model changed from overestimation to significant underestimation
Inclusion of lightning NO reduced the overestimation on July 26, and also reduced the underestimation on July 28 and 29.
This episode led to the increase of surface O3 mixing ratios by almost 20 ppb
Mid-Layer Height(m)
July 26
July 27
Lidar
Base
NLDN
July 28
July 29
O3 (ppb)
O3 (ppb)
O3 (ppb)
O3 (ppb)
O3 (ppb)
O3 (ppb)
O3 (ppb)

## Slide 20
Observed and Simulated Maximum Hourly O3 Across Vertical Layers (1-30)
The same as the previous slide, but show the model predicted vertical profiles beyond the range of the Lidar measurements.
The high O3 mixing ratios were formed in the upper troposphere and not transported down from stratosphere.
Mid-Layer Height(m)
July 26
July 29
July 28
July 27
Lidar
Base
NLDN
O3 (ppb)
O3 (ppb)
O3 (ppb)
O3 (ppb)

## Slide 21: Summary
Lightning strikes produce significant amount of NOX in the Mountain West States during summer time; the CMAQ calculated lightning NO emissions contributed up to 50% of the total column NOX budget on a daily basis and 30% on a monthly basis.
Model simulations including lightning NO captured the variability in surface and aloft measured O3 much better than the case without lightning NO.
With lightning NO, the modeled O3 vertical profiles were significantly improved compared with Lidar measurements.
During the 4-day episode (July 26-29, 2014), the surface O3 mixing ratios were observed to be elevated by more than 20 ppb, which are attributable to lightning NO emissions.

## Slide 22
Animation of lightning strikes and surface O3 difference
Layer 1 O3 (NLDN – BASE)
Hourly NLDN Strikes

## Slide 23
Acknowledgement
We thank NASA for the Tropospheric Ozone Lidar Network (TOLNet) and NOAA Earth System Research Laboratory (ESRL) for the Lidar data used in the analysis.