## Slide 1: Air Quality Impacts of Projections of Natural Gas-Fired Distributed Generation
Jeremy R. Horne, Marc Carreras-Sospedra, Donald Dabdub
K. Max Zhang, Bo Yang
Paul Lemar
Uarporn Nopmongcol, Tejas Shah, Greg Yarwood
David Young, Stephanie L. Shaw, Eladio M. Knipping
CMAS Conference, 2017
Resource Dynamics Corporation

## Slide 2: Centralized vs. Distributed Generation
Central Power Plant
DG
lost excess heat
helectric = 40-60%
fuel in
lost excess heat
helectric = 30-40%
hthermal = 30-40%
hTotal = 60-80%
hTotal = 40-60%
CHP
Combined Heating and Power (CHP) for DG

## Slide 3: Outline
Single-source, near-field air quality modeling of fossil-fueled distributed generation
Regional air quality modeling of future scenarios of fossil-fueled distributed generation deployment
Resource Dynamics Corporation

## Slide 4: Single-source, near-field air quality modeling of fossil-fueled distributed generation

## Slide 5: Comprehensive turbulent aerosol dynamics and gas chemistry (CTAG) model
Computational fluid dynamics (CFD)-based turbulent reacting flow model for complex atmospheric environments
Extensive evaluated for transportation air quality applications with over 20 peer reviewed publications
This project provided an opportunity to further develop, evaluate and implement CTAG for stationary sources.

## Slide 6: Plume Environment : Experiment : Evaluation
Jet-dominated region
Ambient-dominated region
Building-dominated region

## Slide 7: Case study: Simple-cycle NG turbine w/ and w/o heat recovery
More accurate
Method: A new integrated modeling framework
Analysis
A new concept called the heat recovery amplified factor (HRAF), defined as the ratio between the maximum ground-level concentrations (GLC) with HR system and that without HR system, as an indicator of HR impact
We investigated the HR impact on NOx concentrations near a simple cycle gas turbine located in Brentwood, NY, and found very small GLCs (<10 ppb)
HRAF was shown to be much more sensitive to temperature in the Unstable, Low Wind condition than in the Stable, High Wind condition
More computationally efficient
Yang and Zhang, manuscript submitted
GLC
HRAF

## Slide 8: Case study: Distributed Combined and Heat Power Facility
CHP
Tall building
Tall building
CHP
A comparison between the measured emission rates in 2010 and 2015 did not reveal significant difference.
NOx (ppb)
CTAG simulations using measured emission rates as inputs suggest low ground level concentrations of air pollutants.
Yang and Zhang, manuscript in preparation

## Slide 9: Regional air quality modeling of future scenarios of fossil-fueled distributed generation deployment
Resource Dynamics Corporation

## Slide 10: Regional Air Quality Modeling: Workflow
Projection of Future DG Deployment
US-REGEN Modelling of Central EGUs
Emissions Processing for Central EGUs
Air Quality Modeling
Spatial Allocation of DG
Emissions Processing for DG
Resource Dynamics Corporation
Notes: The regional air quality modeling project brings together several teams of researchers. First, RDC (experts on the economics and deployment of CHP/DG systems) will project the deployment of these units from present-day to 2050. This information is used in order to displace central-station EGUs in the REGEN model and the new make-up of the central-station fleet is determined. Using the “unit commitment” mode of the US-REGEN model, electricity generation from different units is calculated and this information is sent to Ramboll-ENVIRON for emissions processing. In parallel, RDC determine the spatial (and temporal) allocation of CHP/DG generation and this information is sent to UCI for emissions processing. UCI takes together the processed emissions from CHP/DG and central-station EGUs and performs the final air quality simulations.
The circles with black bold outlines are those activities on which we’ve made significant progress to date. We expect work to ramp up on all circles of this flowchart and to have results available to present late this year.

## Slide 11: National Assessment of DG Market Potential
Factors to estimate DG market potential
  Utility electricity tariffs, monthly state gas prices
  DG/CHP price and performance information
  Database of manufacturing facilities and commercial buildings with load characteristics
  Economic incentives for CHP

## Slide 12: Economic Potential, by Sector and DG/CHP Classification to 2050
Chart: Economic Potential (MW)
| Base Case | Aggressive DG | AggDG + $4 Gas
CHP - Commercial | 4300 | 5685 | 8650
CHP - Industrial | 9298 | 10462 | 13454
DG - Commercial | 437 | 3160 | 10782
DG - Industrial | 0 | 965 | 6440
The “Base Case” (“Low DG”) and the “Aggressive Case with $4 Natural Gas” (“High DG”) were used for air quality modeling
Notes: This is directly from RDC (I haven’t had time to edit in my own words, but it would simplify what is stated. Note that economics reflect a <10 yr payback period.
In 2014, a National assessment of DG/CHP potential for EPRI was conducted using RDC’s DISPERSE model, with about 14 GW of total economic CHP potential found across the United States
  Utility electricity tariffs, monthly state gas prices, and DG/CHP price and performance information used to evaluate economics
  Estimated total economic potential using database of manufacturing facilities and commercial buildings with load characteristics; known existing CHP installations were identified and removed from results
  Due to benefits of thermal energy and 10% investment tax credit (ITC) for CHP systems, CHP was economically favorable to power-only DG
A market adoption model was applied to the results of 2014 Assessment, estimating potential adoption through 2050 assuming economics remain similar and pool of potential sites unchanged
For this assessment, more aggressive price and performance parameters were considered, favoring power-only DG installations; also, a sensitivity was performed using $4/MMBtu natural gas price
The Aggressive DG price and performance provided stronger economics for power-only DG applications, but lower installed costs also improved the economics for some CHP installations
  Value of recovered thermal energy is still an important economic factor
Lowering the cost of gas to $4/MMBtu had more of an effect on DG economics, creating larger spark spread and limiting the value of thermal energy from potential CHP applications
  The $4/MMBtu gas sensitivity nearly doubled the estimated economic potential for the Aggressive DG scenario

## Slide 13: Projected Market Adoption of DG through 2030
Adoption increases over time as new customers adopt DG
  Based on applying adoption percentages total economic potential
  Decision to adopt re-evaluated every 5 years
Market adoption in 2030 used for:
  Modeling of central EGUs
  Spatial allocation of DG
Chart: Year
| 2015 | 2017 | 2020 | 2022 | 2025 | 2030
Low DG | 581.6625 | 1765.875 | 3126.675 | 3935.3202 | 4862.025 | 6179.875
Medium DG | 1345.8725 | 3946.7085 | 6744.88 | 8133.3725 | 9684.5325 | 11685.0825
High DG | 2810.6475 | 8426.4912 | 14042.335 | 16975.7065 | 20078.835 | 24137.2425
Payback Period | Likelihood of Adoption
0-1 year | 100%
1-2 years | 67%
2-3 years | 60%
3-4 years | 37%
4-5 years | 37%
5-6 years | 18%
6-7 years | 10%
7-10 years | 5%

## Slide 14: Spatial Allocation of DG in 2030
Total installed capacity for the Low DG Scenario is 7.6 GW Total installed capacity for the High DG Scenario is 25.4 GW
Low DG Penetration Scenario High DG Penetration Scenario

## Slide 15: Emission Factors
Emission factors account for geographical differences in regulations
NOX
VOC
CARB Limits
CARB Limits
Notes: Emission factors and emission limits are compiled from the DER technology survey “The Evolving Emissions Profile of Distributed Energy Resource Technologies” (EPRI, 2015). DG units with size <1 MW – 5 MW are assumed to be RICE. DG units with size 5+ MW are assumed to be gas turbines. The emission factors used for the baseline and aggressive $4 gas cases are based on the maximum value reported from manufacturer/test data, with the constrain that they cannot exceed the regional emission limits applicable:
DG emission factor = MIN ( MAX(manufacturer data, test data) , Regional Emission Limits )
If no regulatory limit , emission factors are based on manufacturer data, test data, and literature sources. See section 4 of the methodology report.

## Slide 16: Low DG Penetration – Summer O3 Impacts
Peak delta in maximum daily 8-hr average O3 during summer episode

## Slide 17: High DG Penetration – Summer O3 Impacts
Peak delta in max daily 8-hr average O3 during summer episode

## Slide 18: CARB Certification Scenario – Summer O3 Impacts
Peak delta in max daily 8-hr average O3 during summer episode

## Slide 19: Low DG Penetration – Winter PM2.5 Impacts
Peak delta in 24-hr average PM2.5 during winter episode

## Slide 20: High DG Penetration – Winter PM2.5 Impacts
Peak delta in 24-hr average PM2.5 during winter episode

## Slide 21: CARB Certification Scenario – Winter PM2.5 Impacts
Peak delta in 24-hr average PM2.5 during winter episode

## Slide 22: Conclusions – Regional Impacts of DG
Northeast and southwest are most impacted by DG
  Some effects in the southeast, mostly due to changes in EGU emissions in FL (based on dispatch model results)
Implementing CARB limits minimizes impact of DG on O3 and PM2.5
  CA and NEUS see the greatest air quality benefits

## Slide 23: Manuscript Now Available Regional Modeling
J.R. Horne, M. Carreras-Sospedra, D. Dabdub, P. Lemar, U. Nopmongcol, T. Shah, G. Yarwood, D. Young, S.L. Shaw, E.M. Knipping. Air quality impacts of projections of natural gas-fired distributed generation. Atmospheric Environment 2017. 168, 8-22.
https://doi.org/10.1016/j.atmosenv.2017.08.046

## Slide 24: Manuscripts Available, Submitted and In Preparation Single-Source Modeling
Yang, B., & Zhang, K. M. (2017) CFD-based turbulent reactive flow simulations of power plant plumes. Atmospheric Environment 2017. 150, 77–86. https://doi.org/10.1016/j.atmosenv.2016.11.049
Yang, B., & Zhang, K. M. The effect of heat recovery on near-source plume dispersion of a simple cycle gas turbine. Manuscript submitted to Atmospheric Environment.
Yang, B., & Zhang, K. M. The near-source impacts of a distributed combined and heat power facility: Emission characterization and numerical simulations. Manuscript in preparation