## Slide 1: Assessing the Combustion Performance, Emissions, and Air Quality (AQ) Impacts of Renewable Fuel Blending in the Natural Gas System in California
Michael Mac Kinnon, Ph.D.
Senior Scientist
Advanced Power and Energy Program
University of California, Irvine

## Slide 2: Introduction and Motivation
Interest in increasing the use of renewable gaseous fuels in California as a means of decarbonizing end-use sectors
  Biomethane and hydrogen from renewable sources
    Power-to-Gas
Injection into the existing natural gas grid as a means of storage and transmission

## Slide 3: Natural Gas System Evolution
Fossil Gas
(CH4)
Fossil & Renewable Gas (CH4 & H2)
Renewable Gas
(H2)
Potential pathway to a near-zero emission, renewable gas system
  Renewable H2 converted by fuel cells for generation and motive power
  Provide remaining energy portion not met by electrification
Electrochemical
Combustion
Complementary Generation
Challenging Sectors to Electrify
All End-use Sectors
Challenges and Research Areas
Combustion performance, emissions, and AQ impacts of NG/H2 blends
H2 production and dynamics
Leakage from NG pipeline
NG pipeline material impacts (embrittlement, fatigue)
Economic viability

## Slide 4: Potential Emissions and AQ Impacts
Varying fuel composition can impact combustion devices optimized for operation on unadulterated natural gas
  Performance – stability, efficiency, emissions, etc.
Investigate the potential impact of emissions on AQ in California
  Provide technical insight on how to maximize the GHG and AQ co-benefits of renewable fuels
?
?
Notes: Electricity generation, industry, service, residential, commercial

## Slide 5: Approach – Combustion and Emission Impacts
Assessed emission impacts of fuel blending for nine industrial burners
  Requires numerical models (CFD) and reaction mechanisms with detailed chemical kinetics (CRN)
  3 burner types experimentally validated
Colorado, Andres; McDonell, Vincent. (University of California Irvine, Combustion Laboratory- UCICL). 2016. Effect of Variable Fuel Composition on Emissions and Lean Blowoff Stability Limits. California Energy Commission. Publication number: 500-13-004
Fuels | Mixture
Hydrogen | 76% CH4 - 24% H2
Biogas | 98% CH4 - 2% CO2
Ethane | 94% CH4 - 6% C2H6
Propane | 95% CH4 - 5% C3H8
Industrial Burners
Low-swirl Burner (LSB)
Surface Stabilized Burner (SSB)
Micro Turbine Combustor (MTC)
Oxygas Burner
High Speed Jet Burner (HSJ)
Gas Turbine Combustor (GTC)
Radiant Tube (RT)
Infrared Burner (IRB)
Slot Burner (SB)
CFD solution alone not able to predict NOx shift
Good agreement between UCI method and experimental data
H2 addition increases NOx
Notes:   Computational fluid dynamics and chemical reactor networks for all 9
  Experimental validation at UCICL for (1) The low-swirl burner (LSB), (2) surface stabilized combustion burner (SSCB) and (3) a micro-turbine combustor (MTC)

## Slide 6: Results – Combustion and Emission Impacts
Quantified change in NOx and CO emissions for renewable fuel blends relative to operation on 100% Natural Gas (CH4)
  Significant variation for burners, pollutants, and fuels
 | 1. LSB |  | 2. SSB |  | 3. MTC |  | 4. Oxygas |  | 5. HSJ | 
Fuel Mixture (% by volume w/ CH4) | NOx | CO | NOx | CO | NOx | CO | NOx | CO | NOx | CO
Hydrogen (24%) | 111% | -40% | -64% | -40% | 200% | -50% | 16% | -20% | 48% | -11%
Biogas (2% CO2) | -5% | 11% | -3% | 3% | -17% | 1% | -4% | 3% | -2% | 3%
Ethane (6%) | 5% | 8% | 2% | 3% | 3% | 4% | 5% | 8% | 3% | 4%
Propane (5%) | 9% | 3% | 3% | 6% | 5% | 4% | 4% | 6% | 8% | 5%
 | 6. GTC |  | 7. RT |  | 8. IRB |  | 9. SB |  |  | 
Fuel Mixture | NOx | CO | NOx | CO | NOx | CO | NOx | CO |  | 
Hydrogen (24%) | -20% | -50% | 233% | -35% | -60% | -10% | 58% | -13% |  | 
Biogas (2% CO2) | -3% | 0% | -2% | 2% | -3% | -3% | -2% | 5% |  | 
Ethane (6%) | 3% | 3% | 0% | 4% | 2% | -5% | 3% | 4% |  | 
Propane (5%) | 3% | 3% | 5% | 4% | 1% | -5% | 8% | 6% |  | 
Key (NOx/CO)
% Increase
% Decrease
No Change

## Slide 7: Approach – Scenario Development
Scale-up to economy-wide scenarios in California in 2035
  Requires detailed understanding of feasible applications in energy sectors
  Three burner types mapped – Micro Turbine Combustor, Gas Turbine Combustor, and Surface Stabilized Burner
Surface Stabilized Burner
Food and Agriculture
Oil and Gas
Manufacturing/Industrial
Service/Commercial
Process Heaters
Steam – Pasteurization
Heater-treater
Oil Heating - pumping
Notes: Alzeta SSL
Oil and gas water separator, heater treater
  Oil heaters at pumping stations to pull something out, transmission
  Everything but reciprocating engines
  They are already in that market
  FLUID HEATING
Service and Commercial
  Anything for steam generation
Food and Ag
  Making steam at milk processing plant (CA dairies)
  Juice pasteurizing (Naked juice)
  Not radiant heat ovens like cooking but like steam being generated
  Indirect heat for milk drying
  No reason it couldn’t be
Manufacturing and industrial
  Steam generation yes
  Other things no
  Semi-conductor manufacturing major client
Petroleum Refining
  No
Electricity and Co-Gen
  No
Trends applicable for all SSL

## Slide 8: Results – Scenario Development
Burner Type | Fuel Injection | NOx Impact | CO Impact | Impacted Sources
Gas Turbine Combustor (GTC) | Hydrogen | -20% | -50% | Electric Utility (turbines) Cogeneration (turbines) Manufacturing and Industrial (turbines) Service and Commercial (turbines)
 | Biogas | -3% | None | 
Micro Turbine Combustor (MTC) | Hydrogen | +200% | -50% | Electric Utility (turbines) Cogeneration (turbines) Manufacturing and Industrial (turbines) Service and Commercial (turbines)
 | Biogas | -17% | +1% | 
Surface Stabilized Burner (SSB) | Hydrogen | -64% | -40% | Oil and Gas (process heaters, boilers) Manufacturing and Industrial (boilers) Service and Commercial (boilers, water heaters) Food and Ag (process heaters)
 | Biogas | -3% | +3% | 

## Slide 9: Results – Total NOx and CO Emissions
Chart: 2035 CA NOX Emissions
Off-road Vehicles | 486.5219
On-road Vehicles | 328.3558
Industry | 183.7131
Residential | 60.7019
Electricity | 54.4832
Service/Commercial | 52.4893
Miscellaneous/Other | 33.6464
Net emission impacts in 2035 are generally beneficial
  Exception for NOx MTC operating on H2
  Biogas cases has small impact
Chart: Tons per Day
| GTC_H2 | MTC_H2 | SSBL_H2 | GTC_BG | MTC_BG | SSBL_BG
NOx | -3.2165 | 16.0826 | -37.1134 | -0.4825 | -2.734 | -1.7399
CO | -6.9426 | -6.9426 | -14.8163 | 0 | 0.1389 | 1.1112
Hydrogen Cases
Biogas Cases
GTC
MTC
SSB
GTC
MTC
SSB
Potential Impacts on NOx
H2: -3.1% to +1.3%
BG: Up to 0.2% reduction
Notes: Points:
Hydrogen has a larger impact than biogas which makes sense as biogas is CO2. There are other concerns with biogas related to air toxics generated from contaminants.
The SSBL case has a much larger impact overall due to the sources it impacts, i.e., industrial emissions.

## Slide 10: Approach – Air Quality Modeling
Simulations of atmospheric chemistry and transport
  AQ Model: CMAQ 5.2 w/ 4 km x 4 km grid, Emissions: SMOKE 4.0
  Two seasonal episodes: WRF 3.7
    Summer (July 8-21) for ozone & PM2.5 concentrations
    Winter (January 1-14) for PM2.5 concentrations
Summer 2035 1-hr Ozone
Winter 2035 24-hr PM2.5
Notes:   Model performance evaluation from CARB hourly ozone (145 stations) and daily PM2.5 (17 stations) data
    Mean normalized bias and mean normalized gross error within acceptable parameters according to guidelines from the U.S. EPA

## Slide 11: MTC and GTC H2 – Summer Ozone
-0.10 ppb Max 8-hr O3
+0.49 ppb Max 8-hr O3
MTC H2 Case
200% Increase in NOx Emissions
GTC H2 Case
20% Decrease in NOx Emissions
Notes: These results demonstrate the impact on maximum 8-hr average ground-level ozone from the changes in Nox emissions presented last slide. As would be expected the MTC Case results in worse AQ (increasing ozone levels) and the GTC Case improves AQ (reducing ozone levels). The changes in ozone scale to the emission reductions with peak impacts in the MTC Case an order of magnitude higher due to all impacted sources in the cases being exactly the same (this wouldn’t be true if different sources were impacted). In particular, large natural gas power plants in the south central valley have a major impact. Overall it should be noted that the impacts are fairly minor as the standard for max 8-hr ozone is 75 ppb and the impacts in the MTC Case is .49 ppb. This is because the electricity sector in CA is relatively low-emitting overall due to stringent environmental regulations leading to high levels of renewables and cleaner natural gas plants.

## Slide 12: SSBC H2 – Summer Ozone and Short-term Health Impacts
-0.75 ppb Max 8-hr O3
SSBL H2 Case: 64% Decrease in NOx
Short-term Health Impacts from BenMAP-CE
Ozone -Summer
̴$386,000/day
Notes: These results demonstrate the impact on NOx emissions and ground-level ozone for the SSBL H2 case. The results highlight the importance of how emissions from different sectors and sources impact air pollution differently. For example, the SSBL burners are used in different industries that impact ozone in Northern California while the MTC and GTC impact the Bay Area and Central Valley. Further, the 64% decrease achieves a greater peak impact on ozone in terms of magnitude as the MTC case with a 200% increase.

## Slide 13: SSBC H2 – Summer and Winter PM2.5
SSBL H2 Case: 64% Decrease in NOx
SSBL H2 Case: 64% Decrease in NOx
-0.08 ug/m3 24-hr PM2.5
-0.64 ug/m3 24-hr PM2.5
Notes: These results demonstrate the impact on NOx emissions and ground-level ozone for the SSBL H2 case. The results highlight the importance of how emissions from different sectors and sources impact air pollution differently. For example, the SSBL burners are used in different industries that impact ozone in Northern California while the MTC and GTC impact the Bay Area and Central Valley. Further, the 64% decrease achieves a greater peak impact on ozone in terms of magnitude as the MTC case with a 200% increase.

## Slide 14: Next Steps
Source Impacts
Complete industrial burners – Funded
Residential/commercial appliances – Funded
Integrated source impacts – Funded
Spatial consideration of resource blending
Integrated planning document for managing potential impacts in California
Reciprocating engines
Project Goal
Quantification and monetization of short-term and long-term health impacts via BenMAP-CE
Health Impacts
Scenarios

## Slide 15: Conclusions
Use of existing NG system potentially important mechanism to store and transport renewable gaseous fuels including hydrogen and biomethane
  Achieve GHG policy targets, complement renewable generation
  Technically feasible but significant challenges must be addressed
Renewable fuel blending can reduce or increase emissions from end-uses
  Dependent on fuel mixture, burner configuration, pollutant species, etc.
AQ impacts of industrial burners vary by region and season
  Generally, minor improvements are expected for assessed cases
Future burner deployment strategies may require foresight
  Certain areas may require specific burner types, others may not
  Seasonal impacts may require seasonal mitigation strategies

## Slide 16: Acknowledgements
UCI
  Professor Vince McDonnell
  Professor Andres Colorado
  Dr. Marc Carreras-Sospedra
  Dr. Shupeng Zhu
  Professor G. Scott Samuelsen
  Dr. Li Zhao
  Jeremiah A. Blackburn
  Alejandra Hormaza-mejia
California Energy Commission
  Marla Mueller
  Yu Huo
Thank You!
mam@apep.uci.edu

## Slide 17: Backup Slides

## Slide 18: Electrolysis
Proton Exchange Membrane Electrolyzer
Water reacts at the anode to form oxygen and positively charged hydrogen ions (protons)
The electrons flow through an external circuit and the hydrogen ions selectively move across the PEM to the cathode
At the cathode, hydrogen ions combine with electrons from the external circuit to form hydrogen gas.

## Slide 19: Power-to-Gas (P2G)
Use excess renewable electricity to generate H2 or CH4 ( after methanation) to complement dynamics of solar and wind
  Support renewable integration by providing seasonal-scale storage, grid management and renewable energy transportation and distribution

## Slide 20: Economic Viability
Levelized Cost of Returned Energy (LCORE)
  Future Costs & Efficiencies
  50% capacity factor for all equipment

## Slide 21
Test commercially available mitigation measure
  Copper epoxy applied (Ace Duraflow®)
Chart: Day of Test
| 0 | 6.25E-2 | 0.125 | 0.1875 | 0.25 | 0.3125 | 0.375 | 0.4375 | 0.5 | 0.5625 | 0.625 | 0.6875 | 0.75 | 0.8125 | 0.875 | 0.9375 | 1 | 1.0625 | 1.125 | 1.1875 | 1.25 | 1.3125 | 1.375 | 1.4375 | 1.5 | 1.5625 | 1.625 | 1.6875 | 1.75 | 1.8125 | 1.875 | 1.9375 | 2
H2 | 46.8258 | 46.5488 | 46.5488 | 46.2717 | 45.7175 | 45.4405 | 45.1634 | 44.8863 | 44.8863 | 44.6092 | 43.778 | 43.2239 | 42.9468 | 42.9468 | 43.2239 | 43.5009 | 43.778 | 44.0551 | 44.6092 | 44.6092 | 44.0551 | 43.778 | 43.5009 | 43.2239 | 42.9468 | 42.6697 | 42.1156 | 41.5614 | 41.5614 | 42.1156 | 42.9468 | 43.5009 | 43.778
10% | 46.2717 | 47.38 | 47.6571 | 47.38 | 47.1029 | 47.1029 | 47.1029 | 47.1029 | 46.8258 | 46.5488 | 45.7175 | 45.7175 | 45.7175 | 45.9946 | 47.1029 | 46.8258 | 46.8258 | 47.1029 | 47.6571 | 47.1029 | 46.8258 | 46.8258 | 46.8258 | 46.5488 | 46.5488 | 46.2717 | 45.7175 | 44.6092 | 44.8863 | 44.8863 | 45.4405 | 45.7175 | 45.7175
NG | 46.8258 | 46.2717 | 46.5488 | 46.8258 | 47.6571 | 48.2112 | 48.2112 | 48.4883 | 48.4883 | 48.2112 | 47.9341 | 47.9341 | 47.9341 | 47.9341 | 47.9341 | 47.1029 | 46.8258 | 46.8258 | 46.8258 | 47.38 | 47.6571 | 47.9341 | 47.6571 | 48.4883 | 48.2112 | 47.9341 | 47.6571 | 47.6571 | 47.6571 | 47.38 | 47.1029 | 46.2717 | 45.7175
H2 - Original | 45.705 | 45.151 | 43.212 | 40.719 | 38.78 | 36.287 | 34.348 | 32.409 | 31.024 | 29.639 | 28.808 | 27.977 | 27.146 | 26.592 | 25.484 | 24.376 | 23.268 | 22.991 | 22.714 | 22.437 | 21.606 | 20.498 | 19.667 | 18.559 | 17.728 | 16.897 | 16.62 | 15.789 | 14.958 | 14.127 | 13.85 | 13.019 | 12.465 | 12.465
NG - Original | 46.813 | 44.597 | 42.381 | 40.442 | 38.503 | 36.841 | 35.179 | 33.517 | 32.132 | 30.747 | 28.808 | 27.423 | 26.592 | 26.592 | 26.592 | 26.592 | 25.761 | 25.207 | 23.822 | 22.991 | 21.883 | 20.775 | 20.221 | 19.39 | 18.559 | 17.451 | 0 | 15.789 | 15.512 | 15.789 | 16.066 | 17.451 | 16.066 | 15.512
10% H2 - Original | 46.8194 | 43.772 | 41.4173 | 38.924 | 36.8462 | 34.6299 | 32.6906 | 30.8899 | 29.3661 | 27.8425 | 26.3188 | 24.7951 | 23.5485 | 22.4403 | 21.7476 | 21.055 | 20.501 | 19.947 | 19.5315 | 18.8389 | 18.0078 | 17.3152 | 16.3455 | 15.6529 | 15.0988 | 14.1292 | 13.4367 | 12.4671 | 11.7745 | 11.4974 | 11.4973 | 11.4972 | 11.7743 | 0
Original
After application
Impacts: System Leakage

## Slide 22
Conducted laboratory testing of existing customer-side infrastructure
  Preliminary results indicate NG, H2/NG mixtures, H2 leak at same rate
Chart: Day of Test
| 0 | 0.125 | 0.25 | 0.375 | 0.5 | 0.625 | 0.75 | 0.875 | 1 | 1.125 | 1.25 | 1.375 | 1.5 | 1.625 | 1.75 | 1.875 | 2 | 2.125 | 2.25 | 2.375 | 2.5 | 2.625 | 2.75 | 2.875 | 3 | 3.125 | 3.25 | 3.375 | 3.5 | 3.625 | 3.75 | 3.875 | 4 | 4.125 | 4.25 | 4.375 | 4.5 | 4.625 | 4.75 | 4.875 | 5 | 5.125 | 5.25 | 5.375 | 5.5 | 5.625 | 5.75 | 5.875 | 6 | 6.125 | 6.25 | 6.375 | 6.5 | 6.625 | 6.75 | 6.8750000000002798 | 7.0000000000011804
NG | 46.1793 | 45.2557 | 43.6856 | 41.6538 | 39.8989 | 38.5136 | 38.3288 | 39.1601 | 39.8989 | 38.6983 | 36.9435 | 35.0963 | 33.8956 | 32.972 | 32.8797 | 33.5262 | 34.2651 | 33.7109 | 31.8637 | 30.5707 | 29.2777 | 28.1694 | 27.8 | 28.3541 | 29.0006 | 28.5388 | 27.3382 | 26.1375 | 25.491 | 24.3827 | 24.1056 | 25.3063 | 26.4146 | 26.5993 | 25.6757 | 24.5674 | 23.9209 | 23.182 | 22.8126 | 23.8285 | 24.8445 | 25.0292 | 24.475 | 23.6438 | 23.0897 | 22.0737 | 22.0737 | 23.2744 | 24.0133 | 24.1056 | 23.3667 | 22.3508 | 21.5196 | 20.596 | 20.5036 | 20.7776 | 23.5479
10% H2 | 46.8258 | 46.3641 | 44.8863 | 43.5009 | 42.8544 | 42.485 | 41.469 | 41.469 | 41.7461 | 39.8989 | 39.4372 | 37.9594 | 36.7587 | 36.297 | 35.5581 | 36.1122 | 36.297 | 35.4657 | 34.7269 | 33.4338 | 32.3255 | 32.1408 | 31.5867 | 32.2332 | 32.6026 | 32.2332 | 30.8478 | 29.7395 | 29.3701 | 29.0006 | 28.8159 | 29.3701 | 29.3701 | 29.093 | 28.077 | 26.8764 | 26.2299 | 25.491 | 24.8445 | 25.491 | 26.3222 | 26.4146 | 25.3063 | 24.3827 | 23.7362 | 23.2744 | 23.4591 | 24.2903 | 25.491 | 25.1216 | 23.182 | 21.6119 | 21.2425 | 20.596 | 20.7807 | 22.9049 | 23.69
Impacts: System Leakage

## Slide 23: Water Consumption
Water consumption for P2G provision of hydrogen fuel for the entire LDV sector in California in 2050
  Very small fraction of key Northern California (0.02%) and Southern California (0.11%) supply reservoirs

## Slide 24: BenMAP Summary
Case | Pollutant | Premature Deaths Avoided, All Causes | Reduced Morbidity Incidence | Total
GTC Summer | Ozone Exposure | -31.98 | -1.03 | -98.48
 | PM2.5 Exposure | -62.76 | -2.71 | 
MTC Summer | Ozone Exposure | 8.61 | 0.27 | 21.63
 | PM2.5 Exposure | 12.23 | 0.52 | 
SSB Summer | Ozone Exposure | 239.38 | 6.77 | 385.70
 | PM2.5 Exposure | 133.89 | 5.67 | 
Valuation of health effects from short-term exposure
  Thousands of $ per day

## Slide 25: Health Impact Assessment
BenMAP-CE 1.3 to quantify and monetize health impacts
  Daily avoided costs in $/day for the SSB Case in Summer

## Slide 26: Health Effects: Incidence
Premature Deaths Avoided, All Cause |  |  | 
Endpoint - Health Effects Estimates (# incidences/ppl/yr) | SSB - Summer | MTC - Summer | GTC-Summer
Short-Term Ozone Exposure | 0.0189 (0.0021 ; 0.0357) | -0.0025(-0.0048 ; -0.0003)" | 0.0007(0.0001 ; 0.0013)
Short-Term PM2.5 Exposure | 0.0106 (0.0081 ; 0.0130) | -0.0049(-0.0038 ; -0.0061)" | 0.0010(0.0007 ; 0.0012)
Reduced Morbidity Incidence: Short-Term Ozone Exposure |  |  | 
Emergency Room Visits, Asthma | 0.3461 (0.0624 ; 0.6289) | -0.0557(-0.0100 ; -0.1014)" | 0.0141(0.0025 ; 0.0256)
Hospital Admissions (HA), All Respiratory | 0.0214 (-0.0064 ; 0.0491) | -0.0025(0.0008 ; -0.0058)" | 0.0007(-0.0002 ; 0.0016)
Hospital Admissions (HA), Asthma | 0.0054 (0.0028 ; 0.0081) | -0.0009(-0.0004 ; -0.0013)" | 0.0002(0.0001 ; 0.0003)
Minor Restricted Activity Days^ | 71.0 (29.3 ; 112.6) | -9.6(-4.0 ; -15.2)" | 2.6 (1.1 ; 4.1)
School Loss Days, All Cause | 20.7 (-2.4 ; 43.7) | -3.3(0.4 ; -7.0)" | 0.8(-0.1 ; 1.8)
Short-Term PM2.5 Exposure |  |  | 
Acute Myocardial Infarction, Nonfatal | 0.0029 (0.0011 ; 0.0078) | -0.0014(-0.0037 ; -0.0005) | 
Asthma Exacerbation (Wheeze, Cough, Shortness of Breath) | 1.1496 (-0.0744 ; 2.6312) | -0.5213(-1.1931 ; 0.0337) | 
Asthma, New Onset (Wheeze)** | 0.1853 (-0.0815 ; 0.4515) | -0.0863(0.0379 ; -0.2104) | 
HA, All Cardiovascular (less Myocardial Infarctions) | 0.0115 (0.0078 ; 0.0148//) | -0.0055(-0.0070 ; -0.0037) | 
HA, All Respiratory (less Asthma)* | 0.0105 (0.0064 ; 0.0138) | -0.0050(-0.0066 ; -0.0031) | 
HA, Ischemic Stroke | 0.0060 (0.0020 ; 0.0120) | -0.0029(-0.0010 ; -0.0058) | 
HA and ED Visits, Asthma | 0.0075 (-0.0013 ; 0.0203) | -0.0034(-0.0092 ; 0.0006) | 
Lower Respiratory Symptoms | 0.6475 (0.2460 ; 1.0483) | -0.2915(-0.1107 ; -0.4720) | 
Upper Respiratory Symptoms | 1.2625 (0.2294 ; 2.2942) | -0.5684(-0.1033 ; -1.0330) | 
Minor Restricted Activity Days^ | 27.9 (22.8 ; 33.1) | -12.8(-10.4 ; -15.1) | 
Work Loss Days | 4.8 (4.1 ; 5.6) | -2.2(-1.9 ; -2.5) | 
* This is pooled from HA, Chronic Lung Disease (less Asthma) (18-64) and HA, All Respiratory (65 or older). |  |  | 
** Valuation functions (VFs) for Asthma, New Onset (Wheeze) were not applied, correspondingly not shown in the valuation tables, because SCAQMD did not apply such VFs in their 2016 socioeconomic report; there are VFs for ages 0-18, but the health effects here are estimated for ages 35-99. |  |  | 

## Slide 27: SSB – Summer Ozone and Disadvantaged Communities
Census tracts most impacted (20%) by ozone air pollution
  CalEnviroScreen 3.0
Largest improvements not located in critical regions
  Still beneficial!
  Illustrate the importance of considering impacts spatially

## Slide 28: MTC – Summer Ozone and Disadvantaged Communities
Census tracts most impacted (20%) by ozone air pollution
  CalEnviroScreen 3.0
MTC and GTC summer ozone impacts notable
  Bakersfield region
GTC H2 Case
20% Decrease in NOx Emissions

## Slide 29: Method
NOx emissions as predicted with a CFD (non-kinetic) model, CRN with complete chemistry and experimental results collected at UCI an elsewhere
Source: Colorado, Andres, and Vincent McDonell. "Exploring computational methods for predicting pollutant emissions and stability performance of premixed reactions stabilized by a low swirl injector." Combustion Science and Technology (2017): 1-20.

## Slide 30: MTC and GTC H2 – Summer PM2.5
-0.005 ug/m3 24-hr PM2.5
+0.024 ug/m3 24-hr PM2.5
MTC H2 Case
200% Increase in NOx Emissions
GTC H2 Case
20% Decrease in NOx Emissions
Notes: These results demonstrate the impact on maximum 8-hr average ground-level ozone from the changes in Nox emissions presented last slide. As would be expected the MTC Case results in worse AQ (increasing ozone levels) and the GTC Case improves AQ (reducing ozone levels). The changes in ozone scale to the emission reductions with peak impacts in the MTC Case an order of magnitude higher due to all impacted sources in the cases being exactly the same (this wouldn’t be true if different sources were impacted). In particular, large natural gas power plants in the south central valley have a major impact. Overall it should be noted that the impacts are fairly minor as the standard for max 8-hr ozone is 75 ppb and the impacts in the MTC Case is .242 ppb. This is because the electricity sector in CA is relatively low-emitting overall due to stringent environmental regulations leading to high levels of renewables and cleaner natural gas plants.

## Slide 31: MTC and GTC H2 – Winter PM2.5
-0.31 ug/m3 24-hr PM2.5
+0.38 ug/m3 24-hr PM2.5
MTC H2 Case
200% Increase in NOx Emissions
GTC H2 Case
20% Decrease in NOx Emissions
Notes: Points:
Winter ozone not generally a concern due to low background levels
Impacts on PM in winter are larger and in different areas spatially highlighting the seasonal importance, difference in PM formation dynamics,

## Slide 32: MTC and GTC BG – Summer Ozone
-0.013 ppb Max 8-hr O3
-0.085 ppb Max 8-hr O3
MTC BG Case
17% Decrease in NOx Emissions
GTC BG Case
3% Decrease in NOx Emissions
Notes: These results demonstrate the impact on maximum 8-hr average ground-level ozone from the changes in Nox emissions presented last slide. As would be expected the MTC Case results in worse AQ (increasing ozone levels) and the GTC Case improves AQ (reducing ozone levels). The changes in ozone scale to the emission reductions with peak impacts in the MTC Case an order of magnitude higher due to all impacted sources in the cases being exactly the same (this wouldn’t be true if different sources were impacted). In particular, large natural gas power plants in the south central valley have a major impact. Overall it should be noted that the impacts are fairly minor as the standard for max 8-hr ozone is 75 ppb and the impacts in the MTC Case is .242 ppb. This is because the electricity sector in CA is relatively low-emitting overall due to stringent environmental regulations leading to high levels of renewables and cleaner natural gas plants.

## Slide 33: SSBC BG – Impact on 8-hr Ozone and 24-h PM2.5
-0.024 to +0.019 ppb Max 8-hr O3
SSBL BG Case
3% Decrease in NOx/3% Increase in CO
SSBL BG Case
3% Decrease in NOx/3% Increase in CO
0.014 to +0.032 ug/m3 24-hr PM2.5
Notes: These results demonstrate the impact on NOx emissions and ground-level ozone for the SSBL H2 case. The results highlight the importance of how emissions from different sectors and sources impact air pollution differently. For example, the SSBL burners are used in different industries that impact ozone in Northern California while the MTC and GTC impact the Bay Area and Central Valley. Further, the 64% decrease achieves a greater peak impact on ozone in terms of magnitude as the MTC case with a 200% increase.

## Slide 34
+
-
Electrolyzer
Renewable Electricity
Hydrogen
Water
CO2

## Slide 35: Understanding Air Quality Impacts
Solely quantifying emissions neglects atmospheric impacts
Robust assessment includes simulations of atmospheric chemistry/transport
Emissions
NOx
PM
SO2
CO
Atmospheric Chemistry
VOC
Ambient Concentrations
Deposition
Effects on Receptors
Morbidity & Mortality
Dilution/Mixing/Transport
[Ozone]
[Particulate Matter]
+
+
=

## Slide 36: Impacts: Economic Viability
Direct injection of hydrogen into the natural gas distribution or transmission system (P2H2) yield a lower LCORE than the power-to-methane (P2CH4) cases
  Methanation increases the costs and introduces conversion efficiency penalties
LCORE Results ($/MMBtu): P2H2 vs. P2CH4 Only Future Costs/Future Efficiencies, 50% Capacity Factor

## Slide 37: SSBC H2 – Impact on 24-h NOx
SSBL H2 Case
64% Decrease in NOx
-0.172 kg/hr NOx
Notes: These results demonstrate the impact on NOx emissions and ground-level ozone for the SSBL H2 case. The results highlight the importance of how emissions from different sectors and sources impact air pollution differently. For example, the SSBL burners are used in different industries that impact ozone in Northern California while the MTC and GTC impact the Bay Area and Central Valley. Further, the 64% decrease achieves a greater peak impact on ozone in terms of magnitude as the MTC case with a 200% increase.

## Slide 38: Peak Impacts
 | Summer |  | Winter | 
Scenario | Δ Max 8-hr Ozone | Δ 24-hr PM2.5 | Δ Max 8-hr Ozone | Δ 24-hr PM2.5
GTC_H2 | -0.10 | -0.31 |  | -0.31
MTC_H2 | +0.49 | +0.38 |  | +3.8
SSBL_H2 | -0.75 | -0.08 | +2.16 | -0.64
GTC_BG | -0.013 to +0.020 | -0.279 to +0.039 |  | 
MTC_BG | -0.085 to +0.029 | -0.014 to +0.009 |  | 
SSBL_BG | -0.024 to +0.019 | 0.014 to +0.032 |  | 

## Slide 39: Power-to-Gas (P2G) Overview
Potential pathway to a near-zero emitting, 100% renewable gas system
Gas Supply | Fossil (CH4) | Fossil & Renewable (CH4 and H2) | Renewable (H2)
Conversion | Combustion | Combustion/Electrochemical | Electrochemical
End-uses | All | Complementary Generation | Challenging to electrify

## Slide 40: Power-to-Gas (P2G) Overview
Fossil Gas
(CH4)
Fossil & Renewable Gas (CH4 & H2)
Renewable Gas
(H2)
Potential pathway to a near-zero and renewable gas system
  Renewable H2 used by zero-emission fuel cells for generation and motive power
  Electrification/batteries with priority
    Remaining end-uses and to provide complementary generation for renewables
Electrochemical
Combustion
Complementary Generation
Challenging Sectors to Electrify
All End-use Sectors except Transportation

## Slide 41: Results – Spatial and Temporal Emissions
-1.61 kg/hr Δ 24-h NOx
+8.02 kg/hr Δ 24-h NOx
MTC H2 Case
200% Increase in NOx Emissions
GTC H2 Case
20% Decrease in NOx Emissions
Notes: These results demonstrate the impact on emissions (directly emitted) of nitrogen oxides (NOx) when hydrogen is blended into the pipeline and combusted by end-use combustion devices utilizing microturbine combustors (MTC) and gas turbine combustors (GTC). Each dot of color represents a 4km x 4km grid cell that may contain one or more sources of emissions.

## Slide 42: Approach – Combustion and Emission Impacts
Assessed impacts of fuel blending (H2 and biogas) for nine prototype and commercial industrial burners
  Requires numerical models (CFD) and reaction mechanisms with detailed chemical kinetics (CRN), 3 burner types experimentally validated
NOx emissions for low swirl burner as predicted with a CFD model, CRN with complete chemistry and experimental results
Source: Colorado, Andres, and Vincent McDonell. Combustion Science and Technology (2017): 1-20.
Fuels | Mixture
Hydrogen | 76% CH4 - 24% H2
Biogas | 98% CH4 - 2% CO2
Ethane | 94% CH4 - 6% C2H6
Propane | 95% CH4 - 5% C3H8
Industrial Burners
Low-swirl Burner (LSB)
Surface Stabilized Burner (SSB)
Micro Turbine Combustor (MTC)
Oxygas Burner
High Speed Jet Burner (HSJ)
Gas Turbine Combustor (GTC)
Radiant Tube (RT)
Infrared Burner (IRB)
Slot Burner (SB)
Notes:   Computational fluid dynamics and chemical reactor networks for all 9
  Experimental validation at UCICL for (1) The low-swirl burner (LSB), (2) surface stabilized combustion burner (SSCB) and (3) a micro-turbine combustor (MTC)

## Slide 43: Project Goal
Investigate the potential impact of fuel variability in the natural gas system on emissions and AQ in California
  Determine potential emission changes from relevant sources
  Develop plausible future scenarios at the energy sector level
  Assess the impacts of emission changes on regional AQ
?
?
Provide technical insight on how to maximize the GHG and AQ co-benefits of renewable fuels

## Slide 44: SSBC H2 – Summer Ozone
-0.75 ppb Max 8-hr O3
SSBL H2 Case: 64% Decrease in NOx
Summer
Notes: These results demonstrate the impact on NOx emissions and ground-level ozone for the SSBL H2 case. The results highlight the importance of how emissions from different sectors and sources impact air pollution differently. For example, the SSBL burners are used in different industries that impact ozone in Northern California while the MTC and GTC impact the Bay Area and Central Valley. Further, the 64% decrease achieves a greater peak impact on ozone in terms of magnitude as the MTC case with a 200% increase.

## Slide 45: Pathway Forward
Res. And Com. Appliances – Ongoing
Reciprocating Engines
Industrial Burner Assessment - Funded
Comprehensive Scenarios
Health Impact Assessment
Integrated planning document for combustion end-uses in California