## Slide 1
Modeling Ozone in the Eastern U.S. using a Fuel-Based Mobile Source Emissions Inventory
Brian McDonald1,2, Stuart McKeen1,2, Yuyan Cui1,2, Ravan Ahmadov1,3, Si-Wan Kim1,2, Gregory Frost2, Ilana Pollack1,2, Thomas Ryerson1,2, John Holloway1,2, Martin Graus1,2, Carsten Warneke1,2, Joost de Gouw1,2, Jennifer Kaiser4, Frank Keutsch4, Thomas Hanisco5, Glenn Wolfe5,6, Michael Trainer2
CIRES, Univ. of Colorado, Boulder, CO
Chemical Sciences Division, NOAA ESRL, Boulder, CO
Global Sciences Division, NOAA ESRL, Boulder, CO
Dept. of Chemistry, Univ. of Wisconsin, Madison, WI
Atmospheric Chemistry and Dynamics Laboratory, NASA Goddard, Greenbelt, MD
Joint Center for Earth Systems Technology, Univ. of Maryland-Baltimore, Baltimore, MD
2017 CMAS Conference
Acknowledgments: NASA ROSES ACMAP and NOAA’s High Performance Computing Program.

## Slide 2
Recent Studies Suggest Overestimate in NEI 2011 NOx Emissions
Year | Region | Measurement | Findings
2011 | Baltimore/DC | Aircraft (DISCOVER-AQ) | Mobile sources overestimated by 50-70% [Anderson et al., Atmos. Environ. 2014]

## Slide 3
Recent Studies Suggest Overestimate in NEI 2011 NOx Emissions
Year | Region | Measurement | Findings
2011 | Baltimore/DC | Aircraft (DISCOVER-AQ) | Mobile sources overestimated by 50-70% [Anderson et al., Atmos. Environ. 2014]
2013 | Southeast | Aircraft (SEAC4RS) | Reduce mobile and industrial sources by 30-60% [Travis et al., Atmos. Chem. Phys. 2016]

## Slide 4
Recent Studies Suggest Overestimate in NEI 2011 NOx Emissions
Year | Region | Measurement | Findings
2011 | Baltimore/DC | Aircraft (DISCOVER-AQ) | Mobile sources overestimated by 50-70% [Anderson et al., Atmos. Environ. 2014]
2013 | Southeast | Aircraft (SEAC4RS) | Reduce mobile and industrial sources by 30-60% [Travis et al., Atmos. Chem. Phys. 2016]
2013 | Urban Texas | Satellite Inversion | Reduce mobile, area, point sources by 30-60% [Souri et al., Atmos. Env. 2016]

## Slide 5
Recent Studies Suggest Overestimate in NEI 2011 NOx Emissions
Year | Region | Measurement | Findings
2011 | Baltimore/DC | Aircraft (DISCOVER-AQ) | Mobile sources overestimated by 50-70% [Anderson et al., Atmos. Environ. 2014]
2013 | Southeast | Aircraft (SEAC4RS) | Reduce mobile and industrial sources by 30-60% [Travis et al., Atmos. Chem. Phys. 2016]
2013 | Urban Texas | Satellite Inversion | Reduce mobile, area, point sources by 30-60% [Souri et al., Atmos. Env. 2016]
2013 | Southeast | Aircraft (SEAC4RS) | Reduce total anthropogenic emissions by 14% [Li et al., Atmos. Chem. Phys. Disc. 2017]

## Slide 6
Research Objectives
Assess “Bottom-Up” Mobile Source Emissions
  Focus on NOx, but CO and VOCs can also be assessed
  Construct fuel-based inventory and compare with EPA MOVES2014
Perform “Top-Down” Model Evaluation
  Evaluate emissions with aircraft- and ground-based measurements during Southeast Nexus (SENEX) Study in 2013
(3) Test sensitivity of ground-level O3 to mobile source NOx and biogenic VOC emissions

## Slide 7
Emissions = Activity (kg fuel) x Emission Factor (g/kg fuel)
Trends in U.S. Mobile Source Activity (Fuel Use)
Fuel estimates based on
FHWA and EIA surveys
Similar to fuel use
reported in MOVES2014
Fuel Use (t/d)
Year

## Slide 8
Long-Term Trends in On-Road NOx Emission Factors
Emissions = Activity (kg fuel) x Emission Factor (g/kg fuel)
NOx EF (g/kg fuel)
Year

## Slide 9
Gasoline EF high
by factor of ~2
MOVES EF are default values
Long-Term Trends in On-Road NOx Emission Factors
Diesel EF
within ~20%
Emissions = Activity (kg fuel) x Emission Factor (g/kg fuel)
NOx EF (g/kg fuel)
Year

## Slide 10
NOx Emissions by Mobile Source Category (FIVE vs. MOVES)
Consistent with literature
  Anderson et al., Atmos. Env. 2014 Travis et al., Atmos. Chem. Phys. 2016

## Slide 11
WRF-Chem Modeling for Southeast Nexus (SENEX) Study
WRF-Chem Model v3.7
12 km x 12 km
61 vertical layers
ECMWF-Era-Interim
RACM_ESRL Chemistry
Static Chemical B.C.
Emission Cases:
NEI11 + 1 * BEIS ISO
NEI11 + 2 * BEIS ISO
FIVE13 + 1 * BEIS ISO
FIVE13 + 2 * BEIS ISO
Model run from 6/1 – 7/15 in 2013

## Slide 12
Revise Mobile Source Emissions Only (NEI11 → FIVE13)
Total U.S. NOx emissions decreases by ~15%

## Slide 13
Model Evaluation of NOx Emissions in Urban Plumes
Atlanta (SEARCH site)
Nashville (P-3 aircraft)
NEI11
NEI11
Obs
Obs

## Slide 14
Model Evaluation of NOx Emissions in Urban Plumes
Atlanta (SEARCH site)
Nashville (P-3 aircraft)
NEI11
NEI11
FIVE13
FIVE13
Obs
Obs

## Slide 15
Model Evaluation of NOy and O3 across Southeastern U.S.
Emissions Case | NOy (ppb) | O3 (ppb)
P-3 Obs. | 2.1 | 47
Emissions Case | NOy (ppb) | O3 (ppb)
P-3 Obs. NEI11 + 1 * BEIS ISO NEI11 + 2 * BEIS ISO | 2.1 2.9 (+43%) 2.8 (+34%) | 47 56 (+9) 54 (+7)
Emissions Case | NOy (ppb) | O3 (ppb)
P-3 Obs. NEI11 + 1 * BEIS ISO NEI11 + 2 * BEIS ISO FIVE13 + 1 * BEIS ISO FIVE13 + 2 * BEIS ISO | 2.1 2.9 (+43%) 2.8 (+34%) 2.5 (+21%) 2.3 (+13%) | 47 56 (+9) 54 (+7) 53 (+6) 50 (+3)

## Slide 16
Evaluation of Model O3 with AQ Monitoring Sites (NEI 2011)
Bias in summer 2013 mean daily 8-h maximum
modeled with NEI 2011 vs. AQS data
Model bias =
1220 days

## Slide 17
Improvement in Model O3 when Reducing Mobile Source NOx
Bias in summer 2013 mean daily 8-h maximum
modeled with NEI 2011 vs. AQS data
Model bias =
1220 days
FIVE is worse 
 FIVE is better

## Slide 18
Evaluation of Model on High Ozone Days (>70 ppb)
Bias in summer 2013 O3 exceedance days
(>70 ppb) modeled with NEI 2011 vs. AQS data
FIVE is worse 
 FIVE is better

## Slide 19
High Ozone Days Sensitive to Mobile Source NOx
No. of Sites (>70 ppb)
6/1
6/11
6/21
7/1
7/11
Obs
FIVE13
NEI11
0
50
100
Episode

## Slide 20
Summary
  NOx overestimate seen in model, and partially explained by biases in mobile source emissions
    Biggest discrepancies found in the on-road gasoline sector
    Suggest reducing mobile source NOx emissions by 20-30% to be consistent with roadside studies and ambient measurements of NOy
  In Eastern U.S., ozone sensitive to mobile source NOx
    Small changes in transportation NOx → significant effects on high O3 days