## Slide 1
Mechanistic representation of Soil N in CMAQ v5.1
Quazi Z. Rasool1, Jesse O. Bash2, Ellen J. Cooter2 and Daniel S. Cohan1
1Department of Civil engineering, Rice University
2Computational Exposure Division, NERL, US Environmental Protection Agency
16th Annual CMAS Conference, UNC-Chapel Hill
October 24, 2017

## Slide 2: Reactive soil N in air quality models
Parametrized oxidized N (NO) and soil-atmosphere exchange of NH3
Contributes to ozone and particulate matter
Soil NOx ~ 19% of Global NOx Budget
Large underestimations and uncertainties in modeled soil NO
  Yienger-Levy scheme: No deposition, poor soil moisture representation
Updated parameterized approach (enhanced BDSNP)

## Slide 3: Motivation
Soil nitrogen emissions altered by increasing fertilizer use
Inconsistent treatment of N species in soils and fluxes
  Bi-directional scheme for ammonia but not other species
  NO parameterized; HONO ignored
  Nitrification and denitrification not represented
Need consistent mechanism to model impact of agricultural management on reactive N emissions and air quality

## Slide 4
NH3
NH3
NH4+
N2
N2O
NO
NO N2O
N2
NO N2O HONO
NO2-
NO3-
HNO3
HNO3
Atmosphere
Soil
HNO2
H+
NO2
NO2
H+
Fertilizer, Deposition, Biome
Adapted from Su et al., 2011; Pilegaard, 2013 and Medinets et al., 2015
N (-3)
N (+5)
Nitrification
Denitrification
Org N
NO
N2O
Reactive N cycling schematic
(Parametrized vs Mechanistic)
Org N
Total N
NO
Parametrized
Mechanistic

## Slide 5: Soil biome / Land Cover Dataset Enhancements
GEOS-Chem (0.25° x 0.25°)
CMAQ (12 km x 12 km)
GEOS-Chem
24 MODIS land cover categories
Too coarse for regional modeling
CMAQ
Mapped 40 NLCD categories from Pleim-Xiu to 24 MODIS categories
Köppen-Geiger climate zones
Sub-grid fractionation of biomes

## Slide 6
Environmental Policy Integrated Climate (EPIC) agricultural model
Fertilizer quantity: USDA Agricultural Resource Management Survey database, validated with fertilizer sales data
Fertilizer timing: Determined by plant nutrient stress
Can simulate varied agricultural practices (e.g., tillage, fertilizer type)
Fertilizer Emission Scenario Tool for CMAQ (FEST-C) incorporates EPIC simulated agricultural soil N into CMAQ runs
[Source: Cooter et al., 2012]
Notes: HUSC to Schedule Vegetable Plantings, Predict Harvest Dates and Manage Crops
Temperature controls the development of many organisms that don’t have complex thermoregulatory systems. This allows us to predict the development of different organisms by accurately using development or phenology models which are based on the accumulation of heat units (i.e. degree days) during a growing season.

## Slide 7: Reactive soil N modeling (Parametrized vs Mechanistic)
Soil T and moisture
Canopy reduction factor
Pulsing = f (rain, dry period)
Emission Factor for each biome
EPIC
(N for Agricultural soil)
Fertilizer
Deposition
Soil NO
Non-Agricultural soil properties and
nutrient data#
*Oswald et al., 2013; Su et al., 2011
#Xu et al., 2014
!Parton et al., 2001; Del Grosso et al., 2000
Land use specific HONO, NO estimates*
Parametrized
DAYCENT N module!
(in-line in CMAQ)
Mechanistic
Nitrification and Denitrification
NO
HONO
N2O

## Slide 8: Updates in CMAQ : parameterized to mechanistic
Features in CMAQ | Parameterized | Mechanistic
Species emitted | Nitric oxide (NO), NH3 | NO, NH3, HONO, N2O
Approach | BDSNP equations for NO CMAQ bi-directional for NH3 | DayCENT submodel representing nitrification, denitrification, and mineralization
Variables considered | Total soil N, soil T, soil moisture, rainfall, and biome type | Soil water content, T, NH4+, NO3−, gas diffusivity, and labile C by soil layer
Soil N data source | EPIC (agricultural soil only) | EPIC for agricultural soil Microbial biomass C, N, and properties for non-agricultural
Notes: DAYCENT and EPIC model both based on CENTURY ecosystem model
CENTURY simulates cycling of reactive N (along with other nutrients) between soil, vegetation, atmosphere and water
EPIC differs from DAYCENT since:
  EPIC has been implemented on a regional scale in CMAQ and,
  NH3 Bi-directional feedback implemented in EPIC-CMAQ framework
  (Cooter et al., 2012)
EPIC does not give how much of NO and N2O each came from nitrification and denitrification
N sub model of DAYCENT addresses that mechanistically based on
  soil water content (WFPS), temp, soil NH4+ and NO3− concentrations, gas diffusivity and labile C availability at various soil layers
  (Parton et al 1998; Del Grosso et al., 2000; Parton et al., 2001)
Soil HONO still not addressed in current biogeochemical models

## Slide 9: Approach to include soil HONO
NO and HONO flux from nitrification and denitrification based on:
  NH4+, NO2-, and NO3- availability in soils
  Soil pH
  Soil moisture:
    Nitrification for water-filled pore space <55%
    Denitrification for water-filled pore space >55%
    HONO for water-filled pore space <40%
    For water-filled pore space <20%
      More HONO than NO emissions
  Soil temperature
  Heterotrophic respiration of Soil Org C as CO2

## Slide 10: Comparison of soil NOx flux across schemes
NO (Parametrized)
NO (Mechanistic)
HONO (Mechanistic)
Daily Average soil N flux
(21 April, 2011)

## Slide 11: Modeling NH4 and NO3 available in non-agricultural soil
Soil microbial C
Soil microbial N
Soil Org C
Soil Org N
Recycle
Enzyme Loss
Decay/death
F( C:N ratio)
CO2 respiration from:
  Enzyme production
  Maintenance
  Growth
  Overflow mechanism
Mineralization
NH4-N
Nitrification
f (soil pH, WFPS, soil Temp, volatilization)
NO3-N
Immobilization
Mass balance approach
for C-N dynamics in soil*
*Schimel and Weintraub (2003); Manzoni and Porporato (2009)
Nitrification estimation as done in EPIC and NH3 scheme in CMAQ

## Slide 12: Soil-atmosphere exchange in CMAQ
Uni-directional Bi-directional

## Slide 13: Significance and broader impacts
Key enhancements
  Consistent representation across N species
  Mechanistic representation of actual soil processes
Next steps
  Extend to non-agricultural soil types
  Influence of land management practices on NO and HONO emissions
  Ozone & PM responsiveness to soil emissions
  Validating with DISCOVER-AQ, OMI NO2

## Slide 14: Acknowledgements
NASA Air Quality Applied Sciences Team
NASA grant NNX15AN63G (via UAH)
CED, NERL at US EPA for the opportunity as a visiting researcher
Rui Zhang (Colorado State University)

## Slide 15: Impact of Soil NO scheme on Ozone
Daily Average 8-hourly max. Ozone (Updated Parametrization – Base CMAQ v5.1)

## Slide 16: Impact of Soil NO scheme on PM
Daily Average PM2.5 (Updated Parametrization – Base CMAQ v5.1)

## Slide 17: Biochar as N emission amendment
Studies differ on whether biochar reduces soil NO by 47-67% (Nelissen et al, 2014) or not at all (Xiang et al., 2015)
Impact on O3
Impact on PM2.5

## Slide 18: Rasool GMD paper header

## Slide 19: Impact of Potter vs EPIC Fertilizer Data on Soil NO
Fertilizer
Application (kgN/ha)
Potter
EPIC
Difference in BDSNP
Soil NO (g/s)
EPIC - Potter
*Averaged over July 2011

## Slide 20: Outline: Soil N emissions in CMAQ
Bi-directional NH3 soil-atmosphere exchange already available
Updated parametrized approach to soil NO (Rasool et al. 2016)
  Replaces Yienger & Levy scheme in CMAQ
  Emissions are function of soil N, biome, and meteorology
  Soil N from EPIC agricultural model
  Modeled impact of soil NO on ozone and PM2.5
Next: Mechanistic approach with consistent representation of multiple N species (NO, HONO, N2O, NH3)
  Accounts for soil processes (nitrification, denitrification)

## Slide 21: Mechanistic soil N modeling
DAYCENT and EPIC model both based on CENTURY ecosystem model
CENTURY simulates cycling of reactive N (along with other nutrients) between soil, vegetation, atmosphere and water
EPIC differs from DAYCENT since:
  EPIC has been implemented on a regional scale in CMAQ and,
  NH3 Bi-directional feedback implemented in EPIC-CMAQ framework
  (Cooter et al., 2012)
EPIC does not give how much of NO and N2O each came from nitrification and denitrification
N sub model of DAYCENT addresses that mechanistically based on
  soil water content (WFPS), temp, soil NH4+ and NO3− concentrations, gas diffusivity and labile C availability at various soil layers
  (Parton et al 1998; Del Grosso et al., 2000; Parton et al., 2001)
Soil HONO still not addressed in current biogeochemical models

## Slide 22: References
Bash, J., Cooter, E., Dennis, R., Walker, J., and Pleim, J. (2013). Evaluation of a regional air-quality model with bidirectional NH 3 exchange coupled to an agroecosystem model, Biogeosciences, 10, 1635-1645.
Cooter, E., Bash, J., Benson, V. and Ran, L. (2012). Linking Agricultural Crop Management and Air Quality Models for Regional to National-Scale Nitrogen Assessments. Biogeosciences Discussions, 9: 6095-6127.
CMAS FEST-C 2015: User’s Guide for the Fertilizer Emission Scenario Tool for CMAQ (FEST-C) Version 1.2, Institute of Environment, The University of North Carolina at Chapel Hill, Chapel Hill, NC, available at: https://www.cmascenter.org/fest-c/documentation/1.2/FESTC1_2_userManual.pdf.
Del Grosso, S.J., White, J.W., Wilson, G., Vandenberg, B., Karlen, D.L., Follett, R.F., Johnson, J.M.F., Franzluebbers, A.J., Archer, D.W., Gollany, H.T. and Liebig, M.A., 2013. Introducing the GRACEnet/REAP data contribution, discovery, and retrieval system. Journal of environmental quality, 42(4), pp.1274-1280.
Dinnes, D. L., Karlen, D. L., Jaynes, D. B., Kaspar, T. C., Hatfield, J. L., Colvin, T. S., and Cambardella, C. A. (2002). Nitrogen management strategies to reduce nitrate leaching in tile-drained Midwestern soils, Agronomy journal, 94, 153-171.
Hudman, R. C., Moore, N. E., Mebust, A. K., Martin, R. V., Russell, A. R., Valin, L. C., and Cohen, R. C. (2012). Steps towards a mechanistic model of global soil nitric oxide emissions: implementation and space based-constraints, Atmos. Chem. Phys., 12, 7779-7795, doi:10.5194/acp-12-7779-2012.
Medinets, S., Skiba, U., Rennenberg, H., & Butterbach-Bahl, K. (2015). A review of soil NO transformation: Associated processes and possible physiological significance on organisms. Soil Biology and Biochemistry, 80, 92-117.
Pilegaard, K. (2013). Processes regulating nitric oxide emissions from soils. Philisophical Transactions of the Royal Society: Biological Sciences, (368). Retrieved from http://dx.doi.org/10.1098/rstb.2013.0126.
Pleim, J. E. X. A. (1811). Development of a Land Surface Model. Part II: Data Assimilation. Journal of Applied Meteorology. Dec2003, 42(12).
Potter, P., N. Ramankutty, E.M. Bennett, and S.D. Donner. 2010. Characterizing the Spatial Patterns of Global Fertilizer Application and Manure Production. Earth Interactions 14 (2): 1-22. http://dx.doi.org/10.1175/2009EI288.1.
(S&L) Steinkamp, J., & Lawrence, M. G. (2011). Improvement and evaluation of simulated global biogenic soil NO emissions in an AC-GCM. Atmospheric Chemistry and Physics, 11(12), 6063–6082. doi:10.5194/acp-11-6063-2011
Rasool, Q. Z., Zhang, R., Lash, B., Cohan, D. S., Cooter, E. J., Bash, J. O., and Lamsal, L. N.: Enhanced representation of soil NO emissions in the Community Multiscale Air Quality (CMAQ) model version 5.0.2, Geosci. Model Dev., 9, 3177-3197, doi:10.5194/gmd-9-3177-2016, 2016.
Xiang, J., Liu, D., Ding, W., Yuan, J. and Lin, Y., 2015. Effects of biochar on nitrous oxide and nitric oxide emissions from paddy field during the wheat growth season. Journal of Cleaner Production, 104, pp.52-58.
Yienger, J. J., & Levy, H. (1995). Empirical-Model Of Global Soil-Biogenic Nox Emissions. Journal of Geophysical Research-Atmospheres, 100(D6), 11447-11464. doi: 10.1029/95jd00370.
Vinken, G. C. M., Boersma, K. F., Maasakkers, J. D., Adon, M., & Martin, R. V. (2014). Worldwide biogenic soil NOx emissions inferred from OMI NO2 observations. Atmospheric Chemistry and Physics, 14(18), 10363–10381. doi:10.5194/acp-14-10363.