## Slide 1: Evaluation of Emissions of Nitrogen Oxides in Houston, Texas Using Three-Dimensional Aircraft Observations during the DISCOVER-AQ 2013 Mission
Air Quality Division
Ou Nopmongcol2, Jim Smith1, Greg Yarwood2, Zhen Liu2, Jeremiah Johnson2, Wei Chun2
1Texas Commission on Environmental Quality
2Ramboll Environ, Inc.
Community Modeling and Analysis System (CMAS) 2017 Annual Conference
October 23, 2017

## Slide 2: NOX Emission Over-Estimation?
Many authors have concluded that emissions of Nitrogen Oxides (NOX) used in recent photochemical modeling studies are over-estimated by up to 100% or even more.
The usual suspect is MOVES model-predicted on- and non-road mobile sources.
However, performance evaluation of modeling conducted by the TCEQ shows reasonable agreement between predicted and observed ambient NOX concentrations.
What gives?

## Slide 3: NOX Emission Over-Estimation?
Bai, et al summarized literature studies between 2012 and 2015, results are displayed below:
* Presentations
** Added
ACP – Atmospheric Chemistry and Physics
EST – Environmental Science and Technology
EPRI – Electric Power Research Institute
AGU – American Geophysical Union
AE – Atmospheric Environment
TRB – Transportation Research Board
JAWMA – Journal of Air and Waste Management Assn.
JGR – Journal of Geophysical Research

## Slide 4: Houston-Galveston-Brazoria (HGB) On-Road Mobile Source Emissions
State Implementation Plan revision in 2016: Attainment Demonstration for 2008 Ozone Standard
  2012 base year
  4 km East Texas subgrid
  Travel-demand modeling for HGB was conducted by Houston-Galveston Area Council
  Emissions by link, day-of-week, time-of-day developed by Texas Transportation Institute using MOVES2014

## Slide 5: Houston-Galveston-Brazoria NOX Performance 2012 Base Case (2016 HGB O3 Attainment Demonstration)

## Slide 6: DISCOVER-AQ 2013 Houston
Deriving Information on Surface Conditions from COlumn and VERtically resolved observations – Air Quality

## Slide 7: Modeling the 2013 DISCOVER-AQ Period
36 km
12 km
4 km
WRF (red) and CAMx (blue) modeling domains.

## Slide 8: Meteorological Modeling
WRF test case | Original | ERA.FNMOC | ERA.FNMOC.NoOBS | ERA.G1 | NAM.FNMOC | NAM.FNMOC.KF
Domains | 36/12/4/1.33 km | 36/12/4 km | 36/12/4 km | 36/12/4 km | 36/12/4 km | 36/12/4 km
Microphysics | WSM6 | Thompson | Thompson | Thompson | Thompson | Thompson
LW Radiation | RRTMG | RRTMG | RRTMG | RRTMG | RRTMG | RRTMG
SW Radiation | RRTMG | RRTMG | RRTMG | RRTMG | RRTMG | RRTMG
Surface Layer Physics | MM5 similarity | MM5 similarity | MM5 similarity | MM5 similarity | MM5 similarity | MM5 similarity
Land Surface Model | Noah | Noah | Noah | Noah | Noah | Noah
PBL scheme | Yonsei University (YSU) | YSU | YSU | YSU | YSU | YSU
Cumulus Scheme | 36/12 km: Kain-Fritsch 4/1.3 km: none | 36/12/4 km: Multi-scale K-F(MSKF) | 36/12/4 km: MSKF | 36/12/4 km: MSKF | 36/12/4 km: Grell-Freitas | 36/12/4 km: K-F
BC and IC Source | 12 km NAM | ERA-Interim | ERA-Interim | ERA-Interim | 12 km NAM | 12 km NAM
Analysis Nudging | 36/12 km | 36/12 km | 36/12 km | 36/12 km | 36/12 km | 36/12 km
Obs Nudging | None | 4 km | None | 4 km | 4 km | 4 km
Sea Surface Temp. | RTG | FNMOC | FNMOC | G1 | FNMOC | FNMOC
WRF – Weather Research and Forecasting Model
ERA – European Center for Medium Range Weather Forecasting Re-Analysis
FNMOC – Fleet Numerical Meteorology and Oceanogaphy Center
G1 – NASA Global 1-km Sea Surface Temperature
RRTMG - Rapid Radiative Transfer Model for Global Climate Models
RTG – Real-Time Global Sea Surface Temperatures
MM5 – Mesoscale mMeteorological Model version 5
NAM – North American Meteorological Model
WSM6 – WRF Single-Moment 6-Class Microphysics Scheme

## Slide 9: Meteorological Modeling
WRF test case | Original | ERA.FNMOC | ERA.FNMOC.NoOBS | ERA.G1 | NAM.FNMOC | NAM.FNMOC.KF
Domains | 36/12/4/1.33 km | 36/12/4 km | 36/12/4 km | 36/12/4 km | 36/12/4 km | 36/12/4 km
Microphysics | WSM6 | Thompson | Thompson | Thompson | Thompson | Thompson
LW Radiation | RRTMG | RRTMG | RRTMG | RRTMG | RRTMG | RRTMG
SW Radiation | RRTMG | RRTMG | RRTMG | RRTMG | RRTMG | RRTMG
Surface Layer Physics | MM5 similarity | MM5 similarity | MM5 similarity | MM5 similarity | MM5 similarity | MM5 similarity
Land Surface Model | Noah | Noah | Noah | Noah | Noah | Noah
PBL scheme | Yonsei University (YSU) | YSU | YSU | YSU | YSU | YSU
Cumulus Scheme | 36/12 km: Kain-Fritsch 4/1.3 km: none | 36/12/4 km: Multi-scale K-F(MSKF) | 36/12/4 km: MSKF | 36/12/4 km: MSKF | 36/12/4 km: Grell-Freitas | 36/12/4 km: K-F
BC and IC Source | 12 km NAM | ERA-Interim | ERA-Interim | ERA-Interim | 12 km NAM | 12 km NAM
Analysis Nudging | 36/12 km | 36/12 km | 36/12 km | 36/12 km | 36/12 km | 36/12 km
Obs Nudging | None | 4 km | None | 4 km | 4 km | 4 km
Sea Surface Temp. | RTG | FNMOC | FNMOC | G1 | FNMOC | FNMOC
WRF – Weather Research and Forecasting Model
ERA – European Center for Medium Range Weather Forecasting Re-Analysis
FNMOC – Fleet Numerical Meteorology and Oceanogaphy Center
G1 – NASA Global 1-km Sea Surface Temperature
RRTMG - Rapid Radiative Transfer Model for Global Climate Models
RTG – Real-Time Global Sea Surface Temperatures
MM5 – Mesoscale Meteorological Model version 5
NAM – North American Meteorological Model
WSM6 – WRF Single-Moment 6-Class Microphysics Scheme

## Slide 10: Meteorological Modeling
Notes: Soccer-goal plots show pairs of model performance statistics compared with nominal performance goals. ERA_FNMOC was chosen from among the candidate model configurations based on this analysis.

## Slide 11: Emissions/Boundary Conditions
Mobile source emissions were
based on TCEQ’s 2012 modeling
platform, scaled to 2013.
Episode-specific emissions:
  Model of Emissions of Gases and Aerosols from Nature (MEGAN) with updated isoprene emission factors
  Sea-salt
  Fires using Fire Inventory from NCAR (FINN)
  Hourly emissions from Acid Rain Program Database
2013 boundary conditions from GEOS-Chem
Source |  | NOx | VOC | CO | SO2 | PM2.5
Texas |  |  |  |  |  | 
Non-road |  | 0.934 | 0.947 | 0.985 | 0.897 | 0.926
On-road |  | 0.916 | 0.943 | 0.965 | 0.900 | 0.910
Other states |  |  |  |  |  | 
Non-road | 0.951 |  | 0.943 | 0.989 | 1.009 | 0.946
On-road | 0.920 |  | 0.921 | 0.936 | 0.891 | 0.932
2012 to 2013 Scaling Factors for Mobile Sources

## Slide 12: CAMx Model Configuration
Science Options | Configurations
Model Code | Version 6.4
Horizontal Grid Mesh | 36/12/4 km
Vertical Grid Mesh | 29 Layers
Initial Conditions | 15 days full spin-up for 36/12 km; 5 days for 4 km
Boundary Conditions | Extracted from CAMx 12 km
Emissions Processing | Described in Section 2
Gas-Phase Chemistry | CB6r4 + Halogen
Aerosol Chemistry | ISORROPIA equilibrium and SOAP; CF scheme
Meteorological Processor | WRFCAMx
Horizontal Transport | Piecewise Parabolic Method (PPM scheme)
Horizontal Diffusion | K-theory
Vertical Advection Scheme | WRF
Vertical Eddy Diffusivity Scheme | K-theory
Vertical Diffusivity Corrections | Kv-patch depending on landuse category up to 100 m and to cloud tops
Deposition Scheme | Zhang
CF – Coarse-Fine
ISORROPIA – Greek for Equilibrium
SOAP – Secondary Organic Aerosol Processor
CB6r4 – Carbon Bond Mechanism ver. 6 rel. 4

## Slide 13: CAMx Model Performance: O3
Conroe
Clinton Drive
Notes: 3DMPE_4km was an earlier model run conducted for a previous work order. Generally model performance is much improved.

## Slide 14: CAMx Model Performance: NOX
Houston East
Clinton Drive

## Slide 15: September Hourly Average NOX Base and 50% Texas Onroad NOX Emissions

## Slide 16: September Hourly Average NOX Base and 50% Texas Onroad NOX Emissions

## Slide 17: Vertical Profile Comparison: NOX during DISCOVER-AQ
Deer Park
Conroe
West Houston
Manvel Croix Park

## Slide 18: Vertical Profile Comparison : NOY
Deer Park
Conroe
West Houston
Manvel Croix Park
Notes: NOy is NOx (NO+NO2) + product species such as nitric acid & PAN species.

## Slide 19: Vertical Profile Comparison : NOX
Smith Point
Moody Tower
Channelview
Galveston

## Slide 20: Vertical Profile Comparison : NOY
Smith Point
Moody Tower
Channelview
Galveston

## Slide 21: Column Densities for NO Species
Column densities are layer concentrations integrated vertically. A few large observations skew the regression lines clockwise.

## Slide 22: Conclusions
The new base case significantly improves both meteorological and ozone model performance compared with the simulation conducted for a previous TCEQ project.
Modeled NOX concentrations match observations well during morning rush hour and during day-time, especially at sites near the Houston city core (e.g., Clinton and Houston Texas Avenue).

## Slide 23: Conclusions
We find no strong evidence that TCEQ’s NOX on-road emissions are overstated in contrast to reports that on-road NOX emissions in the NEI are overestimated.
MOVES can produce reasonably accurate NOX inputs for modeling if supplied with accurate, location-specific, temporally and spatially resolved input data.