## Slide 1: Evaluation and intercomparison of five major dry deposition algorithms in North America
Zhiyong Wu1,2,*, Donna Schwede1, Robert Vet2, John T. Walker1, Mike Shaw2, Ralf Staebler2, Leiming Zhang2
1US EPA; 2Environment and Climate Change Canada
*ORISE Fellow; wu.zhiyong@epa.gov
16th Annual CMAS Conference – Oct. 25, 2017

## Slide 2
Background and Objectives
Description of dry deposition models and measured Vd dataset
Evaluation and inter-comparison of five models
Conclusions
Outline

## Slide 3
The inferential method is commonly used in dry deposition monitoring networks and atmospheric chemical transport models (CTMs).
Background
CAPMoN & GEM-MACH: Zhang et al. (2003)
CASTNET: Meyers et al. (1998)
EMEP: Simpson et al. (2003)
WRF-Chem & GEOS-Chem: Wesely (1989)
CMAQ: Pleim and Ran (2011)
…
Different dry deposition algorithms are used in monitoring networks and models:

## Slide 4
CAPMoN vs CASTNET
Schwede et al.(2011), AE
Similar concentration
Very different Vd

## Slide 5
Differences between models reach a factor 2–3 and are often greater than differences between monitoring sites.
A comparison of inferential models across the NitroEurope network
(UK)
(Canada)
(Europe)
(Holland)
Flechard et al. (2011), ACP

## Slide 6
The objectives of this study are:
to evaluate and inter-compare the dry deposition algorithms used in US and Canada
to quantify the magnitudes of model uncertainties
to explore the dominant factors causing the discrepancies.
Objectives

## Slide 7
The five dry deposition models
the Zhang et al. (2003) scheme used in the Canadian Air and Precipitation Monitoring Network (CAPMoN) and several Canadian and American air quality models (termed as ZHANG)
the Noah land surface model coupled with a photosynthesis-based Gas Exchange Model (Niyogi et al., 2009; Wu et al., 2012) (termed as Noah-GEM)
the dry deposition module of the Community Multiscale Air Quality (CMAQ) model version 5.0.2 (Pleim and Ran, 2011) (termed as C5DRY)
the dry deposition module of WRF-Chem which employs the widely-used Wesely (1989) scheme (termed as WESELY)
The multi-layer model used in the US Clean Air Status and Trends Network (CASTNET) based on Meyers et al. (1998)(termed as MLM)
One-big-leaf framework
Multi-layer framework

## Slide 8
Borden Forest
Vegetation Type: 100-year old mixed forest
Canopy Height: 22 m
Peak Leaf Area Index: 4.6 m2 m-2
Observation: 6 levels of O3 and SO2 concentrations
Period : May 2008 - April 2013
Measurements of O3 and SO2 dry depositions at Borden Forest
Modified gradient method:
Wu et al. (2015), ACP
Wu et al. (2016), EP

## Slide 9
Measured Vd(O3) and Vd(SO2) at Borden Forest
Wu et al.(2016), EP

## Slide 10
Evaluation and inter-comparison of five models
All models produced lower Vd values than measured for O3 in summer and SO2 in summer and winter;
There was not a consistent tendency in the models to over- or underpredict for O3 in winter.
Differences in mean Vd values between models were on the order of a factor of 2.

## Slide 11
Monin-Obukhov Similarity Theory (MOST) based
Air resistances (Ra & Rb)
Wind based:
where u* is friction velocity, ψh the stability correction function, Sc the Schmidt number, Pr Prandtl number for air (0.72), Dθ thermal diffusivity, and Dc molecular diffusivity of a specific gas.
where a is a constant depending on stability, u mean wind speed, σɵ standard deviation of the wind direction, α constant depending on gas species, δ characteristic leaf dimension.
(WESELY, Noah-GEM, C5DRY & ZHANG)
(MLM)
or

## Slide 12
Vd,max = 1 / (Ra+Rb)
MLM produced larger Ra and Rb than the MOST-based approaches (WESELY, Noah-GEM, C5DRY & ZHANG).
MOST type
Wind type
MOST type
Wind type

## Slide 13
The contribution of atmospheric resistances to the total resistances of O3 and SO2 was generally small (5-15% in this study).
With reduced Ra in MLM, mean Vd only increased by about 10%.
The main causes of the differences in Vd across the models is mainly due to the differences in the calculated Rc.

## Slide 14
Stomatal resistance (Rs) formulations
Jarvis-style Rs scheme:
Ball-Berry Rs scheme:
(C5DRY, ZHANG & MLM)
(WESELY)
(Noah-GEM)
Surface uptake = Stomatal uptake + Non-stomatal uptake
1/Rc = 1/Rs + 1/Rns

## Slide 15
Rs,min=100 s/m
Rs,min=150 s/m
Rs,min=200s/m
The Rs by the Jarvis-style scheme is very sensitive to the prescribed value of Rs,min.
However, this parameter is mainly derived from empirical fits to field measurements and suffers from large uncertainties.
The Penman-Monteith method:
Stomatal conductance (Gs,x) = 1 / Rs,H2O × (Dx/DH2O)
Notes: Here are the modeled Rs for water vapor. Rs for the O3 or SO2 is scaled by the molecular diffusitivity ratio. Because the MLM model calculates Rs at many layers, it is not easy to input Rs as one value to compare with the other models. Rs by MLM is not shown here. Also I calculated Rs using the inverse of the penman-monteith method which is based on the measurements of water vapor flux. This method works well in summer when the water vapor flux is dominately from plants evaportranspiration.It is the black line with filled circles. As we see, the Rs by Zhang is slightly higher than that from the Penman-Monteith method.
Both Jarvis-style and Ball-Berry-style schemes can produce a reasonable Rs if the main environmental factors are included and the key parameters are proper prescribed.

## Slide 16
The mean Vd for O3 and SO2 in ZHANG increased by 14% and 12%, respectively, if rs,min was reduced by 25%. Similar for the other Javis-type models.
Large discrepancies still exist in Vd between ZHANG and the observations, which can be further attributed to the non-stomatal parameterization (Rns) of the model.

## Slide 17
Non-stomatal conductance (Gns) = 1 / Rns
leaf cuticle
ground
Some model (e.g., ZHANG, Noah-GEM) Rns estimates showed significant diurnal variations, while others do not.
New measurements from chamber and field studies are needed to better understand processes influencing Rns.

## Slide 18
The models performed better in summer than in winter with correlation coefficients for hourly Vd between models and measurements being approximately 0.6 and 0.3, respectively.
All models produced lower Vd values than measured for O3 in summer and SO2 in summer and winter. There was not a consistent tendency in the models to over- or underpredict for O3 in winter.
Differences in mean Vd values of O3 and SO2 between models were on the order of a factor of 2.
Model differences were mainly due to different surface resistance parameterizations for stomatal and non-stomatal uptake pathways.
Although it cannot be concluded which algorithm is most accurate, it is recommended that users of inferential dry deposition models consider an uncertainty factor of 2 or use ensemble modeling results for ecosystem assessment analysis.
Conclusions and Recommendations

## Slide 19: Thank you!
Any questions ?
Notes: Thank you. I am happy to take any question. That is a good question!

## Slide 20: Additional Slides