## Slide 1: Investigating the formation of the high ozone exceedance on 25th September 2013 during the NASA DISCOVER-AQ Texas campaign
17th Annual CMAS Conference
Shuai Pan, University of Houston (UH), now postdoc at Cornell University
Yunsoo Choi, UH
Wonbae Jeon, UH, now at Pusan National University
Anirban Roy, UH, now at California Air Resources Board (CARB)
David Westenbarger, Texas Commission on Environmental Quality (TCEQ)
Hyun Cheol Kim, NOAA Air Resources Laboratory; University of Maryland
10/23/2018

## Slide 2
High O3 episode
O3 time series of the month of Sept. 2013
urban site
industrial/coastal site

## Slide 3
AirNow vs CMAQ
P3B vs CMAQ
O3 obs-model discrepancy in the afternoon of 09/25
Ship channel
industrial area
Zoom-in at industrial and bay areas
1-3 pm 2 pm
11 am - 5 pm
petrochemical and chemical manufacturing facilities

## Slide 4: Possible causes of the high O3

## Slide 5
Meteorological conditions favoring O3 production
sunny
dry
weak wind
frontal passage
High O3 caused by
postfrontal conditions
(Rappenglück et al., 2008;
Ngan and Byun, 2011)

## Slide 6
HRVOCs’ amount
12CST
unexpected episodic flare emissions (Murphy and Allen 2005; Vizuete et al. 2008)
emission upset?

## Slide 7: NOx and local wind
At early morning time,
OBS: calm or very weak westerly
Model: weak northerly, or northwesterly
exceptional high obs.

## Slide 8: Wind reversal and converging zone
09 -> 10 CST
Wind reversal at west coastline of Galveston Bay transported back the pollutants which were previously blown into the bay.
After that, a wind converging zone formed at Ship Channel, and lasted for several hours.

## Slide 9: Possible causes of the high O3
Causes of the high O3 on 25 September 2013
possible episodic flare emissions,
dry sunny postfrontal conditions,
calm or light wind,
nocturnal shallow boundary layer,
land-bay/sea breeze transition, wind reversal.
Reasons of model insufficient performance
Discrepancy in local wind patterns and precursors’ conditions

## Slide 10: Emission and wind adjustment and sensitivity simulations

## Slide 11
UWIND_adj = 1/ratio*abs(VWIND)
VWIND_adj = -1/ratio*abs(UWIND)
ratiohr = ave(sim)/ave(obs)
Adjusted wind 1
00 - 07 CST 3 layers, ~160m
Adjusted conceptual wind fields
weak westerly

## Slide 12
Same converging wind for each hour
Adjusted wind 2
09 - 16 CST 17 layers, ~2000m
Adjusted conceptual wind fields

## Slide 13: 4 Simulation Cases
SENS: SST (updating WRF with hourly NOAA GOES SST)
SENS-EMIS: SST+ unexpected NOx and VOC emissions
SENS-WIND: SST + wind fields adjustments
SENS-TOT: (2)+(3)

## Slide 14: NOx at 05CST
SENS SENS-EMIS
SENS-WIND SENS-TOT
domain-wide increase
increase at grid cells

## Slide 15: O3 at 14CST
SENS SENS-EMIS
SENS-WIND SENS-TOT

## Slide 16: NOx and O3

## Slide 17: O3 at other sites

## Slide 18
P3B vs CMAQ

## Slide 19: Summary
Causes of the high O3 on 25 September 2013
possible episodic flare emissions,
dry sunny postfrontal conditions,
calm or light wind,
nocturnal shallow boundary layer,
land-bay/sea breeze transition, wind reversal.
With “better” emission and wind, model predictions can become more accurate (amount, location, timing).
Suggestions
Improving model’s capability to reproduce small scale meteorological conditions favoring O3 production, such as stagnation and wind reversals, is needed.
Land-sea/bay circulation patterns may last for long time.
Need better industry emissions management, clean transportation.

## Slide 20: Thank you! Questions?
Further questions can be sent to: sp694@cornell.edu or shuaipan87@qq.com

## Slide 21
Observed wind during flight taking off and landing
NOAA MADIS Aircraft Communications Addressing and Reporting System (ACARS)
0-1000 m at 7 CST and 10 CST
0-2000 m at 13 CST and 16 CST
weak westerly
roughly converging

## Slide 22
(Haman et al., 2012; 2014)
On high ozone days,
PBL heights are consistently lower during nighttime/morning;
observed PBL growth rates are lower during early morning
nocturnal shallow boundary layer
UH
PBL
A rapid increase (>1000 m) at noon
06 CST
14 CST

## Slide 23: Dominate flow patterns
1-day backward trajectory using MCIP 10-m wind
09/24 16CST
09/25 16CST

## Slide 24
Impact of biomass burning
Base: baseline emission
BB: Base + fire emission