## Slide 1: Air Quality Modeling of Oil and Gas Emissions
Saravanan Arunachalam1, Srinivas Reka1, Dongmei Yang1,
David Lyon2, Hillary Hull2, Ryan O Connell2, Ananya Roy2,
Beth Trask2, & Jonathan Buonocore3
1Institute for the Environment, The University of North Carolina at Chapel Hill, NC, USA
2Environmental Defense Fund, Washington DC, USA
3Harvard TH Chan School of Public Health, Boston, MA, USA
Presenting at
The 18th Annual CMAS Conference, Chapel Hill, NC, USA
October 21 – 23, 2019

## Slide 2: Introduction
Background:
Air pollution is the largest environmental risk to human health and well-being
Oil and Natural Gas (O/NG) is a key anthropogenic source of air pollution worldwide
O/NG is key fast growing source, with total impact on U.S. GDP was $1.3 trillion in 2015 (API, 2017)
17.6 million people live within ∼1 mile of at least one active O/NG well in the U.S. (Czolowski et al, 2017)
O/NG activities have the potential to increase emissions of VOCs (and methane). Largest source of industrial methane emissions is from O/NG activities
Methane is a potent greenhouse gas (0.97 W/m2 to climate forcing) that also contributes to background levels of ozone pollution (~4 ppbV to surface O3 in 2030)​ (Fiore et al, 2008)
Methane emissions are underestimated in the U.S. inventories by > 60%, due to missing emissions released during abnormal operating conditions (Alvarez et al, 2018)
Objectives:
Assess air quality (and health) impacts due to O/NG activities in the U.S.
  Review/update VOC emissions in NEI based on new synthesis study
  Use CMAQ-DDM (Napelenok et al, 2006) to assess source-specific sensitivities of O3 and PM2.5 to individual shale play precursors

## Slide 3: Oil and Gas (O/NG) Activity and Emissions in the U.S.
np_OG_PM2.5
np_OG_NOx
pt_OG_NOx
pt_OG_PM2.5
pt_OG_VOC
np_OG_VOC
VOCs contribution from O/NG activity is ~25%

## Slide 4: Methane Synthesis Study - Ground-based facility-scale measurements (BU) vs. aircraft measurements (TD)
Top-down (TD) vs. Bottom-up (BU) estimates for 9 regions in the U.S.
9 regions contribute to ~30% of U.S. O/NG production
Alvarez et al, 2018

## Slide 5: Breakdown of O/NG Emissions Precursors by Processing Segment (2016 Beta)
VOCs: Production and production tanks contribution is ~97%

## Slide 6: Approach: CMAQ Model Simulations
 |  | Emissions Year | Brute Force | CMAQ-DDM Inputs |  |  |  |  |  | 
 |  |  |  | Production | Production Tank | Gathering | I CE | Other | # Precursors | Total # Input Parameters
1 | Base Case (Unadjusted) | 2016 | X |  |  |  |  |  |  | 
2 | Adjusted Base Case (EDF inputs) | 2016 | X |  |  |  |  |  |  | 
3 | Adjusted Base Case (EDF inputs) | 2016 |  | X | X | X | X | X | 4 | 20
4 | Group 1 States (TX, PA, CO) | 2016 |  | X | X | X | X | X | 4 | 20
5 | Group 2 States (LA, WY, NM) | 2016 |  | X | X | X | X | X | 4 | 20
6 | Group 3 States (UT, OH) | 2016 |  | X | X | X | X | X | 4 | 20
7 | Group 4 States (ND, OK) | 2016 |  | X | X | X | X | X | 4 | 20
8 | Group 5 States (CA, WV) | 2016 |  | X | X | X | X | X | 4 | 20
9 | Regulatory Scenarios - BAU | 2016 |  | X | X | X | X | X | 4 | 20
10 | Projection Year Scenarios ( 5 ) | 2023 / 2028 |  | X | X | X | X | X | 4 | 20
Use “footprint” CMAQ simulations to isolate plumes from each state/shale play
Track O3 and PM2.5 precursors in CMAQ-DDM from each group separately

## Slide 7: CMAQ Model Settings & Key Inputs
Option | Description
Model version | CMAQv5.2.1 w/ DDM (Napelenok et al, 2006)
Model resolution | 12x12-km
Grid details | 299 rows, 459 cols, 35 layers
Model Period | January, April, July, and October-2016
Chemical mechanism | cb6r3_ae6_aq
Emissions | EPA’s 2016 Beta emissions (2016ff_16j)
CTM_WB_DUST | Use in-line windblown dust emissions
CTM_BIOGEMIS | Calculate in-line biogenic emissions
CTM_PT3DEMIS | Calculate in-line plume rise for elevated point emissions
LTNG_NOx | Included
Meteorology | WRFv3.8.1

## Slide 8
w_OG
Delta
% Delta
w_OG
Delta
% Delta
Annual
July
July & Annual 2016 MDA8 O3 Contributions
MDA8 O3: O/NG contribute a max of up to ~7 ppb (16%) increase in July
vs. ~3 ppb (7%) for Annual Average

## Slide 9: Jan & Jul 2016 Average PM2.5 Contributions
January
July
w_OG
% Delta
Delta
% Delta
w_OG
Delta
PM2.5: O/NG contribute a max of upto ~3 g/m3 (48%) in January
vs. ~2 g/m3 (34%) Annual

## Slide 10
Annual
w_OG
wo_OG
% Delta
Delta
PM2.5 Annual Average Contributions
PM2.5: Denver Basin and Lewis Basin are the highest contributors for Delta and % Delta

## Slide 11
Speciated PM2.5 Contributions
OM aerosol is the highest (Delta) contributor among PM2.5 components

## Slide 12
Speciated PM2.5 Contributions (%)
NO3 aerosol is the highest (% Delta) contributor among PM2.5 components

## Slide 13: Domain-wide O3 and PM2.5 Contributions
Delta PM2.5 |  |  |  | 
 | Domain Max |  | Domain average | 
 | Diff (µg/m3) | Perc Diff (%) | Diff (µg/m3) | Perc Diff (%)
January | 2.916 | 47.6 | 0.033 | 1.9
April | 1.054 | 28.1 | 0.018 | 1.0
July | 1.205 | 28.6 | 0.024 | 1.4
October | 1.481 | 34.7 | 0.030 | 1.6
Annual | 1.653 | 33.8 | 0.026 | 1.5
Delta O3 |  |  |  | 
 | Domain Max |  | Domain average | 
 | Diff (ppbV) | Perc Diff (%) | Diff (ppbV) | Perc Diff (%)
July | 6.66 | 16.1 | 0.370 | 2.1
Annual | 2.67 | 6.7 | 0.239 | 1.6
Speciated PM2.5 Contribution
OM aerosol is the highest (%) contributor among PM2.5 components

## Slide 14: Brute Force vs. DDM for O3 from Key O/NG Segments
O3_ENOx
O3_EVOC
O3_ENOX
O3_EVOC
July: Brute Force (All OG)
O/NG segment: Production
O/NG segment: Production tanks
Production Segment exhibit higher sensitivity to O3 than Production Tanks

## Slide 15
Brute Force vs. DDM for PM2.5 from
Key O/NG Segments
July: Brute Force (All OG)
O/NG segment: Production
O/NG segment: Production tanks
PM2.5_ENOX
PM2.5_EVOC
PM2.5_EPM
PM2.5_ENOX
PM2.5_EVOC
PM2.5_EPM
Production exhibits higher sensitivity to PM2.5 than Production Tanks

## Slide 16
2016v1 platform vs. 2016 Beta emissions
2016v1 platform VOCs emissions decrease by ~3.7%

## Slide 17: Summary
Preliminary assessment of O/NG impacts on O3 and PM2.5 complete, using EPA’s 2016 Beta emissions
  Production and Production tanks contribute ~97% of all O/NG emissions
  Domain average contributions are 1.6% and 1.5% for O3 and PM2.5, while maximum contributions are 16% for O3 (July) and 48% for PM2.5 in Jan
  OM is the largest component (38%) of O/NG-attributable PM2.5
  CMAQ-DDM based results highlight ability to attribute O3 and PM2.5 impacts to specific precursors from specific O/NG segments
Revised assessment using updated VOC estimates in 2016v1 platform in progress
Next Steps
  Calculate sensitivities of O3 and PM2.5 to O/NG emissions precursors from state-specific shale plays using CMAQ-DDM by segment
  Perform health-risk assessment due to O3 and PM2.5 for baseline and various policy options

## Slide 18: Acknowledgments
Saravanan Arunachalam, PI
Environmental Defense Fund (EDF)
U.S. EPA OAQPS
  Alison Eyth and Jeff Vukovich
UNC-IE team
Collaborators
This work used the Extreme Science and Engineering Discovery Environment (XSEDE), which is supported by National Science Foundation grant number ACI-1548562. This work used the XSEDE's Stampede2 at the Texas Advanced Computing Center (TACC) through allocation TG-ATM190010.

## Slide 19
Thank you
Ted Wood/Photo Group
Frans Lanting/Getty Images

## Slide 20
Extra slides

## Slide 21: O/NG segments

## Slide 22
PM2.5: Model Evaluation

## Slide 23
PM2.5: Model Evaluation

## Slide 24
O3: Model Evaluation