## Slide 1: Air pollutant emission impacts of electric vehicle market penetration scenarios
Dan Loughlin, Samaneh Babaee*, Yang Ou*, Carol Lenox, Chris Nolte, and Tai Wu
U.S. EPA Office of Research and Development
* Research participants through the Oak Ridge Institute for Science and Education
Susan Burke, Meredith Cleveland, Chris Ramig, Michael Shell, Ryan Sims, and Aaron Sobel
U.S. EPA Office of Air and Radiation
Steven J. Smith
Joint Global Change Research Institute

## Slide 2: Foreword
Intended audience
  Air quality researchers and managers interested in assessing the multi-decadal and environmental implications of emerging technologies and future scenarios.
Caveats
  All results are intended to be illustrative. Assumptions are not fully described here. Please do not cite the results.
Acknowledgements
  Others who have contributed substantially to the work presented here include Wenjing Shi, a grantee through the Oak Ridge Institute for Science and Education (ORISE), and Gokul Iyer of Pacific Northwest National Laboratory (PNNL).
Disclaimer
  The views expressed in this presentation are those of the authors and do not necessarily represent the views or policies of the U.S. EPA or other author institutions.

## Slide 3: Abbreviations
Models
  GCAM – Global Change Assessment Model
  GCAM-USA – GCAM version with state-level resolution for the United States
Emissions
  BC – Black carbon
  CFCs - Chlorofluorocarbons
  CH4 – Methane
  CO – Carbon monoxide
  CO2 – Carbon dioxide
  GHG – Greenhouse gases
  N2O – Nitrous Oxide
  NOx – Nitrogen oxides
  OC – Organic carbon
  PM – Particulate Matter
  PM2.5 – PM of diameter less than 2.5 microns
  SO2 – Sulfur dioxide
  VOC – Volatile Organic Compounds
Units
  EJ – Exajoules
  MTC – Megatonnes Carbon
  kT – Kilotonnes
Technologies and fuels
  CCS – Carbon Capture and Sequestration
  CHP – Combined Heat and Power
  EV – Electric Vehicle
  CNG – Compressed Natural Gas
Organizations
  JGCRI – Joint Global Change Research Institute
  NREL – National Renewable Energy Laboratory
  ORISE – Oak Ridge Institute for Science and Education
  PNNL – Pacific Northwest National Laboratory
  RGGI – Regional Greenhouse Gas Initiative
  U.S. EPA – United States Environmental Protection Agency
Other
  AEO18 – Annual Energy Outlook 2018
  PC – Personal Computer
  IPM – Integrated Planning Model
  GDP – Gross Domestic Product

## Slide 4: Outline
Background
  Human-earth system models
  Global Change Assessment Model (GCAM)
  GCAM Long-term Interactive Multi-Pollutant Scenario Evaluator (GLIMPSE)
Illustrative application: Electric vehicles
  U.S. national impacts
  U.S. regional impacts
Summary
Next steps

## Slide 5: Background: Human-earth system models
End points
Technology penetrations
Energy
Fuel use and prices
GHG emissions
Climate
Global mean temperature
Air pollutant emissions
Environmental
Policy cost
Economic
Energy prices
Land and food prices
Water use
Health impacts
Scenario
assumptions
Population
growth
Economic growth
Climate change
Technology development
Behavior and preferences
Resource
availability
Policies

## Slide 6: Background: Human-earth system models
Energy
system
Industry
Buildings
Transport
Agriculture
Land use
Water resources
Atmosphere
Land resources
Carbon cycle
Earth systems
Human systems
Simulate each system and their interactions
End points
Technology penetrations
Energy
Fuel use and prices
GHG emissions
Climate
Global mean temperature
Air pollutant emissions
Environmental
Policy cost
Economic
Energy prices
Land and food prices
Simulation model
Water use
Health impacts
Human-earth system models differ in their components, level of detail, and outputs.
Scenario
assumptions
Population
growth
Economic growth
Climate change
Technology development
Behavior and preferences
Resource
availability
Policies

## Slide 7: Background: Global Change Assessment Model with state resolution
End points
Technology penetrations
Energy
Fuel use and prices
GHG emissions
Climate
Global mean temperature
Air pollutant emissions
Environmental
Policy cost
Economic
Energy prices
Land and food prices
GCAM-USA
GCAM development is organized by the Joint Global Change Research Institute
U.S. EPA modifications to GCAM-USA include refined emission factors, emissions controls, air quality and energy policies, and a graphical interface
Time horizon: 2010 – 2100 (typically 2010-2050)
Time steps: 5 years
Spatial coverage:
Global, 32 energy-economic regions
U.S. energy system at 50-state resolution
Sectors:
Electric, industrial, buildings, transportation, ag
Emissions:
GHG: CO2, CH4, N2O, CFCs
Air pollutant: NOx, SO2, PM, CO, VOC, BC, OC
Platform: PC, Mac, or Linux
Availability: Open source, free
Water use
Health impacts
Scenario
assumptions
Population
growth
Economic growth
Climate change
Technology development
Behavior and preferences
Resource
availability
Policies

## Slide 8: Background: Topics that can be explored with GCAM-USA
Estimate future air pollutant and greenhouse gas emissions
Evaluate outputs over alternative scenarios or assumptions
  Population, GDP, technologies, etc.
Evaluate the impacts of various policies and regulations
  Pollutant taxes or caps
  Renewable portfolio standards
  Vehicle efficiency standards
  Subsidies on specific technologies
  Emission standards on new sources
For various technological or policy scenarios
  Characterize cross-sector interactions
  Identify unintended consequences
Develop low-cost management strategies
  Simultaneously considering measures such as controls, energy efficiency, renewable electricity, and fuel switching

## Slide 9: Background: GLIMPSE multi-pollutant scenario evaluator
End points
Technology penetrations
Energy
Fuel use and prices
GHG emissions
Climate
Global mean temperature
Air pollutant emissions
Environmental
Policy cost
Economic
Energy prices
Land and food prices
GLIMPSE
The GLIMPSE graphical interface simplifies setting up and executing modeling runs, visualizing results
Time horizon: 2010 – 2100 (typically 2010-2050)
Time steps: 5 years
Spatial coverage:
Global, 32 energy-economic regions
U.S. energy system at 50-state resolution
Sectors:
Electric, industrial, buildings, transportation
Emissions:
GHG: CO2, CH4, N2O, CFCs
Air pollutant: NOx, SO2, PM, CO, VOC, BC, OC
Platform: PC, Mac, or Linux
Availability: Open source, free
Water use
Health impacts
Scenario
assumptions
Population
growth
Economic growth
Climate change
Technology development
Behavior and preferences
Resource
availability
Policies

## Slide 10: Illustrative application: Energy and emission impacts of electric vehicles
Context
  AEO18 passenger vehicle EV market share in 2050: ~11%
  However, recent EV cost projections are much lower than in AEO18
Research questions
  What EV penetration is projected by GCAM-USA using updated EV costs?
  What are the energy and emission impacts of greater EV penetration?
  How do these impacts differ by U.S. region?
  What drives regional differences?
Methodology
  Compare two scenarios with GCAM-USA:
    Low-EV: calibrated to approximate AEO18
    Higher-EV: projected using GCAM-USA using updated EV costs

## Slide 11: Results: Light duty market penetration
Chart: Billion pass-km
| 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Conventional | 6488.2701 | 6449.6753 | 5979.5614 | 5212.4978 | 4481.7142 | 3776.913 | 3480.016 | 3244.5964 | 3068.5202
Hybrids | 6.7007 | 459.7361 | 1280.1549 | 2156.3978 | 2721.4514 | 3053.056 | 3048.5359 | 2970.4748 | 2896.6894
CNG | 0 | 54.7966 | 126.9063 | 211.3026 | 318.2651 | 446.3989 | 545.4666 | 649.6964 | 757.8765
Electric | 0 | 18.1483 | 87.1035 | 389.5018 | 865.0677 | 1505.5726 | 2094.8201 | 2669.1332 | 3190.5091
Higher-EV
Light duty travel met by EVs, 2050: 31%
Chart: Billion pass-km
| 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Electric | 0 | 6.7827 | 37.6496 | 112.5518 | 429.5093 | 909.8076 | 1382.4612 | 1849.9647 | 2274.8268
CNG | 0 | -0.34818 | 6.7419 | 11.7636 | 25.076 | 34.2784 | 21.2214 | -10.6327 | -57.3124
Hybrids | 0 | -2.8521 | -10.1524 | -79.4284 | -278.8883 | -560.4153 | -810.365 | -1043.2529 | -1244.2186
Conventional | 0 | -7.2692 | -46.4431 | -93.4616 | -204.7366 | -395.871 | -587.8063 | -774.7077 | -938.1955
Higher-EV minus Low-EV
About 60% of offset travel demand is
from hybrid cars and trucks.
How does EV market penetration differ between the Low-EV and Higher-EV scenarios?
What technologies are being displaced by higher EV penetration?
Chart: Billion pass-km
| 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Conventional | 6488.2701 | 6456.9347 | 6025.9331 | 5305.1374 | 4681.6468 | 4159.6201 | 4041.0686 | 3976.5631 | 3956.8547
Hybrids | 6.7007 | 462.587 | 1290.269 | 2235.3854 | 2996.8288 | 3605.5399 | 3843.404 | 3993.2122 | 4110.4295
CNG | 0 | 55.1448 | 120.1657 | 199.5507 | 293.6303 | 410.4098 | 518.26 | 647.1564 | 799.4101
Electric | 0 | 11.4733 | 49.5616 | 278.243 | 445.1952 | 624.1871 | 771.7813 | 912.8725 | 1023.0346
Conventional
Hybrid
EV
CNG
Low-EV
Light duty travel met by EVS, 2050: 11%

## Slide 12: Results: Electricity production
How much additional electricity must be produced in the Higher-EV scenario?
What mix of technologies are used to meet the additional electricity demands?
Chart: Electricity (EJ)
| 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Coal | 0 | 0.0014558 | 0.0078837 | 0.017746 | 0.056155 | 0.11089 | 0.16324 | 0.2141 | 0.26078
Coal w/CCS | 0 | 0 | 0 | 4.4409e-06 | 2.7104e-05 | 5.5738e-05 | 7.556e-05 | 9.6085e-05 | 0.00012036
Gas | 0 | 0.0027782 | 0.012386 | 0.032513 | 0.11376 | 0.22606 | 0.32311 | 0.40879 | 0.47691
Gas w/CCS | 0 | 0 | 0 | 6.7177e-05 | 0.0004342 | 0.00097582 | 0.001362 | 0.0016983 | 0.0019241
Oil | 0 | 0.00010161 | 0.00038528 | 0.0012114 | 0.0037434 | 0.0058912 | 0.0069498 | 0.0081838 | 0.0088143
Oil w/CCS | 0 | 0 | 0 | 2.5334e-05 | 0.00012044 | 0.00018593 | 0.00016189 | 0.00013928 | 0.0001062
Biomass | 0 | 7.6528e-05 | 0.00027367 | 0.0015134 | 0.0063427 | 0.012985 | 0.017831 | 0.022661 | 0.026998
Biomass w/CCS | 0 | 0 | 0 | 4.4182e-06 | 2.9529e-05 | 5.6759e-05 | 5.9274e-05 | 5.5099e-05 | 3.9276e-05
Nuclear | 0 | 1.85e-05 | 0.0010016 | 0.0002447 | 0.0003197 | 0 | 0 | 1e-07 | 0
Geothermal | 0 | 2.6118e-05 | 4.7729e-05 | 0.00076774 | 0.0035275 | 0.0075217 | 0.011225 | 0.014512 | 0.016809
Hydro | 0 | 6.46e-06 | 0.00079159 | 8.0633e-05 | 9.2936e-05 | 0 | 0 | 0 | 0
Wind | 0 | 4.311e-05 | 0.00084397 | 0.0087797 | 0.040312 | 0.088851 | 0.13686 | 0.18569 | 0.23081
Higher-EV minus Low-EV
Some coal that would retire under the Low-EV scenario instead stays in use.
Natural gas, wind, and solar comprise most of the additional generation.
Chart: Electricity (EJ)
| 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Coal | 7.1052 | 4.8698 | 4.6493 | 4.6284 | 4.5601 | 4.4976 | 4.4633 | 4.3813 | 4.3565
Coal w/CCS | 0 | 0 | 0 | 0.00011271 | 0.00017065 | 0.00027838 | 0.00046187 | 0.00067948 | 0.00092565
Gas | 3.3845 | 6.3511 | 6.0364 | 6.1174 | 6.1944 | 6.2871 | 6.4252 | 6.5248 | 6.7055
Gas w/CCS | 0 | 0 | 0 | 0.0014397 | 0.0027144 | 0.0044473 | 0.0067769 | 0.0091302 | 0.011821
Oil | 0.14454 | 0.10497 | 0.077836 | 0.082214 | 0.07865 | 0.081697 | 0.087075 | 0.091886 | 0.097134
Oil w/CCS | 0 | 0 | 0 | 0.00040692 | 0.00050593 | 0.0006425 | 0.00080518 | 0.00080739 | 0.00087873
Biomass | 0.11543 | 0.065587 | 0.045514 | 0.065145 | 0.090606 | 0.12839 | 0.17367 | 0.2153 | 0.26318
Biomass w/CCS | 0 | 0 | 0 | 0.0001422 | 0.00016838 | 0.00022171 | 0.00032401 | 0.00042031 | 0.00056567
Nuclear | 3.0201 | 3.0063 | 2.9599 | 2.9846 | 2.9815 | 2.9692 | 2.9482 | 2.9141 | 2.8598
Geothermal | 0.063273 | 0.090285 | 0.088468 | 0.10426 | 0.1242 | 0.14599 | 0.11836 | 0.12515 | 0.16055
Hydro | 0.94531 | 0.94476 | 0.93009 | 0.94367 | 0.94514 | 0.94531 | 0.94531 | 0.94531 | 0.94531
Wind | 0.34252 | 0.6429 | 1.0211 | 1.1546 | 1.3984 | 1.7238 | 1.8306 | 1.9871 | 2.0765
Coal
Gas
Nuclear
Solar
Wind
Hydro
Low-EV
After 2020, wind and solar make
up a large portion of new generation
Chart: Electricity (EJ)
| 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Coal | 7.1052 | 4.8713 | 4.6572 | 4.6461 | 4.6163 | 4.6085 | 4.6266 | 4.5954 | 4.6173
Coal w/CCS | 0 | 0 | 0 | 0.00011715 | 0.00019775 | 0.00033412 | 0.00053743 | 0.00077556 | 0.001046
Gas | 3.3845 | 6.3539 | 6.0488 | 6.1499 | 6.3082 | 6.5131 | 6.7484 | 6.9335 | 7.1825
Gas w/CCS | 0 | 0 | 0 | 0.0015068 | 0.0031486 | 0.0054232 | 0.0081389 | 0.010829 | 0.013745
Oil | 0.14454 | 0.10507 | 0.078221 | 0.083426 | 0.082393 | 0.087588 | 0.094025 | 0.10007 | 0.10595
Oil w/CCS | 0 | 0 | 0 | 0.00043225 | 0.00062637 | 0.00082843 | 0.00096707 | 0.00094666 | 0.00098492
Biomass | 0.11543 | 0.065663 | 0.045787 | 0.066659 | 0.096948 | 0.14138 | 0.1915 | 0.23796 | 0.29017
Biomass w/CCS | 0 | 0 | 0 | 0.00014662 | 0.00019791 | 0.00027846 | 0.00038328 | 0.00047541 | 0.00060495
Nuclear | 3.0201 | 3.0064 | 2.9609 | 2.9848 | 2.9818 | 2.9692 | 2.9482 | 2.9141 | 2.8598
Geothermal | 0.063273 | 0.090311 | 0.088516 | 0.10503 | 0.12773 | 0.15351 | 0.12959 | 0.13966 | 0.17736
Hydro | 0.94531 | 0.94477 | 0.93088 | 0.94375 | 0.94523 | 0.94531 | 0.94531 | 0.94531 | 0.94531
Wind | 0.34252 | 0.64294 | 1.0219 | 1.1634 | 1.4387 | 1.8127 | 1.9675 | 2.1728 | 2.3073
Higher-EV
By 2050, electricity production has
increased by 7% relative to Low-EV
Low-EV total

## Slide 13: Results: System-wide emissions response at the national level
Chart: Differences in emissions in 2050, Higher-EV minus Low-EV
| CO2 (MTC) | NOx (Kt) | SO2 (Kt) | PM2.5 (Kt)
Electricity | 28.953 | 21.0724 | 11.0581 | 6.0402
Industry | 0.11837 | 0.84353 | 0.80269 | 0.33116
Industry-Fuel chain | -5.4446 | -18.8925 | -17.9292 | -1.301
Residential | 0.045865 | 0.16058 | 0.050196 | 0.27039
Commercial | 0.013746 | 0.054368 | 0.015831 | 0.011071
Transportation-Nonroad | -0.0015262 | -0.010262 | -0.00075415 | -0.00028487
Transportation-Onroad | -48.7607 | -51.0575 | -1.2937 | -0.79696
Net | -25.0759 | -47.8294 | -7.2968 | 4.5546
Categories:
(1) Primary:
Avoided tailpipe emissions (purple)
(2) Secondary:
Avoided refinery emissions (red)
Electricity production emissions (blue)
(3) Tertiary:
Price-induced fuel-switching (light purple,
green, and orange)
There is a net reduction in CO2, NOx, and SO2. PM2.5 increases, driven by the electric sector.
CO2 (MTC) NOx (kT) SO2 (kT) PM2.5 (kT)
Transportation
Electric sector
Fuel extraction, refining
and transport
Net

## Slide 14: Results: System-wide emissions response at the national level
Chart: Differences in emissions in 2050, Higher-EV minus Low-EV
| CO2 (MTC) | NOx (Kt) | SO2 (Kt) | PM2.5 (Kt)
Electricity | 28.953 | 21.0724 | 11.0581 | 6.0402
Industry | 0.11837 | 0.84353 | 0.80269 | 0.33116
Industry-Fuel chain | -5.4446 | -18.8925 | -17.9292 | -1.301
Residential | 0.045865 | 0.16058 | 0.050196 | 0.27039
Commercial | 0.013746 | 0.054368 | 0.015831 | 0.011071
Transportation-Nonroad | -0.0015262 | -0.010262 | -0.00075415 | -0.00028487
Transportation-Onroad | -48.7607 | -51.0575 | -1.2937 | -0.79696
Net | -25.0759 | -47.8294 | -7.2968 | 4.5546
Categories:
(1) Primary:
Avoided tailpipe emissions (purple)
(2) Secondary:
Avoided refinery emissions (red)
Electricity production emissions (blue)
(3) Tertiary:
Price-induced fuel-switching (light purple,
green, and orange)
There is a net reduction in CO2, NOx, and SO2. PM2.5 increases, driven by the electric sector.
CO2 (MTC) NOx (kT) SO2 (kT) PM2.5 (kT)
Transportation
Electric sector
Fuel extraction, refining
and transport
Net

## Slide 15: Results: System-wide emissions response at the national level
Chart: Differences in emissions in 2050, Higher-EV minus Low-EV
| CO2 (MTC) | NOx (Kt) | SO2 (Kt) | PM2.5 (Kt)
Electricity | 28.953 | 21.0724 | 11.0581 | 6.0402
Industry | 0.11837 | 0.84353 | 0.80269 | 0.33116
Industry-Fuel chain | -5.4446 | -18.8925 | -17.9292 | -1.301
Residential | 0.045865 | 0.16058 | 0.050196 | 0.27039
Commercial | 0.013746 | 0.054368 | 0.015831 | 0.011071
Transportation-Nonroad | -0.0015262 | -0.010262 | -0.00075415 | -0.00028487
Transportation-Onroad | -48.7607 | -51.0575 | -1.2937 | -0.79696
Net | -25.0759 | -47.8294 | -7.2968 | 4.5546
Categories:
(1) Primary:
Avoided tailpipe emissions (purple)
(2) Secondary:
Avoided refinery emissions (red)
Electricity production emissions (blue)
(3) Tertiary:
Price-induced fuel-switching (light purple,
green, and orange)
There is a net reduction in CO2, NOx, and SO2. PM2.5 increases, driven by the electric sector.
CO2 (MTC) NOx (kT) SO2 (kT) PM2.5 (kT)

## Slide 16: Results: Comparison of regional emission responses
How do the regional net emission changes compare?
Chart: Net CO2 and NOx changes by region, 2050
| -5.2059159757334654E-2 | -1.7395236182832775E-2 | -8.1638269852990081E-3 | -1.6767176030312071E-2 | -2.5119871438068125E-2 | 5.8333444802314768E-4 | -1.3468034369642152E-2 | -1.0411163281518986E-2 | -3.6310016421201657E-2 | -6.5000000000000002E-2 | -1.7622817535934053E-2
Nox | -0.017009 | -0.011716 | -0.0091102 | -0.0059306 | -0.010306 | -0.0023925 | -0.012552 | -0.0073253 | -0.02337 | -0.022 | -0.010692
Greater reductions
7
3
8
4
6
9
National
1
2
3
4
5
6
7
8
9
Hawaii and Alaska are not included in Region 9 values shown
Pacific
New England

## Slide 17: Results: Differences in regional CO2 emissions
Differences in 2050 CO2 by Census Division and sector, Higher-EV minus Low-EV
Sectoral
Largest decrease: Region 5, Southeast, -6.5 MTC
(MTC)
Net change across all sectors
Net change in CO2 emissions by Census Division
(MTC)
(MTC)
(MTC)
(MTC)
Net

## Slide 18: Results: Factors driving regional differences
The technologies used to meet additional electricity demands differ by region
Chart: Region 6
| 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Coal | 0 | 0.000175 | 0.0010083 | 0.001609 | 0.0045576 | 0.0088281 | 0.013085 | 0.017726 | 0.022085
Coal w/CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Gas | 0 | 0.00021578 | 0.00121 | 0.002215 | 0.0059746 | 0.011335 | 0.016472 | 0.021658 | 0.026435
Gas w/CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Oil | 0 | 8.4234e-06 | 2.3202e-05 | 8.6887e-05 | 0.00021978 | 0.00033985 | 0.00042152 | 0.00052838 | 0.00061376
Oil w/CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Biomass | 0 | 4.2761e-06 | 2.9016e-05 | 7.8272e-05 | 0.00032031 | 0.0007247 | 0.0011307 | 0.0016212 | 0.0021249
Biomass w/CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Nuclear | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Geothermal | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Hydro | 0 | 0 | 1.284e-05 | 0 | 0 | 0 | 0 | 0 | 0
Wind | 0 | 4.3699e-06 | 1.0276e-05 | 0.00020604 | 0.00098821 | 0.0023742 | 0.0039735 | 0.0058782 | 0.0078851
Emission intensity of additional electricity in 2050:
CO2: 24 MTC/EJ
NOx: 21 kT/EJ
Chart: Region 9 (w/o Hawaii and Alaska)
| 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Coal | 0 | 4.898e-05 | 0.00012221 | 0.00048539 | 0.0017525 | 0.0035446 | 0.0052193 | 0.0067695 | 0.0081294
Coal w/CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Gas | 0 | 0.00023999 | 0.00034452 | 0.0049162 | 0.021128 | 0.042685 | 0.060434 | 0.07556 | 0.08668
Gas w/CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Oil | 0 | 4.43e-06 | 3.1529e-06 | 0.00010175 | 0.00033524 | 0.00046777 | 0.00046501 | 0.00048148 | 0.00045802
Oil w/CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Biomass | 0 | 1.3007e-05 | 7.675e-06 | 0.00030915 | 0.0013116 | 0.0024634 | 0.0031033 | 0.003661 | 0.0040256
Biomass w/CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Nuclear | 0 | 0 | 4.1e-05 | 0 | 0 | 0 | 0 | 0 | 0
Geothermal | 0 | 1.2127e-05 | 5.358e-06 | 0.00048837 | 0.0023175 | 0.004885 | 0.0072599 | 0.0093543 | 0.010745
Hydro | 0 | 0 | 0.000544 | 0 | 0 | 0 | 0 | 0 | 0
Wind | 0 | 2.838e-06 | 0.00013481 | 0.0011224 | 0.004726 | 0.0099169 | 0.014494 | 0.018658 | 0.021817
Emission intensity of additional electricity in 2050:
CO2: 19 MTC/EJ
NOx: 7.8 kT/EJ
Chart: RGGI Region
| 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Coal | 0 | -7.272e-06 | 9.277e-06 | -0.00025286 | -0.0010963 | -0.0021616 | -0.0026249 | -0.0029714 | -0.0027179
Coal w/CCS | 0 | 0 | 0 | 2.5911e-06 | 1.4544e-05 | 2.7284e-05 | 3.3842e-05 | 4.022e-05 | 4.952e-05
Gas | 0 | 2.6533e-05 | 5.6213e-05 | 0.00011765 | 0.00048271 | 0.0013445 | 0.0020587 | 0.0024589 | 0.0031375
Gas w/CCS | 0 | 0 | 0 | 2.3702e-05 | 0.00014856 | 0.00032408 | 0.00044368 | 0.00055047 | 0.00062125
Oil | 0 | 1.6443e-06 | 2.6407e-06 | 1.3055e-05 | 2.0455e-05 | 2.2263e-05 | 1.2895e-05 | -2.2279e-06 | -1.6516e-05
Oil w/CCS | 0 | 0 | 0 | 1.0057e-05 | 4.2491e-05 | 6.3721e-05 | 5.3919e-05 | 4.4509e-05 | 3.1052e-05
Biomass | 0 | -9.913e-07 | -6.8857e-06 | 2.0551e-05 | 0.00016536 | 0.00020919 | 4.0083e-05 | -0.00029507 | -0.0006517
Biomass w/CCS | 0 | 0 | 0 | 2.7292e-06 | 1.8263e-05 | 3.429e-05 | 3.5053e-05 | 3.194e-05 | 2.1216e-05
Nuclear | 0 | 0 | 3.65e-05 | 0 | 0 | 0 | 0 | 1e-07 | 0
Geothermal | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Hydro | 0 | 0 | 3.0988e-06 | 0 | 0 | 0 | 0 | 0 | 0
Wind | 0 | 1.4724e-07 | 1.1739e-06 | 0.00053594 | 0.003633 | 0.0086293 | 0.013108 | 0.017454 | 0.021026
Chart: Region 1
| 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Coal | 0 | -4.97e-07 | -6.039e-06 | -4.7559e-05 | -0.00026376 | -0.00058562 | -0.00082712 | -0.0011168 | -0.0011604
Coal w/CCS | 0 | 0 | 0 | 1.6865e-06 | 1.0649e-05 | 1.9138e-05 | 2.2399e-05 | 2.5074e-05 | 3.042e-05
Gas | 0 | 1.9998e-05 | -1.2551e-06 | 0.00015688 | 0.00084896 | 0.0018897 | 0.0025671 | 0.0029159 | 0.0034165
Gas w/CCS | 0 | 0 | 0 | 1.8962e-05 | 0.00012843 | 0.00028121 | 0.00038616 | 0.00048286 | 0.00055114
Oil | 0 | 1.0437e-06 | 1.4638e-06 | 8.7872e-06 | 1.6181e-05 | 1.9496e-05 | 1.4905e-05 | 9.2682e-06 | 3.9783e-06
Oil w/CCS | 0 | 0 | 0 | 5.0687e-06 | 2.6166e-05 | 3.907e-05 | 3.3292e-05 | 2.8839e-05 | 2.1909e-05
Biomass | 0 | -1.1946e-06 | -6.6041e-06 | 1.2376e-05 | 0.00014049 | 0.00017216 | 1.8834e-05 | -0.00027848 | -0.00058211
Biomass w/CCS | 0 | 0 | 0 | 2.1332e-06 | 1.5607e-05 | 2.9015e-05 | 2.9598e-05 | 2.7655e-05 | 2.0174e-05
Nuclear | 0 | 0 | -1.16e-05 | 0 | 0 | 0 | 0 | 1e-07 | 0
Geothermal | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Hydro | 0 | 0 | -2.5012e-06 | 0 | 0 | 0 | 0 | 0 | 0
Wind | 0 | 1.2026e-07 | -8.4708e-07 | 0.00041935 | 0.0030395 | 0.0072129 | 0.010915 | 0.014519 | 0.017488
Emission intensity of additional electricity in 2050:
CO2: -1.9 MTC/EJ
NOx: -0.004 kT/EJ
Intensity calculation: Change in regional electric sector emissions (Higher-EV minus Low-EV)
Change in regional electricity production
The Region 1 response to EVs
reflects RGGI
1
2
3
4
5
6
7
8
9
Regions

## Slide 19: Observations
GCAM-USA suggests that increased EV market share will generally lead to net CO2 and NOx reduction benefits
  Changes in transportation, electric, and refinery sector emissions drive these trends
There is geographic heterogeneity in benefits due to factors such as:
  How additional electricity is produced
  How state and regional policies affect the
  production mix and use of controls
  How electricity is traded among regions
  Refineries activity is concentrated in several states

## Slide 20: Summary
GCAM-USA can be applied to examine the long-term energy and emission impacts of EVs
  Categories of impacts:
    Primary (transportation sector)
    Secondary (electricity production and refining)
    Tertiary (price-induced fuel switching within and across sectors)
  State-level insights informed by:
    Existing technology stock
    Fuel prices and renewable resources
    State, regional, and national policies and regulations

## Slide 21: Next Steps
Re-evaluate EV scenarios with the forthcoming version of GCAM-USA, which has an improved electric sector representation
Explore higher EV penetration scenarios
Link GCAM-USA with IPM to provide a more detailed exploration of electric sector response to EVs, including under alternative charging scenarios

## Slide 22: Questions?
For more information, please contact:
Loughlin.Dan@epa.gov
https://www.epa.gov/air-research/glimpse-computational-framework-supporting-state-level-environmental-and-energy