## Slide 1
Evaluation of the CMAQv5.3 Modeling System
K. Wyat Appel, Christian Hogrefe, Kristen Foley, George Pouliot, Robert Gilliam,
Benjamin Murphy, Havala Pye, Jesse Bash, Jonathan Pleim, Golam Sarwar, Tanya Spero,
Deborah Luecken (retired), Shawn Roselle (retired), Rohit Mathur,
and the CMAQ Development Team
Atmospheric and Environmental Systems Modeling Division
Center for Environmental Measurement and Modeling
Office of Research and Development
U.S. Environmental Protection Agency
22 October 2019
18th Annual CMAS Conference
Chapel Hill, NC

## Slide 2
CMAQv5.3 – Major Updates
Science updates and new features
  Aerosols
    Increased monoterpene SOA (Pye et al. 2015 ES&T, Xu et al. 2018 ACP), uptake of water onto hydrophilic organic aerosol (Pye et al. 2017 ACP), and reorganization of anthropogenic SOA (M. Qin)
  Gas chemistry
    Minor updates to CB6r3 (ClNO3 reaction added; first-order O3 depletion)
    Updated full halogen chemistry and added dimethyl sulfide (DMS) chemistry – included in optional detailed mechanism (Sarwar et al., Atmospheric Environment, 2019)
  Deposition
    Multiple updates to M3Dry deposition scheme (dependence of ozone soil resistance on moisture, gas phase deposition to snow, aerosol deposition)
    New Surface Tiled Aerosol and Gaseous Exchange (STAGE) deposition scheme available
  Emissions
    New Detailed Emissions Scaling, Isolation, and Diagnostic (DESID) module (easier scaling of emissions)
  Source apportionment
    The Integrated Source Apportionment Method (ISAM) has been updated to greatly improve efficiency and runtime
  Updated CMAQ documentation
    Updated CMAQ User’s Guide, science documentation and website (https://www.epa.gov/cmaq)
  Updated CMAQ tools
    ICON, BCON, Site compare, AMETv1.4, MCIPv5.0
Release schedule
  Beta version released October 2018
  Final version released August 2019: https://github.com/USEPA/CMAQ
  Instrumented models – ISAM, Sulfur tracking (available w/ final release); DDM available with future v5.3.1 release (12/2019)

## Slide 3
CMAQ Inputs and Configuration
All simulations are 2016 CONUS 12-km annual simulation
MCIP from the same 2016 WRF v3.8 simulation used in all simulations (WRF simulations use lightning assimilation)
2016 emissions based on “fe” and “ff” beta platform versions (final 2016v1 platform emissions coming soon)
 | CMAQv5.2.1 | CMAQv5.3
WRF Version | 3.8.1 | 3.8.1 and 4.1.1
MCIP Version | 4.5 | 4.5 and 5.0
Boundary Conditions | v5.2.1 Hemispheric CMAQ (with detailed halogen mechanism) | v5.3 Hemispheric CMAQ (with detailed DMS/halogen mechanism)
Chemical Mechanism | CB6r3 | CB6r3
Aerosol Module | AERO6 | AERO7
Deposition Scheme | M3Dry | M3Dry and STAGE
Bi-directional Ammonia | No | Yes and No
Wind-blown Dust | No | No
Lightning NOx | Yes | Yes

## Slide 4
MDA8 O3 Bias (Daily) – v5.2.1 vs v5.3 (M3Dry)
v5.2.1
v5.3
Lower O3 in the late spring, summer, and fall with v5.3
Reduced wintertime O3 underestimation with v5.3

## Slide 5
MDA8 O3 Bias (Monthly) – v5.2.1 vs v5.3 (M3Dry)
v5.2.1

## Slide 6
MDA8 O3 Bias (Monthly) – v5.2.1 vs v5.3 (M3Dry)
v5.2.1
v5.3

## Slide 7
MDA8 O3 Bias (Monthly) – v5.2.1 vs v5.3 (M3Dry)
v5.2.1
v5.3
v5.3 w/ v5.3β BCs

## Slide 8
MDA8 O3 Bias (Monthly) – v5.2.1 vs v5.3 (M3Dry)
v5.2.1
v5.3
v5.3 w/ v5.3β BCs
v5.3 w/ “ff” platform

## Slide 9
v5.2.1
v5.3
v5.3 w/ v5.3β BCs
MDA8 O3 Bias (Monthly) – v5.2.1 vs v5.3 (M3Dry)
v5.3 w/ WRFv4.1.1
v5.3 w/ “ff” platform

## Slide 10
O3: Impact of Incremental System Updates
Winter
Spring
Decrease in springtime O3 due to chemistry updates and BCs
Large increase in wintertime O3 w/ v5.3 due to reduced deposition to snow

## Slide 11
O3: Impact of Incremental System Updates
Summer
Fall
Decrease in summer/fall O3 due to chemistry updates and BCs
Increase in summer and fall O3 due to WRFv4.1.1

## Slide 12
PX LSM Vegetation Fraction and LAI Update
WRFv4.1.1 – WRFv3.8.1 using updated PX LSM (April 2016)
Use of time-varying Veg Fraction and LAI from MODIS satellite retrievals instead of FPAR/LAI from look-up tables significantly reduces vegetation fraction, which in turn reduces O3 dry deposition and increases O3 mixing ratios, particularly in the western US.

## Slide 13
MDA8 O3: CMAQv5.3 - v5.2.1 Seasonal Bias Difference
Winter
Spring
Summer
Fall
Improved Bias
Worse Bias
Improved Bias
Worse Bias
Improved Bias
Worse Bias
Improved Bias
Worse Bias
Cool colors indicate lower bias with v5.3; Warm colors indicate higher bias with v5.3 (range is -10 to +10 ppb)

## Slide 14
PM2.5 Bias (Daily) – v5.2.1 vs v5.3 (M3Dry)
v5.2.1
v5.3
Generally higher PM2.5 in late spring, summer, and fall with v5.3

## Slide 15
v5.2.1
PM2.5 Bias (Monthly) – v5.2.1 vs v5.3 (M3Dry)

## Slide 16
v5.2.1
v5.3 (w/o bidi)
PM2.5 Bias (Monthly) – v5.2.1 vs v5.3 (M3Dry)

## Slide 17
v5.2.1
v5.3 (w/o bidi)
PM2.5 Bias (Monthly) – v5.2.1 vs v5.3 (M3Dry)
v5.3 (w/ bidi)

## Slide 18
v5.2.1
v5.3 (w/o bidi)
PM2.5 Bias (Monthly) – v5.2.1 vs v5.3 (M3Dry)
v5.3 (w/ bidi)
v5.3 w/ new BCs

## Slide 19
v5.2.1
v5.3 (w/o bidi)
PM2.5 Bias (Monthly) – v5.2.1 vs v5.3 (M3Dry)
v5.3 (w/ bidi)
v5.3 w/ new BCs
v5.3 w/ “ff” platform

## Slide 20
v5.2.1
v5.3 (w/o bidi)
PM2.5 Bias (Monthly) – v5.2.1 vs v5.3 (M3Dry)
v5.3 (w/ bidi)
v5.3 w/ new BCs
v5.3 w/ WRFv4.1.1
v5.3 w/ “ff” platform

## Slide 21
Quick PSA on Emissions with v5.3
Potential Combustion SOA (PCSOA)
  Added to CMAQ in v5.2
  Intended to help account for missing PM2.5 from fossil-fuel combustion sources
  PCSOA was not intended to be applied to all combustion sources
    However, limitation prior to CMAQv5.3 to read multiple gridded emissions files lead to PCSOA being applied to unintended sources (e.g. Residential Wood Combustion (RWC))
    As such, CMAQv5.2 simulations with PCSOA enabled would overestimate PM2.5 from RWC
  CMAQv5.3 contains the new DESID option and ability to read multiple gridded emissions files
    This allows for RWC to be treated as an entirely separate emissions source from the rest of the gridded emissions
    As such, DESID allows for PCSOA to be applied to the other gridded combustion sources, but not RWC
    This correctly results in a reduction in PM2.5 from the unintentional application of PCSOA to RWC
If using cb6r3_ae7 with offline biogenic emissions, separate α-pinene from all other monoterpenes:
  Prevents overestimates in PM2.5 SOA as α-pinene should not make SOA through NO3 reaction
  Can still use existing biogenic emission files by updating the emission control file
  No action required for ae6 (any mechanism), in-line biogenics (any mechanism, any aero), or aero7 with SAPRC mechanisms
  See AERO7 overview release notes at https://github.com/USEPA/CMAQ/blob/master/DOCS/Release_Notes/aero7_overview.md
In CMAQv5.3 with PCSOA (default setting):
1. All fire and wood-burning related emissions should be separated from other emissions streams
2. If using CB6r3 with AERO7 and offline biogenics, separate α-pinene from all other monoterpenes

## Slide 22
PM2.5: Impact of Incremental System Updates
Winter
Spring
Large increase in wintertime PM2.5 due to increased oxidants in v5.3
PM2.5 reduced with emission update by not applying PCSOA to res-wood burning

## Slide 23
PM2.5: Impact of Incremental System Updates
Summer
Fall
Large increase in summer/fall PM2.5 due to increased SOA from monoterpene oxidation

## Slide 24
PM2.5: CMAQv5.3 - v5.2.1 Seasonal Bias Difference
Winter
Spring
Summer
Fall
Improved Bias
Worse Bias
Improved Bias
Worse Bias
Improved Bias
Worse Bias
Improved Bias
Worse Bias
Increased SOA in the Southeast with v5.3 leads to higher PM2.5 bias in summer and fall versus v5.2.1
Cool colors indicate lower bias with M3Dry; Warm colors indicate lower bias with STAGE

## Slide 25
CMAQv5.3 – STAGE vs. M3Dry
STAGE
M3Dry
STAGE
M3Dry
NH3
PM2.5

## Slide 26
PM2.5 – STAGE vs. M3Dry Seasonal Bias Difference
Winter
Spring
Summer
Fall
M3Dry Better
STAGE Better
M3Dry Better
STAGE Better
M3Dry Better
STAGE Better
M3Dry Better
STAGE Better
Reduced PM2.5 bias in the eastern US with M3Dry
Reduced PM2.5 bias in the western US with STAGE

## Slide 27
Summary
Ozone
  Higher O3 with v5.3 in winter improves underestimation vs. v5.2.1
    Largely due to changes in the representation of dry deposition in v5.3
  Lower O3 with v5.3 in spring increases underestimation vs. v5.2.1
  Lower O3 with v5.3 in summer/fall improves overestimation vs. v5.2.1
  BCs created using v5.3β (M3Dry) hemispheric CMAQ simulation contribute to lower O3 (vs BCs using v5.2.1)
    largest in the winter and fall
  WRFv4.1.1 results in generally higher O3 mixing ratios, particularly in the winter and spring
    result of time-varying VEGFRA and LAI derived from MODIS instead of the look-up values in the PX data table
Total PM2.5
  Generally higher PM2.5 in the summer/fall with v5.3 vs. v5.2.1
    primarily the result of increased SOA from monoterpene oxidation products
  Similar PM2.5 (to v5.2.1) outside of the summer
  STAGE has consistently higher PM2.5 than M3Dry throughout the year
  M3Dry has smaller warm-season NH3 bias vs. STAGE
  WRFv4.1.1 has a generally small effect on PM2.5 concentration throughout the year

## Slide 28
Acknowledgements and Disclaimer
CMAQ Development Team and Others
  Wyat Appel
  Jesse Bash
  Brian Eder
  Kathleen Fahey
  Kristen Foley
  Robert Gilliam
  Christian Hogrefe
  Bill Hutzell
  Daiwen Kang
  Deborah Luecken (retired)
  Rohit Mathur
  Benjamin Murphy
  Sergey Napelenok
  Chris Nolte
  Jonathan Pleim
  George Pouliot
  Havala Pye
  Limei Ran
  Shawn Roselle (retired)
  Golam Sarwar
  Donna Schwede
  Fahim Sidi
  Tanya Spero
  David Wong
The views expressed in this presentation are those of the authors and do not necessarily reflect the views or policies of the U.S. Environmental Protection Agency.

## Slide 29
Extra Slides

## Slide 30: O3 Changes CMAQv5.3β Minus CMAQv5.2.1
Spring 2016
Summer 2016
Fall 2016
Winter 2016
Annual Average 2016
Increased deposition to soil
Increased depletion due to updated halogen chemistry
Decreased deposition to snow
Overall result of moving to CMAQv5.3β BCs is reduced O3 over the CONUS from the lateral boundaries
30

## Slide 31
MDA8 O3 – CMAQv5.2.1 vs v5.3 (STAGE)

## Slide 32
PM2.5 – CMAQv5.2.1 vs v5.3

## Slide 33
CMAQv5.3 - v5.2.1 (January)
Organic Carbon
Non-Carbon Organic Matter

## Slide 34
CMAQv5.3 - v5.2.1 (July)
Organic Carbon
Non-Carbon Organic Matter

## Slide 35
CMAQv5.2.1 vs v5.3 (Jun – Aug)
Organic Carbon
Non-Carbon Organic Matter

## Slide 36
Hemispheric CMAQ – Winter MDA O3

## Slide 37
Hemispheric CMAQ – Summer MDA O3

## Slide 38
CMAQv5.3 PM2.5 – STAGE vs. M3Dry
STAGE
M3Dry
- 1
1.5
Jan
Mar
May
Jul
Sep
Nov

## Slide 39
CMAQv5.3 NH3 – STAGE vs. M3Dry
STAGE
M3Dry
- 0.8
- 0.1
Jan
Mar
May
Jul
Sep
Nov

## Slide 40
PM2.5: STAGE - M3Dry Seasonal Difference
PM2.5 with STAGE higher in all seasons vs. M3Dry, particularly in the Eastern U.S. and the San Joaquin Valley in California