## Slide 1: Comparing Projected and Modeled Health Benefits of Alternative Energy Futures
Kristen E Brown, PhD
CMAS conference
October 21, 2019

## Slide 2: Objectives
Energy use produces a lot of emissions so we want to:
Calculate benefits of emissions reductions
Analyze potential future outcomes
Determine which calculation method is best suited for 2045 analysis
Notes: Energy more broad than just electricity

## Slide 3: Energy Futures
Modeled four future energy scenarios
  No Fee -- Business as Usual
  HIP -- Fees targeting criteria pollutants
  GHG -- Fees targeting GHGs
  Combo -- Fees targeting criteria pollutants and GHGs
Results for 2045 are analyzed

## Slide 4: Emissions in 2045 in Each Scenario
Chart: kilotons emitted
| No Fee | HIP | Combo | GHG | No Fee | HIP | Combo | GHG | No Fee | HIP | Combo | GHG | NOx |  | PM2.5 |  | SO2
Transportation | 2005.04 | 1755 | 1754.79 | 1764.78 | 81.41 | 81.23 | 81.22 | 81.36 | 38.54 | 38.34 | 38.35 | 38.49
Industry | 1493.92 | 912.16 | 949.67 | 1449.82 | 246.86 | 175.6 | 169.4 | 236.6 | 1592.79 | 643.55 | 636.88 | 1466.78
Electricity | 1436.37 | 324.42 | 274.73 | 903.39 | 46.13 | 16.43 | 16.23 | 66.24 | 1266.49 | 14.36 | 12.83 | 175.29
Notes: This specific policy led to more change in electricity & industry, which you’ll see in AQ changes

## Slide 5: Expectations
Health Benefits
Emissions Changes
Marginal Damages
Tons in MARKAL
$/ton from Fann et al. (2012)
Notes: So we could stop here, or…

## Slide 6: Calculating Health Benefits
Health Benefits
Emissions Changes
Marginal Damages
Health Benefits
Concentration Changes
Health Impact Function
CMAQ
BenMAP
Damage Scaled
Modeled

## Slide 7: CMAQ simulation
CMAQ v5.2
Anthropogenic emissions: 2011 NEI v2
12 km resolution
Year-long simulation
2011 meteorology from WRF
Notes: For CMAS, it would be useful to provide some details on CMAQ simulation (e.g. version, resolution, base case, etc)

## Slide 8: Emissions Scaling
Projected emissions
Scaled separately for each of:
  4 Scenarios
  9 Geographic Regions (Census divisions)
  5 Pollutants: NOx, CO, SO2, VOC, PM2.5
Notes: Is all grow-in-place, scale categories: elc: coal, NG, other; TRN mode; indust

## Slide 9: PM2.5 concentrations (µg/m³) in 2045
No Fee
Combo - No Fee
GHG - No Fee
HIP - No Fee
2
0
-2
10
5
0
Notes: Ug/m3

## Slide 10: O3 concentrations (ppb) in 2045
70
35
0
4
0
-4
Combo - No Fee
GHG - No Fee
No Fee
HIP - No Fee
Season avg. MDA8 [ppb]
Notes: Season avg MDA8 ppb
Does increase in some cities

## Slide 11: Comparison of Health Benefits
Chart: Billion USD
| HIP | Combined | GHG | HIP (same pop.)
Damage Scaled | 134 | 138 | 56 | 134
Modeled | 151 | 152 | 62 | 89

## Slide 12: Differences in Benefit Calculations
Damage Scaled
Assumes marginal changes
Modeling
Captures changing population over time
Captures regional variation
Chart: Emissions
| No Fee | HIP | Combo | GHG | No Fee | HIP | Combo | GHG | NOx |  | SO2
Megatons | 4.9353 | 2.9916 | 2.9792 | 4.118 | 2.8978 | 0.69625 | 0.68806 | 1.6806
Chart: Modeled Benefit
| 2016 | 2040
modeled benefit | 89 | 151

## Slide 13: Cost Benefit Analysis
Chart: Billion USD (2018$)
| Energy System Cost Increase | Modeled Health Benefit | Climate Benefit | Net Benefit
HIP | -96 | 178 | 92 | 173
Combined | -115 | 177 | 128 | 189
GHG | -61 | 70 | 106 | 116
Notes: GHG damages are already projected to the future and don’t care about location

## Slide 14: Future needs
Better characterization of upstream emissions locations
Chart: Megatons
| No Fee | HIP | Combo | GHG | No Fee | HIP | Combo | GHG | No Fee | HIP | Combo | GHG | No Fee | HIP | Combo | GHG | NOx | . | PM10 | . | PM2.5 | . | SO2
Upstream | 0.81796 | 0.94522 | 0.87637 | 0.84492 | 0 | 2.7417 | 0.24714 | 0.23946 | 0.90408 | 0 | 0.95888 | 0.34447 | 0.34075 | 0.50466 | 0 | 0.22531 | 0.13579 | 0.14284 | 0.16574
Other | 5.3743 | 3.4284 | 3.4012 | 4.5477 | 0 | 1.0712 | 0.88268 | 0.87646 | 1.0892 | 0 | 0.67125 | 0.57001 | 0.563 | 0.68055 | 0 | 3.0777 | 0.87484 | 0.86125 | 1.8588
We can’t capture this
Notes: Similarly, locations of scaled emissions can be improved

## Slide 15: Conclusions
Models are useful tools for evaluating health impacts of large emission changes
Consider population changes when evaluating future health effects
Evaluating health impacts is improved with knowledge of the location of affected emissions
Disclaimer: The views expressed in this presentation are those of the author and do not necessarily reflect the views or policies of the U.S. Environmental Protection Agency.
Brown.Kristen@EPA.gov
Notes: These are strong statements. I suggest to soften the language, something like “Models are useful tools for evaluating health impacts of large emission changes”, or “Modeling is critical …”