## Slide 1: Impacts of a National Survey on the Development of the Residential Wood Combustion Component of the National Emissions Inventory
Rich Mason, U.S. Environmental Protection Agency
David Cooley, Abt Associates
18th Annual CMAS Conference
October 22, 2019

## Slide 2: Residential Wood Combustion in the NEI
Residential Wood Combustion (RWC) is a significant source of air pollution
  Approx. 6% of all primary particulate matter =< 2.5 microns in diameter (PM2.5) emissions in 2014
Emissions estimation method uses survey data to estimate:
  Fraction of homes in each county that use wood-burning appliances
  Average amount of wood burned in each appliance
2014 NEI used data from Energy Information Administration’s (EIA) Residential Energy Consumption Survey (RECS)

## Slide 3: NEI Nonpoint Development Process: New!
Previously composed of State/Local/Tribal (SLT) reporting agency data with EPA (default) data “gap-filling”
For the 2017 NEI, SLT reporting agencies may:
  Continue to submit emissions -takes precedence over any other estimates (6 States, 2 Locals, 6 Tribes)
  Accept/supplement with EPA default estimates
  Submit input activity data to refine EPA estimates (3 states)
New “Wagon Wheel” tool, Nonpoint Survey, and Input Template structure facilitates the new process

## Slide 4: The Residential Wood Combustion (RWC) Tool
Access Tool first released in December 2012 for the 2011 NEI
Latest version allows users to submit:
  County-level occupied homes, appliance fractions, burn rates, wood density factors, control factors
  County-level distribution of woodstoves to uncertified vs certified catalytic & non-catalytic devices –to override Census Region defaults
  County-level distribution of central heaters to 1 of 5 device types: indoor pellet boilers, indoor pellet furnaces, indoor cordwood boilers, indoor cordwood furnaces, outdoor cordwood boilers –to override national defaults
  Emission Factors by appliance type (SCC)

## Slide 5: New RWC Tool Features and Adjustments
Uses 2,984 survey responses to compute statistical regression approach for appliance fractions and burn rates based on the following predictor variables:
  Number of heating Degree days (HDD) in 2017 climate zone
  2017 population density from U.S. Census Bureau
  Urban/rural zip code from U.S. Census Bureau
  Percentage of county-level forest cover from Biogenic Emissions Land Database v4.1
  County-level fraction of homes that use natural gas as primary heat in 2017 from American Community Survey
  Type of home: single family detached or attached, multifamily, mobile home)
Normalized state consumption to EIA State Energy Data System (SEDS), applied to all RWC appliances
Sigmoid curve equation applied to central heaters and outdoor recreational equipment in dense urban areas –to zero where housing density approaches 1,000 homes/mi2

## Slide 6: 2017 National Survey: Background
2017 NEI will use data from a national survey supported by the Commission for Environmental Cooperation (CEC) and Northeast States for Coordinated Air Use Management (NESCAUM)
Surveyed 21 states throughout the U.S.
Mailed letters and follow-up post cards; survey conducted by web
Stratified: more surveys sent to areas likely to burn wood
State | # of Responses | # of Surveys Sent | Response Rate (%)
AR | 68 | 2,992 | 2.27
CO | 90 | 2,625 | 3.43
CT | 140 | 4,310 | 3.25
GA | 91 | 4,976 | 1.83
ID | 42 | 1,737 | 2.42
LA | 33 | 2,113 | 1.56
ME | 223 | 5,184 | 4.30
MA | 215 | 6,781 | 3.17
MI | 237 | 7,418 | 3.19
MO | 113 | 5,083 | 2.22
NH | 150 | 3,529 | 4.25
NJ | 46 | 2,216 | 2.08
NY | 240 | 7,738 | 3.10
NC | 183 | 7,011 | 2.61
OH | 170 | 7,117 | 2.39
PA | 301 | 8,640 | 3.48
RI | 34 | 1,118 | 3.04
UT | 37 | 1,007 | 3.67
VT | 126 | 2,538 | 4.96
WA | 181 | 5,006 | 3.62
WI | 264 | 5,363 | 4.92
TOTAL | 2,984 | 94,502 | 3.16

## Slide 7: 2017 National Survey
Survey asked:
  Whether respondent used a particular type of wood-burning appliance
  How much wood they burn (cordwood, pellets, or wax logs)
  When and how often they burn
  Appliance age, model #
  Demographic data
Appliances included:
Conventional Fireplaces
Fireplace inserts
Woodstoves
Wood-fired furnaces
Wood-fired boilers
Pellet stoves
Outdoor recreational equipment (e.g. fire pits)

## Slide 8: Survey (Weighted) Results - Summary
Chart: 
| Do not burn wood | Burn wood
 | 36023061.1937 | 15229856.8063
Chart: 
| Conventional Fireplace | Fireplace with Insert | Woodstove | Pellet stove | Wood-burning Furnace | Wood-burning boiler | Outdoor fire rings/ chimeneas/ fire pits
 | 0.38987 | 0.15603 | 0.2668 | 0.078527 | 0.021585 | 0.03163 | 0.40207
Percentage of households that burn wood
Percentage of wood-burning households that use each appliance

## Slide 9: Survey Results – Primary Use
Primary use of wood-burning appliances
Chart: 
| Conventional Fireplace | Fireplace with Insert | Woodstove | Pellet stove
Pleasure/aesthetics | 0.68514 | 0.34476 | 0.044359 | 0.058586
Supplemental heating | 0.2472 | 0.53404 | 0.67152 | 0.57762
Primary heating | 0.00712 | 0.084994 | 0.27175 | 0.35242

## Slide 10: Survey Results – Cords Burned
Chart: Cords
| Wood-burning furnace | Wood-burning boiler | Outdoor wood-burning fire pits, Chimeneas or fire rings
Weighted Average | 2.9045 | 5.3252 | 0.43513
Average Cords Burned Per Appliance
Chart: Cords
| Conventional Fireplaces | Woodstoves | Fireplace Inserts | Pellet stoves (tons)
Pleasure/ aesthetics | 0.29669 | 1.4543 | 0.60574 | 0.20175
Back-up, room heating or supplemental heating | 0.93244 | 1.5522 | 1.4925 | 1.913
Primary source of heat | 4.8318 | 3.6245 | 3.4318 | 3.4905
Weighted Average | 0.45621 | 2.0879 | 1.2488 | 1.7007

## Slide 11: Appliance Fractions & Burn rates by County Type
Chart: Households
| Conventional Fireplace | Fireplace with Insert | Woodstove | Pellet stove | Wood-burning Furnace | Wood-burning boiler | Outdoor fire rings/ chimeneas/ fire pits
Urban | 0.1301 | 0.044272 | 0.063619 | 0.024136 | 0.003036 | 0.0069339 | 0.11829
Suburban | 0.065261 | 0.040519 | 0.094597 | 0.014878 | 0.0075629 | 0.013424 | 0.10004
Rural | 0.083549 | 0.072957 | 0.18103 | 0.030751 | 0.030959 | 0.023708 | 0.16108
Chart: Cords/appliance
| Conventional Fireplace | Fireplace with Insert | Woodstove | Pellet stove | Wood-burning Furnace | Wood-burning boiler | Outdoor fire rings/ chimeneas/ fire pits
Urban | 0.42077 | 1.0561 | 1.7408 | 1.6463 | 3.221 | 3.7276 | 0.41196
Suburban | 0.47188 | 2.4073 | 2.2524 | 1.684 | 4.0613 | 6.2471 | 0.4648
Rural | 0.88356 | 1.1377 | 2.9353 | 2.0601 | 2.1878 | 7.1937 | 0.5428

## Slide 12: Survey Results – Natural Gas Access
Chart: Households
| Conventional Fireplace | Fireplace with Insert | Woodstove | Pellet stove | Wood-burning Furnace | Wood-burning boiler | Outdoor fire rings/ chimeneas/ fire pits
Natural Gas | 0.11845 | 0.043995 | 0.075669 | 0.023141 | 0.0061324 | 0.0089449 | 0.11999
No Natural Gas | 0.07671 | 0.082012 | 0.13356 | 0.026247 | 0.009233 | 0.017642 | 0.11165
Chart: Cords/appliance
| Conventional Fireplace | Fireplace with Insert | Woodstove | Pellet stove | Wood-burning Furnace | Wood-burning boiler | Outdoor fire rings/ chimeneas/ fire pits
Natural Gas | 0.45485 | 1.2718 | 2.0761 | 1.6741 | 2.8192 | 4.9561 | 0.44527
No Natural Gas | 0.48781 | 1.0629 | 2.1879 | 2.0535 | 3.7558 | 6.0135 | 0.27127

## Slide 13: Survey Results – Type of Dwelling
Chart: Households
| Conventional Fireplace | Fireplace with Insert | Woodstove | Pellet stove | Wood-burning Furnace | Wood-burning boiler | Outdoor fire rings/ chimeneas/ fire pits
Detached single family home | 0.16143 | 0.070437 | 0.11604 | 0.036739 | 0.0092494 | 0.013834 | 0.17773
Attached single family home (e.g. townhome) | 0.083985 | 0.0016479 | 0.036524 | 0.0019118 | 0.0035058 | 0.0045255 | 0.069197
Duplex (two units) | 0.020753 | 0.00051476 | 0.019532 | 0.0049438 | 0.0011901 | 0.0091034 | 0.057706
Multi-resident building (3-5 units) | 0.040684 | 0 | 0 | 0 | 0 | 0 | 0
Apartment (more than 5 units) | 0.038984 | 0 | 0.0041411 | 0 | 0 | 0 | 0
Mobile home | 0.02627 | 0.056904 | 0.078288 | 0.0063193 | 0.006995 | 0.0023556 | 0.054153
Percent of Households Using Each Appliance by Type of Dwelling

## Slide 14: Survey Results – Heating Degree Days
Chart: Cords/appliance
| Conventional Fireplace | Fireplace with Insert | Woodstove | Pellet stove | Wood-burning Furnace | Wood-burning boiler | Outdoor fire rings/ chimeneas/ fire pits
0-10% | 0.3879 | 1.3758 | 2.1559 | 0.81315 | 5.3333 | 6.1748 | 0.17805
10-20% | 0.60158 | 0.82489 | 1.5668 | 0.3013 | 3.8039 | 6.135 | 0.27108
20-30% | 0.42933 | 1.2684 | 1.9123 | 1.4391 | 2.0085 | 1.066 | 0.21073
30-40% | 0.47957 | 1.8955 | 1.5285 | 1.9359 | 0.93843 | 5.7862 | 0.44468
40-50% | 0.28071 | 1.1298 | 2.2294 | 3.9968 | 3.4136 | 3.1149 | 0.16746
50-60% | 0.44431 | 1.5639 | 1.87 | 2.3202 | 1.6817 | 8.0752 | 0.59026
60-70% | 0.42246 | 1.0993 | 2.2185 | 1.7223 | 3.6197 | 4.8442 | 1.7769
70-80% | 0.65778 | 1.3465 | 2.1796 | 2.2065 | 4.2819 | 5.0235 | 0.71556
80-90% | 0.69198 | 0.84888 | 2.9692 | 1.5531 | 2.5543 | 9.7831 | 0.46944
90-100% | 0.74491 | 0.65302 | 3.6241 | 1.582 | 3.2334 | 6.5195 | 0.37942
Average Cords Burned Per Year by Heating Degree Day Bins
Warmest
Coldest

## Slide 15: EPA Default Comparisons: Draft Results New (2017) vs Existing (2014) RWC Tool Estimates
For this analysis, defined counties as Urban, Suburban and Rural based on # of occupied housing units / square mile:
  Urban: > 1,000
  Suburban: 500 – 1,000
  Rural: < 500
Caveat: Does not reflect (3) SLT-submitted inputs

## Slide 16: PM2.5 Total RWC Emissions by Census Region
Notes: 2017 default is ~275K vs 265K for 2014 tool (not NEI2014=315K)

## Slide 17: PM2.5 Estimates by Appliance Type: New vs Old Tool

## Slide 18: National RWC PM2.5 Emissions for Non-rural Counties

## Slide 19: South Region: More Outdoor Recreational Burning & Central Heating

## Slide 20: Northeast Region: More Rec-burning & fireplaces, less woodstoves

## Slide 21: Midwest Region: Large Reductions Woodstoves & Central Heating

## Slide 22: West Region: Fewer Woodstoves, more Central Heating, Fireplaces & Rec-burning

## Slide 23: 2017 (left) & 2014 (right) EPA Tool Total RWC PM2.5 (tons/sq. mile)

## Slide 24: 2017 – 2014 EPA Tool, Total RWC PM2.5 (tons/sq. mile)

## Slide 25: % Homes w/ Natural Gas Access (left), Occupied Housing density (right)

## Slide 26: 2017 (left) & 2014 (right) EPA Tool RWC Outdoor Recreational Burning PM2.5 (tons/sq. mile)

## Slide 27: 2017 – 2014 EPA Tool, RWC Outdoor Recreational Burning PM2.5 (tons/sq. mile)

## Slide 28: 2017 (left) & 2014 (right) EPA Tool RWC Central Heating PM2.5 (tons/sq. mile)

## Slide 29: 2017 – 2014 EPA Tool, RWC Central Heating PM2.5 (tons/sq. mile)

## Slide 30: 2017 (left) & 2014 (right) EPA Tool RWC Noncertified Woodstoves PM2.5 (tons/sq. mile)

## Slide 31: 2017 – 2014 EPA Tool, RWC Noncertified Woodstoves PM2.5 (tons/sq. mile)

## Slide 32: Summary
The survey represents the most comprehensive national assessment of wood-burning activity in the United States to date
The most common wood-burning appliances—fireplaces and outdoor recreational equipment—have the lowest burn rates
There are notable differences in urban, suburban, and rural burning, with wood-burning activity generally being more common in rural areas and areas with little natural gas access
Results compared reasonably well to other state and local surveys
While DEFAULT overall national RWC totals are similar, spatial distribution and appliance allocations changed considerably
  Final RWC NEI estimates, with SLT inputs and emissions will differ –release date 4/30/2020

## Slide 33: Questions?
Appendix slides follow

## Slide 34: Survey Results – Comparison to Other Surveys
Chart: Households
| Conventional Fireplace | Fireplace with Insert | Woodstove | Pellet stove | Wood-burning Furnace | Wood-burning boiler
Current Survey | 0.11585 | 0.046366 | 0.079279 | 0.023334 | 0.0063257 | 0.0094871
NEI 2014 | 0.06004 | 0.054931 | 0.036549 | 0.0050561 | 0.0011837 | 0.0016879
Minnesota 2018 | 0.13738 | 0.017944 | 0.094878 | 0.0037736 | 0.0083266 | 0.016266
Portland 2014 | 0.086711 | 0.06032 | 0.066918 | 0.0075401
Vermont 2014-2015 | 0.0375 | 0.0434 | 0.3033 | 0.0192 | 0.032 | 0.032
Percentage of Households Using Each Appliance Type:
Comparison of Multiple Survey Results

## Slide 35: Survey Results – Comparison to Other Surveys
Average Cords Burned per Appliance Type: Comparison of Multiple Survey Results
Chart: Cords
| Conventional fireplace | Wood stoves | Fireplace inserts | Wood burning forced-air furnaces | Wood boilers | Outdoor recreational equipment
Current Survey | 0.45621 | 2.0879 | 1.2488 | 2.9045 | 5.3252 | 0.43513
National Emissions Inventory 2014 | 0.22518 | 3.0638 | 0.23773 | 6.0952 | 8.6161 | 0.57081
Minnesota, 2014-2015 | 0.28571 | 1.6452 | 0.92308 | 4.5833 | 10 | 0.38854