## Slide 1
marina.astitha@uconn.edu
airmg.uconn.edu
Evaluating Seasonality and Trends in Modeled PM2.5 Concentrations Using Empirical Mode Decomposition
Huiying Luo1, Marina Astitha1, Christian Hogrefe2,
Rohit Mathur2, and S. Trivikrama Rao1,3
1University of Connecticut
2US Environmental Protection Agency
3North Carolina State University

## Slide 2
Scope and Objectives
Analyze and interpret features embedded in PM2.5 observations and model outputs
Assess the model’s ability to reproduce changes/trends in observed PM2.5 concentrations
Propose a new method for model evaluation of PM2.5 and its components without any preselection of temporal scales and assumptions of data linearity and stationarity
How well can we capture changes in PM2.5 and its speciated components induced by variations in meteorology and/or emissions over a decade?

## Slide 3
Data
Model simulations
Coupled 2000-2010 WRF-CMAQ (vers. 5.0.1) with 36-km grid cells over the USA (Gan et al. 2015; Xing et al. 2013)
Observations:
  SO4, NO3, NH4, OC, EC, Cl, and total PM2.5 are retrieved from Chemical Speciation Network (CSN), the Interagency Monitoring of Protected Visual Environments (IMPROVE) and SEARCH networks.
  3 sites are used to demonstrate the proposed method of evaluation.

## Slide 4
Decomposition of total PM2.5 with EMD
Multiple improvements to address mode mixing as well as other problems are included in the most recent version of Improved Complete Ensemble Empirical Mode Decomposition with Adaptive Noise (Improved CEEMDAN) (Wu and Huang, 2009; Yeh et al., 2010; Torres et al., 2011; Colominas et al., 2014).
An IMF must satisfy:
the number of extrema (maxima and minima) and zero-crossings must be equal or differ at most by one;
the local mean, defined as the mean of the upper and lower envelopes, must be zero.
Signal is decomposed to multiple Intrinsic Mode Functions (IMFs) and a residual trend through sifting processes (Huang et al., 1998):
Empirical Mode Decomposition (EMD)
Methodology
A unique technique that enables model evaluation at multiple time scales that is intrinsic to the PM time series.

## Slide 5: (RURAL, IMPROVE)
OBS CMAQ
Mean cycle (days)
Peak cycle (days)
Total PM2.5 - Quabbin Summit, MA

## Slide 6
Very clear annual cycles of PM2.5 exist in both obs and CMAQ, but they are out of phase by up to six months.
Mean cycle (days)
The residual (trend) indicates overestimation of the magnitude of the trend component by CMAQ; decreasing trend by CMAQ while obs show slight decline
Total PM2.5 - Quabbin Summit, MA
OBS CMAQ
ANNUAL
RESIDUAL

## Slide 7
Overestimated amplitude of NO3 (4.3 x obs)
Almost semi-annual shifted OC (-147 days); OC, EC and Cl contribute to the PM2.5 shift
OC directly drives the negative correlations
EC follows the feature of OC in the first four years
PM2.5 components - Quabbin Summit, MA
Decomposed annual cycles (IMF6) from observed and simulated concentrations
Time-dependent correlations
OBS CMAQ
Top of pyramid: correlation of the entire time series (6-yrs)
Point in pyramid: correlation of the time series centered around a specific day

## Slide 8
Mean cycle (days)
Total PM2.5 - Reno, NV and ATL, GA
OBS CMAQ
Reno, NV (urban - AQS, CSN)
ATL, GA (urban - SEARCH)

## Slide 9
PM2.5 components - Reno, NV
OBS CMAQ
Site is situated in a wildfire-prone area
Annual variations for total and speciated PM2.5 are largely underestimated
The modeled phase of SO4, NO3, NH4 and OC agrees with that of observations with few exceptions
EC mimics the Time-Dependent Intrinsic Correlation (TDIC) pyramid of total PM2.5, implying the existence of errors in modeled EC that affected the model performance for total PM2.5 (potential impact of wildfires)

## Slide 10
PM2.5 components - ATL, GA
OBS CMAQ
Simulated total PM2.5 shows a shift of several months (132 days)
Overestimation of NO3; underestimation of NH4 and phase shift of EC (54 days)
Anti-correlated total PM2.5 annual cycles cannot be attributed to the available species
The remaining species clearly played a role in driving the above discrepancies
Anti-correlation likely due to inaccurate representation of the seasonal variation of the non-C portion of OM in the model version analyzed here that has been updated in more recent releases of CMAQ

## Slide 11
Summary
The EMD method enables direct comparison of the relative strengths of the various forcings, operating on different time scales, that are embedded in non-linear and non-stationary time series of observed and modeled concentrations
Coordinated decomposition and evaluation of total and speciated PM2.5 provides a unique opportunity for modelers to assess influences of each PM2.5 species to total PM2.5 concentration in terms of time shifts for various temporal cycles and the magnitude of each component including the trend
At these three sites:
The model generally is more capable of simulating the change in the trend than the absolute magnitude of the long-term trend component
The magnitude of SO4 trend components is well represented across all sites
The model reproduced the amplitude of the annual cycle for total PM2.5, SO4 and OC
The phase difference in the annual cycles for total PM2.5, OC and EC reveal a shift of up to half-year
More recent versions of CMAQ incorporate many updates to the treatment of organic aerosols that are expected to improve the representation of the seasonal cycle
New long-term simulations with CMAQv5.3 are planned for the near future which can be used to confirm this expected improvement

## Slide 12
Acknowledgements
The views expressed in this presentation are those of the authors and do not necessarily represent the views or policies of the U.S. Environmental Protection Agency.
Two of the authors (MA and HL) gratefully acknowledge the support of this work by the Electric Power Research Institute (EPRI) Contract #00-10005071, 2015–2017.