## Slide 1: Ramboll Shair: Integrating realtime sensor measurements and regional/local-scale models in Richmond, California
Justin Bandoro, Julia Luongo, Mike Dvorak, Drew Hill, Tasko Olevski, Kurt Richman, Chris Emery, Greg Yarwood, Shari Libicki
18th CMAS Conference
October 22nd, 2019

## Slide 2: Outline
Background
  AB617 overview
  Air Rangers Community Air Protection
Ramboll Shair Model
  Emission estimates with near-realtime traffic emissions
  CAMx regional and Shairstreet roadway models
  Sensor integration
Feedback and Next Steps
  Communicating results to the Richmond community
Source: Wikipedia (Audiohifi)

## Slide 3: Background
AB617
California Assembly bill
Funds community level air measurement, education, and emissions reductions
Targets disadvantaged communities
AB617 Funded Project in Richmond, CA (“Air Rangers”)
Fill PM and NO2 monitoring gaps
Attribute hotspots to sources
Communicate actionable data to the public in near-realtime
Facilitate healthy outdoor recreation
Local work force development for disadvantaged youth
SB 535 Disadvantaged Communities

## Slide 4: Air Rangers Community Air Protection Grant
Action Plan
Converge strategic partners
Site 50 PM & NO2 sensors; take 70 toxic metals samples
Communicate hyper-local air quality to the public, hourly
Hourly hotspot identification and source attribution

## Slide 5: Sensor network in Richmond
Network of 50 low-cost Clarity sensors
Pollutants: PM2.5, PM10, and NO2
Sited in greenways, parks, and near high traffic roadways, and industrial centers
Groundwork Richmond Air Rangers

## Slide 6
Ramboll Shair

## Slide 7
Ramboll Shair Nowcast Data Timing

## Slide 8
Meteorology
  WRF NAM forecast refreshed every 6 hours
  Nested grids: 9km, 3km, and 1km resolution
CAMx Grids
  1km and 200m resolution
  Captures region’s most influential sources
Chemistry and Deposition
  Fast chemical scheme for O3-NO-NO2
  Wet and dry deposition with ZHANG03 model
Source Attribution
  Tag emissions by source category for source apportionment
Modeled every hour
  Latest emissions combined with previous hour dispersion results
Source: Wikipedia (Audiohifi)
CAMx Modeling

## Slide 9: Realtime Traffic Emissions
Mobile emission inventories (EMFAC, MOVES, COPERT)
Open Street Map data
Realtime speed data from an API
Travel demand model
Retrieve all streets in an area
Calculate real-time traffic flow
Merge data
Traffic emissions
358,269 Modeled Road Links in the Bay Area

## Slide 10: Realtime Traffic Emissions
Total on-road mobile emissions over modeled Richmond domain.
PM2.5

## Slide 11: Additional Source Emissions
Total emissions over modeled Richmond domain.
2016 BAAQMD 1km emissions inventory used for non-mobile sources.
PM2.5

## Slide 12: Shairstreet Modeling
1. Street canyon model
  Calculates additional recirculation contribution for road links that have street canyon-like geometry, using wind speed and direction at top of the canyons. Takes into account vehicle generated mechanical turbulence.
Source: Berkowicz 1997.
Modeled buildings in Richmond
(view from Chanslor Ave and 9th St)
Fine scale resolution of road emissions

## Slide 13: Shairstreet Modeling
Fine scale resolution of road emissions
NO + O3 NO2 + O2 ()
NO2 NO + O3 ()
  Reaction and photolysis rates, and taken from CAMx 200m grid along with background NOx and O3
1. Street canyon model
  Calculates additional recirculation contribution for road links that have street canyon-like geometry, using wind speed and direction at top of the canyons. Takes into account vehicle generated mechanical turbulence.
2. Line source dispersion model
  Road links are modeled as line sources based on Venkatram and Horst 2006 approximate Gaussian dispersion solution at 10x10m resolution.
3. NOx chemistry model
  Simplified NO-NO2-O3 model based on During et al. 2011, with parameterized mixing times based on street-canyon geometry.

## Slide 14: Sensor Integration
Latest Clarity sensor and BAAQMD monitor data pulled
Measurement data undergoes internal quality control checks and adjustment
Objective analysis via Barnes interpolation is used to assimilate sensor measurements
,
Raw model + sensors
Interpolated model error
October 12th 2019, 7:00pm PDT

## Slide 15: Sensor Integration
Latest Clarity sensor and BAAQMD monitor data pulled
Measurement data undergoes internal quality control checks and adjustment
Error between model and observations are calculated
Objective analysis via Barnes interpolation is used to assimilate sensor measurements
,
Assimilated map
October 12th 2019, 7:00pm PDT

## Slide 16
Communicating Results
Web/phone app for Richmond is being developed

## Slide 17
Next Steps
In the coming months, Shair output will be put to use by stakeholders
Groundwork Richmond
  Targeted tree planting as an air pollution intervention
City of Richmond
  Integrate hourly Shair output into the City’s web data dashboard
  Investigate air quality data-driven land use planning activities
  Communicate information to the public
Richmond citizens
  Engage with their environment
  Plan healthier outdoor activities
  Take precautionary actions during localized pollution events
Richmond-San Pablo Community Air Monitoring Steering Committee
  Identify major emissions sources
  Inform their official Community Emissions Reduction Plan (December 2020)

## Slide 18
We’re excited to partner with Ramboll Shair to better understand air quality on a community scale. We need more information to better direct our resources and achieve our climate action goals.
- Adam Lenz, Environmental Services Manager, City of Richmond

## Slide 19: Thank you
Justin Bandoro
jbandoro@ramboll.com
Get a copy of our whitepaper:
https://ramboll-shair.com