## Slide 1: Fire Emissions Inventory Comparison and Processor Development
Jeremiah Johnson1, Pradeepa Vennam1, Xiao Yu2, Cara Scalpone2
1Ramboll
2Texas Commission on Environmental Quality

## Slide 2: Motivation
Fires are large emission sources and Fire Emission Inventories (FEIs) are uncertain
Accurate FEIs needed for Exceptional Event (EE) analyses and State Implementation Plan (SIP) modeling for ozone/PM2.5/regional haze
Processing tools can limit choice of FEI and different processing methods can introduce uncertainties
Source: ABC News, October 3, 2020

## Slide 3: Available Fire Inventories
Area burned
LC-specific biomass loading and EFs
Burned areas
FINN, GFED, BlueSky
Fire Radiative Power
GFAS, QFED, FEER, FLAMBE, GBBEPx, IS4FIRES
Source: https://wildfire.geog.kcl.ac.uk/products-and-data/
Thermal anomalies
LC-specific dry matter
combustion rates and EFs
Source: NASA Disasters Mapping Portal

## Slide 4: Ramboll’s FEI Processor
A Python-based tool that:
  Re-grids emissions to target modeling domain projection/extent
  Speciates using CB6 or CB7 mechanisms
  Temporally and vertically allocates emissions
Implemented for FINN1.0/2.5, GFAS1.2 and QFED2.5 (FEER1.0-G1.2 coming in 2023)
Other global FEIs can be added in the future
Output formatted as netCDF-4 w/ compression to use space efficiently
By U.S. Department of Defense Current Photos - 110426-F-RM405-451,
Public Domain, https://commons.wikimedia.org/w/index.php?curid=51091038

## Slide 5: FEI Processing Diagram

## Slide 6: Temporal Allocation
Diurnal behavior specific to fire type and environment
Gridded FEIs do not discern fire type
Chose a smoothly varying profile to apply to all fires
More improved profiles are needed and are easily implemented
Notes: Higher injection height will typically reduce near‐field downwind concentrations
Reference: Lareau, N.P. and Clements, C.B., 2017. The mean and turbulent properties of a wildfire convective plume. Journal of Applied Meteorology and Climatology, 56(8), pp.2289-2299.

## Slide 7: Vertical Allocation
Smoke injection height and vertical allocation play a vital role in downwind pollutant dispersion
Wilkins et al. (2022) found PBL+500m injection height comparable to Sofiev for 2013 Rim Fire in CA and 2017 Rx burns in KS
PBL500 and Sofiev prescribe injection height only
FEI tool applies PBL500 with SMOKE/Briggs-like vertical allocation
Notes: Wilkins, J. L., Pouliot, G., Pierce, T., Soja, A., Choi, H., Gargulinski, E., Gilliam, R., Vukovich, J., Landis, M. S. 2022. An evaluation of empirical and statistically based smoke plume injection height parametrisations used within air quality models. International Journal of Wildland Fire 31, 193-211. https://doi.org/10.1071/WF20140

## Slide 8: Case Study: April 9, 2019
NOAA HMS Smoke and Fire
GOES-16 Aerosol Optical Depth

## Slide 9: PM2.5 Emissions Comparison
Substantial variation in fire detects and range of PM2.5 emissions
2,098 tpd
2,354 tpd
6,756 tpd

## Slide 10: Case Study: October 8, 2020
NOAA HMS Smoke and Fire
MODIS visible with fire detects
Fire detects

## Slide 11: PM2.5 Emissions Comparison
Considerably more disagreement between FEIs on this day
4,578 tpd
319 tpd
6,603 tpd

## Slide 12: FEI Comparison – 2019 Ozone Season
Chart: PM2.5 Emissions - 2019 Apr-Sep
| California | Texas
FINN2.5 | 55106 | 33311
GFAS1.2 | 40724 | 14820
QFED2.5 | 180636 | 95027
Chart: NOx Emissions - 2019 Apr-Sep
| California | Texas
FINN2.5 | 14406 | 11487
GFAS1.2 | 10106 | 3559
QFED2.5 | 23871 | 18040
QFED PM2.5 ~3x higher than FINN
QFED NOx ~60% higher than FINN

## Slide 13: FEI Comparison – 2019 Ozone Season
FINN VOC ~6-7x higher than QFED
Better agreement for CO
Chart: VOC Emissions - 2019 Apr-Sep
| California | Texas
FINN2.5 | 221797 | 148615
GFAS1.2 | 45544 | 11386
QFED2.5 | 33999 | 21390
Chart: CO Emissions - 2019 Apr-Sep
| California | Texas
FINN2.5 | 411136 | 282219
GFAS1.2 | 424232 | 170429
QFED2.5 | 495357 | 328035

## Slide 14
Next Steps
Implement alternative temporal allocation and Sofiev plume injection height
Use modeling to evaluate ozone and PM2.5 model performance of different FEIs
Add NASA’s FEER1.0-G1.2 product

## Slide 15: Questions?
Contacts:
Jeremiah Johnson JJohnson@ramboll.com
Cara Scalpone Cara.Scalpone@tceq.texas.gov
Notes: Photo by Malachi Brooks on Unsplash