## Slide 1: The Burden of Lightning NOx Emissions over the Contiguous United States and the Northern Hemisphere Derived Using Observational and Climatological Approaches
Office of Research and Development
Center for Environmental Measurement & Modeling
21st Annual CMAS Conference, Chapel Hill, North Carolina
October 17-19, 2022
Daiwen Kang, J. Mike Madden, Christian Hogrefe, Golam Sarwar, Rohit Mathur, and Barron H. Henderson

## Slide 2: Outline
Brief description of ground-based lightning detection networks
Comparison of detected lightning flashes from different networks
Scaling of lightning data from network with low lightning detection efficiency
Spatial and temporal lightning NOx (LNOx) emissions over the Contiguous United States (CONUS) and the relative burden to total NOx emissions
Hemispheric distributions of LNOx emissions

## Slide 3: Overview of Lightning Detection Networks
The National Lightning Detection Network (NLDN):
Started in the early 1980s, it focused on the Contiguous United States (later joined by Canadian lightning network), is the most accurate lightning detection network. and often is considered as the “ground truth” for lightning observations.
  Wideband sensors that operate from approximately 400 Hz–400 kHz radio wave detection
  Detection Efficiency (DE): >95% (over CONUS US)
  Location Accuracy (LA): 50 m (over CONUS US)
Cloud to Ground Flashes

## Slide 4: Overview of Lightning Detection Networks
The World Wide Lightning Location Network (WWLLN):
  Ground-based global lightning detection network was started in the early 2000s and has ~70 sensors.
  Very Low Frequency (VLF, 3-30kHz) radio wave detection (VLF waves propagate through the ionosphere with relatively low attenuation, enabling the detection of these radio atmospherics at great distances between 6000 to 12000 km from the lightning discharge).
  DE: 60-80% for CGs (> 40 kAmp), 10-11% for all strokes. The spatially uniform relative DE is achieved in most regions with deMap correction derived using the average stroke energy distribution (doi:10.1029/2012RS005049).
  LA: 4-5 km

## Slide 5
NAM: North America, CAM: Central America, RUS: Russia, EAS: East Asia, SAS: South Asia, EUR: Europe, NAF: North Africa, MDE: Middle East, and OTH: The rest of the geographic domain.
NE: Northeast, SE: Southeast, OVC: Ohio Valley Central, UM: Upper Midwest, WNC: West North Central, SW: Southwest, NW: Northwest, and the other geographic regions: South and West.
Emission Cases:
NLDN, WWLLN, WWLLNs (scaled WWLLN dataset, to be introduced later), and GEIA (Global Emissions InitiAtive) climatological dataset that provides the same daily LNOx emissions (hourly varying) for each month.
MDE
NAF
EUR
SAS
EAS
RUS
CAM
NAM
OTH
Analysis Regions in the CONUS and Hemispheric Modeling Domain
Notes: u

## Slide 6
50
46
42
38
34
30
26
50
46
42
38
34
30
26
Lightning Flash Rate (flashes/km2·hr x 10-3)
3.6
3.2
2.8
2.4
2.0
1.6
1.2
0.8
0.4
-115 -105 -95 -85 -75
-115 -105 -95 -85 -75
-115 -105 -95 -85 -75
-115 -105 -95 -85 -75
July
September
NLDN
WWLLN
Lightning Flash Density over CONUS: NLDN vs WWLLN in 2016

## Slide 7
2016
2017
2018
Month of the Year
Lightning Flashes (x1000)
10,000
8,000
6,000
4,000
2,000
0
2 4 6 8 10 12
2 4 6 8 10 12
2 4 6 8 10 12
Chart: Mean Ratio (NLDN/WWLLN)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Ocean | 0.37189 | 0.35461 | 0.51733 | 0.51518 | 0.7492 | 0.82041 | 0.95869 | 0.85946 | 0.72697 | 0.54357 | 0.35143 | 0.28538
Land | 0.76457 | 0.70355 | 0.84812 | 1.0432 | 1.5709 | 2.206 | 2.9897 | 2.6433 | 1.9158 | 1.1592 | 0.86841 | 0.50045
3.5
2.5
2.0
1.0
1.5
0.5
0
3.0
3.0
3.5
2.5
2.0
1.0
1.5
0.5
0
Mean Ratio (NLDN/WWLLN)
Jan Feb Mar Apr May Jun Jul Aug Sep Oct Nov Dec
Lightning Flashes over CONUS: NLDN vs WWLLN
Ratio of NLDN/WWLLN monthly means considering data for 2016 – 2018. Ratios are shown for each region as well as aggregated for land vs. ocean cells in the domain
Total lightning flashes by month over CONUS

## Slide 8
Month | Land | Ocean
January | 0.76 | 0.37
February | 0.70 | 0.35
March | 0.85 | 0.52
April | 1.04 | 0.52
May | 1.57 | 0.75
June | 2.21 | 0.82
July | 2.99 | 0.96
August | 2.64 | 0.86
September | 1.92 | 0.73
October | 1.16 | 0.54
November | 0.86 | 0.35
December | 0.50 | 0.29
Monthly NLDN/WWLLN Lightning Flash Ratio over Land & Ocean
1.0
These monthly-varying land ratios are applied uniformly across all CONUS/hemispheric land cells
The ocean ratios < 1 are caused by lower NLDN detection efficiency when lightning strikes are away from the monitors over land, and therefore WWLLNs and WWLLN are identical over ocean cells

## Slide 9: Lightning Flash Density over CONUS: NLDN vs WWLLN
Courtesy of Kaplan and Lau (2021), https://doi.org/10.5194/essd-13-3219-2021
Peak summertime lightning density in WGLC (WWLLN Global Lightning Climatology) is about 40 % of the amount reported by NLDN

## Slide 10
WWLLNs
flashes/km2hr
WWLLN
NLDN
More lightning flashes were observed by NLDN than by WWLLN over land, but the differences were quite small over ocean.
The scaled WWLLN (WWLLNs) flashes are comparable with NLDN flashes both in magnitude and spatial distribution.
Spatial Distribution of Lightning Flash Rate in July 2016

## Slide 11
Monthly Total LNOx Emissions over CONUS in 2016
Domain-wide total annual LNOx emissions are in the range of 0.45 to 0.70 Tg N (compare to the global estimate of 2 – 8 Tg N in literature)
Collectively over the domain, the NLDN, WWLLNs, and GEIA emissions are comparable to each other during warm months. The unscaled WWLLN emissions are lower than all the other cases by more than 25%.
The LNOx production rate for NLDN and WWLLNs: 350 moles/flash
(0.47)
(0.28)
(0.48)
(0.34)
The values after the legend symbols are the annual total LNOx (Tg N) over the domain and the values in the parentheses are the corresponding annual total LNOx over the CONUS land grid cells.

## Slide 12
WWLLNs
GEIA
6.3
5.6
4.9
4.2
3.5
2.8
2.1
1.4
0.7
18
16
14
12
10
8
6
4
2
LNOx Emissions (Tons N)
NLDN
WWLLN
Spring (MAM)
Summer (JJA)
Spatial Distribution of Seasonal Total LNOx Emissions in 2016

## Slide 13
WWLLNs
GEIA
6.3
5.6
4.9
4.2
3.5
2.8
2.1
1.4
0.7
1.8
1.6
1.4
1.2
1.0
0.8
0.6
0.4
0.2
LNOx Emissions (Tons N)
NLDN
WWLLN
Autumn (SON)
Winter (DJF)
Spatial Distribution of Seasonal Total LNOx Emissions in 2016

## Slide 14
Spring (MAM)
Summer (JJA)
Autumn (SON)
Winter (JFD)
Seasonal LNOx to Total NOx Ratios in the U.S. Climate Regions in 2016
0
LNOx to TNOx Ratio (%)
60
50
40
30
20
10
0
LNOx to TNOx Ratio (%)
60
50
40
30
20
10
LNOx to TNOx Ratio (%)
60
50
40
30
20
10
0
LNOx to TNOx Ratio (%)
60
50
40
30
20
10
0
The LNOx to total NOx (TNOx: total anthropogenic NOx + LNOx) ratio displays significant seasonal and geographic variations.
The ratio’s seasonal variation is common to all the LNOx emissions cases.
R_N2A: Ratio of NLDN LNOx to ANOx, R_Ws2A: Ratio of WWLLNs LNOx to ANOx, R_G2A: Ratio of GEIA LNOx to ANOx

## Slide 15
NLDN
GEIA
Spatial Distribution of Seasonal LNOx to Total NOx Ratio in 2016
WWLLNs
Autumn
Winter
Spring
Summer
90
80
70
60
50
40
30
20
10
LNOx to TNOx (%)

## Slide 16
The Trend of Annual ANOx and the LNOx/ANOx Ratio over the CONUS from 2010-2018
The annual total anthropogenic NOx (ANOx) emissions from 2010 to 2018 (extracted from the EQUATES* project) decreased by ~ 5%/year.
The ratio of LNOx/ANOx increased from 11 to 19% from 2010 to 2018 based on the 2016 LNOx level (NLDN) over the CONUS.
*EPA’s Air QUAlity TimE Series Project (https://www.epa.gov/cmaq/equates)

## Slide 17
The Trend of Summer-month (JJA) ANOx and the LNOx/ANOx Ratio over the CONUS from 2010-2018
The total anthropogenic NOx (ANOx) emissions during summer months from 2010 to 2018 (extracted from the EQUATES* project) decreased by ~ 5%/year.
The ratio of LNOx/ANOx during summer increased from 27 to 45% from 2010 to 2018 based on the 2016 LNOx level (NLDN) over the CONUS.
*EPA’s Air QUAlity TimE Series Project (https://www.epa.gov/cmaq/equates)
Notes: Over 60% of the annual lightning NOx emissions over the CONUS is from the summer months (JJA).

## Slide 18
Monthly Total LNOx Emissions in Hemispheric Regions in 2016
The total LNOx emissions from WWLLNs are comparable (within 50%) to the climatological LNOx emissions from GEIA in North America, Central America, West Europe, and Russia.
Similar seasonal variation trends are displayed by all the emissions cases.
Central America
North America
West Europe
Russia

## Slide 19
Monthly Total LNOx Emissions in Hemispheric Regions in 2016
For annual total LNOx emissions, GEIA’s estimates are 3 to 10 times larger than those from WWLLNs in East and South Asia, Middle East, and North Africa.
The seasonal variation trend from GEIA is different from WWLLN and WWLLNs.

## Slide 20
Summary
The lightning flash data from WWLLN, a network with low lightning detection efficiency, is scaled using lightning flash data from NLDN in time and space for lightning NOx production
There are clear differences in the magnitude and distribution of LNOx emissions across CONUS and the Northern Hemisphere with different emission configurations.
WWLLNs generally produces similar LNOx emissions to NLDN in time and space over the CONUS.
LNOx composes an increasingly significant fraction of total NOx emissions over the years; for some regions, it dominates the total NOx emissions budget during summer months.
Compared to WWLLNs, the monthly climatological GEIA LNOx emissions are unrealistically large for parts of Asia and Central Africa but are more comparable (within 50% for total annual values) in other regions such as North and Central America, West Europe, and Russia.

## Slide 21: Disclaimer
References
  Kang, D.; Hogrefe, C.; Sarwar, G.; East, J.D.; Madden, J.M.; Mathur, R.; Henderson, B.H.: Assessing the Impact of Lightning NOx Emissions in CMAQ Using Lightning Flash Data from WWLLN over the Contiguous United States. Atmosphere 2022, 13, 1248. https://doi.org/10.3390/atmos13081248.
  Kang, D., Heath, N., Gilliam, R., Spero, T., and Pleim, J.: Lightning Assimilation in the Weather Research and Forecasting (WRF) Model Version 4.1.1: Technique Updates and Assessment of the Applications from Regional to Hemispheric Scales, EGUsphere [preprint], https://doi.org/10.5194/egusphere-2022-348, 2022.
  Kaplan, J.O.; Lau, K.H.-K. The WGLC global gridded lightning climatology and time series. Earth Syst. Sci. Data 2021, 13, 3219–3237, https://essd.copernicus.org/articles/13/3219/2021.
The views expressed in this presentation are those of the authors and do not necessarily reflect the views or policies of the U.S. EPA