## Slide 1: Applying satellite data assimilation to infer lightning-NOx emissions in CMAQ
James D. East1,2, Barron H. Henderson3, Sergey Napelenok4, Shannon Koplitz3, J. Mike Madden1, Daiwen Kang4, Fernando Garcia Menendez2
1. ORISE Research Fellow at US EPA
2. North Carolina State University, Department of Civil, Construction, and Environmental Engineering
3. US EPA Office of Air Quality Planning and Standards
4. US EPA Atmospheric & Environmental Systems Modeling Division
Office of Research and Development
AESMD
CMAS 2022

## Slide 2
Secondary products of NOx emitted elsewhere can impact US air quality
  Accurate global emissions inventories are critical but are challenging to develop and update
  Satellites, providing data in real time, offer an opportunity to bridge this data gap
Short lifetime of NO2 along with rich dataset of NO2 observed from space provides opportunities to estimate NOx emissions using NO2 satellite data alongside chemical transport models
Why estimate emissions by assimilating satellite data?
Figure: Itahashi et al. 2020, ACP. (Figure 6),
O3
Video: Nitrogen Dioxide from Aura/OMI 2013-2014,
NASA/Goddard Space Flight Center
Notes: https://svs.gsfc.nasa.gov/30014

## Slide 3
Satellite assimilation in CMAQ provides capability to:
  Constrain international emissions
  Improve boundary conditions for US air quality simulations
  Create fast, first-pass estimates of NOx emissions in response to unexpected changes (e.g. COVID-19)
  Estimate NOx emissions from some sources with uncertainty, such as soil NOx
This presentation will:
  Describe the data assimilation system and anthropogenic emissions inversion
  Share new results of a targeted lightning-NOx emissions inversion
This project originated as a HAQAST Tiger Team led by Brad Pierce and Daniel Tong
Data assimilation in CMAQ
Notes: Main point: system is an advancement that utilizes latest satellite technology to fill a need and advance research

## Slide 4
TROPOMI satellite instrument
  2018 launch aboard the Sentinel-5P satellite
  1:30pm equatorial overpass time
  Daily global coverage
  3.5km x 5.5km data resolution
A low bias, particularly in urban areas, was noted in previous TROPOMI NO2 versions
Recent updates have improved the bias
NO2 Satellite data
Notes: …also provides opportunity to compare emissions inferred with OMI & TropOMI

## Slide 5
To estimate emissions, we iterate the finite-difference mass-balance (FDMB) method
Typically, is calculated as the difference between the model and satellite VCD
In our approach, is the difference between the model VCD with 3D-var assimilation and the model VCD without 3D-var assimilation
FDMB introduced in Lamsal et al. 2011
NOx emissions inversion
is NOx emissions
is the NO2 vertical column density (VCD)
is the sensitivity of the modeled NO2 vertical column density to a change in emissions, created by finite differencing in the model

## Slide 6
3D-variational data assimilation produces a statistically optimal combination of modeled and satellite-observed NO2
It accounts for uncertainties in the model and satellite retrieval
In effect, 3D-var “nudges” modeled concentrations closer to the satellite retrieval
In this framework, 3D-var is coupled to CMAQ online, updating model NO2 concentrations at each timestep that coincides with a satellite retrieval
Data assimilation in CMAQ
FDMB NOx Inversion
CMAQ
CMAQ+3D-var
Satellite retrievals
Prior NOx Emissions
background errors
Posterior NOx Emissions

## Slide 7
Upper troposphere ≠ near-surface
  Greater sensitivity of satellite to upper troposphere
  Upper troposphere lengthscales > near-surface lengthscales
  In typical FDMB, this can lead to misallocations for surface emissions
Emissions updates
Framework and emissions inversion:
East et al. 2022. Inferring and evaluating satellite-based constraints on NOx emissions estimates in air quality simulations. ACPD [preprint], https://doi.org/10.5194/acp-2022-435
How to address this?
  Refine lighting NOx emissions to reduce model bias in the upper troposphere
  Data assimilation allows us to split the modeled column into upper and lower
In our framework for updating anthropogenic inversion, emissions are updated in 2 steps:
  Update lightning NOx emissions in a single iteration
  Update anthropogenic NOx emissions iteratively
Change due to satellite assimilation,
separated by vertical level
Notes: 𝚫𝛀 is shown for one iteration of assimilating July 2019 TROPOMI NO2 with background errors for the boundary layer and LNOx emissions updates applied.

## Slide 8
Inversion system was applied to infer 2019 NOx emissions using OMI and TROPOMI
Results showed diverging estimates for OMI and TROPOMI
Large decreases inferred by TROPOMI were attributed to low bias in previous version
Anthropogenic emissions inference
Framework and emissions inversion:
East et al. 2022. Inferring and evaluating satellite-based constraints on NOx emissions estimates in air quality simulations. ACPD [preprint], https://doi.org/10.5194/acp-2022-435
Prior NOx emissions
Inverse estimates
CAMS = 2019 inventory from the Community Atmosphere Monitoring Service
TCR-2 = 2019 inventory from the Tropospheric Community Reanalysis 2

## Slide 9
Before updating anthropogenic emissions, lightning NOx (LNOx) emissions were inferred
Initial LNOx updates, based on climatological emissions, showed impact on upper troposphere ozone
Recent development of a LNOx observation-based inventory for CMAQ and the large impact of LNOx on ozone bias in previous work motivate a more refined, targeted approach to infer lightning NOx emissions
Impact of lightning updates

## Slide 10
Study design
CMAQ WWLLNs lightning NOx emissions:
Kang, D. et al. Assessing the Impact of Lightning NOx Emissions in CMAQ Using Lightning Flash Data from WWLLN over the Contiguous United States. Atmosphere 2022, 13, 1248. https://doi.org/10.3390/atmos13081248
Lightning NOx inversions | 
LNOx Emissions | Satellite NO2 retrievals
GEIA climatological | TROPOMI v2.3.1 (cloud screened)
WWLLNs | TROPOMI v2.3.1 (cloud screened)
WWLLNs | TROPOMI v2.3.1 (not cloud screened)
CMAQ Simulation inputs | 
Anthropogenic NOx emissions | 2019 OMI-inferred
Non-NOx Emissions (North America & rest of hemisphere) | 2017 EPA platform
Non-NOx Emissions (China) | 2015 Tsinghua University
Meteorology | 2019 WRF
Here, 2019 lightning-NOx emissions in CMAQ for the northern hemisphere are inferred using v2.3.1 TROPOMI retrievals
Two prior emissions inventories are used:
  GEIA climatological
  Worldwide Lightning Location Network (WWLLNs) derived emissions for hemispheric CMAQ
For WWLLNs, a separate inversion using NO2 satellite retrievals with clouds is performed

## Slide 11
Lightning NOx emissions
Outside North America, GEIA > WWLLNs
Upper troposphere column is largely controlled by LNOx emissions
See presentations by Mike Madden and Daiwen Kang for more WWLLNs details and model impacts!
LNOx emissions
Upper troposphere NO2 VCD
Notes:   Column cutoff roughly ~720 hPa
  GEIA = climatological
  WWLLNs = year-specific

## Slide 12
Each case initialized with 1-year spinup
All cases are low-biased for ozone
Bias is at its worst in the winter and spring
Simulated ozone using prior emissions
WOUDC ozonesonde
CMAQ ozone
NMB
WWLLNs
GEIA
Notes: ~1100 releases

## Slide 13
Assimilation results
GEIA
WWLLNs
Assimilating TROPOMI NO2:
  Leads to increases in model NO2 in all cases
  Leads to indirect impacts on ozone, decreasing but not erasing model springtime bias
VCD using GEIA a priori increases more than VCD using WWLLNs a priori, but at different latitudes
Splitting the column reduces the anthropogenic emissions signal in VCD
Upper troposphere NO2 VCD due to assimilating satellite NO2
Bias against
ozonesonde

## Slide 14
Inferred emissions
The FDMB inversion leads to:
  Widespread increases for GEIA
  Increases with hotspots in North America, elsewhere for WWLLNs
  Larger relative springtime increases for WWLLNs
The background error covariance and play major roles in determining emissions changes
  Changes are restricted to areas where model emissions already exists, highlighting importance of prior inventory

## Slide 15
GEIA and WWLLNs assimilation includes only “cloud free” scenes
  <30% clouds in the satellite pixel
Including all scenes, regardless of clouds:
  Increased NO2 in mid-latitudes
  Did not have a large overall emissions impact
  Note: scales are much smaller!
Impact of cloud filtering
∆NO2 VCD
Inferred
emissions

## Slide 16
Assimilating TROPOMI NO2 increases model NO2 in all emissions cases
Assimilating NO2 leads to indirect impacts on ozone, improving model bias against ozonesondes
Emissions inversion indicates LNOx is underestimated by both GEIA and WWLLNs
In both cases, geographic distributions largely reflect the prior inventories
Using cloudy scenes did not lead to significant emissions impact, on average, but may have more localized impacts
Future work may include:
  Evaluate the updated emissions comparing model predictions against different types of observations (airborne, sonde, satellite, surface)
  Iterating FDMB inversion
  Exploring impact of cloud filtering on finer scales
Conclusions and next steps

## Slide 17: Thank you!
east.james@epa.gov
Disclaimer: The views expressed in this presentation are those of the authors and do not necessarily represent the views or policies of the U.S. Environmental Protection Agency.
Acknowledgement: James East is supported in part by an appointment to the ORISE participant research program supported by an interagency agreement between the U.S. Environmental Protection Agency (EPA) and the U.S. Department of Energy (DOE).