## Slide 1: Construction of the Advanced Air Quality Modeling System (AAQMS) and the MPAS-CMAQ Coupled Model
David C. Wong1, Jeff Willison1, Jonathan E. Pleim1, Russell Bullock Jr.1, Robert C. Gilliam1, Jerold A. Herwehe1, George A. Pouliot1, Christian Hogrefe1, Daiwen Kang1, and Hosein Foroutan2
1 Office of Research and Development, U.S. Environmental Protection Agency
2 Department of Civil & Environmental Engineering, Virginia Tech
Office of Research and Development
Center for Environmental Measurement and Modeling • Atmospheric and Environmental Systems Modeling Division
22nd Annual CMAS Conference
16–18 October 2023
The views expressed in this presentation are those of the authors and do not necessarily reflect the views or policies of the U.S. EPA.
Notes: Purpose: science talk

## Slide 2: CMAQ Release History
* Created by Sarah Simm

## Slide 3: Development Progression
CMAQ (offline mode)
Relies on Models-3 I/O API (aka IOAPI) for I/O
Utilizes MCIP to prepare meteorological inputs
Requires external model/data to produce IC/BC
Limitations
  Regional simulation rely on LBCs from large scale models or other data sources
  Lack of influence from outside the domain (long range transport, development/usage of Hemispheric CMAQ alleviate this)
  Low frequency of meteorological information
  Lack of interaction with meteorological model

## Slide 4: Development Progression (cont’d)
WRF-CMAQ coupled model
Relies on Model-3 I/O API for I/O and BUFFERED file for coupling
User controls incoming meteorological information frequency
Aerosol information from CMAQ can feedback to WRF and affects SW radiation calculation (radiative aerosol direct effect *)
Requires external model/data to produce IC/BC
Limitations
  Regional simulation rely on LBCs from large scale models or other data sources
  Lack of influence from outside the domain (long range transport, development/usage of Hemispheric CMAQ alleviate this)
*D.C.Wong, J.Pleim, R.Mathur, F.Binkowski, T.Otte, R.Gilliam, G.Pouliot, A.Xiu, J.O.Young, and D.Kang.: WRF-CMAQ two-way coupled system with aerosol feedback: software development and preliminary results, Geosci.Model Dev., 5, 299–312, 2012 www.geosci-model-dev.net/5/299/2012/ doi:10.5194/

## Slide 5: Development Progression (cont’d)
MPAS-CMAQ coupled model
Relies on an ad hoc coupler
Utilizes an internal I/O system
User controls incoming meteorological information frequency
Aerosol information from CMAQ can feedback to MPAS and affects SW radiation calculation (will be implemented soon)
Transport of chemical species is handled by MPAS for numerical consistency and mass conservation

## Slide 6: Various Model Configurations

## Slide 7: Advanced Air Quality Modeling System

## Slide 8: Advanced Air Quality Modeling System (cont’d)

## Slide 9: What is MPAS
Model for Prediction Across Scales (MPAS)
Fully-compressible, non-hydrostatic dynamics
Finite volume discretization on centroidal Voronoi (nominally hexagonal) grids
Single global mesh with seamless refinement to local scales
Regional capability
source: https://www.ecmwf.int/sites/default/files/elibrary/2012/14043-global-nonhydrostatic-
atmospheric-model-mpas-preliminary-results-uniform-and-variable.pdf

## Slide 10: MPAS Updates by EPA
Added US EPA physics routines to MPAS
  ACM2 boundary layer model
  Pleim-Xiu Land Surface Model (PX LSM)
  Updated Kain-Fritsch convective cloud scheme
    including radiation feedback and dynamic lifetime
  All modified EPA physics is consistent between WRFv4.3 and MPAS7.1
Data Assimilation
  Implemented analysis FDDA as in WRF (Bullock et al. 2018)
  Implemented indirect soil moisture data assimilation in PX LSM
Meteorological Evaluation
  Gilliam et al. (2021) showed that the EPA configuration of MPAS performs comparably well with the EPA configuration of WRF for air quality applications

## Slide 11: MPAS and MPAS-CMAQ Computational Performance
120km uniform mesh
92-25km variable mesh

## Slide 12: Surface O3 Over US (120km uniform mesh)
Comparison with AQS sites indicates a seasonally-varying bias for surface 8-hr max ozone concentration over the United States.
Average low bias in spring, average high bias in winter.
No noticeable drift in first three years.

## Slide 13: Surface PM2.5 Over US (120km uniform mesh)
Comparison with AQS sites indicates general low bias but brief high bias in winter
Again, no noticeable drift in three years.

## Slide 14: South Korea O3 Performance (120km uniform mesh)
Overall, max 8hr O3 concentrations (ppb) have little bias for summer (JJA) in South Korea
The coarse mesh is insufficient to resolve high O3 on the outskirts of Seoul or the titration in the Port of Gwangyang

## Slide 15: O3 Performance (92-25km variable mesh)

## Slide 16: PM25 Performance (92-25km variable mesh)

## Slide 17: Global O3 Performance (92-25km variable mesh)

## Slide 18: Global PM25 Performance (92-25km variable mesh)

## Slide 19: Take Away Points
With AAQMS, configurating/constructing CMAQ offline mode, WRF-CMAQ coupled model, and MPAS-CMAQ coupled model can be done seamlessly.
Preliminary results show MPAS-CMAQ coupled model performs reasonably well.
Code is “available” on request.