## Slide 1: Updating Residential Wood Combustion Emissions with the Reactive Organic Carbon Approach
BEN MURPHY
Center for Environmental Measurement and Modeling (CEMM)
Office of Research and Development (ORD)
U.S. EPA
Co-Authors: Karl Seltzer1, Havala O. T. Pye2, Amara Holder2, Gabriel Isaacman-Van Wertz3
1Office of Air Quality Planning and Standards, U.S. EPA
2Office of Research and Development, U.S. EPA
3Virginia Polytechnic Institute and State University
CMAS Annual Conference | October 16-18, 2023
Disclaimer: The views expressed in this presentation are those of the author and do not necessarily reflect the views or policies of the U.S. EPA.

## Slide 2: Residential Wood Combustion (RWC) Emissions
Residential wood combustion is a significant source of multiple pollutants including PM, CO, and VOCs (both toxics and precursors to PM and O3)
Measuring wood smoke emissions and translating to models is challenging:
  Fuel (wood species) vary
  Fuel moisture and condition vary
  Real-world operations vary
  Standard test method procedures may introduce biases
  Emissions chemical composition is complex
Residential Wood Sources PM2.5 Emissions (tons/mi2). EPA 2020 NEI Exploration Tool.
Pollutant | Annual 2020 Emissions [kt yr-1] | Fraction of NEI 2020*
PM2.5 | 484 | 20.0%
VOC | 460 | 4.6%
*Excludes dust, biogenic, and fire (wild, prescribed and agriculture) sources

## Slide 3: Standard methods for measuring RWC emission factors
PM2.5 Measurement
Glass filters collect PM mass
Quartz Filters (not shown) measure OC and EC
IVOCs and SVOCs may condense to the filter or break through
PM emission factor depends on the temperature and concentration of the sample (Robinson et al., 2011)
Method 5H
Impinger
< 120 C
< 20 C
Glass Filters
Method 5G
Dilution Tunnel
< 32 C
Glass Filters
Stack Sample

## Slide 4: Standard methods for measuring RWC emission factors
VOC Measurement
PM2.5 Measurement
Glass filters collect PM mass
Quartz Filters (not shown) measure OC and EC
IVOCs and SVOCs may condense to the filter or break through
PM emission factor depends on the temperature and concentration of the sample (Robinson et al., 2011)
Particles removed by the glass fiber filter before entering the Flame-Ionization Detector (FID).
Uncertain losses to filters, canisters, and bags
FID undercounts oxygenated carbons and doesn’t count non-carbon atoms.
The total NMOG reported depends on definition and losses.
Method 5H
Impinger
< 120 C
< 20 C
Glass Filters
Method 5G
Dilution Tunnel
< 32 C
Glass Filters
Stack Sample
Flame Ionization Detector
Summa Canister or Tedlar Bag
Offline
GC-FID
Method 25a
Method TO-15
> 110 C
These Methods are useful but may not capture the full extent of emissions.
Applying speciation profiles to these bulk metrics adds further uncertainties.

## Slide 5: Standard methods for measuring RWC emission factors
VOC Measurement
PM2.5 Measurement
Glass filters collect PM mass
Quartz Filters (not shown) measure OC and EC
IVOCs and SVOCs may condense to the filter or break through
PM emission factor depends on the temperature and concentration of the sample (Robinson et al., 2011)
Particles removed by the glass fiber filter before entering the Flame-Ionization Detector (FID).
Uncertain losses to filters, canisters, and bags
FID undercounts oxygenated carbons and doesn’t count non-carbon atoms.
The total NMOG reported depends on definition and losses.
Method 5H
Impinger
< 120 C
< 20 C
Glass Filters
Method 5G
Dilution Tunnel
< 32 C
Glass Filters
Stack Sample
Flame Ionization Detector
Summa Canister or Tedlar Bag
Offline
GC-FID
Method 25a
Method TO-15
> 110 C
Research Questions:
Do these Methods account for the mass and character of all reactive organic carbon (ROC) emitted by wood-burning sources?
How can we translate these operational definitions of PM and VOC to standard definitions for use in the NEI and air quality modeling?
What is the impact on RWC carbon emissions and ambient organic aerosol?

## Slide 6: Reactive Organic Carbon (ROC) Framework
CROC (Condensable Reactive Organic Carbon) – compounds with volatility less than C20 (n-Eicosane).
  CROC = [SVOC + LVOC + ELVOC + ULVOC]
GROC (Gaseous Reactive Organic Carbon) – compounds with volatility greater than C20.
  GROC = [IVOC + VOC]
Particle
Gas
Volatility
fOC = organic carbon fraction from speciation profile
OM:OC = ratio of non-carbon to carbon
VOCExempt = gas-phase compounds exempted from the regulatory definition of VOC

## Slide 7: Reactive Organic Carbon (ROC) Framework
Particle
Gas
Volatility
fOC = organic carbon fraction from speciation profile
OM:OC = ratio of non-carbon to carbon
VOCExempt = gas-phase compounds exempted from the regulatory definition of VOC
?
?
CROC (Condensable Reactive Organic Carbon) – compounds with volatility less than C20 (n-Eicosane).
  CROC = [SVOC + LVOC + ELVOC + ULVOC]
GROC (Gaseous Reactive Organic Carbon) – compounds with volatility greater than C20.
  GROC = [IVOC + VOC]

## Slide 8: Use a detailed speciation profile to simulate Test Method measurements
Fireplace pine smoke reported by Schauer et al. (2001) and Nolte et al. (2001)
Schauer et al. (2001): https://pubs.acs.org/doi/full/10.1021/es001331e
Nolte et al. (2001): https://pubs.acs.org/doi/full/10.1021/es001420r
226 explicit species measured
Semivolatile components quantified in both gas and particle phases.
EC fraction = 1.4%
NMOG/OM = 2.1
Unresolved non-methane organic gas = 8.1%
Unresolved particle = 61%

## Slide 9: Assign unspeciated mass to reproduce observed volatility trends
Woodsmoke volatility distribution
(Sinha et al., 2022)
https://pubs.rsc.org/en/content/articlehtml/2023/ea/d2ea00080f
Chart: log10 c* (T = 298)
| -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Speciated | 0.003865 | 0.40596 | 1.4168 | 0.31958 | 0.086613 | 0.68455 | 0.89453 | 0.73577 | 1.783 | 0.58821 | 1.2674 | 5.3309 | 2.8437 | 1.5459
Chart: log10 c* (T = 298)
| -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Speciated | 0.003865 | 0.40596 | 1.4168 | 0.31958 | 0.086613 | 0.68455 | 0.89453 | 0.73577 | 1.783 | 0.58821 | 1.2674 | 5.3309 | 2.8437 | 1.5459
Unspeciated | 0.70628 | 0.031268 | 0.0030406 | 0.11928 | 1.2501 | 0.41775 | 1.1042 | 0.665 | 0.965 | 0 | 0 | 0 | 0 | 0
Particle
Gas
Volatility

## Slide 10: Assign unspeciated mass to reproduce observed volatility trends
PM temperature sensitivity is similar to that observed in previous biomass burning studies
Chart: log10 c* (T = 298)
| -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Speciated | 0.003865 | 0.40596 | 1.4168 | 0.31958 | 0.086613 | 0.68455 | 0.89453 | 0.73577 | 1.783 | 0.58821 | 1.2674 | 5.3309 | 2.8437 | 1.5459
Chart: log10 c* (T = 298)
| -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Speciated | 0.003865 | 0.40596 | 1.4168 | 0.31958 | 0.086613 | 0.68455 | 0.89453 | 0.73577 | 1.783 | 0.58821 | 1.2674 | 5.3309 | 2.8437 | 1.5459
Unspeciated | 0.70628 | 0.031268 | 0.0030406 | 0.11928 | 1.2501 | 0.41775 | 1.1042 | 0.665 | 0.965 | 0 | 0 | 0 | 0 | 0
Particle
Gas
Volatility

## Slide 11: Impact of partitioning on Method 5G and 5H measurements
PM2.5 Measurement
Method 5H
Impinger
< 120 C
< 20 C
Glass Filters
Method 5G
Dilution Tunnel
< 32 C
Glass Filters
Stack Sample
Laboratory conditions –need to discount absorption of IVOCs. Multiply by 0.77 for 5G and 0.72 for 5H.
Ambient conditions –need to add SVOCs broken through the filter. Multiply by 1.55 for 5G and 1.27 for 5H.
Sum EFs for CROC compounds from Schauer profile
CROC/OM =
Calculate particle-phase EF given filter temperature and OA conc.

## Slide 12: Impact of partitioning and functionality on FID detection
VOC Measurement
Flame Ionization Detector
Summa Canister or Tedlar Bag
Offline
GC-FID
Method 25a
Method TO-15
> 110 C
Method TO-15
Canisters and bags:
VOCs
IVOCs
 Temperature independent correction
Lu et al., Atmos, Chem and Phys. 2018.
https://acp.copernicus.org/articles/18/17637/2018/

## Slide 13: Impact of partitioning and functionality on FID detection
VOC Measurement
Flame Ionization Detector
Summa Canister or Tedlar Bag
Offline
GC-FID
Method 25a
Method TO-15
> 110 C
Method TO-15
Canisters and bags:
VOCs
IVOCs
 Temperature independent correction
Lu et al., Atmos, Chem and Phys. 2018.
https://acp.copernicus.org/articles/18/17637/2018/
Hurley et al. Atmos. Meas. Tech. (2020)
https://amt.copernicus.org/preprints/amt-2020-44/amt-2020-44.pdf
Method 25a
Inline FID with glass filter (110 C)
May et al., Journal of Geophys. Res. (2013)
https://agupubs.onlinelibrary.wiley.com/doi/full/10.1002/jgrd.50828

## Slide 14: Impact of partitioning and functionality on FID detection
VOC Measurement
Flame Ionization Detector
Summa Canister or Tedlar Bag
Offline
GC-FID
Method 25a
Method TO-15
> 110 C
Method TO-15
Canisters and bags:
VOCs
IVOCs
 Temperature independent correction
Lu et al., Atmos, Chem and Phys. 2018.
https://acp.copernicus.org/articles/18/17637/2018/
Method 25a
Inline FID with glass filter (110 C)
Method TO-15
Method 25a
GROC/FID: Method TO-15  Multiply by 3.0
Method 25a  Multiply by 1.6 (assuming 110 C)

## Slide 15: Relationship between ROC and Test Methods
At high concentration (low dilution rate), Methods 5H and TO-15 together approximately account for total ROC.  Add OM and NMOG and then speciate with detailed profile.
If Method 5G or Method 25a are used instead, conversion to CROC and GROC should be calculated separately.

## Slide 16: Determine Method basis for each RWC source
SCC Description | Particulate | VOC | Approach
Conventional Woodstoves | Method 5H | Tedlar Bag (TO-15) | A
Certified Woodstoves | Method 5H | Tedlar Bag (TO-15) | A
Indoor Furnaces | Method 5G | Method 25a | B
Fireplaces | Method 5H | Canister (TO-15) | A
Outdoor Wood Burning Devices | Method 5H | Tedlar Bag (TO-15) | A
Synthetic Firelogs | Method 5G | Method 25a | B
Approach A Approach B
Reference 2020 NEI Technical Support Document, AP-42 and supporting studies.
OM
VOC
ROC
Add
Speciate
CROC
GROC
Speciate further
Schauer et al. (2001)
Schauer et al. (2001)
OM
VOC
Convert
CROC
GROC
Speciate further
Schauer et al. (2001)

## Slide 17: Impact of update on RWC emission factors and OA potential
Account for activity, POA partitioning and 1st-generation SOA yields
Left:
NEI
Right:
ROC

## Slide 18: Impact of update on hazardous air pollutants
Total TOG emissions increase by 50% but HAP emissions stay roughly the same.
NEI
ROC

## Slide 19
Contact: murphy.ben@epa.gov
Summary
Proposed revised emission factors for conventional wood stoves and similar combustion sources.
Total ROC increases by 11.3%. This mass is missing in the NEI.
OA potential decreases by -39%.
Larger role for SOA (30% of OA in ROC case)
HAPs are essentially unchanged.
More work to do on cleaner technologies:
  Pellet Stoves
  Catalytic Stoves
  Hydronic Heaters