## Slide 1: Coupling a sub-grid scale plume model for biomass burns with adaptive grid CMAQ: part 2
Aika Yano
Fernando Garcia-Menendez
Yongtao Hu
M. Talat Odman
Gary Achtemeier (USDA Forest Service)
10th Annual CMAS Conference
25 October, 2011

## Slide 2: Motivation
U.S. EPA lists prescribed burning as the 3rd largest source of fine particulate matter.
Smoke plume must be preserved in order to predict downwind concentration accurately in CMAQ
Use of sub grid model and adaptive grid can help resolve smoke plume in CMAQ

## Slide 3: Objective
Find out the ideal relationship between sub-grid model coupling and grid adaptation for burn plumes.
Effectiveness of the coupling method, handover, on both uniform and adaptive grid.
Different methods of inserting smoke emissions
Ground level concentration vs. all vertical layer concentration adaptation (adapt in 2D)
Adaptive weighting function parameters
Frequency of tracer/wall analysis

## Slide 4: Column Injection
Set distance

## Slide 5
Handover
Remain in Daysmoke
Into CMAQ
Notes: Now that the wall is determined,
all the parcels that didn’t reach the wall remain as 1kg parcels to be calculate its trajectory inside Daysmoke
Parcels beyond the wall is converted into concentrations and get passed on to CGRID

## Slide 6: Atlanta Smoke Case Feb. 28 2007
Oconee NF (1542 acres) 5 yr old
10:00 am - 3:00 pm total 5hr
Piedmont NWR (1460 acres) 1 yr old
11:00 am - 2:00 pm
total 3hr
Notes: Case study done for the two national parks’ prescribed burns occurred back in Feb 28 2007 in GA.

## Slide 7: Handover with uniform grid
 | uniform CMAQ | uniform handover CMAQ
Mean fractional error | 76.27% | 69.35%
Chart: Fire Station 8
| 39141.708328703688 | 39141.718745312501 | 39141.729161921263 | 39141.739578530076 | 39141.749995138889 | 39141.760411747673 | 39141.770828356493 | 39141.781244965263 | 39141.791661574054 | 39141.802078182889 | 39141.812494791666 | 39141.822911400479 | 39141.833328009256 | 39141.843744618054 | 39141.854161226867 | 39141.864577835651 | 39141.874994444464 | 39141.885411053234 | 39141.895827662025 | 39141.906244270845 | 39141.916666666664 | 39141.927083333321 | 39141.937500057873 | 39141.94791678241 | 39141.958333506969 | 39141.968750231485 | 39141.979166956022 | 39141.989583680559 | 39142.000000405096 | 39142.010417129633 | 39142.020833854163 | 39142.031250578701 | 39142.041667303223 | 39142.052084027782 | 39142.062500752305 | 39142.072917476871 | 39142.083334201387 | 39142.093750925924 | 39142.104167650454 | 39142.114584375013 | 39142.125001099535 | 39142.135417824073 | 39142.14583454861 | 39142.156251273169 | 39142.166667997684 | 39142.177084722207 | 39142.187501446773 | 39142.197918171281
Observations | 4.3583 | 3.425 | 2.2167 | 4.4333 | 7.3 | 23.3167 | 62.975 | 145.917 | 115.358 | 73.25 | 32.7917 | 16.9333
uniform grid handover | 9.6006 | 9.5422 | 9.681 | 10.2835 | 11.5997 | 12.7655 | 13.1433 | 12.5322 | 11.3209 | 9.8613 | 9.4383 | 9.4806 | 9.7629 | 10.5226 | 12.7323 | 16.8427 | 21.8774 | 26.6231 | 28.8876 | 30.4846 | 31.0712 | 28.8874 | 28.9554 | 35.133 | 44.5796 | 52.1253 | 55.7985 | 56.9037 | 56.4994 | 57.0699 | 54.661 | 46.2784 | 39.1925 | 36.1155 | 34.4525 | 32.8238 | 31.3067 | 30.1763 | 29.3695 | 28.719 | 28.3779 | 28.2905 | 27.8624 | 27.5111 | 27.3332 | 27.5166 | 28.1687 | 28.5574
uniform grid | 8.8427 | 8.8505 | 9.1649 | 9.8054 | 10.4526 | 10.6549 | 10.2217 | 9.2216 | 7.9484 | 7.5483 | 7.642 | 8.3134 | 10.4507 | 14.4637 | 19.504 | 22.5285 | 23.5157 | 21.7611 | 17.1588 | 13.0299 | 11.8606 | 12.6536 | 14.2406 | 16.8203 | 19.7725 | 22.6703 | 25.5652 | 29.0655 | 33.4623 | 37.4888 | 40.0584 | 40.7728 | 40.1683 | 38.6722 | 37.4696 | 35.856 | 33.2693 | 30.4312 | 28.42 | 27.2719 | 26.4921 | 26.0308 | 26.007 | 26.9151 | 28.8771 | 32.2091 | 35.6275 | 38.0203
Chart: Fort McPherson
| 39141.708328703688 | 39141.718745312501 | 39141.729161921263 | 39141.739578530076 | 39141.749995138889 | 39141.760411747673 | 39141.770828356493 | 39141.781244965263 | 39141.791661574054 | 39141.802078182889 | 39141.812494791666 | 39141.822911400479 | 39141.833328009256 | 39141.843744618054 | 39141.854161226867 | 39141.864577835651 | 39141.874994444464 | 39141.885411053234 | 39141.895827662025 | 39141.906244270845 | 39141.916666666664 | 39141.927083333321 | 39141.937500057873 | 39141.94791678241 | 39141.958333506969 | 39141.968750231485 | 39141.979166956022 | 39141.989583680559 | 39142.000000405096 | 39142.010417129633 | 39142.020833854163 | 39142.031250578701 | 39142.041667303223 | 39142.052084027782 | 39142.062500752305 | 39142.072917476871 | 39142.083334201387 | 39142.093750925924 | 39142.104167650454 | 39142.114584375013 | 39142.125001099535 | 39142.135417824073 | 39142.14583454861 | 39142.156251273169 | 39142.166667997684 | 39142.177084722207 | 39142.187501446773 | 39142.197918171281
Observations | 14.7092 | 11.5845 | 10.9297 | 10.8068 | 17.5475 | 35.7498 | 75.7298 | 138.811 | 130.678 | 111.985 | 85.786 | 60.8157
uniform grid handover | 8.7945 | 9.149 | 10.066 | 11.1497 | 11.6427 | 11.1755 | 10.4237 | 9.1186 | 8.4323 | 8.1069 | 8.3708 | 8.9337 | 9.9422 | 11.423 | 13.3432 | 14.6717 | 14.8278 | 15.1854 | 17.2605 | 19.1507 | 18.023 | 17.4708 | 20.7111 | 25.3312 | 27.7776 | 28.8524 | 30.1821 | 33.4684 | 41.64 | 48.0397 | 45.6548 | 41.114 | 39.0878 | 39.6671 | 37.8905 | 33.3878 | 29.441 | 27.6885 | 27.1773 | 27.233 | 27.9609 | 28.9946 | 30.352 | 31.6005 | 32.3043 | 35.2076 | 38.1979 | 39.2947
uniform grid | 8.0125 | 8.8233 | 9.6007 | 9.5845 | 9.0771 | 8.1391 | 7.2997 | 7.0521 | 7.3569 | 8.6278 | 12.0392 | 16.7702 | 20.6865 | 21.965 | 20.8716 | 16.1319 | 12.0794 | 10.2703 | 9.7648 | 9.8529 | 10.2756 | 11.2669 | 12.4268 | 13.8097 | 15.5292 | 17.0873 | 18.4739 | 19.9924 | 21.7957 | 23.429 | 25.4322 | 28.4572 | 31.3843 | 34.3786 | 36.4513 | 37.7079 | 39.1346 | 39.9617 | 40.408 | 41.242 | 42.731 | 45.9923 | 49.2145 | 50.1506 | 50.8254 | 51.2279 | 48.6399 | 43.9561
Chart: South Dekalb
| 39141.708328703688 | 39141.718745312501 | 39141.729161921263 | 39141.739578530076 | 39141.749995138889 | 39141.760411747673 | 39141.770828356493 | 39141.781244965263 | 39141.791661574054 | 39141.802078182889 | 39141.812494791666 | 39141.822911400479 | 39141.833328009256 | 39141.843744618054 | 39141.854161226867 | 39141.864577835651 | 39141.874994444464 | 39141.885411053234 | 39141.895827662025 | 39141.906244270845 | 39141.916666666664 | 39141.927083333321 | 39141.937500057873 | 39141.94791678241 | 39141.958333506969 | 39141.968750231485 | 39141.979166956022 | 39141.989583680559 | 39142.000000405096 | 39142.010417129633 | 39142.020833854163 | 39142.031250578701 | 39142.041667303223 | 39142.052084027782 | 39142.062500752305 | 39142.072917476871 | 39142.083334201387 | 39142.093750925924 | 39142.104167650454 | 39142.114584375013 | 39142.125001099535 | 39142.135417824073 | 39142.14583454861 | 39142.156251273169 | 39142.166667997684 | 39142.177084722207 | 39142.187501446773 | 39142.197918171281
Observations | 4.8 | 4.5 | 2 | 2.7 | 45.4 | 142.5 | 124.6 | 117.6 | 110.3 | 96
uniform grid handover | 9.1023 | 10.6538 | 12.098 | 12.5978 | 11.9881 | 10.2656 | 8.5818 | 8.0373 | 8.0858 | 8.2484 | 8.5066 | 10.2076 | 15.9522 | 25.4766 | 33.3058 | 36.5251 | 37.568 | 37.7614 | 34.7689 | 30.0391 | 33.574 | 42.4505 | 50.3031 | 55.1509 | 57.798 | 59.1887 | 57.9792 | 54.6999 | 49.3403 | 42.2683 | 38.0218 | 36.5812 | 36.0019 | 35.5623 | 35.0093 | 34.2348 | 33.2306 | 32.2971 | 31.6726 | 31.3218 | 31.1391 | 30.8763 | 30.4856 | 29.929 | 29.305 | 29.0442 | 29.0948 | 29.4777
uniform grid | 8.559 | 10.0217 | 10.7046 | 10.3069 | 8.8797 | 7.4319 | 6.8143 | 6.7842 | 6.8987 | 7.1579 | 7.7967 | 9.6954 | 14.1262 | 21.1223 | 26.7231 | 28.9605 | 29.1582 | 28.0232 | 25.9303 | 23.7364 | 22.4448 | 22.6956 | 24.5158 | 28.2855 | 33.172 | 38.5374 | 42.97 | 43.8955 | 42.6717 | 40.5046 | 37.0444 | 33.0548 | 29.9996 | 28.3698 | 27.4902 | 26.8721 | 26.311 | 25.7931 | 25.4642 | 25.4088 | 25.5061 | 25.7809 | 26.0009 | 26.3675 | 27.8452 | 30.6758 | 33.5151 | 36.0832
Chart: Jefferson St.
| 39141.708328703688 | 39141.718745312501 | 39141.729161921263 | 39141.739578530076 | 39141.749995138889 | 39141.760411747673 | 39141.770828356493 | 39141.781244965263 | 39141.791661574054 | 39141.802078182889 | 39141.812494791666 | 39141.822911400479 | 39141.833328009256 | 39141.843744618054 | 39141.854161226867 | 39141.864577835651 | 39141.874994444464 | 39141.885411053234 | 39141.895827662025 | 39141.906244270845 | 39141.916666666664 | 39141.927083333321 | 39141.937500057873 | 39141.94791678241 | 39141.958333506969 | 39141.968750231485 | 39141.979166956022 | 39141.989583680559 | 39142.000000405096 | 39142.010417129633 | 39142.020833854163 | 39142.031250578701 | 39142.041667303223 | 39142.052084027782 | 39142.062500752305 | 39142.072917476871 | 39142.083334201387 | 39142.093750925924 | 39142.104167650454 | 39142.114584375013 | 39142.125001099535 | 39142.135417824073 | 39142.14583454861 | 39142.156251273169 | 39142.166667997684 | 39142.177084722207 | 39142.187501446773 | 39142.197918171281
Observations | 4.1701 | 4.5241 | 3.0306 | 3.2157 | 5.3026 | 21.6223 | 71.9073 | 139.6525 | 98.2379 | 60.9217 | 26.475 | 15.6088
uniform grid handover | 11.2117 | 11.0939 | 11.3713 | 12.2665 | 13.5488 | 14.2766 | 13.7341 | 12.7901 | 11.3679 | 10.6334 | 10.4632 | 10.5866 | 10.9597 | 12.1146 | 15.0924 | 19.8808 | 25.0716 | 28.4941 | 30.1674 | 31.5106 | 30.2931 | 27.5134 | 30.5894 | 39.2552 | 48.1333 | 54.5278 | 56.9868 | 57.4839 | 57.7197 | 58.3132 | 53.6072 | 44.3247 | 38.8518 | 36.9985 | 35.4258 | 33.6855 | 32.3928 | 31.3972 | 30.6552 | 29.9843 | 29.3856 | 28.8346 | 28.3854 | 28.1344 | 28.0805 | 28.6032 | 29.5199 | 29.7623
uniform grid | 11.02 | 11.1472 | 11.7725 | 12.693 | 13.273 | 13.2772 | 12.3418 | 10.8621 | 9.6288 | 9.4475 | 9.6635 | 10.4228 | 12.3274 | 16.1391 | 21.4523 | 25.428 | 27.4066 | 27.4308 | 23.9754 | 18.842 | 16.1664 | 16.6865 | 19.0311 | 23.4987 | 28.7437 | 34.1514 | 39.8841 | 45.4866 | 49.3726 | 50.2647 | 48.243 | 45.1653 | 42.2466 | 39.6364 | 36.9597 | 34.3328 | 32.0448 | 30.2718 | 29.0336 | 28.1313 | 27.5141 | 27.1387 | 27.1138 | 27.6672 | 29.118 | 32.01 | 35.0707 | 37.0712
Notes: Circle 4 sites
About 7% decrease in the error

## Slide 8: Adaptive grid weighting function

## Slide 9: Surface only vs. all layers concentration adaptation
3.6% improvement
 | surface adaptation | all layer adaptation
Mean fractional error | 80.47% | 76.82%
Notes: Red farther away from fire, therefore purple adapts away from the fire, green considers the high concentrations up at the top of the plume

## Slide 10: Global vs. Output time step handover analysis
 | global handover | handover per output
Mean fractional error | 65.08% | 65.19%
Chart: Jefferson St.
| 39141.708328703702 | 39141.718745312501 | 39141.729161921299 | 39141.739578530091 | 39141.749995138889 | 39141.760411747688 | 39141.770828356479 | 39141.781244965277 | 39141.791661574076 | 39141.802078182867 | 39141.812494791666 | 39141.822911400464 | 39141.833328009256 | 39141.843744618054 | 39141.854161226853 | 39141.864577835651 | 39141.874994444443 | 39141.885411053241 | 39141.89582766204 | 39141.906244270831 | 39141.916666666664 | 39141.927083333336 | 39141.937500057873 | 39141.94791678241 | 39141.958333506947 | 39141.968750231485 | 39141.979166956022 | 39141.989583680559 | 39142.000000405096 | 39142.010417129626 | 39142.020833854163 | 39142.031250578701 | 39142.041667303238 | 39142.052084027775 | 39142.062500752312 | 39142.072917476849 | 39142.083334201387 | 39142.093750925924 | 39142.104167650461 | 39142.114584374998 | 39142.125001099535 | 39142.135417824073 | 39142.14583454861 | 39142.156251273147 | 39142.166667997684 | 39142.177084722221 | 39142.187501446759 | 39142.197918171296
Observations | 4.1701 | 4.5241 | 3.0306 | 3.2157 | 5.3026 | 21.6223 | 71.9073 | 139.6525 | 98.2379 | 60.9217 | 26.475 | 15.6088
handover (6,-0.5)t2 | 12.3779 | 11.889 | 12.0791 | 12.057 | 11.704 | 10.9775 | 10.0757 | 9.6026 | 9.404 | 8.152 | 5.9841 | 4.5483 | 3.8451 | 5.0837 | 5.8617 | 15.0453 | 18.3968 | 14.6618 | 12.9259 | 13.196 | 16.3253 | 15.2197 | 19.4441 | 28.5664 | 38.7921 | 37.6994 | 32.5181 | 33.7941 | 47.6355 | 74.5334 | 90.403 | 97.155 | 75.7641 | 42.0865 | 29.1593 | 32.0905 | 28.3271 | 37.2881 | 52.2259 | 57.3452 | 45.0239 | 44.7442 | 49.0977 | 48.6124 | 61.3782 | 69.9476 | 78.3424 | 67.8171
handover (6,-0.5)t1 | 11.9267 | 11.5258 | 10.7879 | 11.1424 | 11.3043 | 11.3185 | 11.2576 | 10.575 | 9.8576 | 9.2752 | 7.1354 | 5.1013 | 3.9404 | 3.2391 | 4.4795 | 8.5945 | 15.7217 | 18.8816 | 19.3375 | 20.8517 | 22.7366 | 22.3133 | 14.6287 | 15.6106 | 24.5234 | 33.5134 | 36.6607 | 31.9409 | 36.5848 | 55.6842 | 69.2577 | 77.2863 | 65.1596 | 61.6604 | 63.2056 | 60.2237 | 56.5911 | 48.6827 | 38.5569 | 32.3595 | 22.408 | 21.2875 | 18.5282 | 36.334 | 51.5605 | 62.6269 | 66.44 | 49.916
Chart: South Dekalb
| 39141.708328703702 | 39141.718745312501 | 39141.729161921299 | 39141.739578530091 | 39141.749995138889 | 39141.760411747688 | 39141.770828356479 | 39141.781244965277 | 39141.791661574076 | 39141.802078182867 | 39141.812494791666 | 39141.822911400464 | 39141.833328009256 | 39141.843744618054 | 39141.854161226853 | 39141.864577835651 | 39141.874994444443 | 39141.885411053241 | 39141.89582766204 | 39141.906244270831 | 39141.916666666664 | 39141.927083333336 | 39141.937500057873 | 39141.94791678241 | 39141.958333506947 | 39141.968750231485 | 39141.979166956022 | 39141.989583680559 | 39142.000000405096 | 39142.010417129626 | 39142.020833854163 | 39142.031250578701 | 39142.041667303238 | 39142.052084027775 | 39142.062500752312 | 39142.072917476849 | 39142.083334201387 | 39142.093750925924 | 39142.104167650461 | 39142.114584374998 | 39142.125001099535 | 39142.135417824073 | 39142.14583454861 | 39142.156251273147 | 39142.166667997684 | 39142.177084722221 | 39142.187501446759 | 39142.197918171296
Observations | 4.8 | 4.5 | 2 | 2.7 | 45.4 | 142.5 | 124.6 | 117.6 | 110.3 | 96
handover (6,-0.5)t2 | 11.9249 | 11.2521 | 11.4389 | 10.7911 | 9.7104 | 9.5285 | 8.3432 | 5.9837 | 4.3128 | 3.293 | 3.2574 | 1.9589 | 4.3161 | 14.2006 | 13.4629 | 6.6972 | 7.6744 | 15.4997 | 17.052 | 20.43 | 20.2063 | 17.0258 | 24.9343 | 30.9537 | 23.4398 | 32.3861 | 72.3131 | 109.9416 | 119.1043 | 97.7249 | 60.2004 | 32.5546 | 19.8493 | 18.0549 | 17.0671 | 26.1401 | 51.4047 | 64.1818 | 57.1101 | 49.1474 | 49.4626 | 57.9528 | 58.8296 | 70.3678 | 70.5565 | 77.1053 | 66.2161 | 33.6256
handover (6,-0.5)t1 | 10.4375 | 9.888 | 9.9154 | 10.8804 | 11.0922 | 9.6365 | 8.9657 | 7.4299 | 5.584 | 4.1219 | 4.0087 | 2.4026 | 2.8221 | 9.3697 | 15.5054 | 21.2308 | 16.2337 | 10.9275 | 11.8461 | 15.0554 | 9.8442 | 9.6152 | 18.2377 | 21.6035 | 21.7457 | 33.0257 | 46.4059 | 53.3077 | 61.2709 | 68.0082 | 48.3165 | 56.9866 | 73.7679 | 68.9318 | 55.4924 | 50.1649 | 43.4787 | 26.3202 | 22.9457 | 19.4484 | 14.5653 | 19.4773 | 33.1074 | 67.2762 | 74.2465 | 72.7897 | 45.7355 | 17.4759
Chart: Fire Station 8
| 39141.708328703702 | 39141.718745312501 | 39141.729161921299 | 39141.739578530091 | 39141.749995138889 | 39141.760411747688 | 39141.770828356479 | 39141.781244965277 | 39141.791661574076 | 39141.802078182867 | 39141.812494791666 | 39141.822911400464 | 39141.833328009256 | 39141.843744618054 | 39141.854161226853 | 39141.864577835651 | 39141.874994444443 | 39141.885411053241 | 39141.89582766204 | 39141.906244270831 | 39141.916666666664 | 39141.927083333336 | 39141.937500057873 | 39141.94791678241 | 39141.958333506947 | 39141.968750231485 | 39141.979166956022 | 39141.989583680559 | 39142.000000405096 | 39142.010417129626 | 39142.020833854163 | 39142.031250578701 | 39142.041667303238 | 39142.052084027775 | 39142.062500752312 | 39142.072917476849 | 39142.083334201387 | 39142.093750925924 | 39142.104167650461 | 39142.114584374998 | 39142.125001099535 | 39142.135417824073 | 39142.14583454861 | 39142.156251273147 | 39142.166667997684 | 39142.177084722221 | 39142.187501446759 | 39142.197918171296
Observations | 4.3583 | 3.425 | 2.2167 | 4.4333 | 7.3 | 23.3167 | 62.975 | 145.917 | 115.358 | 73.25 | 32.7917 | 16.9333
handover (6,-0.5)t2 | 11.6169 | 11.6008 | 11.8726 | 11.7724 | 11.5491 | 10.8426 | 10.3468 | 10.6104 | 10.0053 | 8.6186 | 6.7357 | 4.9541 | 4.1023 | 3.5908 | 3.9745 | 7.0684 | 15.3527 | 15.1468 | 12.823 | 12.7829 | 15.0955 | 16.9883 | 17.2822 | 25.521 | 38.9519 | 43.241 | 38.1146 | 34.1673 | 39.6693 | 67.6929 | 87.0415 | 97.2576 | 87.8328 | 54.2009 | 32.8516 | 32.9163 | 29.9039 | 31.2154 | 46.3931 | 56.4313 | 48.7384 | 41.4475 | 49.9599 | 48.2227 | 59.3488 | 71.0528 | 78.3587 | 74.8815
handover (6,-0.5)t1 | 11.7049 | 10.9688 | 10.6519 | 10.9977 | 10.9356 | 11.1325 | 11.1222 | 10.7404 | 10.3846 | 9.5386 | 8.2047 | 5.9417 | 3.9945 | 3.017 | 3.2637 | 4.1069 | 11.3434 | 15.1495 | 16.7884 | 17.9342 | 20.6176 | 23.829 | 20.1733 | 16.4895 | 21.2908 | 31.849 | 38.0706 | 32.6891 | 34.0046 | 46.3091 | 67.2594 | 76.1777 | 68.3094 | 62.5175 | 65.1443 | 64.1394 | 60.9572 | 53.7271 | 42.3602 | 33.9836 | 24.4856 | 21.7104 | 18.285 | 29.8991 | 44.6771 | 57.5783 | 67.8726 | 55.5353
Chart: Confederate Av.
| 39141.708328703702 | 39141.718745312501 | 39141.729161921299 | 39141.739578530091 | 39141.749995138889 | 39141.760411747688 | 39141.770828356479 | 39141.781244965277 | 39141.791661574076 | 39141.802078182867 | 39141.812494791666 | 39141.822911400464 | 39141.833328009256 | 39141.843744618054 | 39141.854161226853 | 39141.864577835651 | 39141.874994444443 | 39141.885411053241 | 39141.89582766204 | 39141.906244270831 | 39141.916666666664 | 39141.927083333336 | 39141.937500057873 | 39141.94791678241 | 39141.958333506947 | 39141.968750231485 | 39141.979166956022 | 39141.989583680559 | 39142.000000405096 | 39142.010417129626 | 39142.020833854163 | 39142.031250578701 | 39142.041667303238 | 39142.052084027775 | 39142.062500752312 | 39142.072917476849 | 39142.083334201387 | 39142.093750925924 | 39142.104167650461 | 39142.114584374998 | 39142.125001099535 | 39142.135417824073 | 39142.14583454861 | 39142.156251273147 | 39142.166667997684 | 39142.177084722221 | 39142.187501446759 | 39142.197918171296
Observations | 4.8 | 5.5 | 5.7 | 4.6 | 5.5 | 12.5 | 29.3 | 135 | 148.9 | 132.5 | 50.8
global | 11.7564 | 11.2594 | 10.9687 | 10.8164 | 10.6796 | 9.3784 | 8.0932 | 6.7522 | 5.431 | 3.925 | 2.8916 | 3.1385 | 3.1253 | 6.7244 | 15.3873 | 14.4397 | 8.7541 | 10.0815 | 11.0639 | 14.347 | 13.4808 | 12.1073 | 19.4531 | 27.253 | 24.4186 | 20.5412 | 23.1596 | 41.6387 | 73.799 | 87.8574 | 85.7403 | 63.2237 | 30.3169 | 18.6097 | 17.9117 | 22.9333 | 28.0119 | 47.6349 | 52.1426 | 50.024 | 42.0634 | 44.9295 | 42.8018 | 54.1963 | 63.0427 | 71.5166 | 71.7174 | 44.8732
output | 10.232 | 9.8715 | 9.4051 | 9.8427 | 10.4242 | 10.6758 | 9.7867 | 8.5676 | 7.2421 | 5.369 | 3.4413 | 3.6669 | 3.2361 | 3.9918 | 10.2585 | 13.1326 | 16.4432 | 17.8128 | 14.9948 | 18.7939 | 16.7688 | 7.3897 | 8.0682 | 15.7262 | 26.3534 | 24.2136 | 22.6699 | 28.352 | 47.2156 | 55.4217 | 64.9051 | 55.0888 | 51.6611 | 56.3335 | 53.0109 | 48.0274 | 42.3964 | 31.2841 | 25.3275 | 19.7141 | 14.9575 | 13.4499 | 20.8299 | 55.8519 | 64.6522 | 67.2147 | 53.6668 | 29.903

## Slide 11: Plume modeling criteria
Uniform | vs | Adaptive grid
All layer adaption | vs | Surface layer adaption
Colum Injection | vs | Handover
Global time step handover | vs | Output time step handover

## Slide 12: Adaptive grid weight function
Notes: If e1 is negative then smaller cells will be weighted more than larger cells and vice versa.
Thus, choosing e1 to be negative may cause smooth flow features to be under-resolved.
The parameter e2 ¸ 0 provides control over the rate of change of the cell volumes in the
grid. If e2 > 0 then evacuation of grid nodes from regions of uniform concentration will
be inhibited and grid orthogonality will be promoted.
number of smoothing iterations=15?

## Slide 13: Areal adaptation: e1
Chart: 
| 0 | -0.2 | -0.3
mean fractional error | 0.72074 | 0.7576 | 0.75505
Smoothing factor: NSMTH
Chart: Mean fractional error
| 9 | 7 | 6
Mean Fractional Error | 0.75354 | 0.75505 | 0.77031
Chart: NSMTH
| 5 | 6 | 6 | 6 | 8 | 8
 | -0.5 | -0.6 | -0.3 | -0.5 | -0.5 | 0
Mean Fractional Error
Smaller cells weighted more
C reduced

## Slide 14
Chart: Jefferson St.
| 39141.708328703702 | 39141.718745312501 | 39141.729161921299 | 39141.739578530091 | 39141.749995138889 | 39141.760411747688 | 39141.770828356479 | 39141.781244965277 | 39141.791661574076 | 39141.802078182867 | 39141.812494791666 | 39141.822911400464 | 39141.833328009256 | 39141.843744618054 | 39141.854161226853 | 39141.864577835651 | 39141.874994444443 | 39141.885411053241 | 39141.89582766204 | 39141.906244270831 | 39141.916666666664 | 39141.927083333336 | 39141.937500057873 | 39141.94791678241 | 39141.958333506947 | 39141.968750231485 | 39141.979166956022 | 39141.989583680559 | 39142.000000405096 | 39142.010417129626 | 39142.020833854163 | 39142.031250578701 | 39142.041667303238 | 39142.052084027775 | 39142.062500752312 | 39142.072917476849 | 39142.083334201387 | 39142.093750925924 | 39142.104167650461 | 39142.114584374998 | 39142.125001099535 | 39142.135417824073 | 39142.14583454861 | 39142.156251273147 | 39142.166667997684 | 39142.177084722221 | 39142.187501446759 | 39142.197918171296
handover (5,-0.5)t2 | 12.5716 | 11.7282 | 11.6125 | 12.2153 | 11.7451 | 11.5645 | 11.676 | 10.8989 | 10.1486 | 8.6016 | 6.7661 | 5.3748 | 3.7343 | 3.9109 | 6.2926 | 10.4955 | 10.967 | 8.9445 | 13.9348 | 16.2257 | 12.1043 | 16.99 | 25.0754 | 28.9763 | 29.1076 | 37.5826 | 40.7885 | 38.6701 | 51.3009 | 81.2931 | 104.2723 | 94.411 | 61.7245 | 31.2761 | 32.8562 | 31.3414 | 40.4189 | 46.2414 | 56.2905 | 52.9678 | 44.9023 | 44.2537 | 52.178 | 60.8227 | 68.6156 | 56.728 | 41.1429 | 25.8988
handover (6,-0.6)t2 | 12.6316 | 11.4521 | 11.771 | 11.8325 | 11.2634 | 12.2442 | 11.6078 | 10.7392 | 9.926 | 8.1898 | 6.2056 | 5.1257 | 3.6446 | 4.1073 | 5.5002 | 6.9113 | 6.993 | 6.8087 | 11.6432 | 15.6749 | 16.7596 | 20.9068 | 30.8909 | 41.5519 | 47.6612 | 42.7306 | 37.5527 | 34.2462 | 40.5854 | 56.4108 | 58.7569 | 46.0919 | 36.684 | 33.2209 | 35.8376 | 39.9044 | 33.5167 | 46.1722 | 48.3334 | 47.3877 | 29.4428 | 33.2034 | 43.4459 | 47.1802 | 56.4645 | 55.5365 | 46.0115 | 31.0068
Observations | 4.1701 | 4.5241 | 3.0306 | 3.2157 | 5.3026 | 21.6223 | 71.9073 | 139.6525 | 98.2379 | 60.9217 | 26.475 | 15.6088
handover (6,-0.5)t2 | 12.3779 | 11.889 | 12.0791 | 12.057 | 11.704 | 10.9775 | 10.0757 | 9.6026 | 9.404 | 8.152 | 5.9841 | 4.5483 | 3.8451 | 5.0837 | 5.8617 | 15.0453 | 18.3968 | 14.6618 | 12.9259 | 13.196 | 16.3253 | 15.2197 | 19.4441 | 28.5664 | 38.7921 | 37.6994 | 32.5181 | 33.7941 | 47.6355 | 74.5334 | 90.403 | 97.155 | 75.7641 | 42.0865 | 29.1593 | 32.0905 | 28.3271 | 37.2881 | 52.2259 | 57.3452 | 45.0239 | 44.7442 | 49.0977 | 48.6124 | 61.3782 | 69.9476 | 78.3424 | 67.8171
handover (6,-0.5)t1 | 11.9267 | 11.5258 | 10.7879 | 11.1424 | 11.3043 | 11.3185 | 11.2576 | 10.575 | 9.8576 | 9.2752 | 7.1354 | 5.1013 | 3.9404 | 3.2391 | 4.4795 | 8.5945 | 15.7217 | 18.8816 | 19.3375 | 20.8517 | 22.7366 | 22.3133 | 14.6287 | 15.6106 | 24.5234 | 33.5134 | 36.6607 | 31.9409 | 36.5848 | 55.6842 | 69.2577 | 77.2863 | 65.1596 | 61.6604 | 63.2056 | 60.2237 | 56.5911 | 48.6827 | 38.5569 | 32.3595 | 22.408 | 21.2875 | 18.5282 | 36.334 | 51.5605 | 62.6269 | 66.44 | 49.916
handover (6,-0.3)t2 | 11.6203 | 11.8555 | 12.1795 | 11.7067 | 11.402 | 11.4111 | 11.6302 | 11.3441 | 10.3736 | 9.0974 | 6.8471 | 5.2589 | 3.7424 | 4.8531 | 4.9628 | 9.7506 | 12.2793 | 13.0957 | 15.5728 | 13.9519 | 10.4872 | 16.4038 | 26.9346 | 34.9181 | 37.7083 | 36.6818 | 36.698 | 38.3912 | 41.1274 | 66.9047 | 82.3243 | 73.1967 | 55.1721 | 48.5982 | 44.0514 | 37.3247 | 32.1799 | 37.2835 | 35.1668 | 39.2853 | 48.9021 | 47.6518 | 40.7377 | 43.5812 | 41.1859 | 34.1419 | 24.2197 | 18.906
Chart: McDonough
| 39141.708328703702 | 39141.718745312501 | 39141.729161921299 | 39141.739578530091 | 39141.749995138889 | 39141.760411747688 | 39141.770828356479 | 39141.781244965277 | 39141.791661574076 | 39141.802078182867 | 39141.812494791666 | 39141.822911400464 | 39141.833328009256 | 39141.843744618054 | 39141.854161226853 | 39141.864577835651 | 39141.874994444443 | 39141.885411053241 | 39141.89582766204 | 39141.906244270831 | 39141.916666666664 | 39141.927083333336 | 39141.937500057873 | 39141.94791678241 | 39141.958333506947 | 39141.968750231485 | 39141.979166956022 | 39141.989583680559 | 39142.000000405096 | 39142.010417129626 | 39142.020833854163 | 39142.031250578701 | 39142.041667303238 | 39142.052084027775 | 39142.062500752312 | 39142.072917476849 | 39142.083334201387 | 39142.093750925924 | 39142.104167650461 | 39142.114584374998 | 39142.125001099535 | 39142.135417824073 | 39142.14583454861 | 39142.156251273147 | 39142.166667997684 | 39142.177084722221 | 39142.187501446759 | 39142.197918171296
handover (5,-0.5)t2 | 4.1943 | 3.7405 | 2.5227 | 1.3338 | 0.88718 | 2.2702 | 7.6337 | 13.2197 | 24.2233 | 28.0763 | 15.2596 | 9.0723 | 6.1018 | 2.8354 | 5.4851 | 10.3046 | 10.0256 | 4.3995 | 2.646 | 41.4869 | 145.9043 | 124.7483 | 40.9841 | 19.527 | 10.163 | 26.3305 | 35.0235 | 22.6114 | 9.5737 | 6.8259 | 18.7159 | 26.9202 | 49.473 | 43.3917 | 26.0476 | 29.6437 | 49.3657 | 81.6034 | 85.0751 | 83.7718 | 74.8924 | 68.1162 | 36.21 | 22.2219 | 16.456 | 7.2467 | 7.8888 | 9.4438
handover (6,-0.6)t2 | 4.5981 | 3.5914 | 2.2832 | 1.3217 | 0.9253 | 1.6169 | 7.311 | 8.1768 | 18.7532 | 19.5887 | 10.5724 | 8.9069 | 5.9881 | 4.4791 | 7.5624 | 13.126 | 13.9016 | 12.8421 | 11.1136 | 10.4686 | 16.7065 | 43.0433 | 48.7925 | 33.818 | 29.5227 | 21.2929 | 9.1924 | 5.6652 | 11.7899 | 22.0235 | 49.2829 | 66.0771 | 84.2273 | 82.1665 | 58.4256 | 29.1282 | 34.6958 | 93.0624 | 130.5086 | 123.3608 | 81.235 | 65.2971 | 33.1373 | 22.5369 | 15.152 | 7.261 | 6.0947 | 9.0126
Observations | 3.9 | 2.4 | 4.1 | 26.9 | 33.3 | 151.7 | 101.8 | 39.3 | 32.4 | 38.4 | 47 | 87.6
handover (6,-0.5)t2 | 4.6423 | 3.6862 | 2.1777 | 1.2133 | 0.82365 | 2.7999 | 12.9253 | 24.5892 | 29.5061 | 28.0232 | 12.7281 | 7.4223 | 6.7245 | 6.6713 | 4.6241 | 4.078 | 5.5218 | 17.1541 | 15.0459 | 30.9895 | 95.2211 | 120.4827 | 65.0487 | 30.0054 | 11.728 | 8.1072 | 20.4521 | 42.9429 | 26.5352 | 10.6959 | 9.716 | 19.248 | 29.3639 | 82.809 | 76.6355 | 46.9612 | 23.798 | 20.2477 | 44.2815 | 61.9993 | 63.0815 | 63.4503 | 88.4979 | 60.0484 | 44.0167 | 29.5062 | 11.8072 | 8.181
handover (6,-0.3)t2 | 4.1408 | 3.2633 | 2.4279 | 1.4852 | 0.91224 | 1.2274 | 9.2556 | 26.8839 | 40.9879 | 34.6788 | 14.5206 | 8.7973 | 4.0521 | 3.2016 | 7.7963 | 9.6895 | 11.4093 | 11.2816 | 11.252 | 17.7906 | 20.103 | 23.2277 | 63.2241 | 118.244 | 107.5618 | 36.5885 | 16.1298 | 16.6556 | 40.6741 | 41.3233 | 39.3573 | 48.4717 | 49.9137 | 44.9697 | 25.8351 | 21.0685 | 37.378 | 50.8184 | 45.9602 | 57.2039 | 106.4622 | 101.3252 | 74.7988 | 43.4196 | 20.5236 | 11.8291 | 14.0404 | 12.596
handover (6,-0.5)t1 | 4.2462 | 4.2214 | 3.18 | 1.5462 | 0.8263 | 1.4911 | 11.8883 | 17.9039 | 34.2471 | 28.9561 | 19.4783 | 11.4963 | 9.2724 | 6.6419 | 8.5001 | 4.8438 | 2.3866 | 3.969 | 10.5445 | 40.1091 | 94.0845 | 95.7927 | 51.963 | 26.5034 | 20.092 | 13.7099 | 13.744 | 23.4663 | 47.6514 | 65.7167 | 82.919 | 63.25 | 38.3602 | 24.6054 | 22.4805 | 17.1937 | 15.6207 | 13.4228 | 17.8931 | 30.0117 | 72.9959 | 158.5882 | 169.9509 | 107.4851 | 41.7388 | 14.2099 | 6.1665 | 6.1733

## Slide 15: Judging criteria
Normalized Mean Error (%)
Mean Fractional Error (%)
Peak Ratio (%)
Mass Ratio (%)

## Slide 16: Error analysis (NSMTH,e1)
Chart: 
| mass ratio difference | peak ratio difference | Normalized mean fractional error | Normalized abs. mean error
handover (5,-0.5)t2 | 0.34063 | 0.16223 | 0.37987 | 0.2476
handover (6,-0.5)t2 | 0.20128 | 0.36134 | 0.35578 | 0.18402
handover (6,-0.6)t2 | 0.68468 | 0.93227 | 0.66537 | 0.80642
handover (6,-0.3)t2 | 0.60818 | 0.66799 | 0.40903 | 0.43539
handover (8,-0.5)t2 | 0.42565 | 0.26207 | 0.48795 | 0.39233
handover (8,0)t2 | 0.46325 | 0.56154 | 0.38006 | 0.18506

## Slide 17: NSMTH=6, e1=-0.5 using global time step handover analysis with adaptive grid CMAQ models this burn case plume the best.
Chart: Combined Error Analysis
| handover (6,-0.5)t2 | handover (5,-0.5)t2 | handover (8,-0.5)t2 | handover (8,0)t2 | handover (6,-0.5)t1 | handover (6,-0.3)t2 | handover (6,-0.6)t2 | handover (8,-0.3) t1
 | 0.2946 | 0.3099 | 0.60558 | 0.60641 | 0.76518 | 1.108 | 2.3698 | 2.8369

## Slide 18: Summary
Boundary between sub grid model to CMAQ should be determined by analysis on error due to unresolved plume concentration
Optimal parameters for grid adaptation were determined for prescribed burning plumes
Similar analysis to be done for other burn cases

## Slide 19: Acknowledgements
Strategic Environmental Research and Development Program
Joint Fire Science Program
Georgia Department of Natural Resources, Environmental Protection Division
US Forest Service, Southern Research Station

## Slide 20
Chart: handover (5,-0.5)t2
ideal | 0 | 140

## Slide 21: Adaptive Grid