## Slide 1: A Computationally Efficient Model For Estimating Background Concentrations of NOx, NO2, and O3
Sam Pournazeri, Si Tan, Nico Schulte, Qiguo Jing, Akula Venkatram
Department of Mechanical Engineering
University of California, Riverside
12th Annual CMAS Conference
Oct 28th – 30th, 2013, Chapel Hill, NC

## Slide 2: Acknowledgements
Vlad Isakov (US EPA)
Marla Mueller (CEC)
CMAS Conference Committee
CEC 500-08-055

## Slide 3: Motivation
Hybrid Modeling:
Combine regional long-range transport model with short-range transport model
(Isakov et al, 2007) (Stein et al, 2007) (Isakov et al, 2009) and etc.
(Stein et al, 2007)
Notes: Part of Hybrid Model Project-impact of DG
Human exposure need concentration at small scale—total concentration are affected by multiple scales
Pioneered by Isakov

## Slide 4: Introduction
Exposure Studies: (1) need high resolution concentration map
(2) long averaging periods
Comprehensive Models:
computationally cumbersome
Land Use Regression (LUR) Model:
cannot be used to estimate the impact of changes in emissions on concentrations
performance is highly dependent on the measured data
(Jensen et al., 2009)

## Slide 5: Introduction
We need a model that:
Connects concentrations explicitly to emissions and meteorology
(2) Computationally convenient for long-term exposure studies
Urban Background Model (UBM) (Berkowicz, 2000)
straight-line steady dispersion model
Photo-stationary ozone chemistry
Notes: (1) UBM does not account for the effect of VOCs

## Slide 6
zi
5 km
5 km
C
q
Lagrangian Background Model (LBM)
Transport and Chemistry are separated to reduce computational time using average species age
Start
Area of Interest
(Venkatram et al, 1994)
(Venkatram et al, 1998)
Notes: Comprehensive model solve transport and chemistry separately-computationally expensive
We separate transport and chemistry through species age
Dimension of Box
Uniform concentration
Chemistry calculated after Transport
The concept is not new

## Slide 7: Model Formulation
(1) Transport Calculation
Back Trajectory
Concentration calculation
(2) Average Species Age
(3) Chemistry Simulation
Notes: the 3 major step involved in the LBM model

## Slide 8: Transport-Back Trajectory calculated using surface wind speed and direction
Notes: (1) The trajectory is calculated for the past 24 hours in1-hr time steps.

## Slide 9: Transport-Concentration Calculation
Concentration:
Hour 1-23:
(1)
Last Hour:
(2)
(Venkatram and Cimorelli, 2007)
zi-1
5 km
5 km
Ci-1
qi-1
zi
5 km
5 km
Ci
qi
Where Ci = concentration at the current hour
Ci-1 = concentration at previous hour
zi = Boundary layer height at the current hour
zi-1 = Boundary layer height at the current hour
∆mi = mass of pollutant injected into the air parcel
h =initial vertical spread of surface emissions ~ 1 m
q = emission [g/s∙m2]
= time interval
= vertical plume spread
Notes: (1) Last Hour-account for incomplete vertical mixing

## Slide 10: Average Species Age: The average time that the species undergo chemical reactions
(3)
Where Ai = average species age at the current hour
Ai-1 = average species age at previous hour
∆mi = mass of pollutant injected into the air parcel
mi = total mass of pollutant in the air parcel
(Venkatram, 1988)
Notes: (1)No fresh emission-A increases by dt
(2) Fresh emission tend too decrease A

## Slide 11: Chemistry Scheme
Carbon Bond IV (CB-IV)
Generic Reaction Set (GRS)
(Azzi, 1992)
Comparison of GRS and CB-IV
Annual Averaged Hourly O3 Concentration
Notes: (1) GRS-7 empirically determined equation to approximate O3 formation-include VOC
(2) LBM not tied to GRS-can use chemistry scheme of preference

## Slide 12: Model Overview
Notes: input: hourly NOx emission, wind speed, wind direction, and mix layer height
Output: hourly NOx, NO2, and O3 concentration

## Slide 13: Evaluations of LBM

## Slide 14
The San Joaquin Valley Air Basin
The South Coast Air Basin
South Coast
San Joaquin Valley
Observation Database
Contains 21 monitoring stations
Contains 21 monitoring stations

## Slide 15: The South Coast Air Basin (SoCAB)
Gridded Daily Average NOx Emission
Emission Temporal Profile
Notes: (1) No hourly NOx emission available
(1) two peaks corresponding to the rush hours.

## Slide 16: Annual Average Concentration
NOx
NO2
Notes: (1) Hourly Data ran for a whole year at 21 sites
(2) LBM implemented in MatLab—took 2 ½ hours to run
(3) Model performs adequately—most data within factor of 2

## Slide 17: Seasonal Variation
West LA
San Bernardino
NOx
NOx
NO2
NO2
West LA
San Bernardino
Notes: (1) West LA and San Bernardino has different trajectory
(2) LBM is able to capture seasonal variation

## Slide 18: The San Joaquin Valley Air Basin
Gridded Daily Average NOx Emission
Notes: Long narrow bowl shape-trap pollution
Majority of Emission from large cities and roads

## Slide 19: Annual Average Concentration
NOx
NO2
O3

## Slide 20: Seasonal Variation
Bakersfield
Shafter
NOx
NOx
O3
NO2
NO2
O3
Bakersfield
Shafter
Notes: Shafter - 16miles (26 kilometers) northwest of Bakersfield, and is surrounded by rural areas
LBM is able to capture the seasonal variation of NOx, NO2, and O3 at both locations.

## Slide 21: Applications of LBM
Notes: Through the evaluation of LBM model performance in the two air basin, we can conclude that LBM indeed produces good result.
Now lets look at some of the applications of LBM

## Slide 22: Estimate O3 Episode
SoCAB-Azusa
SJVAB-Fresno
Notes: O3 episodes during September 1 - 4, 2007 in Azusa in the SoCAB (upper panel) and July 14 - 17, 2005 in Fresno in the SJVAB (lower panel)
Figure shows that for the O3 episode in the SoCAB, the modeled concentrations are in good agreement with the observed concentrations. In Fresno, the model overestimated the maximum O3 concentration on July 14, and the model predicted a faster O3 destruction rate at nighttime, which could be related to the uncertainties in estimating the nighttime boundary height and the emission.

## Slide 23: Improving Kriging Interpolation Using LBM for Exposure Studies
Simple Kriging
Residual Kriging
Residual Kriging: residuals between model estimate and observation are interpolated using residuals at the observation sites
Notes: Kriging is commonly used
LBM improves the concentration map

## Slide 24: Conclusions
Computational time is greatly reduced
The model can reasonably estimate maximum O3 concentrations.
Model provides adequate descriptions of the spatial and temporal behaviour of NOx and NO2 measurements made in SoCAB during 2007, and in SJVAB during 2005
Model is good for exposure studies

## Slide 25: Thank You! Questions?
References:
Azzi, M., Johnson, G.M., Cope, M., 1992. An introduction to the generic reaction set photochemical smog mechanism. Proceedings of the 11th International Conference of Clean Air Soc. of Aust. and N.Z., Brisbane. 451-462.
Berkowicz, R., 2000. A Simple Model for Urban Background Pollution. Environmental Monitoring and Assessment. 65, 259-267.
Isakov, V., Touma, J.S., Burke, J., Lobdell, D.T., Palma, T., Rosenbaum, A., kÖzkaynak, H., 2009. Combining Regional- and Local-Scale Air Quality Models with Exposure Models for Use in Environmental Health Studies. Journal of the Air & Waste Management Association 59, 461-472.
Isakov, V., Irwin, J.S., Ching, J., 2007. Using CMAQ for Exposure Modeling and Characterizing the Subgrid Variability for Exposure Estimates. Journal of Applied Meteorology and Climatology 46, 1354-1371.
Jensen, S. S., Larson, T., Deepti, K. C., Kaufman, J. D., 2009. Modeling traffic air pollution in street canyons in New York City for intra-urban exposure assessment in the US Multi-Ethnic Study of atherosclerosis and air pollution. Atmospheric Environment. 43(30), 4544-4556.
Stein, A.F., Isakov, V., Godowitch, J., Draxler, R.R., 2007. A hybrid modeling approach to resolve pollutant concentrations in an urban area. Atmospheric Environment 41, 9410-9426.
Venkatram, A., Du, S., Hariharan, R., Carter, W., Goldstein, R., 1998. The concept of species age in photochemical modeling. Atmospheric Environment. 32, 3403-3413.
Venkatram, A., Karamchandani, P., Pai, P., Goldstein, R., 1994. The development and application of a simplified ozone modeling system (SOMS). Atmospheric Environment 28, 3665-3678.
Venkatram, A., Du, S., Hariharan, R., Carter, W., Goldstein, R., 1998. The concept of species age in photochemical modeling. Atmospheric Environment 32, 3403-3413.