## Slide 1: Toward the integration of air quality and climate strategies at the state level
Daniel Cohan
CMAS Conference
October 29, 2014

## Slide 2: Air quality and greenhouse gas challenges at the state level
Ozone attainment
  Possible tighter NAAQS in December
PM attainment
Clean Power Plan would require states to meet power plant CO2 targets for first time
Opportunities to integrate across these challenges?

## Slide 3: Ozone and PM Non-attainment

## Slide 4: Lessons learned from ozone and PM SIPs (Pegues et al., 2012; Cohan and Chen, 2014)
Modeled attainment test performed well
Lack of integration across ozone and PM SIPs
  Different regional boundaries and deadlines
  Most ozone plans did not consider impact of their NOx and VOC controls on PM
Health benefits not quantified
Costs and emissions reductions not always quantified on measure-by-measure basis

## Slide 5: Performance of Ozone SIP Model Predictions
Chart: 2009 Observed Ozone DV (ppb)
| 80 | 77 | 86 | 79 | 86 | 87 | 85
Atlanta, GA | 81 | 77 | 82 | 80 | 86 | 80 | 79
Baltimore, MD | 84 | 77 | 80 | 75 | 85 | 82
Boston-Lawrence-Worcester (E. Mass), MA | 80 | 79 | 82 | 74 | 82 | 66 | 72
Charlotte-Gastonia-Rock Hill, NC-SC | 78 | 84 | 75 | 85 | 83 | 84 | 76
Cleveland-Akron-Lorain, OH | 82.8 | 88.8 | 82.9 | 79.4
Dallas-Fort Worth, TX | 88.7 | 84.8 | 78.8 | 88.6 | 83.9 | 85.6 | 84.8 | 80.9
New York-N. New Jersey-Long Island,NY-NJ-CT | 77 | 83 | 83 | 84 | 84 | 77 | 87 | 85 | 90 | 85 | 84 | 88 | 69 | 74 | 84 | 85 | 74 | 85
Philadelphia-Wilmin-Atlantic Ci,PA-NJ-MD-DE | 78 | 77 | 77 | 76 | 81 | 88 | 79 | 79 | 81 | 65 | 87 | 87 | 81 | 86 | 92
Poughkeepsie, NY | 80 | 73 | 81
Providence (All RI), RI | 80 | 77 | 81
Springfield (Western MA), MA | 65 | 75
Washington, DC-MD-VA | 79 | 78 | 81 | 75 | 73 | 81 | 86 | 75 | 85 | 83 | 82 | 77 | 78 | 74 | 79
Pegues et al., JA&WMA 2012

## Slide 6: Performance of PM2.5 SIP model predictions
Chart: OBSERVED pm2.5 dV, 2009
| 14.1 | 13.3 | 12.8 | 12.7 | 12.5 | 12.1 | 12.5 | 12.5 | 12.8 | 12.9 | 12.7 | 11.4 | 13.1
MO | 15.53 | 14.54 | 13.62 | 13.42 | 13.1 | 12.7 | 13.09 | 12.99 | 13.29 | 12.91 | 12.54 | 10.94 | 12.59
IN | 14.4 | 12.2 | 13.2 | 13.9 | 13.6 | 12.4 | 14.6 | 11.7 | 12.5 | 12.9 | 13.3 | 13 | 13.3 | 13.2 | 12.7 | 12.8 | 12.7 | 12.8 | 12.4 | 12.1 | 12.7 | 12.1 | 11.6 | 11.2 | 11.8 | 11.8
NJ | 15.3 | 14.1 | 14.2 | 12.5 | 13.3 | 14 | 11.8 | 12.6 | 12.3 | 12.4 | 14.3 | 13.9 | 13.7 | 13.5 | 12.9 | 13 | 12.8 | 12.6 | 12 | 12.9 | 13.3 | 13.3 | 12.4 | 11.9 | 12 | 11.8 | 11.8 | 11.4 | 11.7 | 12.1 | 11.5 | 11.4 | 11.4 | 11.3 | 11.2 | 11.2 | 11.8 | 11.8 | 10.8 | 10.4 | 10.4 | 10.4 | 10.4 | 10.1 | 10.2 | 9.3 | 10.6
KY | 14.8 | 14.2 | 13.6 | 13.1 | 12.8 | 12.7
CT | 15.3 | 14.4 | 14.2 | 14.3 | 12.4 | 14.3 | 13.5 | 13.3 | 13.3 | 13.3 | 13.3 | 12.3 | 11.8 | 11.4 | 11.7 | 12.1 | 11.5 | 11.4 | 11.3 | 11.2 | 11.2 | 11.8 | 12.1 | 10.9 | 10.4 | 11 | 10.6 | 10.4 | 10.4 | 10.1 | 10.3 | 9.3 | 10.7
GA | 14.4 | 13.6 | 12.3 | 13.9 | 14.3 | 12.5 | 14
NC | 13.1 | 13.4 | 11.5
MD | 13.8 | 13.8 | 14.4 | 13 | 13.2 | 11.9 | 12.9 | 12.6 | 11.5 | 12.4 | 10.7 | 12.1 | 11.8 | 10.5 | 10.1 | 10.4 | 11.2 | 11.3 | 10.4 | 10.4
LADCO | 14.1 | 14.4 | 13.9 | 13.8 | 13.7 | 14.2 | 14.4 | 15.1 | 14.1 | 13.8 | 12.4 | 12.8 | 13.4 | 13 | 14.2 | 13.1 | 15.8 | 13.1 | 13.5 | 13.1 | 13.5 | 15.2 | 14.4 | 15 | 14 | 12.9 | 12.7 | 11.7 | 14.5 | 12.8 | 14 | 12.9 | 13.4 | 14.7 | 12.8 | 13.5 | 12.8 | 13.2 | 12.1 | 14 | 12.6 | 13 | 12.3
PA | 12.6 | 11.3 | 12.6 | 13.3 | 12.3 | 12.3 | 12.1 | 12.4 | 13.3 | 11.3 | 12.9 | 11.9 | 13.5 | 12.7 | 13.3 | 11.3 | 11.8 | 12.2 | 13.5 | 14.3 | 13.6 | 13 | 12.7 | 11.6 | 13
Cohan and Chen, JA&WMA 2014

## Slide 7: Cost and benefit quantification in ozone SIPs
Pegues et al., 2012

## Slide 8: US EPA Proposed Clean Power Plan
30% reduction in power plant CO2 nationally by 2030 from 2005 levels
  Interim standard for 2020-2029
Target for each state, or share across states
Flexibility for efficiency, demand reduction, renewables, fuel switching, carbon capture
State plans would be due June 30, 2016
  Can add 1-2 years to finalize commitments
  Ozone SIPs due in 2015; later if new NAAQS

## Slide 9: Projected impact of Clean Power Plan on CO2 and Electricity Generation
Brattle Group based on EPA RIA and EIA data

## Slide 10: EPA projections of how states might meet Clean Power Plan standards
Brattle Group

## Slide 11: Implications of state Clean Power Plan choices for air quality and health
EPA projects 2700-6600 premature deaths, 140-150k asthma attacks averted annually
Actual impacts depend on how targets are met
  Nuclear, renewables, and reduced demand would nearly eliminate offset coal emissions
  Natural gas would avert SO2, reduce NOx
  Heat rate improvements or carbon capture at coal plants might yield little air quality benefit
  Location of the averted coal emissions matters for attainment and health

## Slide 12: Challenges to integrating Clean Power Plan with ozone and PM SIPs
More than a dozen states have sued
Additional agencies involved: public utility commissions, energy agencies, grid operators
Different timelines and geographic scope
  CO2 controls likely to occur after NAAQS deadlines
Separate policy structures for control
  Ambient standards for criteria pollutants
  Emissions reduction targets for CO2
Lack of experience integrating AQ and ghg control

## Slide 13: Air quality co-benefits uncertain, can be comparable to climate benefits
*Nemet et al., 2010
Air quality co-benefits*: $49/tCO2 ($2-$196 depending on study)
Climate impact of CO2 reductions**: $43/tCO2 ($12-64 depending on discount rate)
**From US Interagency Working Group, for 2020 with 3% discount rate

## Slide 14: SO2 (PM) is expected to dominate health impact of Clean Power Plan
US EPA Regulatory Impact Analysis of Clean Power Plan, 2014

## Slide 15: CO2 and SO2 emission rates of coal-fired power plants not well correlated
Based on EGRID data for 2010

## Slide 16: Health impacts of SO2 control depend on location (adjoint modeling by D. Henze)
Daven Henze presentation to AQAST4

## Slide 17: Separate approaches to attainment
NOx and VOC control options
Ozone Attainment Modeling
Health Benefits Assessment
NOx, VOC, SO2, NH3, and PM control options
PM
Attainment Modeling
Power sector CO2 control options
Power
Sector
modeling
Health Benefits Assessment
Co-Benefits Assessment
Ozone NAAQS
PM NAAQS
Clean Power Plan

## Slide 18: Joint Attainment of NAAQS & Clean Power Plan
Jointly consider ozone, PM, and CO2 control options
AQ modeling of ozone and PM attainment
Health Benefits Assessment
Impacts inform strategy selection (Wesson et al 2010; Fann et al 2011)
Power sector modeling to inform strategy
Co-Benefits Assessment
Co-benefits inform strategy selection
Location-specific impacts influence strategies

## Slide 19: Integrating Clean Power Plan with NAAQS Attainment
Atmospheric Modeling
Simulate impacts on ozone and PM via:
Scenario analyses
Decoupled direct method
Adjoint method
Energy Modeling
Heat rate, new source, and control options
Capacity investments
Dispatch modeling
Energy supply, demand, and prices
Problem Definition
Goals and Objectives
Constraints
Policy options to consider

## Slide 20: Defining the challenge
Objectives and constraints
  Attain Clean Power Plan at minimal cost?
    Quantify AQ and health co-benefits of chosen strategy
  Attain CO2, O3, and PM rules at minimal cost?
  Attain CO2, O3, and PM rules at optimal net benefits?
    Requires valuation of health benefits and CO2
    Consider upstream emissions?
Clean Power Plan policy scenarios
  Renewable portfolio standards?
  Efficiency programs?
  Cap-and-trade or emissions fees?
  Facility-by-facility approaches?
  State-by-state or multi-state?
Informed by location-specific impacts??

## Slide 21: Photochemical modeling approaches for simulating benefits of controls
Scenario modeling: Impact of set of scenarios
Decoupled direct method: Simulate impact of defined sources on all pollutants
Adjoint modeling: Simulate response of aggregate impact metric to all sources
Health benefits model: Link BenMAP or other tool to each of above to quantify impacts

## Slide 22: Energy modeling options: Integrated Planning Model
Used by EPA for RIA of Clean Power Plan
  Identified expected approach to compliance, with co-benefits quantified later
Multi-region, dynamic linear programming electric sector model
Proprietary model not readily available to states and others
  Efforts to develop alternative model

## Slide 24: NESCAUM approach to integrating GHG and air quality co-benefits (Applied with NYSERDA to New York)

## Slide 25: Integration of energy, photochemical, and health models to compute co-benefits (Thompson et al., Nature Climate Change 2014)
MIT US Regional Energy Policy Model
CAMx
BenMAP
SMOKE
Economy-wide cap and trade (CAT) achieved lower costs (and thus higher co-benefits per cost) than electricity (CES) or transportation (TRN) sector policies

## Slide 26: Linking ReEDS and RWGTM to simulate electricity sector scenarios
Regional Energy Development System
  Capacity expansion model developed by NREL
  Detailed representation of electricity generation, transmission, and renewable resources
  Projects cost-optimized electricity technologies to meet constraints every two years through 2050
Rice World Gas Trade Model
  Dynamic spatial general equilibrium model
  Optimizes resource extraction and capacity expansion
  Adapting to provide natural gas price supply curves to ReEDS for each region of United States

## Slide 27: Electricity modeling regions in ReEDS
NREL

## Slide 28: Previous applications of ReEDS to analyze impacts of RPS and CO2 cap
NREL, 2010

## Slide 29: Plan for ReEDS-RWGTM modeling
Simulate state-by-state and regional options under Clean Power Plan
  Cap-and-trade
  Renewable portfolio standard
  Demand-side measures
Simulate interactions between natural gas supply, prices, and exports and electric sector capacity expansions and deployment
Subsequent work to consider dispatch

## Slide 30: Conclusions
Clean Power Plan provides opportunities and challenges for achieving air quality co-benefits from CO2 reductions
Atmospheric models and energy systems models can inform strategy development
Choices for how to consider AQ co-benefits in state plans for Clean Power Plan
  Quantify impacts of Clean Power Plan approach?
  Inform selection of Clean Power Plan approach?
  Influence design of options?