## Slide 1: DISCOVER-AQ SJV surface measurements and initial comparisons with photochemical model simulations
Melinda Beaver1, Russell Long1, Jim Szykman1, Rachelle Duvall1, Kirk Baker1, James Kelly1, Andy Weinheimer2, David Knapp2, Denise Montzka2, Sally Pusede3, and Ron Cohen3
1- US EPA; RTP, NC
2 – National Center for Atmospheric Research; Boulder, CO
3- University of California; Berkeley, CA
CMAS Conference
October 29, 2014

## Slide 2
California currently has many counties violating the PM2.5 NAAQS
Many counties still projected to be nonattainment in the future
Challenges in California: complex terrain, large and diverse emissions sources
Motivation to study the San Joaquin Valley, CA

## Slide 3: DISCOVER-AQ 2013 – San Joaquin Valley, CA
Deriving Information on Surface Conditions from Column and Vertically Resolved Observations Relevant to Air Quality
Success of study relies on quality measurements of gas and particle species (and properties) aloft and at the surface
San Joaquin Valley study from 16 Jan – 06 Feb 2013
10 flight days/~170 spirals/~150 missed approaches = Huge database!
All data publically available at: http://www-air.larc.nasa.gov/cgi-bin/ArcView/discover-aq.ca-2013

## Slide 4
A brief look at PM2.5 episodes during the DISCOVER-AQ San Joaquin Valley, CA study
High PM2.5 concentrations valley-wide:
NH4NO3 was observed to account for ~half the PM2.5 mass in Fresno:
NH4NO3
organics
*(data from Zhang group, UC Davis)
*Grey lines indicate flight days
*(data from CARB and SJVAPCD sites)

## Slide 5
Supplemented surface monitoring sites in Visalia and Bakersfield with direct and more specific NO2 measurements
  How do direct and indirect NO2 measurement methods compare in near-roadway setting?
  How do the surface site measurements compare with the P3B missed approaches conducted at the airport?
An Evaluation of CMAQ’s ability to predict PM2.5 concentrations and precursor species.
  Objective is to combine routine observation data with non-routine measurements from field campaigns like DISCOVER-AQ to evaluate meteorological and photochemical model performance for periods of elevated PM2.5 in California.
EPA’s efforts in DISCOVER-AQ SJV:
Visalia

## Slide 6
EPA’s NO2 Methods Development
EPA’s current Federal Reference Method (FRM) determines NO2 indirectly by catalytically (thermally) converting NO2 to NO, and determining NO by chemiluminescence.
thermal
converter
NO + O3 rxn chamber
O3 generator
PMT
NO channel
NOx channel
Ambient air
Heated bed -chemiluminescence
“NO2” = NOx - NO
Advantages: long term data record exists; provides an NO measurement
Disadvantages: Interferences from higher oxides of nitrogen (more on next slide); indirect method

## Slide 7
FRM is subject to interferences from higher oxides of nitrogen (PANs or ANs).
During summer of 2011, in Baltimore, we observed the interference in the FRM monitor overpredicts by ~50% during the hours surrounding noon.
Difference is correlated with ozone  implies interference is related to photochemical activity.
FRM (ppb)
ΔNO2 = FRM_NO2 – photo_NO2
Baltimore, MD (July 2011)
Why evaluate EPA’s Method for NO2?

## Slide 8
EPA’s NO2 Methods Development
Photolysis cell
λ~ 400 nm
NO + O3 rxn chamber
O3 generator
PMT
NO channel
NOx channel
Ambient air
photolytic-
chemiluminescence
A recently designated Federal Equivalent Method (FEM) replaces the headed bed conversion cell with a photolysis cell. (NO2 + hv  NO + O; hv = 350-420 nm)
Advantages: more specific to NO2; provides an NO measurement
Disadvantages: non-unity conversion efficiency; still an indirect technique

## Slide 9
EPA’s NO2 Methods Development
Cavity Ring-Down Spectroscopy:
Commercial, direct, optical methods have recently become available and are being investigated.
Measurement based on light absorption at 405 or 450 nm.
Two methods based on a cavity-enhanced method have been designated as FEMs.
Advantages: direct method, fast (10 seconds)
Disadvantages: measures light absorption at 405 or 450 nm as NO2; no NO measurement
Gas Sample
τ0
τ
Laser or LED
PMT

## Slide 10
Visalia Municipal Airport (SJVAPCD site)
inlets ~35m from CA-99 (60,000 AADT); 17% heavy duty truck traffic
Thermal conversion, Photolytic conversion, and CRDS analyzers compared
Visalia, CA
EPA’s NO2 Methods Development

## Slide 11
Visalia Municipal Airport Results
21 days, 1 minute data
Overall, good agreement
More scatter between indirect methods than between direct and indirect. Why?
y = 1.03x-1.22
R2 = 0.88
y = 1.02x+0.95
R2 = 0.79

## Slide 12
Visalia Municipal Airport Results
Could the scatter be related to the NO mixing ratios?
|deltaNO|= absolute value of the difference between adjacent NO data points.

## Slide 13
 | fit | R2 | n
All points | y=1.0x+1.0 | 0.79 | 24,468
¦ΔNO¦ < 5ppb/min | y=1.0x+1.3 | 0.85 | 15,954
¦ΔNO¦ < 0.4ppb/min | y=0.99x+1.4 | 0.90 | 7,900
Visalia Municipal Airport Results
Under conditions with slowly changing NO, less scatter between the two indirect methods.
The comparison between the direct and FRM analyzers doesn’t depend on the NO concentrations.
Hypothesis: the NO2 concentrations are affected by the switching between the NO and NOx channels during quickly changing NO distributions.

## Slide 14
Visalia Municipal Airport Results
Did we see any interference in the FRM NO2 measurement from higher oxides of nitrogen during the SJV deployment?
~ 5% during midday hours

## Slide 15
Ground site data compared with P3B Missed Approaches
Radar altitude during missed approaches between 30-40 m AGL.
On January 22, 2013, surface and P3B NO2 and O3 were in good agreement.

## Slide 16
Ground site data compared with P3B Missed Approaches
Radar altitude during missed approaches ~35 m AGL.
On February 1, 2013, surface and P3B NO2 and O3 were in good agreement during 2 of 3 missed approaches.
Elevated surface NO2 was observed on the first missed approach of the day (~10:00 local time)
The sum of NO2 and O3 were in good agreement during all 3 missed approaches.

## Slide 17
21 Missed Approaches with concurrent surface and P3 data
Median altitude of missed approaches = 35 m
Surface monitors observed higher NO2 than P3 on Feb04, Feb01, Jan30, and Jan18
Ground site data compared with P3B Missed Approaches

## Slide 18
Ground site data compared with P3B Missed Approaches

## Slide 19
Model/Observation Comparison at Visalia: NOx

## Slide 20
Model/Observation Comparison at Fresno: PM components

## Slide 21: Source Apportionment of PM2.5 Ammonium Nitrate using CMAQ
Contribution of onroad NOX emissions to modeled NOX mixing ratios
Contribution of onroad NOX emissions to modeled PM2.5 nitrate ion conc.

## Slide 22
Differences amongst NO2 monitoring methods were observed at the near-roadway, and these differences are the most pronounced under conditions with rapidly changing NOx distributions.
Direct optical methods are preferable to the indirect methods in these locations.
NOz Interferences in the FRM were <10% at the Visalia site.
Good agreement between (NO2+O3)surface and (NO2+O3)P3B at all missed approaches over the Visalia Airport.
Despite the low altitudes of these missed approaches (~35m), ozone titration events were observed during ~20% of the missed approaches.
We are conducting model evaluations using the DISCOVER-AQ dataset along with CMAQ source apportionment tools to better understand PM formation and improve emissions in California’s San Joaquin Valley.
Conclusions

## Slide 23
Acknowledgements
NASA (Jim Crawford, Ken Pickering, Mary Kleb, Luci Crittenden)
SJVAPCD (Nathan Trevino)
City of Visalia (Mark Bettencourt)
MDE (Jennifer Hains, Ryan Auvil)
DISCLAIMER – Although this work was reviewed by EPA and approved for presentation, it may not necessarily reflect official Agency policy.

## Slide 25
Modeled Jan and Feb 2013 to match DISCOVER-AQ field intensive in San Joaquin Valley
CMAQ v5.0.2
SAPRC07 gas-phase chemistry
ISORROPIA2 inorganic chemistry
4 km resolution domain (right)
35 vertical layers
2013 EGU (and fires)
2011 NEI v1 based emissions for all other sectors
BEIS v3.14 biogenic emissions
WRF v3.5.1 meteorology

## Slide 26
Ground site data compared with P3B Missed Approaches

## Slide 27
Bakersfield Municipal Airport Results
y = 1.05x-1.4
R2 = 0.86

## Slide 28: Working towards improved NH3 emissions
Average daily total NH3 emissions in SJV are similar for CARB and EPA inventories (left)
Spatial allocation of NH3 emissions differs in SJV: CARB’s emissions are more concentrated in major source regions than EPA’s (right)

## Slide 29: DISCOVER-AQ 2013 – San Joaquin Valley, CA
NASA P-3B
NASA King Air
EPA, State, Local, and Temporary Ground sites
Deriving Information on Surface Conditions from Column and Vertically Resolved Observations Relevant to Air Quality
Success of study relies on quality measurements of gas and particle species (and properties) aloft and at the surface

## Slide 30
Visalia Municipal Airport (SJVAPCD site)
inlets ~35m from I-99 (60,000 AADT); 17% heavy duty truck traffic
Thermal conversion, Photolytic conversion, and CRDS analyzers compared
Bakersfield Municipal Airport (SJVAPCD site)
SE of downtown Bakersfield
Thermal conversion and Photolytic conversion analyzers compared
Visalia, CA
Bakersfield, CA
EPA’s NO2 Methods Development

## Slide 31
 | fit | R2 | n
All points | y=1.0x+1.0 | 0.79 | 24,468
¦ΔNO¦ < 5ppb/min | y=1.0x+1.3 | 0.85 | 15,954
¦ΔNO¦ < 0.4ppb/min | y=0.99x+1.4 | 0.90 | 7,900
 | fit | R2 | n
All points | y=1.0x-1.2 | 0.88 | 19,000
¦ΔNO¦ < 5ppb/min | y=1.0x-1.5 | 0.88 | 13,821
¦ΔNO¦ < 0.4ppb/min | y=1.05x-1.7 | 0.88 | 6,851
Visalia Municipal Airport Results

## Slide 32
 | FRM | Photo | CRDS
Measurement approach | Thermal conversion-chemiluminescence | Photolytic conversion-chemiluminescence | Direct, optical technique (cavity ring down spectroscopy)
Designation | FRM | FEM | FEM*
Advantages | Long term record; provides an NO measurement | More specific; provides an NO measurement | Direct; fast response
Disadvantages | Interference from higher oxides of nitrogen (NOz species); indirect method | Non-unity conversion efficiency; indirect method | Other absorbers at 405 or 450 nm (rare!); no NO measurement
Evaluation of EPA’s NO2 Method
FRM = Federal Reference Method; FEM = Federal Equivalent Method

## Slide 33
 | FRM | Photo | CRDS
Measurement approach | Thermal conversion-chemiluminescence | Photolytic conversion-chemiluminescence | Direct, optical technique (cavity ring down spectroscopy)
Designation | FRM | FEM | FEM*
Advantages | Long term record; provides an NO measurement | More specific; provides an NO measurement | Direct; fast response
Disadvantages | Interference from higher oxides of nitrogen (NOz species); indirect method | Non-unity conversion efficiency; indirect method | Other absorbers at 405 or 450 nm (rare!); no NO measurement
Evaluation of EPA’s NO2 Method
FRM = Federal Reference Method; FEM = Federal Equivalent Method