## Slide 1
Comprehensive model evaluation of
PM2.5 species over Japan:
－Comparison among AERO5,
AERO6, and AERO6-VBS models
The 13th Annual CMAS Conference, October 28, 2014
ーContentsー
１．Introduction － PM2.5 in Japan / PM2.5 modelling
２．Methodology － Chemical transport models / Observations
３．Results － Model evaluations
４．Summary
ーAcknowledgementー
Funds： Environment Research and Technology Development Fund (5-1408, S12-1, 5B-1101)
Technical support: K. Suto and T. Noguchi (NIES)
Yu Morino, Tatsuya Nagashima, Seiji Sugata, Kei Sato, Kiyoshi Tanabe,
Akinori Takami, Hiroshi Tanimoto, and Toshimasa Ohara
National Institute for Environmental Studies, Japan

## Slide 2: PM2.5 in Japan
Urban (N=12)
Rural (N=5)
Roadside (N=16)
2001 2002 2003 2004 2005 2006 2007 2008 2009 2010
PM2.5 environmental standard
in Japan (Sept. 2009 ‒)
Annual mean: 15 μg m-3
Daily mean: 35 μg m-3
Temporal variations during 2001-2010
Ministry of Environment (2012)
PM2.5 concentrations
Ministry of Environment (2013)
PM2.5 standard was not attained in western Japan and Tokyo Metropolitan Area.
PM2.5 env. standard
○：Attained
■▲：Not-attained
Spatial variations in 2012
Attained
Unattained
1. Introduction

## Slide 3: PM2.5 modelling in Tokyo Metropolitan Area (in summer 2007)
Model intercomparison of PM2.5 species (Morino et al., JSAE, 2010)
(CMAQ v4.7.1 and CMAQ 4.6 were used.)
All models significantly underestimated OA.
S1: Komae, S2: Kisai, S3: Maebashi, S4: Tsukuba
Organic aerosol
1. Introduction
Fossil-SOA: Underestimation by a factor of 6-8
Model evaluation of fossil- and biogenic SOA (Morino et al., ES&T, 2010)
(CMAQ–MADRID was used.)
Biogenic-SOA: Underestimation by a factor of 1.5 - 2

## Slide 4
 | #Gas | # Reaction | Aerosol models
MCM v3.2 | 5731 | 16933 | Pankow
CACM -MADRID2 | 366 | 366 | MADRID2
SAPRC99 -AERO4 | 79 | 214 | AERO4
SAPRC99 -AERO5 | 88 | 224 | AERO5
SAPRC99 -VBS | 92 | 214#1 | VBS
#1: exclude aging reactions |  |  | 
MCM, CACM-MADRID: Explicitly simulate multi-generation oxidation
AERO4, AERO5: Yield models
Volatility Basis Set (VBS): Grouping of SVOC and IVOC based on volatility
from
CMAQ-MADRID
CMAQ v4.6
CMAQ v4.7.1
Intercomparison of SOA models in TMA (in summer 2004)
(Morino et al., JGR, in revisions)
Obs
S=0.193 mgm-3/ppbv
VBS
S=0.130
CACM
S=0.016
Others
S=0.003-0.011
1. Introduction

## Slide 5: Background of PM2.5 modelling in Japan
SOA models:
  OA concentrations were largely underestimated by yield and mechanical models in TMA, Japan.
  VBS model better reproduced SOA in TMA.
Limitation of observational data:
  Simultaneous measurement of PM2.5 chemical composition were limited in Japan.
  → Model evaluation of PM2.5 species were spatially and temporally limited.
  Simultaneous measurements of PM2.5 species over Japan were conducted in 2012.
1. Introduction
Objectives of this study
Model performance of PM2.5 chemical composition were evaluated using the observational data over Japan in 2012.
Results of three simulation models, including the VBS model, were compared.

## Slide 6
Global-scale CTM
MIROC-ESM-CHEM
Δx = 300 km
Regional-scale CTM
WRF/CMAQ
Δx = 60km
Δx = 15km
Chemical transport models
 | Models | Chemical Modules | Aerosol modules
① | CMAQ v4.7.1 | SAPRC99 | AERO5
② | CMAQ v5.0.2 | CB05 | AERO6
③ | CMAQ v5.0.2 | CB05 | AERO6VBS
Target | Emission data | Spatial resol.
Anthropogenic (Japan) | JATOP | ~1km (vehicles) ~10km (others)
Anthropogenic (Easi Asia) | REAS v2.1 | 0.25°
Biomass burning | GFED v3.1 | 0.5°
Volcano | AEROCOM/JMA | Points
Biogenic VOC | MEGAN v2.10 | ~0.04°
Three versions of CMAQ
Setups of emission data
2. Methodology

## Slide 7
SOA models ー yield models
AERO5
AERO6
PNCOM
POC
aging
AERO6
Carlton et al., 2010
2. Methodology
Notes: Carlton_10EST_CMAQ.pdf

## Slide 8
Merit 1：
Merit 2：
SOA (V)
POA
VOC
Emission sources
SVOC1
cond./
evapo.
oxidation
VBS model
Yield model
emis.
emis.
SOA (I/S)
aging
aging
SVOC1
SVOC2
SVOC3
cond./
evapo.
cond./
evapo.
emis.
SVOC3
aging
SVOC2
aging
cond./
evapo.
Merit 1
Merit 2
Simulate primary emissions and oxidation (aging) of SVOC/IVOC (semi-/intermediate- VOC)
Simulate aging processes of oxidation products from VOCs
2. Methodology
SOA models ー Volatility basis-set (VBS) model

## Slide 9
 | Remote | Urban/rural
Kyusyu | #1:Tsushima | #2:Dazaifu
Chugoku | #3:Oki | #4:Matsue
Kinki | #5:Kyotango | #6: Osaka #7:Otsu
Chubu | #8:Tateyama #11:Sadoseki | #9:Toyama #10:Niigata
Hokkaido | #13:Rishiri | #12:Sapporo
■Periods:
－Winter: Jan 9 – 20
－Spring: May 6 – 12
－Summer: Jul 24 – Aug 1
■Points
Observations of PM2.5 species in 2012
2. Methodology
■Sampling duration: 6 h or 12 h
■Target species
－Ion (SO42–, NO3–, NH4+): IC
－Carbon (EC and OC) : TOT (IMPROVE protocol)

## Slide 10
SO42– | 
NO3– | 
NH4+ | 
EC | 
OA | 
#6: Osaka
#7: Shiga
#5: Kyotango
#6 Urban ( Osaka)
#7 Urban (Shiga)
#5 Rural (Kyotango)
Temporal variations of PM2.5 species (winter)
3. Results

## Slide 11
SO42– | ・Largely underestimated both in urban and remote areas.
NO3– | ・Overestimated at all sites. ・Better reproduced when Vd of HNO3&NH3 were enhanced (×5). (Neuman et al., 2004; Shimadera et al., 2014)
NH4+ | ・Combined trends of SO42– and NO3–.
EC | ・Well reproduced at the urban site and underestimated at the rural site.
OA | ・Large underestimation ・Similar results by the all three models.
3. Results
Temporal variations of PM2.5 species (winter)
#6 Urban ( Osaka)
#7 Urban (Shiga)
#5 Rural (Kyotango)

## Slide 12
3. Results
SO42– | ・Generally reproduced, though some peaks were underestimated.
NO3– | ・Low NO3– was reproduced.
NH4+ | ・Combined trends of SO42– and NO3–.
EC | ・Reproduced at the urban site and underestimated at the rural site.
OA | ・Underestimated by the yield models. ・VBS better reproduced the observation.
Temporal variations of PM2.5 species (summer)
VBS Obs
AERO5
AERO6
#6 Urban ( Osaka)
#7 Urban (Shiga)
#5 Rural (Kyotango)

## Slide 13
3. Results
Winter
Spring
SO42– | 
NO3– | 
NH4+ | 
EC | 
OA | 
Comparison of observed and simulated PM2.5 species
Urban/rural
Remote
VBS
AERO5
AERO6
Model
Observed
Summer
Vd×5

## Slide 14
Comparison of observed and simulated PM2.5 species
3. Results
Winter
Spring
Summer
SO42– | ・Underestimated in winter and spring. ・Well reproduced in summer.
NO3– | ・Overestimated in winter and spring. ・Better reproduced when we enhance Vd (×5) of HNO3&NH3.
NH4+ | ・Combined characteristics of SO42– and NO3–.
EC | ・Well reproduced (with some variability).
OA | ・Underestimated over the three seasons ・Better reproduced by the VBS.
Model
Observed
VBS
AERO5
AERO6

## Slide 15
CMAQ v4.7.1
SAPRC99-AERO5
CMAQ v5.0.2
CB05-AERO6
In spring and summer, AERO6VBS simulated the highest OA over Japan.
Simulated spatial distributions of organic aerosol
3. Results
OA (μg m-3)
OA (μg m-3)
OA (μg m-3)
Spring (May)
Winter (Jan.)
Summer (Jul.)
CMAQ v5.0.2
CB05-AERO6VBS

## Slide 16
In spring and summer, AERO6VBS simulated the highest OA over Japan.
Simulated spatial distributions of organic aerosol
3. Results
AERO6VBS–AERO5
AERO6VBS
AERO6VBS–AERO6
AERO6VBS
Winter (Jan.)
Spring (May)
Summer (Jul.)
Ratio
OA (μg m-3)
CMAQ v5.0.2
CB05-AERO6VBS

## Slide 17
High OA concentrations by the AERO6VBS model are due to high ASOA concentrations.
Simulated average OA over Japan
3. Results
OA concentrations (μg m–3)
Winter (Jan.)
Spring (May)
Summer (Jul.)

## Slide 18: Summary
Performance of three simulation models on PM2.5 species were evaluated over Japan in 2012.
Concentrations of SO42– , NO3–, and NH4+ were well reproduced by the all models in summer, while SO42– was underestimated NO3– was overestimated in winter and spring.
OA concentrations were underestimated by all the models in winter and spring.
OA concentrations were largely underestimated by AERO5 and AERO6 summer, and better reproduced by AERO6-VBS because higher ASOA was simulated by AERO6-VBS.

## Slide 20: Uncertainty analysis of VBS
 | AERO6VBS |  | Tsimpidi
 | Anthro. | BB | Anthro.
Nonvolatile | 0.4 | 0.27 | 
C*=10^(-2) |  |  | 0.03
C*=10^(-1) |  |  | 0.06
C*=10^(0) | 0.26 | 0.27 | 0.09
C*=10^(1) | 0.40 | 0.42 | 0.14
C*=10^(2) | 0.51 | 0.54 | 0.18
C*=10^(3) | 1.43 | 1.50 | 0.30
C*=10^(4) |  |  | 0.40
C*=10^(5) |  |  | 0.50
C*=10^(6) |  |  | 0.80
 | AERO6VBS | Tsimpidi
k(AVOC +OH) | 2×10^(-11) | 1×10^(-11)
k(BVOC +OH) | 0 | 0
k(S/IVOC +OH) | 4×10^(-11) | 4×10^(-11)
SOA yields
SVOC emission profiles
SVOC aging reaction rates (cm3/molec/sec)

## Slide 21: Uncertainty analysis of VBS
Simulation | [SOA]/[Ox] | [V-SOA]/[Ox] | [SI-SOA]/ [Ox] | POA
 | (μg m-3/ppmv) | (μg m-3/ppmv) | (μg m-3/ppmv) | (μg m-3)
Standard | 151.3 | 93.7 | 57.6 | 0.27
No aging | 1.3 | 1.3 | – | 0.19
Aging of BVOC | 152.6 | 95.0 | 57.6 | 0.27
Aging rate × 10 | 503.4 | 343.9 | 159.5 | 0.29
Aging rate ÷ 10 | 6.4 | 4.3 | 2.1 | 0.20
SVOC of Shrivastava et al. [2011] | 290.4 | 117.7 | 172.8 | 1.45
SVOC of Tsimpidi et al. [2010] (low volatility case) | 115.8 | 86.0 | 29.7 | 0.60
SVOC of Tsimpidi et al. [2010] (high volatility case) | 188.3 | 101.0 | 87.3 | 0.28
Nonvolatile POA | 89.1 | 89.1 | – | 2.36
Nonvolatile POA/no aging | 15.5 | 15.5 | – | 2.36
AERO6VBS | 178.0 | 94.6 | 83.4 | 
Obs | 192.6 |  |  | 2.36