## Slide 1
Evaluation of the Community Multiscale Air Quality (CMAQ) Model Version 5.2
K. Wyat Appel, Sergey Napelenok, Christian Hogrefe, Kristen M. Foley, George Pouliot, Ben Murphy, Deborah Luecken, Nicholas Heath and the CMAQ development team
U.S. EPA, National Exposure Research Laboratory,
Computational Exposure Division, RTP, NC
15th Annual CMAS Conference – October 26, 2016
Chapel Hill, NC

## Slide 2
Major Updates in the CMAQv5.2
Modeling System
Transition from WRFv3.7 to WRFv3.8
  PAR function and impact on transpiration modified by Jon Pleim
  Numerous other updates in WRFv3.8 (http://www2.ucar.edu/wrf/users/wrfv3.8/updates-3.8.html)
WRFv3.8 with lightning assimilation
  Assimilation of lightning strike data from the National Lightning Detection Network (NLDN)
  Force deep convection where lightning is observed; only allow shallow convection where it is not
Science updates in CMAQv5.2
  Increased O3 deposition to wetted surfaces (particularly important in the early morning hours)
  Updated organic aerosol (OA) with semivolatile primary OA and empirical secondary OA formation from combustion sources (presentation yesterday by Ben Murphy)
    Large decreases in primary OA in both summer (75-95%) and winter (55-90%)
    In winter, the lack of photochemistry results in overall decreases in OA (and PM2.5) in many cities
    In summer, increase in OA at due to the increased role from secondary OA formation pathways
  Updated windblown dust scheme (presentation yesterday by Hosein Foroutan)
  Updated sub-grid cloud scheme
Update from the 2011 NEI v2 eh to 2011 NEI v2 ek platform
  Updated from MOVES2014 to MOVES2014a for mobile emissions (updates for TX, OH, NJ, CA, AZ)
  Revised spatial surrogates for underway emissions from commercial marine
Update from the CB05e51 to CB6r3 chemical mechanism
  Generally lower O3 and NO2 from lower production of alkyl nitrates (winter), lack of NOX recycling, lower HO2 and higher heterogeneous removal of nitrates
Transition from GEOS-Chem to hemispheric CMAQ for lateral boundary conditions

## Slide 3
CMAQ Simulations Details
Model Version | CMAQ v5.1 | CMAQ v5.2
Domain | CONUS 12km | CONUS 12km
Meteorological Model | WRF v3.7 | WRF v3.8 w/ Lightning assim.
MCIP Version | MCIPv4.3 | MCIPv4.3
Emissions Platform | 2011 NEI v2 eh (Inline) | 2011 NEI v2 ek (inline)
BELD Version | BELD Version 4 | BELD Version 4
Lightning NO Emissions | Yes | Yes (Updated)
OMI Data | Yes | Yes
Photolysis | Inline | Inline
AERO Version | AERO6 | AERO6 (svPOA)
Chemical Mechanism | CB05e51 | CB6r3
Boundary Conditions | GEOS-Chem | Hemispheric CMAQ
Gravitational Settling | Yes | Yes
Wind-blown Dust | Yes (v5.2 version) | Yes
Halogen Chemistry | Yes | Yes
Multipollutant | No | No

## Slide 4
Ozone

## Slide 5
O3 decreased as a result of almost all the updates made to the CMAQ system, but in particular the WRF updates, updates in CMAQv5.2 (increased O3 dry deposition), CB6r3 chemical mechanism and the updated lightning NO calculation
July
O3 (all hours)
Emissions Update
CMAQv5.1 Modeled O3 Mixing Ratio
CMAQv5.2 (LTGNO) – CMAQv5.1
WRFv3.8
Lightning Assimilation
Updates in CMAQv5.2
Lightning NO Calculation Update
CB6r3 Chemical Mechanism
Large decrease in O3 mixing ratios across the entire CONUS between v5.1 base and v5.2 final

## Slide 6
Impact of Hemispheric BCs on July O3
Hemispheric CMAQ boundary conditions further lowers ozone mixing ratios in July

## Slide 7
v5.1 Base
O3 Mixing Ratio
O3 Bias

## Slide 8
v5.1 Base
v5.1 w/ WRF Updates
O3 Mixing Ratio
O3 Bias

## Slide 9
v5.1 Base
v5.1 w/ WRF Updates
v5.2 CB05e51 (ek emis)
O3 Mixing Ratio
O3 Bias

## Slide 10
v5.1 Base
v5.1 w/ WRF Updates
v5.2 CB05e51 (ek emis)
v5.2 CB6r3
O3 Mixing Ratio
O3 Bias

## Slide 11
v5.1 Base
v5.1 w/ WRF Updates
v5.2 CB05e51 (ek emis)
v5.2 CB6r3
Lightning NO Update
O3 Mixing Ratio
O3 Bias

## Slide 12
v5.1 Base
v5.1 w/ WRF Updates
v5.2 CB05e51 (ek emis)
v5.2 CB6r3
Lightning NO Update
Hemispheric CMAQ BCs
O3 Mixing Ratio
O3 Bias

## Slide 13
Worse Bias
Improved Bias
Worse Bias
Improved Bias
Worse Error
Improved Error
CMAQv5.2 (LTGNO) – CMAQv5.1 – Difference in MDA8 O3 Absolute Bias July 2011

## Slide 14
PM2.5

## Slide 15
January NO3
Large decrease in NO3 due to hemispheric CMAQ BCs
CMAQv5.1 Modeled NO3 Concentration
Emissions Update
CMAQv5.2 – CMAQv5.1
WRFv3.8
Lightning Assimilation
Updates in CMAQv5.2
Hemispheric CMAQ BCs
CB6r3 Chemical Mechanism
NO3 increases in the Northeast and decreases across the rest of the CONUS
Increase in NO3 due to lightning assimilation and CB6r3 chemical mechanism
Mixed changes do to changes in v5.2 and the emissions update

## Slide 16
January
Primary OA
CMAQv5.1 Modeled POA Conc.
Emissions Update
CMAQv5.2 – CMAQv5.1
WRFv3.8
Lightning Assimilation
Updates in CMAQv5.2
Hemispheric CMAQ BCs
CB6r3 Chemical Mechanism
Very large decrease in POC due to updates in CMAQv5.2 (as expected)
Very small increase due to lightning assimilation and emission updates

## Slide 17
CMAQv5.1 Modeled SOA Conc.
Emissions Update
CMAQv5.2 – CMAQv5.1
WRFv3.8
Lightning Assimilation
Updates in CMAQv5.2
Hemispheric CMAQ BCs
CB6r3 Chemical Mechanism
January
Secondary OA
Very large increase in SOA due to updates in CMAQv5.2 (increased role of SOA pathways)
Smaller increases near the southern boundary due to hemispheric BCs

## Slide 18
Small increase in PM2.5 in the Northeast and mid-Atlantic due to inclusion of lightning assimilation
Mixed increases/decreases in PM2.5 due to changes in CMAQv5.2 (decreased POA and increased SOA)
Mixed increases and decreases in PM2.5 across the CONUS between v5.1 base and v5.2 final
Small effect on PM2.5 from the other updates
January PM2.5
CMAQv5.1 Modeled PM2.5 Conc.
Emissions Update
CMAQv5.2 – CMAQv5.1
WRFv3.8
Lightning Assimilation
Updates in CMAQv5.2
Hemispheric CMAQ BCs
CB6r3 Chemical Mechanism

## Slide 19
v5.1 Base
PM2.5 Concentration
PM2.5 Bias

## Slide 20
v5.1 Base
v5.1 w/ WRF Updates
PM2.5 Concentration
PM2.5 Bias

## Slide 21
v5.1 Base
v5.1 w/ WRF Updates
v5.2 CB05e51
PM2.5 Concentration
PM2.5 Bias

## Slide 22
v5.1 Base
v5.1 w/ WRF Updates
v5.2 CB05e51
v5.2 CB05e51 (ek emis)
PM2.5 Concentration
PM2.5 Bias

## Slide 23
v5.1 Base
v5.1 w/ WRF Updates
v5.2 CB05e51
v5.2 CB05e51 (ek emis)
v5.2 CB6r3
PM2.5 Concentration
PM2.5 Bias

## Slide 24
v5.1 Base
v5.1 w/ WRF Updates
v5.2 CB05e51
v5.2 CB05e51 (ek emis)
v5.2 CB6r3
Hemispheric CMAQ BCs
PM2.5 Concentration
PM2.5 Bias

## Slide 25
Worse Bias
Improved Bias
Worse Bias
Improved Bias
Worse Error
Improved Error
CMAQv5.2 (Hemi) – CMAQv5.1 – Difference in PM2.5 Absolute Bias January 2011

## Slide 26
CMAQv5.1
CMAQv5.2
CMAQv5.1
CMAQv5.2
January PM2.5 Speciated Stacked Bar Plot

## Slide 27
July SO4
Decreased SO4 due to changes in CMAQv5.2 (likely due to sub-grid cloud updates)
Mixed change in SO4 due to lightning assimilation
CMAQv5.1 Modeled SO4 Conc.
Emissions Update
CMAQv5.2 – CMAQv5.1
WRFv3.8
Lightning Assimilation
Hemispheric CMAQ BCs
Updates in CMAQv5.2
CB6r3 Chemical Mechanism
Increased SO4 due to WRFv3.8, CB6r3 chemical mechanism and hemispheric BCs

## Slide 28
July
Primary OA
CMAQv5.1 Modeled POA Conc.
Emissions Update
CMAQv5.2 – CMAQv5.1
WRFv3.8
Lightning Assimilation
Updates in CMAQv5.2
Hemispheric CMAQ BCs
CB6r3 Chemical Mechanism
Large decrease in primary OA due to updates in CMAQv5.2 (semivolatile POA)
Smaller changes due to WRFv3.8, lightning assimilation and emission updates

## Slide 29
CMAQv5.1 Modeled SOA Conc.
Emissions Update
CMAQv5.2 – CMAQv5.1
WRFv3.8
Lightning Assimilation
Updates in CMAQv5.2
Hemispheric CMAQ BCs
CB6r3 Chemical Mechanism
July
Secondary OA
Smaller increases due to WRFv3.8 and lightning assimilation
Large increase in SOA due to updates in CMAQv5.2 (new SOA formation pathways) and Hemispheric BCs
Small decrease in the SOA in the southeast due to CB6r3 chemical mechanism update

## Slide 30
Large increase in PM2.5 across much of the CONUS due to updates in CMAQv5.2
Large increase in PM2.5 across the CONUS between v5.1 base and v5.2 final
Relative large increase in PM2.5 due to hemispheric CMAQ BCs
Mixed increases/decreases in PM2.5 due to the WRFv3.8 and lightning assimilation
July PM2.5
CMAQv5.1 Modeled PM2.5 Conc.
Emissions Update
CMAQv5.2 – CMAQv5.1
WRFv3.8
Lightning Assimilation
Updates in CMAQv5.2
Hemispheric CMAQ BCs
CB6r3 Chemical Mechanism

## Slide 31
v5.1 Base
PM2.5 Concentration
PM2.5 Bias

## Slide 32
v5.1 Base
v5.1 w/ WRF Updates
PM2.5 Concentration
PM2.5 Bias

## Slide 33
v5.1 Base
v5.1 w/ WRF Updates
v5.2 CB05e51
PM2.5 Concentration
PM2.5 Bias

## Slide 34
v5.1 Base
v5.1 w/ WRF Updates
v5.2 CB05e51
v5.2 CB05e51 (ek emis)
PM2.5 Concentration
PM2.5 Bias

## Slide 35
v5.1 Base
v5.1 w/ WRF Updates
v5.2 CB05e51
v5.2 CB05e51 (ek emis)
v5.2 CB6r3
PM2.5 Concentration
PM2.5 Bias

## Slide 36
v5.1 Base
v5.1 w/ WRF Updates
v5.2 CB05e51
v5.2 CB05e51 (ek emis)
v5.2 CB6r3
Hemispheric CMAQ BCs
PM2.5 Concentration
PM2.5 Bias

## Slide 37
Worse Bias
Improved Bias
Worse Bias
Improved Bias
Worse Error
Improved Error
CMAQv5.2 (Hemi) – CMAQv5.1 – Difference in PM2.5 Absolute Bias July 2011

## Slide 38
CMAQv5.1
CMAQv5.2
CMAQv5.1
CMAQv5.2
July PM2.5 Speciated Stacked Bar Plot

## Slide 39
Windblown Dust

## Slide 40
PM2.5
PM10
Soil
CMAQv5.1 Soil Concentration (no WBD)
CMAQv5.1 Soil Contribution from WBD
CMAQv5.1 PM2.5 Contribution from WBD
CMAQv5.1 PM10 Contribution from WBD
CMAQv5.1 PM2.5 Concentration (no WBD)
CMAQv5.1 PM10 Concentration (no WBD)

## Slide 41
Summary
Ozone
  O3 primarily increases over the CONUS in January (not shown)
    Improved bias in many areas (exception being California)
  O3 mixing ratios greatly reduced across the CONUS in July
    Large improvement in bias, particularly the eastern U.S.
PM2.5
  PM2.5 largely decreases in January
    Improved bias in many areas, particularly the eastern U.S.
    Primarily due to inclusion of semivolatile POA in CMAQv5.2
  PM2.5 concentrations increase significantly in July
    Large improvement in bias across the CONUS
    Primarily due to increased SOA (potential SOA from combustion sources) in CMAQv5.2 and hemispheric CMAQ BCs
    Smaller contribution from WRFv3.8 updates and lightning assimilation in WRF
  New windblown model produces reasonable PM2.5 and PM10 in desert areas

## Slide 42
CMAQv5.2 Release
CMAQv5.2 beta code should be available soon
  Will include all the updates shown here
CMAQv5.2 final release planned for spring 2017
  No major additional updates planned

## Slide 43
Extra slides

## Slide 44
July O3 Binned Bias/RMSE

## Slide 45
July PM2.5 Binned Bias/RMSE

## Slide 46
Increased O3 due to hemispheric CMAQ boundary conditions
O3 primarily increases over the CONUS between v5.1 base and v5.2 final
January
O3 (all hours)
Emissions Update
CMAQv5.1
CMAQv5.2 (Hemi) – CMAQv5.1
WRFv3.8
Lightning Assimilation
Updates in CMAQv5.2
Hemispheric CMAQ BCs
CB6r3 Chemical Mechanism
Decreased O3 due to updates in v5.2 (increased O3 dry deposition) and the CB6r3 chemical mechanism

## Slide 48
Worse Bias
Improved Bias
Worse Bias
Improved Bias
Worse Error
Improved Error
CMAQv5.2 (Hemi) – CMAQv5.1 – Difference in MDA8 O3 Absolute Bias January 2011

## Slide 49
January SO4
Small decreases due to changes in CMAQv5.2 and hemispheric BCs
CMAQv5.1
Emissions Update
CMAQv5.2 – CMAQv5.1
WRFv3.8
Lightning Assimilation
Updates in CMAQv5.2
Hemispheric CMAQ BCs
CB6r3 Chemical Mechanism

## Slide 50
NO3
Very small changes in NO3 over the CONUS. Relatively large change over the eastern Atlantic Ocean due to changes in PM speciation in CMAQv5.2
CMAQv5.1
Emissions Update
CMAQv5.2 – CMAQv5.1
WRFv3.8
Lightning Assimilation
Updates in CMAQv5.2
Hemispheric CMAQ BCs
CB6r3 Chemical Mechanism

## Slide 51
NO2

## Slide 52
NO2
Increased NO2 due to lightning assimilation and emission updates
Overall NO2 mixing ratios decrease over the CONUS in January
CMAQv5.1
Emissions Update
CMAQv5.2 – CMAQv5.1
WRFv3.8
Lightning Assimilation
Updates in CMAQv5.2
Hemispheric CMAQ BCs
CB6r3 Chemical Mechanism
Decreased NO2 due to emission updates, CB6r3 and hemispheric CMAQ BCs

## Slide 53
Decreased NO2 due to CMAQv5.2 updates and CB6r3 chemical mechanism
NO2
Mixed NO2 changes due to WRFv3.8 updates, lightning assimilation and emission updates
NO2 mixing ratios largely decreases in July

## Slide 54
EC

## Slide 55
Elemental Carbon
EC generally increases due to lightning assimilation and emission updates

## Slide 56
Elemental Carbon
Very small overall increase in EC due primarily to WRFv3.8, lightning assimilation, changes in CMAQv5.2 and emission updates

## Slide 57
OC

## Slide 58
January
Organic Carbon
CMAQv5.1 Modeled OC Conc.
Emissions Update
CMAQv5.2 – CMAQv5.1
WRFv3.8
Lightning Assimilation
Updates in CMAQv5.2
Hemispheric CMAQ BCs
CB6r3 Chemical Mechanism
OC changes mixed due decrease in POA and increase in SOA from updates in CMAQv5.2

## Slide 59
July
Organic Carbon
CMAQv5.1 Modeled OC Conc.
Emissions Update
CMAQv5.2 – CMAQv5.1
WRFv3.8
Lightning Assimilation
Updates in CMAQv5.2
Hemispheric CMAQ BCs
CB6r3 Chemical Mechanism
Large increase in OC due to changes in CMAQv5.2 (increased SOA) and hemispheric BCs
Small increase in OC due to WRFv3.8 and lightning assimilation

## Slide 60
PM10

## Slide 61
January PM10
PM10 increases due primarily to speciation changes in CMAQv5.2 and from additional PM10 in the hemispheric CMAQ BCs
CMAQv5.1
Emissions Update
CMAQv5.2 – CMAQv5.1
WRFv3.8
Lightning Assimilation
Updates in CMAQv5.2
Hemispheric CMAQ BCs
CB6r3 Chemical Mechanism

## Slide 62
July PM10
PM10 increases due to speciation changes in CMAQv5.2 and from additional PM10 in the hemispheric CMAQ BCs
CMAQv5.1
Emissions Update
CMAQv5.2 – CMAQv5.1
WRFv3.8
Lightning Assimilation
Updates in CMAQv5.2
Hemispheric CMAQ BCs
CB6r3 Chemical Mechanism