## Slide 1: What’s new in the Atmospheric Model Evaluation Tool (AMET) version 1.3
K. Wyat Appel and Robert C. Gilliam
16th Annual CMAS Conference October 25th, 2017

## Slide 2: Brief History of AMET
AMET v1.0
Early AMET
AMETv1.2
AMETv1.3
Appel et al. (2011) Environ. Modell. Softw., 26, 434-443.
Bug fixes, new scripts
Significant updates over previous version
Available through GitHub for the first time
First developed by Rob Gilliam for MM5 meteorological applications (early 2000s)
First public release through CMAS Center
AMETv1.1
Extended to AQ applications by Wyat Appel (mid-2000s)
Feb 2008
May 2008
July 2013
July 2017
Minor update
https://github.com/USEPA/AMET

## Slide 3: General Overview of AMET
Model evaluation tool for both AQ and MET models
  WRF, MPAS (MM5 no longer supported)
  CMAQ, CAMx (requires some pre-processing)
Utilizes open source software
  MySQL database software: Data storage and access
  Fortran (post-processing tools)
  R statistical software: Database interface and analysis
Advantages of AMET
  Capable of managing large datasets efficiently
  Partially automated system, therefore easy to use
  Relational database allows for unique querying of data
  Pre-defined analysis scripts for common analysis across groups
  Users can easily develop their own custom analyses in R
    Or leverage output files to do their own analyses
(AQ only)
(AQ only)

## Slide 4: Examples of AMET-MET Module Plots

## Slide 5: Examples of AMET-AQ Module Plots

## Slide 6: Key Updates to the AMETv1.3 MET and AQ Modules
GitHub version control repository
  Easier development, maintenance, and distribution of code
All Perl code has been removed
  Perl code has either been deprecated or replaced with R scripts
Database setup and project creation have been simplified
The number of required input files has been reduced
MySQL credential management has been made more robust
Improved MET and AQ data loading speed

## Slide 7: Key Updates to the AMETv1.3 MET Module
Direct read of MADIS netCDF observation files within R
Simple text file observation format for non-MADIS observations
Dynamic MET site accounting
  Master site list is updated each observation file read with only new sites
  Interpolation weights are only computed for new sites which improved speed
Model for Prediction Across Scales (MPAS) compatibility
MPAS-MADIS obs matching using barycentric interpolation
  center of mass triangulation of surrounding three center grid points implemented by Russ Bullock). Shown to improve statistics over nearest neighbor
MADIS metar and maritime observation datasets now have global observations
  Allows for global model evaluation for MPAS modelers
Simpler version of the AutoFTP option for acquiring MADIS data

## Slide 8: Add-on MET Evaluation Components
Not all MET components in AMETv1.2 were converted from Perl to R yet
Development of the surface matching will make it fairly simple to add these components
  Updates will be a simple replacement of (R_db_code/MET*) existing matching codes
  Git-Hub archive will allow users to easily update and contribute code
Baseline Solar Radiation Network
  Global Shortwave radiation network matched with WRF/MPAS at various time scales
RAOB
  matching WRF/MPAS with 2-4 times daily rawinsonde soundings (θ, RH, WS, WD)
PROFILER
  Hourly PBL and tropospheric wind profiler matching with WRF/MPAS (θv, WS, WD)
ACARS profiles
  Aircraft profiler data (θv, WS, WD) matched with WRF/MPAS
PRISM precipitation
  Daily, monthly or episodic matching of WRF/MPAS output
  4 km National gridded precipitation dataset from Oregon State University

## Slide 9: Overview of the AMETv1.3 AQ Module
Designed to work directly with CMAQ output
  Can be modified to work with any data though (e.g. water measurements)
Directly supports data from a number of routine networks
  NA: AQS, IMPROVE, CSN, CASTNET, NADP, MDN, SEARCH, AMON, AIRMON, FLUXNET
  Europe: AIRBASE, AURN, EMEP, AGANET, ADMN, NAMN
  Stores each network separately for more robust analysis
Utilizes Site Compare to do the model/observation matching
  Fortran based utility that is provided with CMAQ and AMET
  Requires properly formatted observation files
    These files are available for download

## Slide 10: Key Updates to the AMETv1.3 AQ Module
Added support for the AMON, AIRMON and FLUXNET networks
More robust data loading process
  Previously model species were predefined when a new project was created
    Unused/unnecessary species were carried along
  New method adds species as necessary
    This makes it easier to add new species and networks to AMET-AQ
Data loading is also faster due to several code updates
Added several new analysis scripts and updated almost all the existing scripts
16 years of AMET compatible AQ observation files available for download
More robust and faster AQ data loading process
Added several AQ new analysis scripts
AMET-AQ “Batch” script for quickly and easily creating plots

## Slide 11: AMET-AQ Observation Data Files
Observations are paired with model data using Site Compare
  Site Compare requires properly formatted data files
Unlike the AMET-MET module, AMET-AQ requires pre-generated observation files
  User’s were previously given guidance on how to download and format these data
  Now however, the AMET-AQ ready files are available for download directly
The CMAS Center has posted these data files on a Google drive
  See the CMAS website for instructions on accessing these files
  https://www.cmascenter.org/download/data.cfm (North American Air Quality Observation Data)
  Note that while these data files are updated periodically, user’s may want to refer to the data source for latest data

## Slide 12
AMET-AQ Initialization (database setup)
create_amet_user.csh
delete_db.csh
Required input files:
None
AMET-AQ Project
(project creation and database population)
aqProject.csh
Required input files:
AQ_species_list.input
sites_meta.input
CMAQ model data (combine files)
Observation data (CMAS center website)
AMET-AQ Analysis
Various AQ analysis scripts
Required input files:
Each analysis script has
its own input file
AMET-AQ Batch Analysis
Single AQ analysis script
Required input files:
Single input file
AMET Web Interface (Beta)
PHP based webpage interface for AMET-MET and AMET-AQ
Will be provided as beta code via GitHub for testing

## Slide 13: AMETv1.3 AQ Module Query/Plot Options
Temporal specific queries
  Date range; specific year, month or day; day of week; hour of day; etc.
Spatial specific queries
  State(s); RPOs; pre-defined regions; lat/lon box
Data specific queries
  Query based on model/ob value
  Cross query with other data
Custom queries can also be created
  Can create queries based on any data in the database
Many plots are customizable
  Control data ranges, colors, symbols, titles, etc.

## Slide 14: Analysis Scripts in the AMET-AQ Module
Boxplot
  Hourly
  Day of Week
  MDA8
  Roselle
  Solar Radiation
Bugle Plot
Histogram
Overlay File
Spatial Plot
  Difference
  Model to Model
  Ratio
Monthly Stat Plot
Raw Data
Scatter Plots
  Binned
  Density
  Model to Model
  Percentiles
  Single Network
  Forecast Skill
  Soil
“Soccergoal” Plot
Spectral Analysis
Stacked Bar Plots
  AERO6
  Panel
  AERO6 Panel
  Soil
Stats and Plots
Temporal
Time Series
  Model to Model
  Multi-Network

## Slide 15: Batch Processing Analysis in the AMET-AQ Module
A new “batch processing” analysis script in AMET-AQ in v1.3
Allows for “mass production” of plots using a single script
  User can select which plots to create
  Utilizes a single namelist file
Can produce all available AQ analysis plots
  Neatly organized directory tree is created
  Removes the need for configuring and running individual analysis script
Batch script will be part of a unified post-processing script for CMAQ
  Currently developing a “master” CMAQ post-processing script
  Single script to run combine, site compare and create batch plots
  Will not require AMET to be installed (but more options with AMET installed)

## Slide 16: Web-based Graphical User Interface for AMET
Web based (PHP) GUI for AMET
  Project selection through a drop-down menu
  Easy selection of plotting options
  Sub-setting of sites/locations
Overlays on top of existing AMET release code
  Requires two additional configuration files
  No other AMET code modifications required
Does require user to run Apache web-server
Beta version will be made available on Git-Hub
  Limited support available
Web-based GUI has been used at EPA for years with good success

## Slide 17: Obtaining AMET and Documentation
AMET now resides in a GitHub repository
  https://github.com/USEPA/AMET/tree/master
  AMET versions 1.2 and 1.3 are currently available there
  Release notes available on AMET GitHub main page
  AMET code is also linked from the CMAS Center website
Installation and User’s guides available
  https://github.com/USEPA/AMET/blob/1.3/docs/AMET_Users_Guide_v1.md
  https://github.com/USEPA/AMET/blob/1.3/docs/AMET_Install_Guide_v13.md
A development space will added to the AMET GitHub repository
  Space where user contributed code can be shared
  AMET web interface code (beta version) will initially reside here

## Slide 18
Obtaining AMET and Documentation
AMETv1.3.1 likely available later this year or early next year. Includes minor bug fixes and support for upper-air analyses in AMET-MET (possible in AMET-AQ as well)

## Slide 19: AMET Version 1.3.1 (Yup, already)
Include AMET-MET parts that did not make v1.3 release
  upper-air and profile analyses
Ability to read site compare .csv files directly without database access
  lose some querying capability
  limited functionality, but batch scripting will remain functional
Various minor bug fixes from the v1.3 release
Release scheduled for sometime in late 2017 or early 2018

## Slide 20: Thanks to:
Zac Adelman (UNC)
  Code testing and documentation
Kristen Foley (EPA)
  Endless help with GitHub
Ben Murphy (EPA)
  Also helped with GitHub
Christian Hogrefe (EPA)
  Support for AMET-AQ tools