## Slide 1: Regional Air Quality Modeling of Wildfires for Health Assessments over the Continental United States
Cesunica E. Ivey, Cong Liu, Yang Liu, Howard Chang, Matt Strickland, and Heather A. Holmes
AAAR Meeting, Raleigh, NC
Thursday, 19 October 2017
10:00 AM, Room 306B
Source: http://www.latimes.com/local/la-me-rim-fire-20140808-story.html

## Slide 2
NASA’s Health and Air Quality Applied Sciences Team
Investigate links between wildfire smoke exposure and asthma in Colorado.
Background
State and city partners (highlighted
in green) of the CDC Tracking network.
Associations between same day PM2.5 levels during the 2012 Colorado wildfires and all-ages ED visits for asthma.
Notes: What the HAQAST project is about

## Slide 3
Objective
State and city partners (highlighted
in green) of the CDC Tracking network.
Associations between same day PM2.5 levels during the 2012 Colorado wildfires and all-ages ED visits for asthma.
Estimate daily wildfire smoke exposure metrics for a multi-year health study using a chemical transport model (CMAQ).
Notes: What the HAQAST project is about

## Slide 4
Goal
State and city partners (highlighted
in green) of the CDC Tracking network.
Associations between same day PM2.5 levels during the 2012 Colorado wildfires and all-ages ED visits for asthma.
Understand the model response to wildfire emissions inventories.
Notes: What the HAQAST project is about

## Slide 5
Chemistry and transport: CMAQ Model, v5.2 beta
Emissions:
  Fire Inventory of NCAR, v1.5
  National Emissions Inventory 2011 (wildfires omitted)
Study period: 2013 and 2014
Modeling domain: 12 km horizontal resolution and 34 vertical terrain-following layers
Wildfire Modeling
Obtain annual FINN emissions and integrate with the WRAP plume profile
Replace NFEI fire emissions with FINN emissions
Simulate episode with both emissions using CMAQ
Notes: Wildfire smoke and human health

## Slide 6
Fire Inventory of NCAR
Available in three versions:
  GEOS-CHEM* (Harvard)
  MOZART-4 (NCAR)
  SAPRC99*
Wiedinmyer et al., Geoscientific Model Development, 2011
Current study:
  Carbon Bond V (CB05) mechanism
  Combination of GEOS and SAPRC emissions
Emission Factors by Vegetation Type
Notes: General info
Mapping: https://github.com/barronh/geos2cmaq/blob/master/mapping/cb05cl_ae6_aq.csv

## Slide 7
National Emissions Inventory
Estimated using BlueSky (2011) modeling framework and local activity data
Available every three years (2002,2005,2008,2011,etc.)
Update available for wildfires in between years through EPA
Developed by state managers and compiled by EPA
FINN
Emission factors are derived from MODIS land cover product
Available at daily frequency
Active fires are detected using MODIS thermal and fire products
Developed at National Center for Atmospheric Research (NCAR)
NEI vs. FINN
Notes: MODIS thermal anomalies product
MODIS rapid response, MODIS data processing system

## Slide 8
NEI vs. FINN
Carbon Monoxide Emissions (Mmoles/day)
17 Sep 2014
NEI
FINN
Notes: Wildfire smoke and human health

## Slide 9
NEI vs. FINN
Total Wildfire Emissions for Continental U.S.
Chart: Wildfire Emissions (Metric Tons)
FINN 2013 | 142.78 | 18938.08 | 2951.7715
FINN 2014 | 105.88 | 12954.2 | 2206.1795
NEI 2011 | 1819363.8195 | 20488035.792 | 314959.8295
(Blue Sky)
PM2.5
CO
NOx
Notes: Bar charts of total emissions comparisons---write the code tomorrow

## Slide 10
Colorado Evaluation
AQS Site 080310002
NAMS Hourly O3
SLAMS Hourly PM2.5
2105 Broadway, Denver, CO
Notes: King fire overview----change the pictures

## Slide 11
Colorado Evaluation
AQS Site 080310002, Denver, CO
Chart: Observed O3 (ppm)
Hourly Ozone: June 26 – July 9, 2014
Notes: King fire overview----change the pictures

## Slide 12
Colorado Evaluation
AQS Site 080310002, Denver, CO
Chart: Observed FRM (ug/m3)
Hourly PM2.5: June 26 – July 9, 2014
Notes: King fire overview----change the pictures

## Slide 13
Started on 17 Aug 2013
Considered out on 4 Nov 2014
Over 250,000 acres burned
Largest fire in Sierra Nevada history
Hunter’s illegal campfire fire got out of control
Yosemite Rim Fire
2013 Rim Fire in Yosemite National Park
Source: http://www.latimes.com/local/la-me-rim-fire-20140808-story.html
Notes: Rim fire overview

## Slide 14
Yosemite Rim Fire
August 21, 2017: Hourly (UTC) PM2.5 and CO
PM2.5
CO
Notes: Rim fire overview

## Slide 15
Yosemite Rim Fire
August 12-22, 2013: PM2.5
CMAQ
MODIS True color
Chart: Reno, NV
| 41498 | 41499 | 41500 | 41501 | 41502 | 41503 | 41504 | 41505 | 41506 | 41507
OBS | 24.2739 | 23.9042 | 31.2292 | 26.6 | 23.387 | 29.5708 | 31.8375 | 28.0292 | 18.6708 | 11.8042
CMAQ | 8.727 | 9.7801 | 9.4428 | 10.817 | 9.1425 | 6.7559 | 6.512 | 16.201 | 9.6279 | 4.8424
corr = 0.30, slope = 0.59, intercept = 19.5
Notes: Rim fire overview

## Slide 16
Started on 13 Sep 2014
Ended 14 October 2014
97,000 acres burned
Started allegedly by an arsonist
King Fire
2014 King Fire as seen from Lake Tahoe
Source: http://wildfiretoday.com/2014/09/14/california-king-fire-near-pollock-pines/
Left: King Fire haze impacting visibility and sunlight in Reno, midday.
Notes: King fire overview

## Slide 17
King Fire
September 17, 2014: Hourly (UTC) PM2.5 and CO
CO
PM2.5
Notes: King fire overview----change the pictures

## Slide 18
King Fire
September 11-21, 2014: PM2.5
MODIS True color
CMAQ
Chart: Reno, NV
| 41893 | 41894 | 41895 | 41896 | 41897 | 41898 | 41899 | 41900 | 41901 | 41902
OBS | 8.8261 | 5.9565 | 6.7917 | 11.8333 | 37.875 | 39.7917 | 32.875 | 100.9583 | 27.4167 | 9.875
CMAQ | 10.42 | 8.0183 | 9.129 | 9.9349 | 13.397 | 6.0869 | 5.3835 | 7.7615 | 4.1908 | 4.5769
Notes: King fire overview----change the pictures

## Slide 19
Known:
  Plume direction subject to meteorological uncertainty
  Fire detection is impacted by cloud cover
Challenges and Uncertainties
Alkali Fire (20,000 acres, July 24, 2014)
FINN Emissions: 24 July 2014 15:00 UTC
Notes: What the HAQAST project is about

## Slide 20
Current Study:
  Capturing magnitude of emissions
  Capturing aerosol formation in wildfire smoke
Challenges and Uncertainties
Alkali Fire (20,000 acres, July 24, 2014)
FINN Emissions: 24 July 2014 15:00 UTC
Notes: What the HAQAST project is about

## Slide 21
FINN emissions improve spatial and temporal distribution of fire emissions
Low bias in estimated emissions, however there are fewer false alarms
CMAQ-modeled PM, CO, ozone will be used as exposure surrogates in H-AQAST health studies (2011-2014)
Future: simulations will include FINN-v2 wildfire emissions; plume direction improvement
Summary
Notes: summary

## Slide 22
Backup Slides
Notes: summary

## Slide 23
CMAQv5.2 beta
Compiled with mvapich2, pnetcdf,
Seasonal runs with 10-day spinup
16-cores per season (1 season run with 12 cores)
Timing: ## computational hrs per simulation day
Wildfire Modeling
Place holder
Notes: Slide for CMAS

## Slide 24
Monitor Locations
Fresno
  CSN: 060190008 (may be decommissioned)
  SLAMS: 060190011
Reno
  CSN: 320310016
Notes: summary

## Slide 25
FINN Species Equivalents
GEOS-CB05 Equivalents
Source: https://github.com/barronh/geos2cmaq/blob/master/mapping/cb05cl_ae6_aq.csv
Notes: summary

## Slide 26
Fire Inventory of NCAR
Daily to hourly emissions using diurnal consumption
WRAP Diurnal Profile