## Slide 1: Wildfires Impacts on Regional Air Quality A Case Study on Colorado
Cheng-En Yang, Joshua S. Fu, Xinyi Dong, Jian Sun,
Qingzhao Zhu, Yang Liu, Yongqiang Liu
10/23/2018

## Slide 2: Percentage of Annual Burned Area
1880
(Source: Sargent,1884; Pyne, 2010)
Farmers clearing land
Hunters leaving fires to burn in abandoned camps
1997-2014
(Source: Global Fire Emissions Database, Version 4.1)
Hotter and drier meteorological conditions in the western US

## Slide 3: Historical Major Fire Distributions
1980–2013 major fires (>50K acres burned) only
Major fire months:
April–October
(Data from Yongqiang Liu, USFS)
November–December:
more large fire events
in recent years

## Slide 4: Annual Wildfires in The US
(National Interagency Fire Center;
National Interagency Coordination Center )
Western US (WUS)
10/16 years > 50%

## Slide 5: Seasonal Dust Concentration
(Source: Hand et al., 2016)
Peaks in spring and early summer
Dust vs. wildfire contributions on PM2.5
Southwest US

## Slide 6: Experimental Design
Domain: Colorado
Duration: 2011−2014
Resolution: 12km x 12km, 25 layers
Meteorology: WRF v3.8.1
Initial / boundary conditions: GEOS-Chem v11-01
Emission: 2011, 2014 National Emission Inventory (NEI),
scaled 2012−2013, fire emissions from Dr. Kirk Baker
Scenarios: Base, noFire, and noDust by CMAQ v5.2

## Slide 7: Results – Monthly PM2.5 in Base Case
  Modeled PM2.5 (μg/m3)
  AQS/IMPROVE PM2.5 (μg/m3)
  Goals (best)
  MFB ≤ ±30%
  MFE ≤ 50%
  Criteria
  (acceptable)
  MFB ≤ ±60%
  MFE ≤ 75%
  Generally underestimated PM2.5 with some best and some acceptable performance
Notes: Goals (the level of accuracy that is considered to be close to the best a model can be expected to achieve) and Criteria (the level of accuracy that is considered to be acceptable for modeling applications)
(Boylan JW, Russell AG. PM and light extinction model performance metrics, goals, and criteria for three-dimensional air quality models. Atmospheric Environment. 2006;40:4946–4959.)
201304, 201206, 201306, 201406, 201110 acceptable

## Slide 8: 2011 Monthly Mean PM2.5 – Dust vs. Fires
  APR
  JUN
  OCT
  Base - noDust
  Base - noFire
  2011
Observed major wildfires
(http://www.denverpost.com)
  No significant dust contribution
  Monthly mean max PM2.5 by fires at surface: up to 12.9 µg/m3
Max = 1.5
Max = 12.9
Max = 1.9
Max ~ 0.003
Max ~ 0.001
Max ~ 0.001
Notes: Source: https://www.denverpost.com/2014/06/07/colorado-wildfires-major-fires-from-1971-2013-interactive-graphic/

## Slide 9: 2012−2013 Monthly Mean PM2.5 by Fires
  APR
  JUN
  OCT
  2013
  Base - noFire
  2012
  Base - noFire
  2012
  2013
Observed major wildfires
(http://www.denverpost.com)
Max = 0.3
Max = 0.3
Max = 18.5
Max = 2.3
Max = 67.6
Max = 0.5
Notes: Source: https://www.denverpost.com/2014/06/07/colorado-wildfires-major-fires-from-1971-2013-interactive-graphic/
No big fires in Colorado during 2014

## Slide 10: Maximum of Hourly Mean PM2.5 Changes
Case | Year | APR | MAY | JUN | JUL | AUG | SEP | OCT
Base − noDust | 2011 | 0.09 | 0.01 | 0.05 | 0.03 | 0.05 | 0.01 | 0.01
Base − noFire | 2011 | 18.9 | 27.2 | 116.2 | 4.8 | 13.1 | 8.7 | 32.4
 | 2012 | 7.1 | 10.2 | 54.9 | 58.9 | 8.1 | 10.5 | 17.4
 | 2013 | 4.3 | 3.8 | 307.2 | 112.3 | 9.2 | 5.1 | 5.2
 | 2014 | 8.6 | 16.4 | 11.0 | 11.0 | 7.1 | 11.9 | 8.1
  2011 hourly mean PM2.5 attributed by dust: < 0.1 µg/m3
  Significant fire contributions on PM2.5 during early summertime
  (Unit: µg/m3)

## Slide 11: Summary
Generally underestimated monthly-mean PM2.5 compared to AQS/IMPROVE sites in Colorado during 2011–2014
No significant dust contributions on 2011 PM2.5 in Colorado, even during spring and early summertime
Contribution of fires on PM2.5
  Monthly: up to 68 µg/m3 (Jun 2013)
  Hourly maximum: up to 307 µg/m3 (Jun 2013)

## Slide 12: Ongoing Work
The western US domain
Future wildfire emissions by Dr. Yongqiang Liu using USFS statistical fire model
Meteorology
CESM
WRF
MCIP
downscale
Initial /Boundary
Conditions
0.5°×0.5°
CAM-Chem
CMAQ
IC/BC
Emission
Base
12km CONUS
Future
12km
WUS
CMAQ v5.2
0.5°×0.5°
IIASA Global
12km
WUS

## Slide 13: Acknowledgements
This study was supported by the U.S. EPA Science to Achieve Results (STAR) Grant R835869. This research used resources of the Oak Ridge Leadership Computing Facility at the Oak Ridge National Laboratory, which is supported by the Office of Science of the U.S. Department of Energy under Contract No. DE-AC05-00OR22725.
Notes: It has not been formally reviewed by EPA. The views expressed in this document are solely those of the authors and do not necessarily reflect those of the Agency. EPA does not endorse any products or commercial services mentioned in this presentation.

## Slide 14: Thank You Questions?

## Slide 15: It Becomes Hotter…
Decadal mean temperature changes relative to 1901–1960 average
(Source: NOAA NCDC / CICS-NC)

## Slide 16: EPA AQS and IMPROVE Sites Locations

## Slide 17: WRF Validations
2011 MCIP data from US EPA
2012 − 2014 WRF v3.8.1 (same schemes as 2011)
Notes: 1. Only 2014/10 temperature may be out of the criteria
2. Zhang et al., (2014). Evaluation of a seven-year air quality simulation using the Weather Research and Forecasting (WRF)/Community Multiscale Air Quality (CMAQ) models in the eastern United States. Sci. Total Environ., 473, 275–285, 2014.

## Slide 18: 2011−2013 Daily Mean Fire Contributions on PM2.5
  2011
  06/08 – 06/09
  2012
  06/10 – 06/11
  2012
  06/26 – 06/27
  2013
  06/11 – 06/12
  2011
  2012
  2013
Notes: Source: https://www.denverpost.com/2014/06/07/colorado-wildfires-major-fires-from-1971-2013-interactive-graphic/
No big fires in Colorado during 2014

## Slide 19
Meteorology
CESM
WRF
MCIP
downscaling
Initial conditions
Boundary conditions
(CB05e51_ae6nvPOA_aq)
CAM-Chem
CMAQ
IC/BC
Emission
(CB05e51_
ae6nvPOA
_aq)
Base years
12km CONUS
Future years
12km
WUS
CMAQ
0.5°×0.5°
Global
12km
WUS
WUS grid info
Notes: CESM-WRF downscaling reference: Gao et al., 2012, ERL
IC/BC & emission for future year emissions: Gao et al., 2013, JGR
Aerosol module uses ae6nvPOA to fit the inputs from CAM-Chem