## Slide 1
Karen E. Cady-Pereira1 , Mark W. Shephard2, Shailesh K. Kharol2, Enrico Dammers2, Cynthia Whaley2, Cristen Adams2, Jesse Thompson2 , Nolan Dickson2, Ed Hare2, Matt Alvarado1 and Chantelle Lonsdale1
CrIS Observations of Ammonia: Retrievals, Validation and Spatiotemporal Variability
1Atmospheric and Environmental Research (AER), Lexington, Massachusetts, USA
2 Environment and Climate Change Canada (ECCC), Toronto, Ontario, Canada
Forest Fires Sources
Agricultural Sources

## Slide 2
Why are we interested in measuring ammonia (NH3)?
Mostly Agricultural Emissions in Canada
Air, Soil, and Water Quality
  Ammonia is listed as a Criteria Air Contaminant (CAC) as it is a main precursor to the secondary production of fine particulate matter (PM2.5); a key contributor to smog
    PM2.5 associated with increased risk of cardiovascular and respiratory diseases
      Input into the Air Quality Health Index (AQHI)
  Ammonia is one of the most important reactive nitrogen species
    Reactive nitrogen deposition from ammonia leads to soil acidification and water eutrophication (e.g. algal blooms)
    Ammonia (ammonium) is the least well known part of the nitrogen cycle
      Ammonia + Acidic Species (i.e. nitric and sulphuric acid from NOx and SOx) = PM2.5
PM2.5
Soil Acidification
Water Eutrophication

## Slide 3
RPC Emission Scenarios
Why are we interested in measuring ammonia (NH3)?
Ammonia (NH3) is the only PM2.5 precursor that is both currently increasing and expected to continue to increase in the future
ECCC’s National Pollutant Release Inventory (NPRI)
Mostly Agricultural Emissions in Canada
Global (NH3) emissions are forecast to increase:
  Demand for more and better food in developing countries
    More livestock production
    Greater use of fertilizer
SOx, NOX in general have been decreasing due to increased emission controls
  Catalytic converters on vehicles (NOx)
  Scrubbers installed in power plant stacks (SOx)
2.5
2.0
1.5
1.0
0.5
0
Emissions (Tg/yr)
Canada-USA Transboundary Particulate Matter Science Assessment, 2013

## Slide 4
Cross-Track Infrared Sounder (CrIS)
  Launched in fall 2011 on S-NPP
  Also now flying on JPSS1: three more to follow through 2038
  Spatial Resolution = 14 km (diameter)
  ~1:30 and 13:30 overpass: ideal for NH3
  Global spatial coverage
  Spectral Resolution (cm-1) @ 970 cm-1 = 0.625
  Excellent noise
    NEdT ~0.05K at 270K
    ~4x better noise than similar sensors
  TES-like sensitivity with IASI/AIRS-like spatial coverage

## Slide 5: CrIS Fast Physical Retrieval (CFPR) Algorithm for NH3
Observations
CrIS Obs
CrIS Obs
No NH3
NH3
H2O
O3
Observation – Forward Model Calculations
Observations
CrIS Obs
No NH3
Initial Guess
NH3
H2O
O3
Observation – Forward Model Calculations
Observations
CrIS Obs
No NH3
Initial Guess
Retrieval
NH3
H2O
O3
Observation – Forward Model Calculations
Observations
For more details see: Shephard M.W. and K. E. Cady-Pereira, AMT, 2015
  developed in collaboration between Canada (ECCC) and USA (AER)
  TES heritage
  optimal estimation (Rodgers, 2000) implemented in IDL
  OSS as forward model
Detectability is ~ 0.25 ppbv under ideal conditions
Thermal contrast plays an important role
Thermal Contrast: Surface- Air Temperature
NH3 Signal vs TCON

## Slide 6: CrIS Fast Physical Retrieval (CFPR) for NH3
CrIS most sensitive to NH3 between 950 and 700 mb (~0.5 to 3 km)
Sensitivity varies from profile-to-profile
Surface retrieved values are driven by sensitivity in boundary layer
~1 piece of information:
  DOFS~1
For more details see: Shephard M.W. and K. E. Cady-Pereira, AMT, 2015

## Slide 7: How do CrIS NH3 retrievals compare with other measurements?
CrIS: an instantaneous profile over a footprint at least 14 km in diameter
Most ground measurements: point data at the surface
  Often a bi-weekly average:
    Ammonia Monitoring Network (AMoN)
    Canadian Air and Precipitation Monitoring Network (CAPMoN)
Ground-based Fourier Transform InfraRed (FTIR)
  Profile and total column measurements
  Instantaneous cloud-free sampling (middle of the day)
Aircraft: profiles of point data
  DISCOVER-AQ campaigns in California and Colorado
All measurements come with large uncertainties:
  NH3 is sticky, highly reactive and has high spatial and temporal variability validation is not straightforward

## Slide 8: Validation: Uncertainty in aircraft profiles
Sample profiles from the California DISCOVER AQ campaign January-February 2013
Picarro slow response leads to hysteresis:
  Overestimates on ascent and underestimate on descent
PTR-ToF-MS signal is very noisy

## Slide 9: Surface NH3 from CrIS and the AMoN Network
Initial assessment shows that the satellite and AMoN surface obs agree well despite sampling differences
Correlation of 0.76
Mean difference of +0.4 ppbv (~+15%)
Shailesh Kharol et al., in preparation, 2018

## Slide 10: CrIS and ground-based FTIR
Total column comparisons with ground-based Fourier Transform InfraRed (FTIR) obs. at several locations globally
  Bremen, Germany; Toronto Canada; Boulder USA, Pasadena USA, Wollongong, Australia; Lauder, New Zealand, Mexico City, Mexico
Results look good with mean relative column differences of ~0 to -5% for the medium to large values
  CrIS shows slight overestimate of smaller values
Enrico Dammers et al., Validation of the CrIS fast physical NH3 retrieval with ground-based FTIR, Atmos. Meas. Tech., 10, 2645-2667, https://doi.org/10.5194/amt-10-2645-2017, 2017.
Satellite
FTIR

## Slide 11: CrIS during DISCOVER-AQ California 2013
Jan 30 NASA P3B flight
What does NOT applying the instrument operator tell you?

## Slide 12: Surface NH3 during SENEX Campaign
CrIS
CMAQ
CMAQ – NOAA P3 3
CrIS and aircraft data both indicate that CMAQ is overestimating NH3

## Slide 13
NH3 Dry Deposition
Flux at Surface
Satellite derived dry deposition flux of nitrogen from ammonia (NH3)
F = - Vd x C
Surface Concentration of NH3 (from CrIS Satellite)
Deposition Velocity (from Big-Leaf model (BLM);
(Leiming Zhang et al., 2003 (ACP))
Meteorological Data
(GEM Model)
CrIS (NASA/NOAA)
(Shephard & Cady-Pereira, 2015 (AMT))
Applying an approach similar to Caroline Nowlan, Randall Martin, et. al, (2014) used for NO2 and SO2

## Slide 14
Mostly NH3
Mostly NO2
Ratio of N dry deposition flux over North America
NO2 dry deposition flux hot-spots dominates in urban regions and power plants (e.g. North-East).
NH3 dry deposition flux dominates mostly in agricultural and remote regions (e.g. Mid-West)
Decreasing trends in NO2 emissions +increasing trends in NH3
NH3 dominates Nr dry deposition over most regions.
Ratio = NO2 Flux / (NO2 + NH3) Flux

## Slide 15
NH3 Emissions from Wildfires Fort McMurray : May 2016
Canada’s wildfire smoke model
16 May 2016
MODIS - Aqua
CrIS – NH3
Adams et al., in preparation, 2018
Total NH3 Emissions from Fort McMurray Wildfires
M = mass of NH3 (from CrIS)
𝛕 = NH3 lifetime
tc = time in box = f(wind speed, box size)

## Slide 16: Large Scale Inversion for Emissions
2013 May Total Column NH3
CrIS
GEOS-Chem

## Slide 17
Seasonal Cycle over India in 2014
Jan
Apr
Jul
Oct

## Slide 18
Where to get the data?
NASA is implementing an all FORTRAN version (ESSPA)
Global operational product will become available in 2019
CrIS NH3 from the CFPR algorithm
  over North America from 2013 through 2017
  available from Environment Canada
Contact Mark Shephard:
  mark.shephard@Canada.ca

## Slide 19
  Captures expected temporal and spatial distributions of ammonia
      Spring fertilizer applications (May over Canada)
      Episodic events (e.g. Northern forest fires in middle of summer)
Monthly Spatiotemporal Variability of Surface NH3 over North America in 2013
(Click here to view movie)
ppbv

## Slide 20
From each observation:
Radiances
Noise estimate
First guess emissivity from
University of Wisconsin database
From previous retrievals (CLIMCAPS):
Water vapor profiles
Temperature profiles
Surface temperature
Optimal estimation first step
Refinements of
  Surface temperature
  Emissivity
Optimal estimation second step
NH3 profiles
Error estimates
Averaging kernels
For more details see: Shephard M.W. and K. E. Cady-Pereira, AMT, 2015
Operational algorithm currently under implementation at the SNPP SIPS
ESSPA software: FORTRAN retrieval code with OSS as forward model
Optimal estimation: same a priori profiles/constraints/selection as CFPR
Use radiances for
a priori selection from three possible profiles
Cloud screening

## Slide 21: Satellite Validation: Ground-based FTIR profiles
Profile comparisons done by applying the FTIR instrument operator
CrIS
CrIS-FTIR
FTIR AVK