## Slide 1: Quantification of Lightning NOX and its Impact on Air Quality over the Contiguous United States
Office of Research and Development
Computational Exposure Division, National Exposure Research Laboratory
Daiwen Kang, Rohit Mathur, Limei Ran, Gorge Pouliot, David Wong, Kristen Foley, Wyat Appel, and Shawn Roselle
Computational Exposure Division, National Exposure Research Laboratory, U.S. Environmental Protection Agency,
Research Triangle Park, NC 27711, USA
17th Annual CMAS Conference, Chapel Hill, NC
October 24, 2018

## Slide 2: Facts on Lightning-induced NO Emissions
Lightning is a major atmospheric source of NOX (NO + NO2; NO is produced initially, but quickly oxidized into NO2 in the atmosphere)
Global lightning NOX (LNOX) production is ~2-8 Tg N yr-1 (~10-15% of the total NOX budget)
Lightning activity varies spatially and seasonally, which affects NO emissions.
Most lightning-induced NO enters upper troposphere; can affect surface AQ through mixing.

## Slide 3: Lightning NO Production in CMAQ
Starting with CMAQv5.2, lightning NO production is driven by hourly National Lightning Detection Network (NLDN) lightning flash data.
The NO yield is 350 moles/flash.
Vertical distribution of lightning NO is the same as in previous CMAQ versions.

## Slide 4: Model configuration and simulations
Modeling System (WRF3.8 and CMAQ5.2) with WRF lightning assimilation (Heath et al., 2016, J. Adv. Model. Earth Syst.) as the met input.
Domain: 12km horizontal resolution with 35 vertical layers over the contiguous United States.
Boundary conditions: hemispheric CMAQ simulations
Simulation period: April-September, 2011
Emissions: 2011 NEI, NH3 bidi, inline biogenic emissions
Without lightning NO (Base) and with lightning NO (NLDN)

## Slide 5
Edgewood, MD
Beltsville, MD
Wallops Island, VA
Analysis Regions and O3 Sonde Locations
Huntsville, AL
Boulder, CO

## Slide 6
NOX Emissions and LNOx Ratios in July, 2011
a. Anthropogenic NOX
b. LNOX
d. Ratio of LNOX to total NOX emissions
%
c. Soil NO

## Slide 7
Chart: LNOX Ratio (%)
| April | May | June | July | August | September
Domain | 12.28 | 11.67 | 18.78 | 22.08 | 21.09 | 9.53
NE | 3.3714 | 5.1783 | 11.1029 | 9.9472 | 10.2761 | 5.226
SE | 15.5235 | 11.2859 | 24.863 | 26.401 | 24.9655 | 13.7291
UM | 9.9875 | 11.5973 | 20.712 | 22.5173 | 15.7552 | 5.0697
LM | 15.2612 | 12.9622 | 12.0348 | 12.7703 | 17.1458 | 10.5002
RM | 1.8788 | 8.255 | 17.4481 | 29.8885 | 28.1659 | 9.6889
PC | 0.064435 | 0.97932 | 0.89765 | 2.5855 | 1.9855 | 2.6716
Regions
LNOX Contribution to the Total NOX Emissions by Month and Region

## Slide 8
Chart: Southeast
Chart: Rocky Mountains
Daily LNOX contribution to the total NOX emissions
Ratio of LNOX to Total NOX (%)

## Slide 9
Km-2
Lightning Flash Rate (daily sum)
surface maximum hourly O3 change (NLDN-Base)
Lightning Flashes and Surface O3 Change
(NLDN-Base) on July 11, 2011
The maximum change of hourly O3 mixing ratios ranges mostly from 6 ppbv to 30 ppbv in the regions of lightning strikes. Even though the most lightning flashes occurred in the Upper Midwest region, the corresponding changes in O3 are not as significant, because the change of O3 at a location depends not only on the intensity of lightning strikes, but also on the timing of the strikes and the relative contribution of LNOX to the total NOX emissions.

## Slide 10
Monthly Mean Error Difference (NLDN-Base) of DM8HR O3 for July 2011
Significant error reduction over the mountain states and northeast coastal regions
Slight error increase over the southeast region and California
Over the domain, more error reductions than increases
9

## Slide 11
Time series of DM8HR O3 and MB Difference
In SE, LNOX makes the overprediction slightly worse in July and August.
In RM, the underprediction is consistently reduced on all the days in July and August.
SE
RM
SE
RM

## Slide 12
Diurnal Profiles of Hourly O3
SE
RM
Domain
Lightning NO has minimal impact on the domain-wide mean diurnal profile, while differing impacts on different regions: slight increase in SE and significant increase in RM. Other regions (not shown here): decrease in NE, UM, and PC (especially during daytime hours), and increase in LM with model overprediction in all these regions.

## Slide 13
Altitude (km)
0 2 4 6 8 10
O3 mixing ratios aloft are consistently increased and brought closer to the observations by LNOX.
Sonde
Base
NLDN
Altitude (km)
0 2 4 6 8 10
Altitude (km)
0 2 4 6 8 10
Beltsville, MD
Edgewood, MD
Wallops, VA
40 60 80 100 120 140
O3 Mixing Ratio (ppb)
40 60 80 100 120 140
O3 Mixing Ratio (ppb)
40 60 80 100 120
O3 Mixing Ratio (ppb)
Vertical profiles of hourly O3: Modeled vs. Observed (Average of Multiple Launches)

## Slide 14
Boulder, CO
Huntsville, AL
Altitude (km)
0 2 4 6 8 10 12
Altitude (km)
0 2 4 6 8 10
40 60 80 100 120 140
O3 Mixing Ratio (ppb)
40 60 80 100 120
O3 Mixing Ratio (ppb)
Sonde
Base
NLDN
Vertical profiles of hourly O3: Modeled vs. Observed (Average of Multiple Launches)

## Slide 15
Overlay of the measured O3 by aircraft (P3B) during the DISCOVER-AQ campaign on July 28, 2011
Base
NLDN
Altitude (km)
0 1 2 3 4 5
Altitude (km)
0 1 2 3 4 5
40 45 50 55 60 65 70 75 80 85 90
O3 Mixing Ratio (ppb)
40 45 50 55 60 65 70 75 80 85 90
O3 Mixing Ratio (ppb)
Increase aloft to reduce the underprediction
Decrease near the surface to alleviate the overprediction

## Slide 16
< 0 0.02 0.04 0.06 0.08 0.1 1.2 1.4 1.6 1.8 2 <
Altitude (km)
0 5 10 15
NO
NO (ppb)
< 0 0.02 0.04 0.06 0.08 0.1 1.2 1.4 1.6 1.8 2 <
Altitude (km)
0 5 10 15
NOx
NOx (ppb)
<-5 -2 0 2 4 6 8 10 15 20 30 <
Altitude (km)
0 5 10 15
O3
O3 (ppb)
Difference of vertical cross-section along the P3B path
Majority of LNOx is injected in the middle to upper troposphere (above 6 km) with small amounts being put near the surface.
O3 is significantly enhanced aloft, but reduced near the surface.

## Slide 17: Summary
The contribution of LNOX emissions to the total NOX emissions ranges from 10% (September) to 22% (July) over the contiguous US.
Averaged over the six-month period (April - September), SE has the largest LNOX ratios (19.5%) followed by RM (16%).
During July and August, the largest LNOX ratios are observed for the RM region (30% and 28%, respectively).

## Slide 18: Summary
CMAQv5.2 contains a LNOx algorithm that uses observed lightning flashes along with an assumed NOx production per flash and a scheme to distribute the NOx vertically.
CMAQ simulation for summer 2011 shows that the addition of LNOx emissions reduces the daily CMAQ low bias for DM8HR O3 by as much as 5 ppbv in the RM region.
Comparisons with surface observations show no improvement with LNOx where surface O3 is already overpredicted. However, vertical structure is improved with LNOx at all sites, especially aloft.
*The main content of this presentation will appear in the A&WMA’s EM magazine next month (November, 2018)

## Slide 19: Disclaimer
The views expressed in this presentation are those of the authors and do not necessarily reflect the views or policies of the U.S. EPA

## Slide 20
Additional Plots

## Slide 21
Lightning Strikes and Surface O3 Change (NLDN-Base) on July 11
Lightning Flash Rate (km-2)
Layer 1 O3[NLDN] – O3[Base]

## Slide 22
LNOX ratios on July 11, 2011

## Slide 23
Diurnal Profiles for other regions

## Slide 24
Daily Mean NOX Time Series in July, 2011