## Slide 1: Modeled Ammonia Nitrogen Deposition Source Apportionment at Rocky Mountain National Park for RoMANS2
Mike Barna1
Marco Rodriguez2
Kristi Gebhart1
Bret Schichtel1
Bill Malm3
1 NPS, Fort Collins, CO
2 AECOM, Fort Collins, CO
3 CIRA, Fort Collins, CO
CMAS Annual Meeting
UNC-Chapel Hill
October 15-17, 2012

## Slide 2: Nitrogen deposition at Rocky Mt NP
http://www.nature.nps.gov/air/Pubs/pdf/rmnp-trends/rmnp-trends_2010.pdf
Nitrogen deposition and ecosystem change has been extensively studied at RMNP
  NADP and CASTNet
  RoMANS (2006)
  RoMANS2 (2009)
‘resource management goal’ of 1.5 kg/ha/yr
Notes: 2

## Slide 3: N dep ‘glide path’ at Rocky Mountain NP
Specified as NADP wet deposited nitrogen
Notes: 3

## Slide 4: What is the total N deposition at RMNP?
NADP and CASTNet are invaluable resources for investigating trends and patterns in nitrogen deposition, but can’t answer everything
Limitations inherent in monitoring:
  Not all species of interest are accounted
  Dry deposition not a true flux measurement
  Spatial and temporal resolution
Use chemical transport models to fill in gaps
  Estimate deposition in unmonitored areas
  Round-out the ‘total N deposition’ budget
Notes: 4

## Slide 5: ‘Missing’ (read: unmonitored) nitrogen
Reduced organic nitrogen gases
  Ammonia, amines
‘Nighttime’ nitrogen
  N2O5, nitrate radical
Gas-phase organic nitrates
  PAN, isoprene nitrate
Particle-phase organic nitrates
  High uncertainty, maybe important (Lin et al., 2010)
Notes: 5

## Slide 6: Simulated HNO3 and NH3 dry dep
HNO3
NH3
Nitric acid is monitored by CASTNet, but ammonia obs are rare
Notes: 6

## Slide 7: Simulated ‘total’ N dry dep at ROMO
Notes: 7

## Slide 8: Observed & predicted N at RMNP
Reduced N:
NH3
NH4+
Oxidized N:
HNO3
NO3-
Ammonia predictions are too low
Notes: 8

## Slide 9
Colorado Romans2 NH3 emissions
Colorado Totals | NH3 (tons/yr)
Area | 76
Onroad | 4,484
Nonroad | 49
Point | 526
Fires | 2,152
Livestock | 54,078
Fertilizer | 14,527
Wild Animals | 5,626
Domestic | 2,099
Oil & Gas | 350
Biogenic | 0
Windblown Dust | 0
Total Colorado | 83,967

## Slide 10
Romans2 Colorado NH3 emissions
Livestock Numbers
(Adelman and Omary, 2011)
Spatially redistribute county-wide NH3 CAFO emissions relative to CAFO size using Jay Ham’s (CSU) inventory
RMNP

## Slide 11: Use a ‘top down’ approach for NH3 EI?
Clarisse et al., 2009, Nature Geoscience
IASI – Infrared Atmospheric Sounding Interferometer
“good qualitative agreement”
“emissions significantly underestimated in northern hemisphere”
Notes: 11

## Slide 12: NH3 regions: which impact RMNP?
865
867
864
862
861
857
853
852
845
844
842
834
855
858
860
859
856
001
002
778
820/003
819
821
866
851
Use CAMx PSAT with ~20 source regions:
Notes: 12

## Slide 13: NH3 impacts by region: January
January
Model Mean = 0.018 ug/m3
Model Max = 0.057 ug/m3
Notes: 13

## Slide 14: NH3 impacts by region: July
July
Model Mean = 0.200 ug/m3
Model Max = 1.865 ug/m3
Notes: 14

## Slide 15: Apportionment depends on location
Annual NH3 Source Apportionment receptor transect
820
821
819
Notes: 15

## Slide 16: Summary
A variety of local and non-local sources are contributing to ammonia at RMNP
  Boundary conditions in winter (lower NH3)
  California, Snake River Valley, Front Range, others, in summer (higher NH3)
  Results are easily influenced by transport, i.e., not getting easterly flow to RMNP
Model inter-comparison would be nice
  Influence of bi-directional flux
  Estimation of dry deposition velocities
Notes: 16

## Slide 17: Summary (continued)
What is the role of unmonitored N?
  Ammonia
  Gas-phase reduced organic N
  Gas-phase organic nitrates
  Particle organic nitrates
  N2O5 and NO3 radical
Accounting for ‘missing’ nitrogen can almost double the estimated dry deposition at RMNP (1.2 vs 2.2 kg/ha/yr).
Notes: 17

## Slide 18: Acknowledgements
Zac Adelman and Mohammad Omary (UNC-Chapel Hill)
Jay Ham (Colorado State U.)
Jeff Collett, Jr (Colorado State U.)
Notes: 18