## Slide 1: Impact of MOVES2014 on Emission Inventories from On-road Mobile Sources
Alexis Zubrow, Darrell Sonntag, Harvey Michaels, David Brzezinski, Alison Eyth

## Slide 2: MOVES2014
EPA’s mobile emission model
  Used for State Implementation Plan and Transportation Conformity Analysis
Replaces the MOVES2010 series
Estimates emissions and energy use from all on-road sources at the national, county, and project scales
Contains the impacts of recent regulations:
  Light-duty and Heavy-duty Greenhouse Gas and Fuel Economy Standards
  Tier 3 Vehicle Emissions and Fuel Standards Program
    (emission standards and sulfur content in gasoline)
Contains new emissions and activity data for on-road vehicles
Adds nonroad emission capabilities through the incorporation of NONROAD2008

## Slide 3: New Emission Test Programs & Data
Fuel Effects
  EPAct study on Gasoline fuel effects (funded by DOE, CRC and EPA)
  Effects of E85 on emissions
  EPA In-Use Sulfur Test Program
  Updated renewable fuel usage and future fuel supply
Evaporative Emissions
  Ethanol, RVP, leak magnitude study
  High Evap Field Study – leak frequency
  Running loss vapor leak study
  Multiday Diurnal Testing
PM Emissions
  Speciation of Kansas City light-duty gasoline study
  New PM Speciation profiles for diesel and CNG from literature
Temperature Effects
  EPA Cold Temperature Study
Heavy Duty
  In-Use Compliance Program emissions data
  Literature review of CNG Transit bus emissions
Population and Activity
  R.L. Polk Vehicle Population for 2011
  Updated Vehicle Sales Projections
  Updated FHWA VMT estimates
  Updated Flex-fuel vehicle penetrations
  National average speed distribution using GPS data
  Updated truck weights based on Weigh-in-Motion data
Notes: Note for Alexis: These are just some of the major updates. We had many more updates, which make it difficult to attribute changes to which update.

## Slide 4: Air Quality Modeling using MOVES2014
Chemical Transport Model
MOVES
VOC and PM2.5 emission rates by model year, fuel type, regulatory class, emission process
SPECIATE
PM2.5 and VOC Speciation Profiles
SMOKE
Prepares emissions in gridded, hourly form needed for Chemical Transport Model
Speciation incorporated into MOVES2014
  Formerly conducted within SMOKE through COMBO files
MOVES2014 estimates
  CB05 mechanism species
  18 PM2.5 species needed for CMAQv5 Aerosol Module Version 6 and CAMx5.4
Allows differentiation in VOC and PM speciation profiles by:
  Technology/Regulatory class
    (e.g. light-duty/heavy-duty)
  Model year
    (e.g. pre-2007/2007+ diesel)
  Fuel Type
    (gasoline, E85, diesel, CNG)
  Emission process
    (e.g. running, start, extended idle, evaporative)
Plan to update supported mechanisms to include CB6 and other mechanisms
Notes: MOVES produces 55 toxics, EC, sulfate makes 57 unique species
      i.e. account for mix of pre- and post-2007 diesel
    No model year distinction, fuel distinction, emission process distinction in SCC
    Custom weighted speciation profiles need to be applied for each calendar year

## Slide 5: 3-city comparisons
State-supplied National Emission Inventory (NEI) inputs for 3 urban counties
  Unique fleet mix, fuels, temperatures, age distributions, inspection & maintenance programs, average speed distributions, road types, etc.
Projections to 2030 using national default growth assumptions
Consistent inputs were developed for both MOVES2010b and MOVES2014
  Note: certain fleet characteristics are different between the models, e.g. fuel splits

## Slide 6: Highway-Source NOx
2011
  Reduced truck weights
  Updated gasoline fuel effects
2030
  Large changes due to emission and fuel regulations (Tier 3 and HD GHG reductions)
 | NOx
2011 | -21% to -5%
2030 | -57% to -53%
Relative change with MOVES2014

## Slide 7: Highway-Source VOC
 | VOC
2011 | -21% to -5%
2030 | -33% to -13%
2011
  Updates to evaporative and fuel effects for gasoline vehicles
2030
  Reductions in 2017+ vehicles (Tier 3 Low Sulfur rule)
  Increase in temperature sensitivity for newer gasoline vehicles (MY 2010+)
Relative change with MOVES2014

## Slide 8: Highway-Source PM2.5
2010
  PM running emissions less sensitive to temperature (lowers emissions esp. in cold weather
2030
  Tier 3 reductions
Relative change with MOVES2014
 | PM
2011 | -19% to -6%
2030 | -58% to -42%

## Slide 9: 3 State Comparison
Comparison of 2011 NEIv1 vs 2011 NEIv2 (draft) for 3 states
  GA, IA, MD
Cumulative impact from change in model from MOVES2010b to MOVES2014 AND changes in inputs
Using MOVES in emissions rate mode (SMOKE-MOVES)

## Slide 10: Updated Inputs
Inputs revised for 2011 NEIv2 (draft):
  Age distribution
    New default county specific age distribution for light duty vehicles (LDV), from CRC A-88
  Regional long-haul splits
    Changes split between short vs long-haul for the single unit (52, 53) and combination (61, 62) trucks, from CRC A-88
    Impacts hotelling
  Regional fuels
  Representative counties
    Previously 163 representative counties, now 284 within CONUS domain
    Revised age bins and added ramp fraction
    Includes state comments

## Slide 11: Updated Inputs (2)
Input changes (cont) :
  Hotelling
    Includes extended idle and auxiliary power units (APU)
    Distributed based on urban + rural restricted combination long-haul VMT (62)
    New type of run: rate-per-hour (RPH) that takes hotelling hours directly
    Limited number of states supplied hotelling hours
  Revised CDBs
    Some states supplied updated CDBs for 2011 NEIv2.
  Temporalization
    Incorporated monitoring data VTRIS with state submitted MOVES CDB data
  Spatial surrogates
  Meteorology

## Slide 12: 3 State
PM10 increasing across all states: change in brake and tire wear EF

## Slide 13: 3 State: Broad Vehicle
Shift in Iowa VMT from passenger -> trucks (primarily LDT) based on improved population inputs
Increase in Iowa diesel “All trucks and buses” emissions primarily from changes in hotelling (EXT and APU)
NOx
VMT

## Slide 14: Observations
With equivalent inputs, MOVES2014 estimates lower emissions in urban areas
Larger reductions typically observed for future years
  Due to projected impact of EPA regulations
Revised inputs can create greater changes in the emissions than changes to MOVES alone
  Shifts in vehicle distribution can have subtle impacts
  Setting up “equivalent” inputs is difficult for SMOKE-MOVES
    New source classification codes

## Slide 15: Next Steps
Compare results across more scenarios
Run AQ sensitivities
Compare SMOKE-MOVES for a change in MOVES alone with “consistent” inputs
Evaluate future year impacts

## Slide 16: Acknowledgments
EPA: Laurel Driver, Rich Cook, Chris Dresser, David Choi, Ted Maciag (SEE)
ERG: Allison DenBlyker, John Koupal, Scott Fincher
CSC: Chris Allen, James Beidler
UNC: BH Baek, Catherine Seppanen
MOVES MJO Workgroup

## Slide 17: Extra 3-City Slides

## Slide 18: 3-city comparisons
Consistent Input Data between MOVES2010b and MOVES2014
State-supplied data for the National Emission Inventory
  Base year (2011) Vehicle Miles Traveled and vehicle population
  Vehicle Age distribution (2011)
  Average speed distribution
  Road type distribution (e.g. urban vs. rural)
  Temporal VMT distribution (vehicle travel by hour of day, day of week, month of year)
  Inspection/Maintenance Program
Common Projections to 2030
  National VMT growth rates
  National vehicle population growth rates
  Modeled future changes to age distributions (based on 2011 state supplied age distributions)
MOVES default Data
  Meteorology data (same between runs)
  Fuel Formulation and Fuel Supply data from MOVES2014 (did not specify E85 fuel usage in 2010b)
Differences between runs
  Emission rates, fuel effects, temperature effects,
  “Internal default vehicle classifications in MOVES”
    Fuel Split (e.g. diesel, gasoline, CNG E85) by vehicle model year and vehicle type
    Mileage accumulation rates by vehicle classes
    Vehicle weights
  Default extended idle activity

## Slide 25: Differences in 3 State Inputs
Extended idle
  MOVES2010b used vehicle population (VPOP) of heavy-duty diesel vehicles (SCC7 2230074) to calculate extended idle emissions
  MOVES2014 uses hotelling hours directly to calculate extended idle emissions
SCCs
  MOVES2010b uses MOBILE6 based SCCs
  MOVES2014 uses codes more inline with MOVES IDs. No 1-1 mapping between 2 types of SCCs. To compare:
    Map fuels to all non-diesel or diesel
    Map source types to: motorcycles, passenger cars, all trucks and buses.
    Within “all trucks and buses”, MOVES2014 has a different composition of the fleet

## Slide 26: Differences in 3 State Inputs (cont.)
Activity data
  No clean mapping between SCCs -> difficult to match VMT and VPOP exactly between two runs
  Equivalent at the aggregate level (e.g. All trucks and buses)
  Distribution within fuels and within source type may be different in the two runs